| Transmitted by the expert from Japan | Informal document No. GRSP-48-29 (48th GRSP, 7 - 10 December 2010, agenda item 22(d)) |
| --- | --- |

Proposal to amendment to ECE/TRANS/WP29/2010/145

(Revision of the Consolidated Resolution on the Construction of Vehicles (R.E.3))

Note: The modifications to ECE/TRANS/WP29/2010/145 are marked in bold and strikethrough characters.

- PROPOSAL

Paragraph 2.2.4.4. and Paragraph 2.2.4.5., amend to read:

2.2.4.4. 	Class A: Vehicles designed to carry standing passengers; a vehicle of this class has seats and may have provision for standing passengers and having a capacity not exceeding 22 passengers in addition to the driver.

2.2.4.5.	 Class B: Vehicles not designed to carry standing and having a capacity not exceeding 22 passengers in addition to the driver.

- JUSTIFICATION

With regard to Class A vehicles and Class B vehicles, the restriction of passengers is described in Regulation No.52 (UNIFORM PROVISIONS CONCERNING THE APPROVAL OF M2 AND M3 SMALL CAPACITY VEHICLES WITH REGARD TO THEIR GENERAL CONSTRUCTION).

R.E.3 should be harmonized with Regulation No.52.

(Reference Regulation No.52)

  - "Vehicle" means a single-deck vehicle of category M2 or M3 1/ designed and constructed for the carriage       of seated, or seated and standing persons and having a capacity not exceeding 22 passengers in addition to the driver. There are two classes of vehicles:

2.1.1.	Class A: Vehicles designed to carry standing passengers; a vehicle of this class has seats and may have provision for standing passengers.

2.1.2.	Class B: Vehicles not designed to carry standing passengers; a vehicle of this class has no provisions for standing passengers.