|  | United Nations | ECE/TRANS/WP.15/AC.2/2011/21 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 31 May 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the
European Agreement concerning the International Carriage
of Dangerous Goods by Inland Waterways (ADN)
(ADN Safety Committee)

Nineteenth session

Geneva, 22-25 August 2011

Item 4 of the provisional agenda

Proposals for amendments to the Regulations annexed to ADN

5.4.1.1.2

Transmitted by the Government of Belgium

Introduction

1.	The text of 5.4.1.1.2 (c) states that the data in column (5) of Table C of Chapter 3.2 should be contained in the transport document. For substances assigned to some generic entries (e.g. UN 1202) or a N.O.S. entry these data may typically be N1, N2, N3, CMR, F or S. The filler and the carrier, however, need the real data for the specific product to be able to use the flowchart.

2.	Therefore 5.4.1.1.2 (c) should contain a clarification about the data required in the transport document in the case of transport of products assigned to such group entries.

Proposal

3.	Add the following text to 5.4.1.1.2 (c):

"For substances not mentioned by name in Table C (assigned to a generic entry or a N.O.S. entry) only the actual dangerous properties of the substance shall be mentioned."

# Footnotes

Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/2011/21.

In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106; ECE/TRANS/2010/8, programme activity 02.7 (b)).