|  | INF.3 |
| --- | --- |
| Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Joint Meeting of Experts on the Regulations annexed to the European Agreement concerning the International Carriage of Dangerous Goods by Inland Waterways (ADN) (ADN Safety Committee) Eighteenth session Geneva, 24–27 January 2011 Item 4 of the provisional agenda Proposals for amendments to the Regulations annexed to ADN | 20 December 2010 |

3.2.3 Table C

Transmitted by the Government of Germany

Introduction

1.	At the 17th meeting of the Safety Committee, held from 23-26 August 2010, document WP.15/AC.2/17/INF.6 was presented. It describes the results of the informal working group on ‘Substances’ when it revised Table C at its 2nd session. After the discussion of this document the Safety Committee asked for a formal proposal for amendments for its 18th session (see report of the 17th session of the Safety Committee, ECE/TRANS/WP.15/AC.2/36 paras. 51-56).

Proposal

2.	Based on the results of the informal working group on ‘Substances’ the proposal is intended to amend Table C as listed under item 5. The amendments are based on ADN 2009 including the corrigendum (ECE/TRANS/203, Vol. I and II and ECE/TRANS/203/Corr.1) as well as on the draft amendments to the Regulations annexed to ADN including the two corrigenda (ECE/ADN/9, ECE/ADN/9/Corr.1 and ECE/ADN/9/Corr.2). Any remarks and comments received to date were also taken into account.

3.	In addition, it is further proposed to include a new remark 40 under 3.2.3 of the explanations of Table C, column 20, as prepared by the informal working group on ‘Substances’. This new remark 40 reads:

"This substance may contain over 0.1% carcinogenic substances. In this case "+CMR’ has to be entered into column 5." It is to be allocated to the entries for UN 1011 BUTANE and UN 1969 ISOBUTANE."

The informal working group on ‘Substances’ will explain its proposal verbally.

| UN No. or substance identification No. | Name and description | Class | Classification code | Packing group | Dangers | Type of tank vessel | Cargo tank design | Cargo tank type | Cargo tank equipment | Opening pressure of the high-velocity vent valve in kPa | Maximum degree of filling in % | Relative density at 20 °C | Type of sampling device | Pump room below deck permitted | Temperature class | Explosion group | Anti-explosion protection required | Equipment required | Number of cones/blue lights | Additional requirements/Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 1010 | 1,3-BUTADIENE, STABILIZED | 2 | 2F |  | 2.1+unst.+ CMR | G | 1 | 1 |  |  | 91 |  | 1 | No | T2 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 2; 3; 31 |
| 1010 | BUTADIENE STABILIZED or BUTADIENES AND HYDROCARBON MIXTURE, STABILIZED, having a vapour pressure at 70 °C not exceeding 1.1 MPa (11 bar) and a density at 50 °C not lower than 0.525 kg/l | 2 | 2F |  | 2.1+unst. | G | 1 | 1 |  |  | 91 |  | 1 | No | T2 | II B II B4) | yes | PP, EX, A | 1 | 2; 3; 31 |
| 1011 | BUTANE | 2 | 2F |  | 2.1+CMR 2.1+(CMR) | G | 1 | 1 |  |  | 91 |  | 1 | No | T2 | II A | yes | PP, EX, A | 1 | 31; 99 31; 40 |
| 1040 | ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1 MPa (10 bar) at 50 °C | 2 | 2TF |  | 2.3+2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes no | T2 | II B | yes | PP, EP, EX, TOX, A | 2 | 2: 3; 11; 31 |
| 1127 | CHLOROBUTANES (2-CHLOROBUTANE) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.87 | 2 | yes | T4 3) T3 | II A | yes | PP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (1-CHLORO-2-METHYLPROPANE) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.88 | 2 | yes | T4 3) T3 | II A | yes | PP, EX, A | 1 | 23 |
| 1135 | ETHYLENE CHLOROHYDRIN (2-CHLOROETHANOL) | 6.1 | TF1 | I | 6.1+3 6.1+3+N3 | C | 2 | 2 |  | 30 | 95 | 1.21 | 1 | no | T2 | II A 8) | yes | PP, EP, EX, TOX, A | 2 |  |
| 1153 | ETHYLENE GLYCOL DIETHYL ETHER | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.84 | 3 | yes | T4 3) T4 | II B4) II A 7) | yes | PP, EX, A | 0 |  |
| 1157 | DIISOBUTYL KETONE | 3 | F1 | III | 3+N3+F | N | 3 | 3 |  |  | 97 | 0.81 | 3 | yes | T4 3) T2 | II B4) | yes | PP, EX, A | 0 |  |
| 1160 | DIMETHYLAMINE AQUEOUS SOLUTION | 3 | FC | II | 3+8 3+8+N3 | C | 2 | 2 | 3 | 50 | 95 | 0.82 | 2 | yes | T2 | II B4) II A | yes | PP, EP, EX, A | 1 | 23 |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | TFC | I | 6.1+3+8+ N2+CMR | C | 2 | 2 | 3 | 50 | 95 | 0.78 | 1 | no | T3 | II B4) II C | yes | PP, EP, EX, TOX, A | 2 | 23 |
| 1167 | DIVINYL ETHER, STABILIZED | 3 | F1 | I | 3+unst. | C | 1 | 1 |  |  | 95 | 0.77 | 1 | yes | T2 | II B7) II B | yes | PP, EX, A | 1 | 2; 3 |
| 1171 | ETHYLENE GLYCOL MONOETHYL ETHER | 3 | F1 | III | 3+CMR | N | 2 | 3 | 3 | 10 | 97 | 0.93 | 3 | yes | T3 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 1172 | ETHYLENE GLYCOL MONOETHYL ETHER ACETATE | 3 | F1 | III | 3+N3+ CMR | N | 2 | 3 | 3 | 10 | 97 | 0.98 | 3 | yes | T2 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 1175 | ETHYLBENZENE | 3 | F1 | II | 3+N3 | N | 2 | 2 |  | 10 | 97 | 0.87 | 3 | yes | T2 | II B II A | yes | PP, EX, A | 1 |  |
| 1177 | 2-ETHYLBUTYL ACETATE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.88 | 3 | yes | T3 | II A II A7) | yes | PP, EX, A | 0 |  |
| 1179 | ETHYL BUTYL ETHER (ETHYL tert-BUTYL ETHER) | 3 | F1 | II | 3+N3 | N | 2 | 2 |  | 10 | 97 | 0.74 | 3 | yes | T2 | II B II B4) | yes | PP, EX, A | 1 |  |
| 1188 | ETHYLENE GLYCOL MONOMETHYL ETHER | 3 | F1 | III | 3+CMR | N | 2 | 3 | 3 | 10 | 97 | 0.97 | 3 | yes | T3 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 1191 | OCTYL ALDEHYDES (2-ETHYLCAPRONALDEHYDE) | 3 | F1 | III | 3+F 3+N3+F | C | 2 | 2 |  | 30 | 95 | 0.82 | 2 | yes | T4 | II A II A7) | yes | PP, EX, A | 0 |  |
| 1202 | GAS OIL or DIESEL FUEL or HEATING OIL (LIGHT) (flash-point not more than 60 °C) | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * | < 0,85 | * | yes |  |  | no | PP * | 0 | *see flowchart |
| 1202 | GAS OIL or DIESEL FUEL or HEATING OIL (LIGHT) (flash-point more than 60 °C but not more than 100 °C) | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * | < 1,1 | * | yes |  |  | no | PP * | 0 | *see flowchart |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL | 3 | F1 | II | 3+N2+CMR+F | N | 2 | 3 | 3 | 10 | 97 | 0,68 - 0,72 10) | 3 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 |  |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL, WITH MORE THAN 10 % BENZENE BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR+F 3+N2+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL WITH MORE THAN 10 % BENZENE 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR+F 3+N2+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL WITH MORE THAN 10 % BENZENE 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR+F 3+N2+CMR+F | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL WITH MORE THAN 10 % BENZENE BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR+F 3+N2+CMR+F | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1208 | HEXANES (n- HEXANE) | 3 | F1 | II | 3+N1 3+N2 | C N | 2 | 2 3 | 3 | 50 | 95 97 | 0.66 | 2 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1214 | ISOBUTYLAMINE | 3 | FC | II | 3+8 3+8+N3 | C | 2 | 2 | 3 | 50 | 95 | 0.73 | 2 | yes | T2 | II A II A7) | yes | PP, EP, EX, A | 1 | 23 |
| 1218 | ISOPRENE, STABILIZED | 3 | F1 | I | 3+unst.+N2+ CMR | N | 1 | 1 |  |  | 95 | 0.68 | 1 | yes | T3 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 2; 3; 5;16 |
| 1220 | ISOPROPYLE ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.88 | 3 | yes | T2 | II A II A7) | yes | PP, EX, A | 1 |  |
| 1223 | KEROSENE | 3 | F1 | III | 3+N2+F | N | 3 | 3 |  |  | 97 | ≤ 0,83 | 3 | yes | T3 | II A II A7) | yes | PP, EX, A | 0 | 14 |
| 1224 | KETONES, LIQUID, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1224 | KETONES, LIQUID, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14; 27 *see flowchart |
| 1235 | METHYLAMINE, AQUEOUS SOLUTION | 3 | FC | II | 3+8 3+8+N3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 |  |
| 1247 | METHYL METHACRYLATE MONOMER, STABILIZED | 3 | F1 | II | 3+unst. 3+unst.+N3 | C | 2 | 2 |  | 40 | 95 | 0.94 | 1 | yes | T2 | II A | yes | PP, EX, A | 1 | 3; 5; 16 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 > 175 kPa | 3 | F1 | I | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | I | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | I | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 29; 38 |
| 1267 | PETROLEUM CRUDE OILWITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL | 3 | F1 | I | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 29; *see flowchart |
| 1267 | PETROLEUM CRUDE OIL | 3 | F1 | II | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 29; *see flowchart |
| 1267 | PETROLEUM CRUDE OIL | 3 | F1 | III | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14; *see flowchart |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 > 175 kPa | 3 | F1 | I | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60°C | 3 | F1 | I | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60°C | 3 | F1 | I | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60°C | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60°C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29; 38 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60°C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 | 0.765 | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 60°C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T 3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S, WITH MORE THAN 10 % BENZENE, vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10 % BENZENE or PETROLEUM PRODUCTS, N.O.S, WITH MORE THAN 10 % BENZENE, vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | II | 3+N2+CMR+F | N | 2 | 3 | 3 | 10 50 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES; N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) 110 kPa < vp50 ≤ 150 kPa | 3 | F1 | II | 3+N2+CMR+F | N | 2 | 3 | 3 | 10 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 14; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) vp50 ≤ 110 kPa | 3 | F1 | II | 3+N2+CMR+F | N | 2 | 3 |  | 10 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 14; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S, or PETROLEUM PRODUCTS, N.O.S. (BENZENE HEART CUT) vp50 ≤ 110 kPa | 3 | F1 | II | 3+N2+ CMR+F | N | 2 | 3 |  | 10 | 97 | 0.765 | 3 | yes | T3 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 14; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | 3 | F1 | I | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14; 27 *see flowchart |
| 1277 | PROPYLAMINE (1-aminopropane) | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T32) T2 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 1280 | PROPYLENE OXIDE | 3 | F1 | I | 3+unst.+N3+ CMR | C | 1 | 1 |  |  | 95 | 0.83 | 1 | yes | T2 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 2; 12; 31 |
| 1294 | TOLUENE | 3 | F1 | II | 3+N3 | N | 2 | 2 |  | 10 | 97 | 0.87 | 3 | yes | T1 | II A8) II A | yes | PP, EX, A | 1 |  |
| 1578 | CHLORONITROBENZENES, SOLID, MOLTEN (p-CHLORONITROBENZENE) | 6.1 | T2 | II | 6.1+N2+S | C | 2 | 1 | 2 | 25 | 95 | 1.37 | 2 | no | T43) T1 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17; 26 |
| 1595 | DIMETHYL SULPHATE | 6.1 | TC1 | I | 6.1+8+N3+ CMR | C | 2 | 2 |  | 25 | 95 | 1.33 | 2 3 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 30; 34 *see flowchart |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 30; 34 *see flowchart |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 1764 | DICHLOROACETIC ACID | 8 | C3 | II | 8+N1 | C | 2 | 2 |  | 35 | 95 | 1.56 | 2 | yes | T1 | II A II A7) | yes | PP, EP, EX, A | 0 | 17 6: 17°C; 17 |
| 1848 | PROPIONIC ACID with not less than 10% and less than 90% acid by mass | 8 | C3 | III | 8+N3 | N | 3 | 3 |  |  | 97 | 0.99 | 3 | yes | T1 | II A7) | yes no | PP, EP, EX, A PP, EP | 0 | 34 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE vp50 > 175 kPa | 3 | F1 | I | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR+F | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE vp50 < 110 kPa 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR+F | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE | 3 | F1 | I | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 29 *see flowchart |
| 1863 | FUEL, AVIATION, TURBINE ENGINE | 3 | F1 | II | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 29 *see flowchart |
| 1863 | FUEL, AVIATION, TURBINE ENGINE | 3 | F1 | III | 3+(N1, N2, N3, CMR, F) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14 *see flowchart |
| 1922 | PYRROLIDINE | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 | 0.86 | 2 | yes | T2 | II A II A7) | yes | PP, EP, EX, A | 1 |  |
| 1969 | ISOBUTANE | 2 | 2F |  | 2.1 2.1(+CMR) | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 1) | II A II A7) | yes | PP, EX, A | 1 | 31; 99 31; 40 |
| 1987 | ALCOHOLS, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | PP, EX, A * | yes | PP, EX, A | 1 | 14; 27; 29 *see flowchart |
| 1987 | ALCOHOLS, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | PP, EX, A * | yes | PP, EX, A | 0 | 14; 27 *see flowchart |
| 1989 | ALDEHYDES, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1989 | ALDEHYDES, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14; 27 *see flowchart |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 >175 kPa | 3 | F1 | I | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | I | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. | 3 | F1 | I | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1993 | FLAMMABLE LIQUID, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14; 27; 29 *see flowchart |
| 1993 | FLAMMABLE LIQUID, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14; 27 *see flowchart |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 23; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE BOILING POINT > 115 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 27; 29 |
| 2022 | CRESYLIC ACID | 6.1 | TC1 | II | 6.1+8+3+S | C | 2 | 2 |  | 25 | 95 | 1.03 | 2 | no | T1 | II A II A7) | yes | PP, EP, EX, TOX, A | 2 | 6: +16 ºC; 17 |
| 2046 | CYMENES | 3 | F1 | III | 3+N2+F | N | 3 | 3 |  |  | 97 | 0.88 | 3 | yes | T2 | II A II A7) | yes | PP, EX, A | 0 |  |
| 2047 | DICHLOROPROPENES (2,3- DICHLOROPROP-1-ENE) | 3 | F1 | II | 3+N2+CMR | C | 2 | 2 |  | 45 | 95 | 1.2 | 2 | yes | T1 | II A II A7) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 |  |
| 2047 | DICHLOROPROPENES (MIXTURES of 2,3-DICHLOROPROP-1-ENE and 1,3-DICHLOROPROPENE) | 3 | F1 | II | 3+N2+CMR 3+N1+CMR | C | 2 | 2 |  | 45 | 95 | 1.23 | 2 | yes | T21) | II A II A7) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 |  |
| 2047 | DICHLOROPROPENES (MIXTURES of 2,3-DICHLOROPROP-1-ENE and 1,3-DICHLOROPROPENE) | 3 | F1 | III | 3+N2+CMR 3+N1+CMR | C | 2 | 2 |  | 45 | 95 | 1.23 | 2 | yes | T21) | II A II A7) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 2047 | DICHLOROPROPENES (1,3-DICHLOROPROPENE) | 3 | F1 | III | 3+N2+CMR 3+N1+CMR | C | 2 | 2 |  | 40 | 95 | 1.23 | 2 | yes | T21) | II A7) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 2051 | 2-DIMETHYLAMINO ETHANOL | 8 | CF1 | II | 8+3+N3 | N | 3 | 2 |  |  | 97 | 0.89 | 3 | yes | T3 | II A II A7) | yes | PP, EP, EX, A | 1 | 34 |
| 2057 | TRIPROPYLÈNE | 3 | F1 | II | 3 3+N2 | N | 2 | 2 |  | 10 | 97 | 0.744 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 2057 | TRIPROPYLENE | 3 | F1 | III | 3 3+N2 | N | 3 | 2 |  |  | 97 | 0.73 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 0 |  |
| 2205 | ADIPONITRILE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.96 | 2 | no | T43) T4 | II B4) | yes | PP, EP, EX, TOX, A | 0 | 17 6: 6°C; 17 |
| 2218 | ACRYLIC ACID, STABILIZED | 8 | CF1 | II | 8+3+unst.+N1 | C | 2 | 2 | 4 | 30 | 95 | 1.05 | 1 | yes | T2 | II A7) II B | yes | PP, EP, EX, A | 1 | 3; 4; 5; 17 |
| 2227 | n-BUTYL METHACRYLATE, STABILIZED | 3 | F1 | III | 3+unst. 3+unst.+N3+F | C | 2 | 2 |  | 25 | 95 | 0.9 | 1 | yes | T3 | II A | yes | PP, EX, A | 0 | 3; 5 |
| 2238 | CHLOROTOLUENES (o-CHLOROTOLUENE) | 3 | F1 | III | 3+S 3+N2+S | C | 2 | 2 |  | 30 | 95 | 1.08 | 2 | yes | T1 | II A7) | yes | PP, EX, A | 0 |  |
| 2238 | CHLOROTOLUENES (p-CHLOROTOLUENE) | 3 | F1 | III | 3+S 3+N2+S | C | 2 | 2 |  | 30 | 95 | 1.07 | 2 | yes | T1 | II A7) | yes | PP, EX, A | 0 | 6: +11 ºC; 17 |
| 2241 | CYCLOHEPTANE | 3 | F1 | II | 3+N2 | N | 2 | 3 |  | 10 | 97 | 0.81 | 3 | yes | T4 3) | II A II A7) | yes | PP, EX, A | 1 |  |
| 2259 | TRIETHYLENETETRAMINE | 8 | C7 | II | 8+N2 | N | 3 | 3 |  |  | 97 | 0.98 | 3 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 34 6: 16°C; 17; 34 |
| 2265 | N,N-DIMETHYLFORMAMIDE | 3 | F1 | III | 3+CMR | N | 2 | 3 | 3 | 10 | 97 | 0.95 | 3 | yes | T2 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 0 |  |
| 2266 | DIMETHYL-N-PROPYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T4 | II A II A7) | yes | PP, EP, EX, A | 1 | 23 |
| 2288 | ISOHEXENES | 3 | F1 | II | 3+unst. 3+unst.+N3 | C | 2 | 2 | 3 | 50 | 95 | 0.735 | 2 | yes | T2 | II B4) | yes | PP, EX, A | 1 | 3; 23 |
| 2289 | ISOPHORONEDIAMINE | 8 | C7 | III | 8+N2 | N | 3 | 3 |  |  | 97 | 0.92 | 3 | yes | T2 | II A II A7) | yes | PP, EP, EX, A | 0 | 17; 34 6: 14°C; 17; 34 |
| 2321 | TRICHLOROBENZENES, LIQUID (1,2,4-TRICHLOROBENZENE) | 6.1 | T1 | III | 6.1+N1+S | C | 2 | 2 | 2 | 25 | 95 | 1.45 | 2 | no | T1 | II A II A7) | yes | PP, EP, EX, TOX, A | 0 | 7; 17 |
| 2325 | 1,3,5-TRIMETHYLBENZENE | 3 | F1 | III | 3+N1 | C | 2 | 2 |  | 35 | 95 | 0.87 | 2 | yes | T1 | II A II A7) | yes | PP, EX, A | 0 |  |
| 2357 | CYCLOHEXYLAMINE | 8 | CF1 | II | 8+3+N3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T3 | II A8) II B4) | yes | PP, EP, EX, A | 1 | 34 |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | TF1 | I | 6.1+3+CMR | C | 2 | 2 |  | 50 | 95 | 0.83 | 1 | yes no | T4 3) | II C II C5) | yes | PP, EP, EX, TOX, A | 2 |  |
| 2383 | DIPROPYLAMINE | 3 | FC | II | 3+8 3+8+N2 | C | 2 | 2 |  | 35 | 95 | 0.74 | 2 | no yes | T3 | II A | yes | PP, EP, EX, A | 1 |  |
| 2397 | 3-METHYLBUTAN-2-ONE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.81 | 3 | yes | T1 | II A II A7) | yes | PP, EX, A | 1 |  |
| 2404 | PROPIONITRILE | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 45 | 95 | 0.78 | 2 | no | T19) | II A II A7) | yes | PP, EP, EX, TOX, A | 2 |  |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (NONYLPHENOL, ISOMERIC MIXTURE, MOLTEN) | 8 | C4 | II | 8+N1+F | C | 2 | 1 2 | 2 | 25 | 95 | 0.95 | 2 | yes | T2 | II A7) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (NONYLPHENOL, ISOMERIC MIXTURE, MOLTEN) | 8 | C4 | II | 8+N1+F | C | 2 | 2 1 | 4 | 25 | 95 | 0.95 | 2 | yes |  |  | no | PP, EP | 0 | 7; 17; 20: +125 ºC |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | TF1 | I | 6.1+3+N1 | C | 2 | 2 | 2 | 35 | 95 | 1,0711) | 2 1 | no | T4 3) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 2486 | ISOBUTYL ISOCYANATE | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 40 | 95 |  | 2 | no | T4 3) | II B4) | yes | PP, EP, EX, TOX, A | 1 2 |  |
| 2491 | ETHANOLAMINE or ETHANOLAMINE SOLUTION | 8 | C7 | III | 8+N3 | N | 3 | 2 |  |  | 97 | 1.02 | 3 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 17; 34 6: 14°C; 17; 34 |
| 2531 | METHACRYLIC ACID, STABILIZED | 8 | C3 | II | 8+unst.+N3 | C | 2 | 2 | 4 | 25 | 95 | 1.02 | 1 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 3; 4; 5; 17 3; 4; 5; 7; 17 |
| 2564 | TRICHLOROACETIC ACID SOLUTION | 8 | C3 | III | 8+N1 | C | 2 | 2 |  | 25 | 95 | 1,6211) | 2 | yes | T1 | II A7) | yes no | PP, EP, EX, A PP, EP | 0 | 22 |
| 2574 | TRICRESYL PHOSPHATE with more than 3% ortho isomer | 6.1 | T1 | II | 6.1+S 6.1+N1+S | C | 2 | 2 |  | 25 | 95 | 1.18 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2618 | VINYLTOLUENES, STABILIZED | 3 | F1 | III | 3+unst.+F 3+unst.+N2+F | C | 2 | 2 |  | 25 | 95 | 0.92 | 1 | yes | T1 | II B4) | yes | PP, EX, A | 0 | 3; 5 |
| 2672 | AMMONIA SOLUTION (relative density between 0.880 and 0.957 at 15 °C in water, with more than 10% but not more than 35 % ammonia) | 8 | C5 | III | 8+N1 | C | 2 | 2 |  | 50 | 95 | 0,8810) - 0,9610) | 2 | yes |  |  | no | PP, EP | 0 | 34 |
| 2709 | BUTYLBENZENES | 3 | F1 | III | 3+N1+F | C | 2 | 2 |  | 35 | 95 | 0.87 | 2 | yes | T2 | II A II A7) | yes | PP, EX, A | 0 |  |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. (2-AMINOBUTANE) | 3 | FC | II | 3+8 3+8+N1 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T4 3) | II A II A7) | yes | PP, EP, EX, A | 1 | 23 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 2789 | ACETIC ACID, GLACIAL or ACETIC ACID SOLUTION, more than 80 % acid, by mass | 8 | CF1 | II | 8+3 | N | 2 | 3 | 2 | 10 | 95 | 1,05 with 100% acid | 3 | yes | T1 | II A II A7) | yes | PP, EP, EX, A | 1 | 7; 17; 34 |
| 2790 | ACETIC ACID SOLUTION, not less than 50 % but not more than 80 % acid, by mass | 8 | C3 | II | 8 | N | 2 | 3 |  | 10 | 95 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 34 |
| 2790 | ACETIC ACID SOLUTION, more than 10 % and less than 50 % acid, by mass | 8 | C3 | III | 8 | N | 2 | 3 |  | 10 | 95 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 34 |
| 2850 | PROPYLENE TETRAMER | 3 | F1 | III | 3+N1+F | C | 2 | 2 |  | 35 | 95 | 0.76 | 2 | yes | T3 | II B4) | no yes | PP PP; EX, A | 0 |  |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. (2- PROPANOL AND DIDECYLDIMETHYL-AMMONIUM CHLORIDE, AQUEOUS SOLUTION) | 8 | CF1 | II | 8+3+F | N | 3 | 3 |  |  | 95 97 | 0.95 | 3 | yes | T3 | II A | yes | PP, EP, EX, A | 1 | 34; |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | I | 3+8+(N1, N2, N3, CMR, F or S) | C | 2 | 2 | * | * | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EP, EX, A * | 1 | 27; 29 *see flowchart |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | II | 3+8+(N1, N2, N3, CMR, F or S) | C | 2 | 2 | * | * | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EP, EX, A * | 1 | 27; 29 *see flowchart |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | III | 3+8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EP, EX, A * | 0 | 27; 34 *see flowchart |
| 3082 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S. | 9 | M6 | III | 9+(N1, N2, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP * | 0 | 22; 27 * see flowchart |
| 3175 | SOLIDS CONTAINING FLAMMABLE LIQUID, N.O.S., MOLTEN, having a flash-point up to 60 °C (2- PROPANOL AND DIALKYL-(C12 to C18)-DIMETHYLAMMONIUM CHLORIDE) | 4.1 | F1 | II | 4.1 | N | 3 | 3 | 4 |  | 95 | 0.86 | 3 | yes | T2 | II A II A7) | yes | PP, EX, A | 1 | 7; 17 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 60 °C, at or above its flash-point (Low QI Pitch) | 3 | F2 | III | 3(???+F) | N | 3 | 1 | 4 |  | 95 | 1,1-1,3 | 3 | yes | T2 | II B | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 7 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 60 °C, at or above its flash-point | 3 | F2 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | 95 |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 7; 27 *see flowchart |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S. at or above 100 °C and below its flash-point (including molten metals, molten salts, etc.) | 9 | M9 | III | 9+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | 95 |  | * | yes |  |  | no | PP * | 0 | 7; 20:+115 ºC; 22; 24; 25; 27 *see flowchart |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S. at or above 100 °C and below its flash-point (including molten metals, molten salts, etc.) | 9 | M9 | III | 9+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | 95 |  | * | yes |  |  | no | PP * | 0 | 7; 20:+225 ºC; 22; 24; 27 *see flowchart |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | I | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | II | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | III | 8+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP, EP * | 0 | 27; 34 *see flowchart |
| 3271 | ETHERS, N.O.S. vp50 ≤ 110 kPa ETHERS, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14, 27; 29 *see flowchart |
| 3271 | ETHERS, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14, 27 *see flowchart |
| 3272 | ESTERS, N.O.S. vp50 ≤ 110 kPa ESTERS, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T2 | II B4) | yes | PP, EX, A * | 1 | 14, 27; 29 *see flowchart |
| 3272 | ESTERS, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14, 27 *see flowchart |
| 3289 | TOXIC LIQUID, CORROSIVE, INORGANIC, N.O.S. BOILING POINT > 115 °C | 6.1 | TC3 | I | 6.1+8+ (N1, N2, N3, CMR, F or S) | C | 2 | 2 | * | * | 95 |  | 2 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 *see flowchart |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. CONTAINS ISOPRENE AND PENTADIENE (vp 50 > 110 kPa), STABILIZED | 3 | F1 | I | 3, unst. (N2, CMR) 3+unst. +N2+CMR | C | 2 | 2 | 3 | 50 | 95 | 0,678 | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 3, 27, 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | 3 | F1 | I | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14, 27; 29 *see flowchart |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | 3 | F1 | II | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 1 | 14, 27; 29 *see flowchart |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | 3 | F1 | III | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 14, 27 *see flowchart |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (POLYCYCLIC AROMATIC HYDROCARBONS MIXTURE) | 3 | F1 | III | 3+CMR+F | N | 2 | 3 | 3 | 10 | 97 | 1.08 | 3 | yes | T1 | II A | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 14 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 > 175 kPa | 3 | F1 | I | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | I | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | I | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | I | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE 110 kPa < vp50 ≤ 175 kPa | 3 | F1 | II | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR | C | 1 | 1 |  |  | 95 |  | 1 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT ≤ 60 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23: 27; 29: 38 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 23; 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | II | 3+CMR | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 1 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 60 °C < BOILING POINT ≤ 85 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 23; 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa 85 °C < BOILING POINT ≤ 115 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 27; 29 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. WITH MORE THAN 10 % BENZENE vp50 ≤ 110 kPa BOILING POINT > 115 °C | 3 | F1 | III | 3+CMR | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T4 3) | II B4) | yes | PP, EX, A PP, EP, EX, TOX,A | 0 | 27; 29 |
| 3446 | NITROTOLUENES, SOLID, MOLTEN (p-NITROTOLUENE) | 6.1 | T2 | II | 6.1+S 6.1+N2+S | C | 2 | 2 | 2 | 25 | 95 | 1.16 | 2 | no | T2 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 3451 | TOLUIDINES, SOLID, MOLTEN (p-TOLUIDINE) | 6.1 | T2 | II | 6.1 6.1+N1 | C | 2 | 2 | 2 | 25 | 95 | 1.05 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 3455 | CRESOLS, SOLID, MOLTEN | 6.1 | TC2 | II | 6.1+8 6.1+8+N3 | C | 2 | 2 | 2 | 25 | 95 | 1,03 - 1,05 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 9001 | SUBSTANCES WITH A FLASH-POINT ABOVE 60 °C handed over for carriage or carried at a TEMPERATURE WITHIN A RANGE OF 15K BELOW THE IR FLASH-POINT OF SUBSTANCES WITH A FLASH-POINT > 60 °C, HEATED TO LESS THAN 15 K FROM THE FLASH-POINT | 3 | F 3 |  | 3+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes | T4 3) | II B4) | yes | PP, EX, A * | 0 | 27 *see flowchart |
| 9002 | SUBSTANCES HAVING A SELF-IGNITION TEMPERATURE ≤ 200 °C and not otherwise mentioned | 3 | F4 |  | 3+(N1, N2, N3, CMR, F or S) | C | 1 | 1 | * | * | 95 |  | 1 | yes | T4 | II B4) | yes | PP, EX, A * | 0 | *see flowchart |
| 9003 | SUBSTANCES WITH A FLASH-POINT ABOVE 60 °C BUT NOT MORE THAN 100 °C or SUBSTANCES WHERE 60° C < flash‑point ≤ 100° C, which are not affected to another class | 9 |  |  | 9+(N1, N2, N3, CMR, F or S) | * | * | * | * | * | * |  | * | yes |  |  | no | PP * | 0 | 27 *see flowchart |
| 9005 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S, MOLTEN | 9 |  |  | 9+(N3, CMR, F or S | * | * | * | * | * | 97 |  | * | yes |  |  | no | PP * | 0 | *see flowchart |
| 9006 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S. | 9 |  |  | 9+(N3, CMR, F or S | * | * | * | * | * | 97 |  | * | yes |  |  | no | PP * | 0 | *see flowchart |

# Footnotes

Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/18/INF.03.