|  | United Nations | ECE/TRANS/WP.29/2011/59 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 1 April 2011 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

154th session

Geneva, 21–24 June 2011

Item 4.8.2 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRRF

Proposal for Supplement 13 to Regulation No. 13-H (Brakes of M1 and N1 vehicles)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-ninth session to align the electronic stability control malfunction tell-tale with those of Federal Motor Vehicles Safety Standards (FMVSS) No. 126, and to clarify the periodic technical inspection requirements. It is based on ECE/TRANS/WP.29/GRRF/2010/24 and on ECE/TRANS/WP.29/GRRF/2011/6, both not amended (ECE/TRANS/WP.29/GRRF/69, paras. 10 and 16). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.1.4.2., amend to read:

"5.1.4.2.	It shall be possible to verify, in a frequent and simple way, the correct operational… available."

Insert new paragraph 5.1.4.2.1., to read:

"5.1.4.2.1.	Where the operational status is indicated to the driver by warning signals, as specified in this regulation, it shall be possible at a periodic technical inspection to confirm the correct operational status by visual observation of the warning signals following a power-on."

Paragraph 5.1.4.2.1. (former), renumber as paragraph 5.1.4.2.2.

Annex 9, paragraph 3.4.4., amend to read:

"3.4.4.	The manufacturer may use the ESC malfunction tell-tale in a flashing mode to indicate ESC intervention and/or the intervention of ESC-related systems (as listed in paragraph 3.4.1.9.)."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208/, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.