| Submitted by the representative of by OICA | Informal document No. WP.29-153-15 (153rd WP.29, 8-11 March 2011 agenda item 4.7.2.) |
| --- | --- |

Proposal for the 04 series of amendments

to Regulation No. 10 (Electromagnetic compatibility)

OICA comments to ECE/TRANS/WP.29/2011/8

Introduction

While the document WP.29/2011/8 presented by GRE can generally be supported, some figures should be updated.

The proposed modifications are not technical modifications but only a clarification of some figures for vehicle tests in configuration “RESS charging mode coupled to the power grid”.

These modifications proposed concern the following four figures:

- Annex 4, Appendix, Figure 3

- Annex 6, Appendix, Figure 4

- Annex 13, Appendix 1, Figure 1

- Annex 14, Appendix 1, Figure 1

A.	Proposal

Annex 4 - Appendix

Replace figure 3 by the following:

Vehicle in configuration "RESS charging mode coupled to the power grid”

Elevation

Plane

Annex 6 - Appendix

Replace figure 4 by the following:

Vehicle in configuration "RESS in charging mode coupled to the power grid”

Annex 13 – Appendix 1

Replace figure 1 by the following:

Vehicle in configuration "RESS charging mode coupled to the power grid"

Annex 14 – Appendix 1

Replace figure 1 by the following:

Vehicle in configuration "RESS charging mode coupled to the power grid"

B.	Justification

Annex 4, Appendix, Figure 3

- Vertical dash line moved close to the vehicle side to clarify the distance requirements from the vehicle part (Figure 3, elevation)

- Replacement of “Cable (shall be shortened to appropriate length” by “Cable (shall be shortened to appropriate length), 100 ± 25 mm above ground and at least 10 cm from the car body” for consistency with elevation view (Figure 3, plane)

- Clarification of the 0,8 (+0,2 / -0) m distance requirement which applies between the vehicle and the AN (artificial network) and not between the vehicle and the AN and PM (power mains). The proposed clarification also concerns an additional dash line on vehicle side and a move of the PM

Annex 6, Appendix, Figure 4

- Clarification of the 0,8 (+0,2 / -0) m distance requirement which applies between the vehicle and the AN (artificial network) and not between the vehicle and the AN and PM (power mains). The proposed clarification also concerns an additional dash line on vehicle side and a move of the PM square

- Additional dash point for reference point representation

Annex 13, Figure 1

- Clarification of the 0,8 (+0,2 / -0) m distance requirement which applies between the vehicle and the AN (artificial network) and not between the vehicle and the AN and PM (power mains). The proposed clarification also concerns an additional dash line on vehicle side and a move of the PM square

Annex 14, Appendix 1, Figure 1

- Replacement of AN (artificial network) by IS (impedance stabilization) to be consistent with the wording used in Annex 14, paragraph 3.2.

- Additional dash line on vehicle side

----------------------------

# Text boxes

At least 0,1m from car body

10,0 ± 0,2 m

(100±25) mm

0,8 (+0,2 / -0) m

PM

AN

(3,00 ± 0,05 m)

Artificial Network

Power Mains

3,00 ± 0,05 m

(1,80 ± 0.05) m

0,8 (+0,2 / -0) m

Cable (shall be shortened to appropriate length), (100 ± 25) mm above ground and at least 10 cm from the car body

(et support)

AN

PM

Vehicle

Artificial Network

Power mains

(10,0 ± 0,2) m

(3,00  ± 0,05 m)

(et support)

Vehicle

Reference point

0,8 (+0,2 / -0) m

Cable (shall be shortened to appropriate length), (100 ± 25) mm above ground and at least 10 cm from the car body

AN

PM

Artificial Network

Power mains

≥ 2,0 m

(et support)

Vehicle

0,8 (+0,2 / -0) m

Cable (shall be shortened to appropriate length)

AN

PM

Artificial Network

Power mains

Power cable (shall be shortened to appropriate length)

Communication cable (shall be shortened to appropriate length)

0,8 (+0,2 / -0) m

Impedance Stabilization

IS

PM

Power mains

Vehicle