The Partial Amendment to Announcement of Specifying Details

of the Safety Regulations for Road Vehicles

1. Background

For the sake of promoting the international harmonization of vehicle regulations for automotive parts and equipment without degrading the levels of the national safety and environmental regulations, the Government of Japan acceded to the Agreement Concerning the Establishing of Global Technical Regulations for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles, done at Geneva on 25 June 1998 (hereinafter, referred to as “the 1998 Agreement), in 1999, and has been working on the establishment of the Global Technical Regulations (gtr) under the 1998 Agreement so far.

The gtr regarding measurement procedure for two-wheeled motor cycles equipped with a positive or compression ignition engine with regard to the emission of gaseous pollutants, CO2 emission and fuel consumption (WMTC) was established in 2005.

Based on these, the Ministry of Land, Infrastructure, Transport and Tourism of Japan made necessary amendments to the national regulations as outlined below.

It is expected that these amendments will further seek smoothing the international distribution of vehicle and its equipments, reduction of costs for production and development, etc. and promote the effective measures for vehicle environment.

2. Summary of amendments

2.1 Scope

The amendments provided below will apply to the emission of two-wheeled motorcycles with an engine cylinder capacity exceeding 50cm3 or a maximum design speed exceeding 50 km/h.

2.2 Amendments

2.2.1 Introduction of exhaust gas measurement cycle

The WMTC (World-wide Motorcycle Test Cycle) gtr established in the World Forum For Harmonization of Vehicle Regulations (UN/ECE/WP29) will be introduced to national regulations as a new test cycle. (more details; see Appendix)

2.2.2 Modification of the regulation value

The current regulation value will be replaced to the equivalent value that is measured with the WMTC mode. (more details; see Appendix)

2.3 Lead time

The amendments will apply to;

- Type-Designated vehicle manufactured on or after 1 October, 2012 except imported vehicle.

- Type-Designated import vehicle manufactured on or after 1 September, 2013.

2.4 Schedule

The amendments are scheduled to be promulgated by the end of October 2010 and to be entered into force immediately.

Appendix

Test cycle and limit values under WMTC mode

1. Vehicle classification

<< Class 1 >>

Vehicles that fulfill the following specifications belong to class 1:

50 cm³ < engine capacity ≤ 150 cm³ and vmax < 50 km/h or

Engine capacity < 150 cm³ and 50 km/h ≤ vmax < 100 km/h,

<< Class 2>>

Vehicles that fulfill the following specifications belong to class 2:

Engine capacity < 150 cm³ and 100 km/h ≤ vmax < 115 km/h or

Engine capacity ≥150 cm³ and vmax < 115 km/h	subclass 2-1,

115 km/h ≤ vmax < 130 km/h	subclass 2-2

<< Class3>>

Vehicles that fulfill the following specifications belong to class 3:

130 ≤ vmax < 140 km/h	subclass 3-1,

vmax ≥ 140 km/h	subclass 3-2.

2. Weighting factors for the final emissions

| Vehicle class | Cycle | Weighting |
| --- | --- | --- |
| Class 1 | Part 1, Low Speed | Cold | 50% |
|  | Part 1, Low Speed | Hot | 50% |
| Class 2 | subclass 2-1 | Part 1, Low Speed | Cold | 30% |
|  |  | Part 2, Low Speed | Hot | 70% |
|  | subclass 2-2 | Part 1 | Cold | 30% |
|  |  | Part 2 | Hot | 70% |
| Class 3 | subclass 3-1 | Part 1 | Cold | 25% |
|  |  | Part 2 | Hot | 50% |
|  |  | Part 3, Low Speed | Hot | 25% |
|  | subclass 3-2 | Part 1 | Cold | 25% |
|  |  | Part 2 | Hot | 50% |
|  |  | Part 3 | Hot | 25% |

3. Driving Schedule

4. Limit values under WMTC mode

| Engine capacity | CO (g/km) | THC | NOX |
| --- | --- | --- | --- |
|  |  | (g/km) | (g/km) |
| Engine capacity ≤ 125 cm³ | 2.2 | 0.45 | 0.16 |
| Engine capacity > 125 cm³ | 2.62 | 0.27 | 0.21 |

The above limit values are the values in which the weight was added to the value of the test result.

- - - - -

# Text boxes

Part 1, Low speed

Part1

vehicle speed in km/h

Vehicle speed in km/h

Cycle part 3

Part 2, Low speed

Part 2

vehicle speed in km/h

time in sec

Part 3, Low speed

Part 3

time in sec

Cycle part 1

time in sec

Cycle part 2