|  | United Nations | ST/SG/AC.10/C.3/2012/12 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 3 April 2012 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-first session

Geneva, 25 June – 4 July 2012

Item 3 (a) of the provisional agenda

Listing, classification and packing:

proposals of amendments to the list of dangerous goods of Chapter 3.2

Packing group of UN 3316

Transmitted by the expert from Germany

Introduction

1.	The dangerous goods list does not provide any information on the packing group of UN 3316 CHEMICAL KIT or FIRST AID KIT. This is due to the fact that the packing group has to be determined according to the most stringent packing group assigned to any individual substance in the kit, see Special provision 251 of Chapter 3.3. Nevertheless many users are not aware of the necessity to determine the packing group, as column 5 of the dangerous goods list does not contain any information.

2.	Furthermore, the information “0” and “E0” in columns 7a and 7b is often misinterpreted in a way that there is no possibility to consign these articles as limited or excepted quantities.

Proposal

3.	It is proposed to include two separate entries for UN 3316 in the dangerous goods list, one for packing group II and another one for packing group III. In column 7a and 7b a reference to special provisions 251 and 340 should be inserted, as appropriate. It is presented in the same way as in the International Maritime Dangerous Goods Code.

4.	This would lead to the following entries:

| UN No | Name and description | Class or division | Subsidiary risk | UN PG | Limited and excepted quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | LQ | EQ | PI | Special packing provisions | Instructions | Special provisions. |
| 3316 | CHEMICAL KIT or FIRST AID KIT | 9 |  | II | See SP251 | See SP340 | P901 |  |  |  |
| 3316 | CHEMICAL KIT or FIRST AID KIT | 9 |  | III | See SP251 | See SP340 | P901 |  |  |  |

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).