UN/SCETDG/43/INF.3

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 20 March 2013 Forty- third session Geneva, 24–28 June 2013 Item 3 (c) of the provisional agenda Listing, classification and packing: miscellaneous

New organic peroxide formulations be listed in 2.5.3.2.4 and IBC 520 – ST/SG/AC.10/C.3/2013/1 – Correction

Note by the secretariat

In document ST/SG/AC.10/C.3/2013/1, the table in paragraph 3 should read as follows:

| ORGANIC PEROXIDE | Concentration (%) | Diluent type A (%) | Diluent type B 1) (%) | Inert solid (%) | Water | Packing Method | Control temperature (°C) | Emergency temperature (°C) | Number (Generic entry) | Subsidiary risks and remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CORRECT: |  |  |  |  |  |  |  |  |  |  |
| DIBENZOYL PEROXIDE | >51 - 100 |  |  | ≤ 48 |  | OP2 |  |  | 3102 | 3) |
| INTO |  |  |  |  |  |  |  |  |  |  |
| DIBENZOYL PEROXIDE Remark: typing error since 8th revision | >52 - 100 |  |  | ≤ 48 |  | OP2 |  |  | 3102 | 3) |
| CHANGE: |  |  |  |  |  |  |  |  |  |  |
| tert-BUTYL CUMYL PEROXIDE | >42 - 100 |  |  |  |  | OP8 |  |  | 3107 |  |
| INTO |  |  |  |  |  |  |  |  |  |  |
| tert-BUTYL CUMYL PEROXIDE | >42 - 100 |  |  |  |  | OP8 |  |  | 3109 |  |
| CHANGE: |  |  |  |  |  |  |  |  |  |  |
| DICETYL PEROXYDICARBONATE | ≤ 100 |  |  |  |  | OP7 | +30 | +35 | 3116 |  |
| INTO |  |  |  |  |  |  |  |  |  |  |
| DICETYL PEROXYDICARBONATE | ≤ 100 |  |  |  |  | OP8 | +30 | +35 | 3120 |  |
| CHANGE2: |  |  |  |  |  |  |  |  |  |  |
| tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE | >32-100 ≤ 32 | ≥ 68 |  |  |  | OP7 OP8 |  |  | 3105 3109 |  |
| INTO |  |  |  |  |  |  |  |  |  |  |
| tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE | >37-100 ≤ 37 | ≥ 63 |  |  |  | OP7 OP8 |  |  | 3105 3109 |  |

# Footnotes

2 	This change is proposed because in packing instruction IBC520, this product with a concentration of ≤ 37% is already listed as UN 3109