|  | INF.28 |
| --- | --- |
| Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Joint Meeting of Experts on the Regulations annexed to the European Agreement concerning the International Carriage of Dangerous Goods by Inland Waterways (ADN) (ADN Safety Committee) Twenty-first session Geneva, 27–31 August 2012 | 28 August 2012 |

Further editorial proposals for UN1268

Transmitted by Belgium

Table C, UN1268, 11th entry

- With a vapor pressure of 175kPa the opening pressure of the HV valve (in column 10) should be 50 instead of 10 and cargo tank equipment 3 (in column 9) should be deleted.

- In all entries of UN1268 in table 1.6.7.4.2 the word “NAPHTHA” should be written in capital letters.

- As a consequence remark 27 in column 20 for the 11th entry (first NAPHTHA entry) UN1268 should be deleted

- The entry proposal for Table C would look like this :

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UN-No. or substance identification No. | Name and description | Class | Classification code | Packing group | Dangers | Type of tank vessel | Cargo tank design | Cargo tank type | Cargo tank equipment | Opening pressure of the high-velocity vent valve in kPa | Maximum degree of filling in % | Relative density at 20 °C | Type of sampling device | Pump room below deck permitted | Temperature class | Explosion group | Anti-explosion protection required | Equipment required | Number of cones/blue lights | Additional requirements/Remarks |
| 1268 | PETROLEUM DISTILLATES, N.O.S. OR PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) 110kPa < vp50 = ≤ 175kPa | 3 | F1 | II | 3+N2+ CMR+F | N | 2 | 3 | - | 50 | 97 | 0,735 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14; 29 |

____________________