|  | United Nations | ECE/TRANS/WP.29/2012/14 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 22 December 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

156th session

Geneva, 13–16 March 2012

Item 4.9.8 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 7 to the 01 series of amendments to Regulation No. 74 (Installation of lighting and light-signalling devices (mopeds))

Submitted by the Working Party on Lighting and Light-Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-sixth session in order to introduce Class A and B headlamps with LED. It is based on ECE/TRANS/WP.29/GRE/2011/65, not amended (ECE/TRANS/WP.29/GRE/66, para. 28). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 6.2.1.(a), insert a new footnote *, to read:

"6.2.	Passing beam headlamp

6.2.1. 	Number

One or two of approved type according to:

(a)	Regulation No. 113; *

(b)	Class A of Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 56;

(e)	Regulation No. 57;

(f)	Regulation No. 72;

(g)	Regulation No. 76

(h)	Regulation No. 82.

________________

*	Headlamps of Class A of Regulation No. 113 with LED modules only on vehicles with a maximum design speed not exceeding 25 km/h"

________________

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.