Transmitted by the expert from India                                                Informal Document No. GRRF-72-16

(72nd   GRRF, Agenda item 7(a))

Additional Comments from India on the GTR for Passenger Vehicle Tyres under formulation by the Working Group on Tyres

Giving below our comments on Tyre Document gtr-12-01e after September 16,  2011 meeting,  Harmonized provisions concerning pneumatic tyres for passenger and light truck (commercial) vehicles.

| Clause 3.19 High speed performance test for LT/C tyres. |
| --- |
| Comments | Tyre conditioning (if there is change in Inflation pressure) before testing.(Ref-3.19.2.3 of gtr-12-01e) |
| Justification | Test procedure of FMVSS139 for High Speed performance says “If loss of air exceeds 14 kPa (2 psi) during the conditioning period, determine cause, correct if possible, and recycle tire through the conditioning period” Ref : TIRE CONDITIONING (S6.2.1.1.2 and S6.2.1.1.3) - but the same not covered in gtr. |
| Clause 3.8.2.2 and 3.8.2.3 |
| Comments | Ref Test numbers IEC 60651 1979/A1:1993 and IEC 60942:1988 to be verified for the latest version(tyre gtr-12-01e) |
| Justification | These are the test methods established by International Electro-technical Commission for calibrating sound measuring instruments. Test numbers to be verified for the latest version for e.g.: Test number IEC 60651 has been replaced by IEC 61672-1 ed 1. |
| Clause 3.13 |
| Comments | “The tyre does not exhibit a change in the deflected section height ,compared to the deflected section height at the start of the test ,higher than 20 percent” |
| Justification | The term “-higher than 20 percent” creates confusion, to simplify the term, it may be written as follows “The difference between the deflected section height measured after the test and the deflected section height measured at the start of the test should not be more than 20 percent”. |
| Clause 3.14 |  |
| Comments | Inflation Pressure : Inflate it to the pressure corresponding to the maximum load, or maximum dual load where there is both a single and dual load marked on tyre. |
| Justification | Test procedure of FMVSS 119 says “Use the single maximum load value when the tire is marked with both single and dual maximum loads”. This needs to be verified. |
| Clause 3.2 - Markings |
| Comments | Markings for Asymmetric tyres and Directional tyres to be included in the marking requirements. |
| Justification | For Asymmetric tyre – the outboard sidewall or tire facing outside should be marked otherwise the expected benefits of Asymmetric tyres cannot be achieved, if fitted other way. For Directional tyres – the direction of rotation marking should be marked on the Outboard sidewall otherwise the expected traction and benefits of directional tyres cannot be achieved. |
| Clause 3.11 (3.11.2 & 3.11.4) |
| Comments | Preparation of tyres with speed symbols “S” and below, excluding “H” & Preparing of tyres with speed symbols “T” and above, including “H” – creates confusion can be simplified. |
| Justification | In order to avoid confusion the sentence can be reframed as “Preparation of tyres with speed rating 180 km/h and below” and “Preparation of tyres with speed rating 190 km/h and above” |