UN/SCETDG/44/INF.39

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 20 November 2013 Forty-fourth session Geneva, 25 November – 4 December 2013 Item 4 (a) of the provisional agenda Miscellaneous proposals for amendments to the Model Regulations on the Transport of Dangerous Goods: ethylene oxide and propylene oxide mixtures

Provisions for the transport of UN 2983 (Ethylene oxide and propylene oxide mixtures)

Transmitted by the expert from the United States of America

Introduction

1.	This document provides proposed amendments as presented in working paper ST/SG/AC.10/C.3/2013/45.

Proposal

2.	Amend Column 8 of the Dangerous Goods List for the entry UN2983 to read P001

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provi-sions | Limited and excepted quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| - | 3.1.2 | 2.0 | 2.0 | 2.0.1.3 | 3.3 | 3.4 | 3.5 | 4.1.4 | 4.1.4 | 4.2.5 / 4.3.2 | 4.2.5 |
| 2983 | ETHYLENE OXIDE AND PROPYLENE OXIDE MIXTURE, not more than 30% ethylene oxide | 3 | 6.1 | I |  | 0 | E0 | P200 P001 |  | T14 | TP2 TP7 TP13 |

3.	Remove the entry for UN2983 in Packing Instruction P200, Table 3.

| P200 | PACKING INSTRUCTION (cont'd) | P200 |
| --- | --- | --- |
| Table 3: SUBSTANCES NOT IN CLASS 2 |
| UN No. | Name and description | Class or Division | Subsidiary risk | LC50 ml/m3 | Cylinders | Tubes | Pressure drums | Bundles of cylinders | MEGCs | Test period, years | Test pressure, bar | Filling ratio | Special packing provisions |
| 2983 | ETHYLENE OXIDE AND PROPYLENE OXIDE MIXTURE, not more than 30% ethylene oxide | 3 | 6.1 |  | X |  | X | X |  | 5 | 10 |  | z |

_____________