|  | Nations Unies | ST/SG/AC.10/C.3/2014/100 |
| --- | --- | --- |
|  | Secrétariat | Distr. générale 12 septembre 2014 Français Original: anglais |

Comité d’experts du transport des marchandises dangereuses
et du Système général harmonisé de classification
et d’étiquetage des produits chimiques

Sous-Comité d’experts du transport des marchandises dangereuses

Quarante-sixième session

Genève, 1er-9 décembre 2014

Point 7 de l’ordre du jour provisoire

Nouvelles propositions d’amendements au Règlement type
pour le transport des marchandises dangereuses

N-Aminoéthylpipérazine (ONU 2815): risque subsidiaire 6.1

Communication de l’expert des États-Unis d’Amérique

Introduction

Dans la Liste des marchandises dangereuses, la N-Aminoéthylpipérazine est actuellement inscrite sous le no ONU 2815, classe 8, groupe d’emballage III.

Les données disponibles indiquent toutefois que la N-Aminoéthylpipérazine, actuellement classée dans la Liste des marchandises dangereuses en tant que matière corrosive pour la peau, devrait aussi se voir attribuer un risque subsidiaire de la division 6.1 pour raison de toxicité à l’absorption cutanée.

Les données de toxicité à l’appui de cette évaluation sont résumées dans la Base de données internationale sur les informations chimiques unifiées (IUCLID) tenue en application du Règlement européen concernant l’enregistrement, l’évaluation et l’autorisation des substances chimiques, ainsi que les restrictions applicables à ces substances (REACH). La fiche de données de la N-Aminoéthylpipérazine figure à l’annexe 1 du présent document. Les données d’essais de toxicité pertinentes sont reproduites à l’annexe 2 et indiquent que la N-Aminoéthylpipérazine présente une toxicité par absorption cutanée pour une dose de 866 mg/kg. Cette valeur correspond, pour une matière toxique à l’absorption cutanée, au groupe d’emballage III.

Compte tenu des propriétés de toxicité cutanée décrites ci-dessus, et conformément au paragraphe 2.0.3 du Règlement type (Ordre de prépondérance des caractéristiques de danger), la N-Aminoéthylpipérazine resterait affectée à la classe 8, avec un risque subsidiaire 6.1. Il est donc proposé d’apporter les modifications nécessaires à la Liste des marchandises dangereuses, tel qu’indiqué ci-après. Après examen des Principes directeurs, outre l’ajout du risque subsidiaire, aucune autre modification (à savoir, la modification des dispositions relatives aux emballages ou aux citernes) n’est nécessaire.

Proposition

Modifier la rubrique 2815 de la Liste des marchandises dangereuses comme suit:

| No ONU | Nom et description | Classe ou division | Risque subsidiaire | Groupe d’emballage | Dispositions spéciales | Quantités limitées et quantités exceptées | Emballages et GRV | Citernes mobiles et conteneurs pour vrac |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Instructions d’emballage | Dispositions spéciales | Instructions de transport | Dispositions spéciales |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 2815 | N-AMINOÉTHYLPIPÉRAZINE | 8 | 6.1 | III |  | 5 L | E1 | P001 IBC03 LP01 |  | T4 | TP1 |

Annexe 1

[Anglais seulement]

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by……..United States	Date….4 September 2014

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name	N-Aminoethylpiperazine

1.2	Chemical formula 	C6H15N3

1.3	Other names/synonyms	2-piperazin-1-ylethanamine

1.4.1	UN number 	2815	1.4.2		CAS number 	140-31-8

1.5	Proposed classification for the Recommendations

1.5.1	Proper shipping name (3.1.2) N-Aminoethylpiperazine

1.5.2	Class/division   8	…. subsidiary risk(s)   6.1

packing group   III

1.5.3	Proposed special provisions, if any  Not Applicable

1.5.4	Proposed packing instruction(s)  Not Applicable ………………….

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range ………..-19 °C

2.2	Boiling point or range ………...220.4 °C

2.3	Relative density at:

2.3.1……15 °C

2.3.2……20 °C	0.98 g/cm3

2.3.3……50 °C

2.4	Vapour pressure at:

2.4.1……50 °C		5.15 Pa @ 20 °C

2.4.2……65 °C

2.5	Viscosity at 20 °C ……………….14.1 mPa – sec @ 20 °C

2.6	Solubility in water at 20 °C ……..g/100ml  > 100 g/l

2.7	Physical state at 20°C (2.2.1.1)	liquid

2.8	Appearance at normal transport temperatures, including colour and odour
Clear liquid; Amine odor

2.9	Other relevant physical properties

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3) 99 °C cc

3.1.2	Is combustion sustained? (2.3.1.3)	no

3.2	Autoignition temperature 	>300 °C

3.3	Flammability range (LEL/UEL) 1.1 – 9.4 %

3.4	Is the substance a flammable solid? (2.4.21)	no

3.4.1 If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?		no

If yes, state:

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.11) no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41) no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11) no

If yes, state:

4.4.1	Exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ..................°C

Is the temperature control required? (2.4.2.3.41) 	yes/no

4.4.2	Proposed control temperature for a 50 kg package		°C

4.4.3	Proposed emergency temperature for a 50 kg package		°C

4.5	Is the substance pyrophoric? (2.4.31) 	no

4.5.1 	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 		no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.1) 		no

If yes state:

4.7.1	Exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package? ……………°C

Is temperature control required? (2.5.3.4.11) 	yes/no

4.7.2	Proposed control temperature for a 50 kg package		°C

4.7.3	Proposed emergency temperature for a 50 kg package		°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 	no

4.8.1	If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)	no

4.9.1	If yes, give details	.

4.10	Corrosivity (2.81) to:

4.10.1 ……mild steel 	0.005 mm/year 	at 25 °C

4.10.2 ……aluminium	mm/year  	at	°C

4.10.3 ……other packaging materials (specify)

mm/year	at	°C

mm/year	at	°C

4.11	Other relevant chemical properties  None

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)    2140 mg/kg  Rat

5.2	LD50, dermal (2.6.2.1.21)   866 mg/kg  Rabbit

5.3	LC50, inhalation (2.6.2.1.31)	mg/l	Exposure time	hours

or	 6 ml/m3	Animal species

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)   50 - 75 ppm

5.5	Skin exposure (2.81) results   30 - 60 minutes  Rabbit

5.6	Other data     PG III

5.7	Human experience

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

6.1.2	Spillage

6.2	Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.81)	yes

6.2.2	Intermediate Bulk Containers (6.51)?  yes

6.2.3	Portable tanks (6.71)?	yes

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)  Currently Authorized Containers

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)  Currently Authorized IBCs

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known)   Currently Authorized Tanks

9.2	Minimum test pressure

9.3	Minimum shell thickness

9.4	Details of bottom openings, if any

9.5	Pressure relief arrangements

9.6	Degree of filling

9.7	Unsuitable construction materials ………………………………………………………………………………

Annexe 2

[Anglais seulement]

# Footnotes

Conformément au programme de travail du Sous-Comité pour la période 2013-2014, adopté par le Comité à sa sixième session (voir ST/SG/AC.10/C.3/84, par. 86, et ST/SG/AC.10/40, par. 14).

2 	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1		This and similar references are to chapters and paragraphs in the Model Regulations on the transport of Dangerous Goods.