# Proposal for amendments to ECE/TRANS/WP.29/GRRF/2014/2

I.	Proposal

Insert a new paragraph 2.15.9., to read:

"2.15.11 	the letters "IND" after the nominal rim diameter marking in case of tyres for construction application (industrial tractors)"

Annex 5,

Add a new table 8, to read:

"Table 8 – Tyres for Construction Applications (Industrial Tractors)

| Tyre Size Designation | Theoretical rim width code (A1) | Nominal section Width (S1) (mm) | Overall Diameter (D) (mm) | Nominal rim Diameter (d) (mm) |
| --- | --- | --- | --- | --- |
|  |  | Radial | Diagonal | Radial | Diagonal |  |
| 14.9-24 | 13 | 378 | 378 | 1 245 | 1 240 | 610 |
| 14.9-28 | 13 | 378 | 378 | 1 350 | 1 345 | 711 |
| 16.9-24 | 15 | 429 | 429 | 1 320 | 1 310 | 610 |
| 16.9-28 | 15 | 429 | 429 | 1 420 | 1 410 | 711 |
| 16.9-34 | 15 |  | 429 |  | 1 560 | 864 |
| 17.5L-24 | 15 | 445 | 445 | 1 250 | 1 241 | 610 |
| 18.4-24 | 16 | 467 | 467 | 1 395 | 1 375 | 610 |
| 18.4-26 | 16 |  | 467 |  | 1 425 | 660 |
| 18.4-28 | 16 | 467 | 467 | 1 490 | 1 477 | 711 |
| 18.4-30 | 16 |  | 467 |  | 1 525 | 762 |
| 19.5L-24 | 17 | 495 | 495 | 1 320 | 1 314 | 610 |
| 21L-24 | 18 | 533 | 533 | 1 395 | 1 378 | 610 |
| 23.1-26 | 20 |  | 587 |  | 1 580 | 660 |

II.	Justification

Editorial corrections.