Proposal for Supplement 2 to the 04 series of amendments to Regulation No. 17 (Strength of seat)

The text reproduced below was prepared by the expert from Germany aimed to close the gap for sidefacing seats in certain vehicle categories.

I.	Proposal

Paragraph 5.1.1, amend to read :

"5.1.1. The installation of side-facing seats shall be prohibited in vehicles of categories M1,

N, M2 (of class II, III and B) and M3 of a technically permissible laden mass not

exceeding 10 tonnes (of class II, III and B)."

II.	Justification

UN Regulation No. 17 prohibits side-facing seats in Passenger Cars of category M1 and light Lorries or Vans of category N1. Heavier vehicles of the categories N2 and N3 are not mentioned  in this Paragraph, because this vehicles are designed and constructed for the carriage of goods  and not for the carriage of passengers.

In the new Annex XI of  Directive 2007/46/EC there is a slight change in the footnote “G” and it will be amend to read “In case of multi-stage approval, requirements according to the category of the base/incomplete vehicle (e.g. the chassis of which was used to build the special purpose vehicle) may also be used.”. The reference to the requirements of base/incomplete vehicles of the corresponding category N (based on max. mass) will be deleted. Due to this a special purpose vehicle, for example a M1 Motor-Caravan  < 3,5 tonnes based on incomplete N2 vehicle could install side-facing seats, because Directive 74/408/EC an Regulation No. 17 do not prohibit side-facing seats for vehicle of the categories N2 and N3.

To close this gap and to avoid an installation of side-facing seats in those vehicles, Paragraph 5.1.1 should be amended  from N1 to N.