|  | United Nations | ST/SG/AC.10/C.3/2015/11 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 24 March 2015 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-seventh session

Geneva, 22 – 26 June 2015

Item 3 of the provisional agenda

Listing, classification and packing

Substances which could be identified as toxic and corrosive

Transmitted by the expert from the Republic of Korea

Introduction

1.	At the eighteenth session of the IMO Sub-Committee on Dangerous Goods, Solids cargoes and Containers (DSC 18, 2013), the Republic of Korea made a proposal (DSC18/7/8) on marine pollutant information on the Dangerous Goods List in the IMDG Code concerning the substances which meet the criteria for environmentally hazardous substances according to the GESAMP Hazard Profiles (BLG.1/Circ.34, Annex 7).

2.	The proposal was made to provide correct information for shipper and carriers, and the Sub-Committee agreed the proposal and these substances are identified as marine pollutants in the IMDG Code (Amendment 37-14) after verification of E&T 20.

3.	As same purpose above, assuming that the GESAMP hazard evaluation criteria and the classification of oral and dermal toxicity or skin irritation and corrosion of the United Nations Model Regulations follow the same United Nations  GHS criteria, the information of oral and dermal toxicity or skin irritation and corrosion of the substances in the GESAMP Hazard Profiles (PPR.1/Circ.1, Annex 5) could be valuable data to determine the hazard of substances which are listed in the Dangerous Goods List (DGL) of the United Nations Model Regulations.

Discussion

4.	The grouping criteria of the Division 6.1 for oral and dermal toxic substance and Class 8 for skin corrosive substance in the  Model regulations are the same as the criteria in the GESAMP Hazard evaluation procedure (GESAMP Revised Reports and Studies No.64, second edition).

5.	The grouping criteria for the oral toxicity (LD50) and dermal toxicity (LD50) are shown in C1 and C2 of the table 1 according to the revised GESAMP Hazard evaluation procedure. And the grouping criteria for toxic substances in the provision 2.6.2.2.4.1 of the Model Regulations are shown in the table 2.

Table 1 Revised GESAMP Hazard evaluation procedure

Table 2 Grouping criteria for toxic substances of the  Model Regulations

| Packing Group | Oral toxicity LD50 (mg/kg) | Dermal toxicity LD50 (mg/kg) | Inhalation toxicity By dusts and mists LC50 (mg/L) |
| --- | --- | --- | --- |
| Ⅰ | ≤ 5.0 | ≤ 50 | ≤ 0.2 |
| Ⅱ | > 5.0 and ≤ 50 | > 50 and ≤ 200 | > 0.2 and ≤ 2.0 |
| Ⅲ | > 50 and ≤ 300 | > 200 and ≤ 1000 | > 2.0 and ≤ 4.0 |

6.	Along the same lines, the grouping criteria for the skin corrosive substance also could be compared with the GESAMP Hazard evaluation procedure. The grouping criteria of Numerical Rating for the skin irritation and corrosion are also shown in D1 of the table 1. And the grouping criteria for corrosive substance in the provision 2.8.2.5 of the Model Regulations are shown in the table 3.

Table 3 Grouping criteria for corrosive substance of the  Model Regulations

| Packing Group | Exposure time | Observation period | Effect |
| --- | --- | --- | --- |
| Ⅰ | ≤ 3 min | ≤ 60 min | Full thickness destruction of intact skin |
| Ⅱ | > 3 min ≤ 1 h | ≤ 14 d | Full thickness destruction of intact skin |
| Ⅲ | > 1 h ≤ 4 h | ≤ 14 d | Full thickness destruction of intact skin |
| Ⅲ | - | - | Corrosive rate on either steel or aluminium surfaces exceeding 6.25mm a year at a test temperature of 55℃ when tested on both materials |

7.	The EHS Working Group of GESAMP circulates the GESAMP Hazard Profiles (PPR.1/Circ.1) according to the GESAMP Hazard evaluation procedure.

Proposal

8.	Following the GESAMP Hazard Profiles (PPR.1/Circ.1, Annex 5), if substances meet 2 and over in the Numerical Rating in column C1 and C2 which are not classified as Division 6.1 in the  Model Regulations could be considered as potential toxic substances according to the criteria in provision 2.6.2.2.4.1 of the  Model Regulations (refer to table 4).

Table 4 Comparison of the grouping criteria of the toxic substance 
in GESAMP Hazard evaluation procedure and  Model Regulations

| UN Model Regulations | Oral toxicity LD50 (mg/kg) | Dermal toxicity LD50 (mg/kg) | GESAMP Hazard Profiles |
| --- | --- | --- | --- |
| Packing Group |  |  | Numerical Rating |
| Ⅰ | ≤ 5.0 | ≤ 50 | 4 |
| Ⅱ | > 5.0 and ≤ 50 | > 50 and ≤ 200 | 3 |
| Ⅲ | > 50 and ≤ 300 | > 200 and ≤ 1000 | 2 |

9.	Also following the GESAMP Hazard Profiles (PPR.1/Circ.1, Annex 5), if substances meet 3A, 3B or 3C in the Numerical Rating in column D1 which are not classified as Class 8 in the  Model Regulations could be considered as potential corrosive substances according to the criteria in provision 2.8.2.5 of the  Model Regulations (refer to table 5).

Table 5 Comparison of the grouping criteria of the skin corrosive substance

in GESAMP Hazard evaluation procedure and Model Regulations

| UN Model Regulations | Grouping criteria of the skin corrosive substance (Exposure time) | GESAMP Hazard Profiles |
| --- | --- | --- |
| Packing Group |  | Numerical Rating |
| Ⅰ | ≤ 3 min | 3C |
| Ⅱ | > 3 min ≤ 1 h | 3B |
| Ⅲ | > 1 h ≤ 4 h | 3A |

10.	Among the results, substances that are not classified as Division 6.1 in the Model Regulations while the names of the substances meet the criteria of the Hazard evaluation procedure in the GESAMP Hazard Profiles (PPR.1/Circ.1, Annex 5) are shown in the Table 6.

11.	In addition, substances that are not classified as Class 8 in the Model Regulations while the names of the substances meet the criteria of the Hazard evaluation procedure in the GESAMP Hazard Profiles (PPR.1/Circ.1, Annex 5) are shown in the Table 7.

Table 6 Substances lists which could be possible to classified as Division 6.1

| UN Model Regulations DGL | GESAMP Hazard Profiles |
| --- | --- |
| UN No | Class | Proper shipping Name | EHS Name | C1 | C2 |
| 1005 | 2.3(8) | AMMONIA, ANHYDROUS | Ammonia(anhydrous and aqueous, 28% or less) | 1 | (2) |
| 1036 | 2.1 | ETHYLAMINE | Ethylamine | 2 | 2 |
| 1125 | 3(8) | n-BUTYLAMINE | Butylamine | 2 | 2 |
| 1130 | 3 | CAMPHOR OIL | Camphor oil, white | 2 | NI |
| 1154 | 3(8) | DIETHYLAMINE | Diethylamine | 1 | 2 |
| 1160 | 3(8) | DIMETHYLAMINE, AQUEOUS SOLUTION | Dimethylamine(40-50% aq.sol) | 2 | 0 |
| 1221 | 3(8) | ISOPROPYLAMINE | Isopropylamine | 2 | 2 |
| 1235 | 3(8) | METHYLAMINE, AQUEOUS SOLUTION | Methylamine solution 42% or less | 2 | (2) |
| 1277 | 3(8) | PROPYLAMINE | Propylamine | 2 | 2 |
| 1296 | 3(8) | TRIETHYLAMINE | Triethylamine | 1 | 2 |
| 1431 | 4.2(8) | SODIUM METHYLATE | Sodium Methylate (21-30% in Methanol) | 2 | (2) |
| 1604 | 8(3) | ETHYLENEDIAMINE | Ethylene diamine | 1 | 2 |
| 1754 | 8 | CHLOROSULPHONIC ACID | Chlorosulphonic acid | (2) | (3) |
| 1778 | 8 | FLUOROSILICIC ACID | Fluorosilicic acid | 2 | (2) |
| 1796 | 8 | NITRATING ACID MIXTURE | Acid mixtures(nitrating acid) | 3 | 3 |
| 1814 | 8 | POTASSIUM HYDROXIDE SOLUTION | Potassium hydroxide(sol.) | 2 | (2) |
| 2048 | 3 | DICYCLOPENTADIENE | Dicyclopentadiene(80-90%)/Co-dimers(10-20%), mixtures | 2 | 0 |
| 2054 | 8(3) | MORPHOLINE | Morpholine | 1 | 2 |
| 2079 | 8 | DIETHYLENETRIAMINE | Diethylene triamine | 1 | 3 |
| 2209 | 8 | FORMALDEHYDE SOLUTION | Formaldehyde (37-50% solution) | 2 | 2 |
| 2215 | 8 | MALEIC ANHYDRIDE | Maleic anhydride | 1 | 2 |
|  |  | MALEIC ANHYDRIDE, MOLTEN |  |  |  |
| 2225 | 8 | BENZENESULPHONYL CHLORIDE | Benzene sulphonyl chloride | 1 | (2) |
| 2248 | 8(3) | DI-n-BUTYLAMINE | Di-n-butylamine | 2 | 2 |
| 2259 | 8 | TRIETHYLENETETRAMINE | Triethylenetetramine | 0 | 2 |
| 2264 | 8(3) | N,N-DIMETHYL-CYCLOHEXYLAMINE | N,N-Dimethyl cyclohexylamine | 1 | 2 |
| 2270 | 3(8) | ETHYLAMINE, AQUEOUS SOLUTION | Ethylamine solutions (72% or less) | 2 | 2 |
| 2320 | 8 | TETRAETHYLENEPENTAMINE | Tetraethylene pentamine | 0 | 2 |
| 2357 | 8(3) | CYCLOHEXYLAMINE | Cyclohexylamine | 2 | 2 |
| 2361 | 3(8) | DIISOBUTYLAMINE | Diisobutylamine | 2 | (2) |
| 2389 | 3 | FURAN | Furfural | 2 | (2) |
| 2493 | 3(8) | HEXAMETHYLENEIMINE | Hexamethyleneimine | 3 | 1 |
| 2511 | 8 | 2-CHLOROPROPIONIC ACID | 2-Chloropropionic acid | 1 | (3) |
| 2529 | 3(8) | ISOBUTYRIC ACID | Isobutyric acid | 2 | 2 |
| 2815 | 8 | N-AMINOETHYLPIPERAZINE | N-Aminoethylpiperazine | 0 | 2 |
| 3320 | 8 | SODIUM BOROHYDRIDE AND SODIUM HYDROXIDE SOLUTION | Sodium borohydride/sodium hydroxide mixture (soln.) | (2) | (1) |

Table 7 Substances lists which could be possible to classified as Class 8

| UN Model Regulations DGL | GESAMP Hazard Profiles |
| --- | --- |
| UN No | Class | Proper shipping Name | EHS Name | D1 |
| 1131 | 3(6.1) | CARBON DISULPHIDE | Carbon disulphide | 3A |
| 2023 | 6.1(3) | EPICHLOROHYDRIN | Epichlorohydrin | 3A |
| 2313 | 3 | PICOLINES | 2-Methyl pyridine | 3A |
|  |  |  | 3-Methyl pyridine | 3 |
|  |  |  | 4-Methyl pyridine | 3 |

12.	The Hazard Profiles can serve as valuable information for industries and shippers in evaluating hazardous substances. Therefore the expert from the Republic of Korea is of the opinion that if the lists of substances contained in table 6 and 7 are considered as potential substances as toxic or corrosive, they also could be identified as toxic substances or corrosive substances in the DGL of the  Model Regulations.

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2015–2016 approved by the Committee at its seventh session (see ST/SG/AC.10/C.3/92, paragraph 95 and ST/SG/AC.10/42, para. 15).