|  | United Nations | ECE/TRANS/WP.29/GRE/2015/23 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 2 February 2015 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Seventy-third session

Geneva, 14 – 17 April 2015

Item 7 (j) of the provisional agenda
Other Regulations – Regulation No. 112 (Headlamps emitting an asymmetrical passing-beam)

Proposal for a corrigendum to the 01 series of amendments to Regulation No. 112

Submitted by the expert from France*

The text reproduced below was prepared by the expert from France to correct an inconsistency between the text and Figure B of Annex 3.

- Proposal

Annex III, Figure B, correct as follows (in blue):

II.	Justification

1.	The text of paragraph 6.2.4. specifies the test point as follows:

"6.2.4.	The passing beam shall meet the luminous intensities at the test points referred to in the tables below and in Annex 3 figure B (or mirrored about the VV line for left-hand traffic):

| Headlamps for RH Traffic** | Class A Headlamp | Class B Headlamp |
| --- | --- | --- |
| Test Point Designation | Test Point Angular Coordinates - Degrees | Required luminous intensity cd | Required luminous intensity cd |
|  |  | Max | Min | Max | Min |
| B 50 L | 0.57U, 3.43L | 350 |  | 350 |  |
| BR | 1.0 U, 2.5R | 1 750 |  | 1 750 |  |
| 75 R | 0.57D, 1.15R |  | 5 100 |  | 10 100 |
| 75 L | 0.57D, 3.43L | 10 600 |  | 10 600 |  |
| 50 L | 0.86D, 3.43L | 13 200 |  | 13 200 |  |
| 50 R | 0.86D, 1.15R |  | 5 100 |  | 10 100 |
| 50 V | 0.86D, 0 |  |  |  | 5 100 |
| 25 L | 1.72D, 9.0L |  | 1 250 |  | 1 700 |
| 25 R | 1.72D, 9.0R |  | 1 250 |  | 1 700 |
| Any point in zone III (bounded by the following coordinates in degrees) 8 L 8 L 8 R 8 R 6 R 1.5 R V-V 4 L 1 U 4 U 4 U 2 U 1.5 U 1.5 U H-H H-H | 625 |  | 625 |  |
| Any point in zone IV (0.86D to 1.72D, 5.15 L to 5.15 R) |  | 1 700 |  | 2 500 |
| Any point in zone I (1.72D to 4D, 9 L to 9 R) | 17 600 |  | < 2I* |  |

2.	The angular limits of ZONE I are 1.72D to 4D vertically and 9L to 9R horizontally. However, in the figure B in Annex 3, the lower limit of zone I is at 5°D. We propose to correct this inconsistency which appears in 01 series of amendments in the drawing.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.