## Slide 1: Proposals from IWG-R55 to GRRF-82
Minor corrections and clarifications
  Typos in Annex 5 figures 12 and 17
Submitted by the Secretary of the
IWG on Regulation No. 55
Informal document GRRF-82-02
82nd GRRF, 20-23 September 2016
Agenda item 5

## Slide 2: Proposals from IWG-R55 to GRRF-82
Minor corrections and clarifications
  Articulation angles as installed.
    5th-wheels pivoting around a transvers axis
      6° to the front and 7° to the rear
    Drawbars with drawbar couplings
      ±90° around a vertical axis
      ±20° around a transvers axis by rear mounted couplings
      ±6° around a transvers axis by underslung mounted couplings
        In this case the drawbar is considered to be an endless line starting in the coupling point

## Slide 3: Proposals from IWG-R55 to GRRF-82
Minor corrections and clarifications
  Identification of worst case for testing
    Clarification that worst case is supposed to be used
  Linguistic change in relation to calculation based approval of “simple designs”
    The word “check” is exchanged to “assessment”

## Slide 4: Proposals from IWG-R55 to GRRF-82
Attachment points for secondary coupling devices
  Broadened definition of secondary coupling device
    Addresses coupling devices in general rather than just Class B
  Attachment point required for towing bracket/drawbeam aimed at towing of O1 and O2 trailers.
    Location of a single or a double attachment point stated.
    Alternatively attachment point may be integrated to the coupling mounted on the towing bracket/drawbeam
  Attachment point required for coupling head/drawbar eye aimed at towing of O1 and O2 trailers.
  Performance and test requirements detailed

## Slide 5: Proposals from IWG-R55 to GRRF-82
Separation of approval process from application assessment
  Components can be approved without knowing anything about the vehicles where they will be installed.
    In essence definitions and the annexes 5 and 6 set the requirements
  The way application requirements are calculated sets the safety margin
  All application assessment formulae are moved in the new annex 8

## Slide 6: Proposals from IWG-R55 to GRRF-82
Adding multi vehicle combination assessment formulae
  The traditional two vehicle combination formulae are moved to annex 8
    Note, only the formula for full trailer can be used to decide towable mass, however then it is just one out of several decisive factors.
  Then the formulae for more than two vehicle combinations according to ISO18868 are added to annex 8
    These formulae are by necessity more complex
      Support structures e.g. web applications will supply easy to use vehicle combination assessment tools
      Vehicle combinations commonly seen in the roads today can then be assessed at the same safety level in different markets

## Slide 7: Proposals from IWG-R55 to GRRF-82
Adding Dc/V-trade-off possibility to annex 8
  Some multi vehicle combinations require high Dc-performance in combination with a low V-performance
OK, Practice of today
NOK, Practice of today
OK, Practice of tomorrow