## Slide 1: GTR – Tyres LIGHT TRUCK / C-TYPE HARMONIZED HIGH SPEED TEST
Status and Recommendation for GTR No. 16
GRBP September 2018
Document GRB-68-24
Agenda item 19

## Slide 2: High Speed Test for LT/C type Tyres
2014: GTR No. 16 (Tyre GTR) adopted with non-harmonized provisions for LT/C type tyres
Phase 2: Working to harmonize high speed test for LT/C type tyres
Two high speed tests listed in Tyre GTR:
  UNECE R 30 high speed test
  USA FMVSS 139 high speed test
Key test components that affect test severity:
  Test load
  Test temperature
  Test inflation pressure
Harmonization Goal:
Where multiple tests exist, select most severe test for each tyre type
Assessment Method:
For high speed test, assess test severity by speed rating

## Slide 3: Approach for Passenger Car Tyre HS Test Harmonization
Analysis UNECE Reg 30 HS test to the FMVSS 139 HS test
  For passenger tyres with speed symbol (“SS”) >/= T, agreed that Reg 30 HS was more severe
  For passenger tyres with SS </= S, agreed that FMVSS 139 HS was more severe
GTR-Tyres specifies these HS requirements in clauses 3.11.3 and 3.11.4
The HS analysis and agreement was based on testing tyres until reaching an ‘end of test’ condition and reporting the number of test steps above the appropriate minimum speed level (Steps Above Limit)
Industry used same approach to assess HS test for LT/C type tyres

## Slide 4: Non-harmonized High Speed Tests for LT/C type Tyres
UNECE R 54
~100%
~91%
60 min
~240 min

## Slide 5: Initial Assessment of LT/C HS Test Severity
Earlier data mining, analyses and limited testing (circa 2013) validated:
  SS >/= S ECE Reg 54 HS was more severe
  SS </= Q FMVSS 139 HS was more severe
  SS = R relative severity was inconclusive
ECE Reg 54 HS Test is a more ‘efficient’ test
  Does not include 2 hour break-in and resulting cool down (FMVSS 139 carry over provision from bias tyres; no longer justified)
  60 minute Reg 54 test duration vs 90 minute FMVSS 139
  Over 3 hour shorter duration test

## Slide 6: Industry test program for SS </= R (2017)
Agreed to validate for SS Q; apply same solution for SS R
Tested all tyres to SS Q limit (160 km/h) regardless of actual tyre speed symbol
Increased temperature of Reg 54 HS test to 38°C ambient to increase test severity
All results based on SAL test analysis (same as earlier passenger tyre HS test analysis)
SAL for both Modified Reg 54 & FMVSS 139: 10 minutes @ + 5 km/h

## Slide 7: Testing Summary (2017)
Seven Manufacturers / test locations
29 tyre pairs tested (1 to FMVSS 139; 1 to Modified Reg 54)
Wide variety of tyres representative of global market:
  17 C-type tyres
  11 LT-Metric
  1 High Flotation
Tyre Types in Study:
  13 “Summer” (normal tyres)
  6 Winter (3PMSF; includes one all-terrain with 3PMSF)
  7 All Season (include one all-terrain w/o 3PMSF)
  3 not identified

## Slide 8: Testing Summary (continued)
Speed Symbols (all tyres tested to Q conditions)
  2 tyres SS Q − 5 tyres SS S
  21 tyres SS R − 1 tyre SS T
Load Index (Range of ‘Single’ Load Index values)
  LI 102 – 110 - 10 tyres
  LI 111 – 116 - 7 tyres
  LI 120 – 125 - 12 tyres
Load Range (“LR”) (17 of 29 tyres are DOT marked; other have no LR marked)
  LR C 1 tyre
  LR D 3 tyres
  LR E 13 tyres

## Slide 9: LT/C HS Test Results
Each manufacturer followed internal guidelines for test removal criteria
Results analyzed by Steps Above Limit (SAL) Ratio
  # SAL FMVSS ÷ # SAL Modified Reg 54
  Ratio of 1.00 is equal severity; > 1.00 means Reg 54 is more severe
Dispersion rates were typical of HS testing, but could be reduced with additional replicate testing
Industry members opted for greater variety of tyre types, sizes, manufacturers instead of replicate testing of fewer SKUs.
Results showed FMVSS 139 test and the modified Reg 54 test to be equal in severity, with overall average SAL of 0.99 to 1.01, depending on analysis method

## Slide 10: Harmonized LT/C High Speed Recommendation
Previous industry recommendations acknowledged by CPs:
  Tyres with SS >/= S: Existing ECE Reg 54 HS test
    Final test speeds are based on the speed symbol of the tyre
    20° to 30°C ambient temperature
Current industry recommendations for consideration by CPs:
  Tyres with SS = R: test to 170 km/h (106 mph) at 38°C ambient temperature*
  All tyres with SS </= Q: test to 160 km/h (99 mph) at 38°C ambient temperature*
10
* proposed 36.5 °C ± 1.5°C (TBC)