## Slide 1: Proposals from the Informal Working Group on AEBS to amend UN R. No. 152
Informal Working Group on AEBS for Light Vehicles
Informal document WP.29-182-19
182nd WP.29, 10-12 Nov. 2020 Item 3.6.4.
Car to Bicycle scenario in the regulation (Slides based on GRVA-07-70)

## Slide 2
Chair and Secretary IWG AEBS – GRVA 07
Informal Working Group on AEBS for Light Vehicles
Car to Bicycle scenario

## Slide 3
Informal Working Group on AEBS for Light Vehicles
Final Specifications in GRVA-2020-27 or 28 - Car to Bicycle – Speed reduction
Maximum Impact Speed (km/h) for M1
Maximum Impact Speed (km/h) for N1
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
38 | 0.00 | 0.00
40 | 10.00 | 0.00
45 | 25.00 | 25.00
50 | 30.00 | 30.00
55 | 35.00 | 35.00
60 | 40.00 | 40.00
Subject vehicle speed (km/h) | Maximum mass | Mass in running order
20 | 0.00 | 0.00
25 | 0.00 | 0.00
30 | 0.00 | 0.00
35 | 0.00 | 0.00
36 | 0.00 | 0.00
38 | 15.00 | 0.00
40 | 25.00 | 0.00
45 | 30.00 | 25.00
50 | 35.00 | 30.00
55 | 40.00 | 35.00
60 | 45.00 | 40.00
Chair and Secretary IWG AEBS – GRVA 07
IWG proposed two options for existing vehicles.
Single step: full collision avoidance from 20km/h from 5/2026
2 step: full collision avoidance from 30km/h from 5/2026
20 km/h from 9/2028

## Slide 4
Informal Working Group on AEBS for Light Vehicles
Difference between single step and 2 step: Summary
Approaches | Suppl. or Series | New Type Approvals | Existing Type Approvals
Single step approach | Car-to-bicycle (as a Suppl. 2 to the 01 series) | May 2024 | Can be mandated as from May 2026
2 step Approach (more info in GRVA-07-12) | Car-to-bicycle – Step 1 (as a Suppl. 2 to the 01 series) | Date of Entry Into Force and before May 2024 | Shall be accepted until September 2028
 | Car-to-bicycle – Step 2 (as a new 02 series) | May 2024 | Can be mandated as from September 2028
Chair and Secretary IWG AEBS – GRVA 07