| E/ECE/324 E/ECE/TRANS/505 |  | Rev.1/Add.88/Corr.1 |
| --- | --- | --- |
| 24 June 2008 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 88:  Regulation No. 89

## Corrigendum 1

#### Corrigendum 1 to the original version of the Regulation, subject of Depositary Notification C.N.250.2008.TREATIES-1 dated 8 April 2008

Uniform provisions concerning the approval of:

I.	Vehicles with regard to limitation of their maximum speed or their adjustable speed limitation function

II.	Vehicles with regard to the installation of a speed limiting device (SLD) or adjustable speed limitation device (ASLD) of an 	approved type

III.	Speed limitation devices (SLD) ) and adjustable speed limitation device (ASLD)

_________

### UNITED NATIONS

Paragraph 2.1.3., correct to read:

"2.1.3.	"Stabilized speed Vstab" means the mean vehicle speed specified in paragraph 1.1.4.2.3.3. of Annex 5 and in paragraph 1.5.4.1.2.3 of Annex 6 to this Regulation;"

Annex 5

Paragraph 1.1.4.2.2.3., correct to read:

"1.1.4.2.2.3.	the stabilized speed conditions specified in paragraph 1.1.4.2.3. shall be attained within 10 s of first reaching Vstab;"

Paragraph 1.1.4.3.3.3. (former), renumber as paragraph 1.1.4.2.3.3. (French text only).

Annex 6, paragraph 1.5.4.1.1.3., correct to read:

"1.5.4.1.1.3.	the stabilized speed conditions specified in paragraph 1.5.4.1.2. shall be attained within 10 s of first reaching Vstab;"

Annex 6, paragraph 1.5.4.1.2.1., correct to read:

"1.5.4.1.2.1.	speed shall not vary by more than 3 km/h of Vstab;"

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

GE.08-