|  | E/ECE/324/Rev.1/Add.66/Rev.3/Amend.3−E/ECE/TRANS/505/Rev.1/Add.66/Rev.3/Amend.3 |
| --- | --- |
|  |  | 24 June 2014 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 66 – Regulation No. 67

Revision 3 - Amendment 3

Supplement 13 to the 01 series of amendments – Date of entry into force: 10 June 2014

Uniform provisions concerning the approval of:

I.	Specific equipment of vehicles of category M and N using liquefied petroleum gases in their propulsion system

II.	Vehicles of category M and N fitted with specific equipment for the use of liquefied petroleum gases in their propulsion system with regard to the installation of such equipment

_________

UNITED NATIONS

Insert a new paragraph 2.20., to read:

"2.20.	"Hose assembly" means an assembly of a flexible hose and couplings;"

Paragraphs 9.6. and 9.6.1., amend to read:

"9.6.	Every hose assembly which is applied in the high pressure class (Class 1) according to the classification as prescribed in paragraph 2. of this Regulation, shall, during half a minute, be subjected to a test with gas under a pressure of 3,000 kPa by the approval holder.

9.6.1.	Every hose assembly which is applied in the high pressure class (Class 0) according to the classification as prescribed in paragraph 2. of this Regulation, shall, during half a minute, be subjected to a test with gas under a pressure of the declared WP by the approval holder."

Insert a new paragraph 17.1.2.1., to read:

"17.1.2.1.	Notwithstanding the provisions of paragraph 17.1.2., if the LPG electronic control unit is integrated into the engine electronic control unit and is covered with a vehicle installation type approval according to Part II of this Regulation and to Regulation No. 10, no separate type approval of the LPG electronic control unit is necessary. The vehicle type approval shall also be approved pursuant to the applicable provisions laid down in Annex 14 of this Regulation."

Annex 8, insert a new paragraph 2.7.1., to read:

"2.7.1.	If hose and couplings are not assembled by the approval holder, the approval shall consist of:

(a)	Hose;

(b)	Couplings; and

(c)	Assembly instruction.

The assembly instruction shall be written in the language of the country to which the type of hose or couplings will be delivered, or at least in English. It shall include detailed characteristics of equipment used for the assembly operation."

Paragraphs 2.7.1. to 2.7.3.1. (former), renumber as paragraphs 2.7.2. to 2.7.4.1.

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.