|  | E/ECE/324/Rev.2/Add.116/Rev.3/Corr.1−E/ECE/TRANS/505/Rev.2/Add.116/Rev.3/Corr.1 |
| --- | --- |
|  |  | 8 May 2014 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 116 – Regulation No. 117

Revision 3 - Corrigendum 1

Corrigendum 4 to 02 series of amendments – Date of entry into force: 12 March 2014

Uniform provisions concerning the approval of tyres with regard to rolling sound emissions and/or to adhesion on wet surfaces and/or to rolling resistance

_________

UNITED NATIONS

Annex 7,

Paragraph 3.1.1., correct to read:

"3.1.1.	Test course

The braking tests shall be done on a flat test surface of sufficient length and width, with a maximum 2 per cent gradient, covered with packed snow.

The snow surface shall be composed of a hard packed snow base at least 3 cm thick and a surface layer of medium packed and prepared snow about 2 cm thick.

The air temperature, measured about one meter above the ground, shall be between -2 °C and -15 °C; the snow temperature, measured at a depth of about one centimetre, shall be between -4 °C and -15 °C.

…"

Appendix 2,

Paragraph 2.1., correct the table to read:

"

|  | At start of tests | At end of tests | Specification |
| --- | --- | --- | --- |
| Weather |  |  |  |
| Ambient temperature |  |  | -2 °C to -15 °C |
| Snow temperature |  |  | -4 °C to -15 °C |
| CTI index |  |  | 75 to 85 |
| Other |  |  |  |

"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.