| E/ECE/324/Rev.1/Add.47/Rev.6/Amend.5/Corr.1−E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Amend.5/Corr.1 |
| --- |
|  |  | 7 June 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 47: Regulation No. 48

Revision 6 – Amendment 5 – Corrigendum 1

Corrigendum 1 to the 05 series of amendments to the Regulation, subject of Depositary Notification C.N.156.2011.TREATIES-4 dated 28 April 2011

Uniform provisions concerning the approval of vehicles with regard to the installation of lighting and light-signalling device

UNITED NATIONS

Paragraph 6.2.7.6.1., amend to read:

"6.2.7.6.1.	The dipped-beam headlamps shall be switched ON and OFF automatically relative to the ambient light conditions (e.g. switch ON during nighttime driving conditions, tunnels, etc.) according to the requirements of Annex 13; or"

Paragraph 6.2.7.6.3.3., amend to read:

"6.2.7.6.3.3.	A tell-tale visual, auditory or both, shall be activated only in reduced ambient lighting conditions as defined in Annex 13 to inform the driver that the dipped beam headlamps should be switched ON. Once the tell-tale is activated, it shall only be extinguished when the dipped beam headlamps have been switched on or the device which starts and/or stops the engine (propulsion system) is set in a position which makes it impossible for the engine (propulsion system) to operate."

Paragraph 12.22., correct to read:

"12.22.	As from 48 months from the official date of entry into force of the 05 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by the 05 series of amendments. However, as from 66 months for new vehicles types of categories M1 and N1 and 84 months for new vehicle types of other categories after the official date of entry into force of the 05 series of amendments to this Regulation, Contracting Parties applying this Regulation shall grant approvals only if the new vehicle type to be approved meet the requirements of this Regulation as amended by the 05 series of amendments excluding paragraphs 6.2.7.6.2. and 6.2.7.6.3. to 6.2.7.6.3.3. Existing approvals under this Regulation granted before these dates will remain valid indefinitely and extensions of these approvals shall continue to be granted after."

Paragraph 12.27., shall be deleted.

Annex 12, renumber as Annex 13.

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.