| E/ECE/324/Rev.1/Add.47/Rev.6/Corr.4−E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Corr.4 |
| --- |
|  |  | 7 June 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 47: Regulation No. 48

Revision 6 – Corrigendum 4

Corrigendum 3 to Revision 6 of the Regulation, subject of Depositary Notification C.N.184.2011.TREATIES-5 dated 28 April 2011

Uniform provisions concerning the approval of vehicles with regard to the installation of lighting and light-signalling devices

UNITED NATIONS

Paragraph 5.21.1., amend to read:

"5.21.1.	Additional lamps satisfying all the position, geometric visibility, colorimetric and photometric requirements for the above indicated lamps shall be activated when the apparent surface in the direction of the reference axis of these lamps is more than 50 per cent hidden by the movable component; or"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.