| E/ECE/324/Rev.1/Add.47/Rev.6/Corr.1−E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Corr.1 |
| --- |
|  |  | 27 October 2010 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 47: Regulation No. 48

Revision 6 – Corrigendum 1

Corrigendum 2 to Supplement 3 to the 04 series of amendments to the Regulation, subject of Depositary Notification C.N.557.2010.TREATIES-9 dated 3 September 2010

Uniform provisions concerning the approval of vehicles with regard to the installation of lighting and light-signalling devices

UNITED NATIONS

Paragraph 5.7.2.1, amend to read:

“5.7.2.1. 	Either the total area of the projection of the distinct parts on a plane tangent to the exterior surface of the outer lens and perpendicular to the reference axis shall occupy not less than 60 per cent of the smallest quadrilateral circumscribing the said projection, or the distance between two adjacent/tangential distinct parts shall not exceed 15 mm when measured perpendicularly to the reference axis. This requirement shall not apply to a retro-reflector.”

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.