|  |  | 4 June 2012 |
| --- | --- | --- |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 48: Regulation No. 49

Revision 5 – Corrigendum 1

Corrigendum 1 to Revision 5 of the Regulation - Date of entry into force:  14 March 2012

Uniform provisions concerning the measures to be taken against the emission of gaseous and particulate pollutants from compression-ignition engines for use in vehicles, and the emission of gaseous pollutants from positive-ignition engines fuelled with natural gas or liquefied petroleum gas for use in vehicles

UNITED NATIONS

Paragraph 2.1.65., correct to read:

"2.1.65.	"Unladen ... driver of 75 kg, passengers or load, ..."

Annex 2A,

Appendix,

First paragraph, correct to read:

"As noted in Appendix 5 to Annex 1 ..."

Annex 4A,

Appendix 2,

Pparagraph 3.8.2.2., correct to read:

"3.8.2.2.		Raw exhaust measurement

...

For calculation ... Therefore, the response time of the exhaust gas mass flow system and each gaseous emissions analyzer shall be determined ..."

Annex 4B,

Paragraph 6.9., correct to read:

"6.9.	Specification of the reference fuel

The reference fuel ... for C.I. engines and in Annex 5 for CNG and LPG fuelled engines ...

..."

Paragraph 7.4.7., correct to read:

"7.4.7.	...

If auxiliaries/equipment are fitted in accordance with paragraph 6.3.1. and Appendix 7, Mf  and Mr are zero.

..."

Paragraph 8.4.1.1., correct to read:

"8.4.1.1.	Introduction

For calculation ... For the determination of the exhaust mass flow rate one of the methods described in paragraphs 8.4.1.3 to 8.4.1.7. may be used."

Paragraph 8.4.1.2., correct to read:

"8.4.1.2.	Response time

For the purpose of ... one of the methods described ...

…"

Paragraph 8.4.1.5., correct to read:

"8.4.1.5.	Tracer measurement method

…

ρe is the density of the exhaust gas, kg/m³ (cf. Table 5)

…"

Paragraph 9.2.1.1.., correct to read:

"9.2.1.1.	Introduction

A linearity ... Table 7 refer to the maximum ..."

Paragraph 9.3.2.7., correct to read:

"9.3.2.7.	Air to fuel measurement

The air to fuel ... in paragraph 8.4.1.6. shall ...

..."

Paragraph 9.3.8., correct to read:

"9.3.8.		Efficiency of the non-methane cutter (NMC)

... of the NMHC emission mass flow rate (see paragraph 8.6.2.)."

Paragraph 9.4.5.6.., correct to read:

"9.4.5.6.	Calibration of the flow measurement instrumentation

... requirements of this Regulation. For the flow reference values ... "

Paragraph 9.4.6.1., correct to read:

"9.4.6.1.	System response time

For the control ... (see paragraph 8.4.1.2.) and the partial flow ...

..."

Paragraph 9.4.6.2., correct to read:

"9.4.6.2.	Specifications for differential flow measurement

…

(b)	... For details see paragraph 9.4.6.3.

…"

Paragraph 9.5.4., correct to read:

"9.5.4.	Calibration of the subsonic venturi (SSV)

Calibration of the ... in equation 53 (see paragraph 8.5.1.4.)."

Paragraph 9.5.5., correct to read:

"9.5.5.	Total system verification

The total accuracy ... paragraph 8.5.2.3. except ..."

Appendix 6,

Paragraph A.6.3., correct to read:

"A.6.3.	Gaseous emissions (diesel fuel)

…

Step 3: ... the cycle (paragraph 8.4.2.3. of this annex)

…

Step 4: ... Table 5 (paragraph 8.4.2.3. of this annex)

..."

Annex 4C,

Paragraph 5.1., correct to read:

"5.1.		Time alignment

For partial ... to paragraph 1.3.7. of Appendix 1 to this annex."

Annex 9B,

Paragraph 4.2.1., correct to read:

"4.2.1.	Selection of the monitoring technique

Approval authorities ...  (i.e. through technical ..."

Paragraph 4.5., correct to read:

"4.5.	Requirements for malfunction classification

...

If an MECS ... The malfunction shall then be assigned to the class that takes precedence in the discriminatory display strategy."

Annex 9C,

Paragraph 7.1., correct to read:

"7.1.	...

The OBD system ... in Appendix 6 to Annex 9B) for the ...

..."

Annex 10,

Paragraph 5.1.2., correct to read:

"5.1.2.	...

(d)		Its operation ... tests. The overall effect of such an ..."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.