| E/ECE/324/Rev.1/Add.93/Rev.1/Corr.2−E/ECE/TRANS/505/Rev.1/Add.93/Rev.1/Corr.2 |
| --- |
|  |  | 15 July 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 93: Regulation No. 94

Revision 1 – Corrigendum 2

Corrigendum 2 to Revision 1 of the Regulation, subject of Depositary Notification C.N.562.2019.TREATIES-1 dated 17 September 2009

Uniform provisions concerning the approval of vehicles with regard to the protection of the occupants in the event of a frontal collision

UNITED NATIONS

Annex 3,

Paragraph 2.1.1., amend to read:

"2.1.1. 	A dummy corresponding to the specifications for HYBRID III 1/ fitted with a 45º ankle and meeting the specifications for its adjustment shall be installed in each of the front outboard seats in accordance with the conditions set out in Annex 5.  The ankle of the dummy shall be certified in accordance with the procedures in Annex 10."

Annex 5,

Paragraph 2.4.3.1., amend to read:

"2.4.3.1. "H" point

The "H" point of the driver and passenger test dummies shall coincide within 13 mm in the vertical dimension and 13 mm in the horizontal dimension, with a point 6 mm below the position of the "H" point determined using the procedure described in Annex 6 except that the length of the lower leg and thigh segments of the "H" point machine shall be adjusted to 414 and 401 mm, instead of 417 and 432 mm respectively."

Annex 10,

Paragraph 1.2., amend to read:

"1.2. 	The complete Hybrid III lower leg assembly, left (86-5001-001) and right (86-5001-002), equipped with the foot and ankle assembly, left (78051-614) and right (78051-615), shall be used, including the knee assembly.

The load cell simulator (78051-319 Rev A) shall be used to secure the knee assembly (79051-16 Rev B) to the test fixture."

Annex 10,

Paragraph 2.2., amend to read:

"2.2.	The complete Hybrid III lower leg assembly, left (86-5001-001) and right (86-5001-002), equipped with the foot and ankle assembly, left (78051-614) and right (78051-615), shall be used, including the knee assembly.

The load cell simulator (78051-319 Rev A) shall be used to secure the knee assembly (79051-16 Rev B) to the test fixture."

Annex 10,

Paragraph 3.2., amend to read:

"3.2. 	The complete Hybrid III lower leg assembly, left (86-5001-001) and right (86-5001-002), equipped with the foot and ankle assembly, left (78051-614) and right (78051-615), shall be used, including the knee assembly.  The load cell simulator (78051-319 Rev A) shall be used to secure the knee assembly (79051-16 Rev B) to the test fixture.  The foot shall be fitted with the shoe specified in Annex 5, paragraph 2.9.2."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.