| E/ECE/324/Rev.2/Add.109/Rev.1/Amend.2−E/ECE/TRANS/505/Rev.2/Add.109/Rev.1/Amend.2 |
| --- |
|  |  | 4 October 2010 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 109: Regulation No. 110

Revision 1 – Amendment 2

Supplement 9 to the original version of the Regulation: Date of entry into force: 19 August 2010

Uniform provisions concerning the approval of:

I.	Specific components of motor vehicles using compressed natural gas (CNG) in their propulsion system;

II.	Vehicles with regard to the installation of specific components of an approved type for the use of compressed natural gas (CNG) in their propulsion system

UNITED NATIONS

Insert a new paragraph 17.9.4., to read:

“17.9.4. 	For vehicles of categories M2, M3, N2 and N31, the filling unit (receptacle) shall comply with the drawing specifications detailed in Figure 2 of Annex 4F or with the drawing specifications detailed in Figure 1 of Annex 4F”.

Annex 4F,

Paragraph 2.1., amend to read:

“2.1.	The filling unit shall comply with the requirements laid down in paragraph 3. and shall have the dimensions of paragraph 4.”

Paragraph 2.2., amend to read (including the insertion of a new footnote 2):

“2.2.	Filling units designed in accordance with ISO 14469-1 first 
edition 2004-11-011 or ISO 14469-2:20072 and meeting all the requirements therein are deemed to fulfill the requirements of paragraphs 3. and 4. of this annex.

____________________

2	Road vehicles — Compressed natural gas (CNG) refueling connector — Part 2: 20 MPa (200 bar) connector, size 2”

Paragraph 4.1., footnote 2 should be renumbered as footnote 3

Insert a new paragraph 4.2., to read:

“4.2.	Figure 2 shows the dimensions of the filling unit for vehicles of categories M2, M3, N2 and N33”

Insert, after Figure 1, a new Figure 2, to read:

# “Figure 2

# 20 MPa Filling unit Size 2 (receptacle) for M2, M3, N2 and N3 vehicles

”

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, don’t at Geneva on 20 March 1958.