| E/ECE/324 E/ECE/TRANS/505 |  | Rev.2/Add.107/Corr.2 |
| --- | --- | --- |
| 24 June 2008 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 107:  Regulation No. 108

## Corrigendum 2

#### Corrigendum 2 to the original version of the Regulation, subject of Depositary Notification C.N.256.2008.TREATIES-1 dated 9 April 2008

Uniform provisions concerning the approval for the
production of retreaded pneumatic tyres
for motor vehicles and their trailers

_________

### UNITED NATIONS

Annex 7, insert a new paragraph 2.5.7., to read:

"2.5.7.	however, for tyres suitable for maximum speed of 300 km/h (speed symbol "Y"), the duration of the test is 20 minutes at the initial test speed step and 10 minutes at the last speed step."

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

GE.08-