Informal Document No. 5

30th GRSP, 3-6 December 2001,

Agenda Item 1.3.1.)

# PROPOSAL FOR DRAFT AMENDMENTS TO ECE REGULATION No. 16 (Safety-belts)

# (TRANS/WP.29/GRSP/2001/23)

# TRANSMITTED BY EXPERT FROM JAPAN

# Background

This document is intended to complete the draft proposal of TRANS/WP.29/GRSP/2001/23.

Note:

Words added to proposed texts in TRANS/WP.29/GRSP/2001/23, are underlined.

*Proposed paragraph 6.4.1.2.5, amend to read:

        - In the case of a safety-belt with tension-reducing device, it shall be subjected to a durability test with such a device in operation mode according to paragraph 6.2.5.2.3. or 6.2.5.3.5. before a dynamic test. The dynamic test shall be then conducted on condition that the tension-reducing device is in operation mode.

# JUSTIFICATION (6.4.1.2.5)

It is necessary to take into account if the retractor is ALR.

*Paragraph 7.6.4.2, amend to read:

      - Before the dynamic test described in paragraph 7.7 the seated dummy which is clothed with a cotton shirt shall be tilted frontward until 350 mm of the strap withdrawn from retractor, and then release to the initial position.

# JUSTIFICATION (7.6.4.2)

This is to adopt the existing requirement of ECE R16.

*******