Turkey

Instruction Manual of Radiation Detection System at Border Gates

- There should be a book of record in every gate where the radiation detection system exists.

Every page of this book should be stamped and signed by the competent custom

chief.

- The above mentioned book of record comprises parts of date, time, information about shift change, condition of the system and a section for explanation.

3.    Change of shift should be done after checking the system with calibration source.

4.    Customs enforcement officer should make all necessary controls and

measurements for the system as described in the radiation detection system user manual.

If there is an increase in the radiation level when a vehicle passes through the port of entry,

the vehicle that carries the suspected goods should be moved to a solitary place which is

under the control of customs enforcement administration instead of forwarding it to the

customs administration for customs formalities. Then, a security zone should formed around

the vehicle to prevent anyone from contacting the radioactive material. After taking all these

precautions the vehicle should be investigated with the hand-held detector.

- For every alarm case Nuclear and Radioactive Material Incident Notification Form

(Example-2)  should be filled and sent to TAEK (0 312 287 87 61) via fax  and also it should

be confirmed by phone (0 312 287 52 46 – 0 312 287 57 23) that it is received by TAEK.

6.     If there is need for a declaration of an incident to TAEK at the weekends, formal holidays and

after working hours, the custom enforcement officers should have to call TAEK security

officers on duty from the number 0 312 287 15 29 so as to inform TAEK from the incident.

Also again they have to fill nuclear and radioactive material incident notification form and sent

to TAEK via fax.

7.     TAEK should evaluate the incident as soon as possible and sent its decision to the relevant

custom enforcement via fax.

8.     Relevant custom enforcement administration should have to make the necessary

transactions according to TAEK’s evaluations and should inform the General Directorate.

9.      If the goods that contain the radioactive material have a control certificate, this certificate

should also attached to nuclear and radioactive incident notification form and should be sent

to TAEK via fax. The officer who filled this notification form should also state his/her name,

surname,  title and employment record number and his/her signature on the form. This form

should be kept in a dossier.(if the gate  is included in ”Denunciation and Land Gate

Prosecution Program” the necessary information about the incident should be stated in the

explanation section of this program.)

10.    If the custom enforcement administration have only the radiation pagers, they have to fill

only necessary sections related with radiation pagers in the Nuclear and Radioactive

Material Incident Notification Form and should follow the instructions stated above.

11.   So as to avoid the vehicles to hit the panel detectors, custom enforcement should have to

take the necessary precautions.

12.    In the case of any strike of vehicles to panel detectors or any fail in the system because of

different cause, should be stated as a report, describing clearly  the cause of incident and the

condition of the system. Custom enforcement should inform General Directorate about the

event immediately.

- In the case of a failure in the panel detectors, the usual controls should be performed by

hand-held detectors.