## Slide 1: Status Report to 78th Session of GRBP (August 2023)
New Task Force on Quiet Road Transportation Vehicle (UN-R138-02)
Transmitted by Secretary of New TF QRTV
Informal Document GRBP-78-11
78th GRBP, 30 August - 1 September 2023,
agenda item 6

## Slide 2: New TF Quiet Road Transportation Vehicle
Targets
Roles
TF QRTV homepage
Improve boundary condition for AVAS and interaction with R51
Improve stability of test results
Minimize uncertainty
Chair: Germany
Secretariat: OICA
New TF-QRTV (UN-R138-02) - Transport - Vehicle Regulations - UNECE Wiki
Participants
CPs.: Canada, France, Germany, Switzerland, Netherland, Spain, United Kingdom, Japan, China, European Commission, Norway
NGO‘s: OICA, ETRTO, ISO, IMMA, NFB,EBU

## Slide 3: Current status for first step
The TF QRTV worked to find a balance between Safety and Environmental aspects
Measurement uncertainty reduction is possible by change the data analyzing method and the option to use five instead of one microphone for Over All Sound pressure level and 1/3 Octave band per side as proposed by ISO
Mandatory speed range is between -20 and +20 km/h
Mandatory test speeds during type approval are -6 km/h . +10 und +20 km/h, other not tested speeds have to be declared by manufacturer declaration
Optional AVAS sound between > 20 and 50 km/h, with noise level reduction > 32 km/h following the maximum level requirements
Maximum SPL of 75 dB(A) at 2 m distance has to be fulfilled also in opposite driving direction.
Therefore at indoor testing the maximum SPL shall be measured in the front and the rear of the vehicle to ensure the complete vehicle has no higher sound emission than allowed

## Slide 4: Next steps and open questions
No stationary sound in “P” allowed
Stationary in „D“ and „R“ is under discussion. National Federation of the Blind and European Blind Union appreciate sound under these conditions, with environmental impact.
To avoid unexpected solutions BEV with sound enhancement systems will have to fulfil R51 with document for reference GRB68-03 with much lower tolerances for BEV compare to ICE

## Slide 5: Details
Mandatory speed range: At any speed greater 0 up to including 20 km/h, reverse and forward, a sound shall be emitted. Nominal test speeds are 6 km/h in reverse, 10 und 20 km/h in forward direction. The tolerance for speed changed from ±1 km/h to +2 km/h of test with rolling tyres
Stepwise minimum SPL changes between or around the tested speeds
Type approval nominal test speeds are 6 km/h in reverse, 10 und 20 km/h in forward direction. The tolerance changed from ±1 km/h to +2 km/h
Manufacturer declaration for all the not tested speeds during type approval
Method (E), component test, has been deleted
For measurements indoors two additional microphones are necessary to measure the maximum noise level on both ends of the vehicle
COP requirements in case of a physical tests are only Over All level tests, not 1/3rd octave band test