## Slide 1: IWG on Electromagnetic Compatibility (IWG EMC) Status report to GRE-90 April / May 2023
Informal document GRE-90-33
90th GRE, 29 April - 03 May 2024
Agenda item 8
Submitted by the experts of IWG EMC

## Slide 2
Proposal for a new 07 series of amendments to UN Regulation No. 10:
The frequency range of electromagnetic immunity test was extended to 6 GHz in order to ensure robustness regarding state-of-the-art mobile services (e.g. mobile phone standards and wireless networks, 4G, 5G, Wi-Fi).
The reverberation chamber for ESA electromagnetic immunity test was introduced. This test method is a state-of-the-art immunity test method.
The minimum number of steady state operating conditions of vehicle propulsion systems have to be considered in the test plan. This is necessary because the default test conditions may not trigger all intended operating modes.
Definitions regarding automated driving systems (ADS), Acoustic Vehicle Alerting System (AVAS), Accident Emergency Call Systems (AECS) were introduced as well as additional operating conditions and failure criteria have been defined for those systems.
New flow charts have been developed for each concerned annex to clarify which charge mode must be conducted with which cable.
New alternative test methods have been created for longer, wider or higher vehicles with the aim to have a harmonized testing procedure of these vehicles.
IWG EMC - Status Report

## Slide 3
Road map for a new 08 series of amendments to UN Regulation No. 10:
IWG EMC - Status Report
2024
The working group develops new topics and regulatory objectives
2025 / 26
Discussions based on technical documents
2026 / 27
Drafting a working document for the 08 series of amendments

## Slide 4
Topics for a new 08 series of amendments to UN Regulation No. 10:
IWG EMC - Status Report
AECS during immunity test
Whole vehicle approval based on ESAs only
Emission limits for electric vehicles in charging mode
New technologies on charging modality in the vehicle
Peak detector as method of measurement
Normal conditions of use (2nd phase)
ADS suitability (screening of the Regulation)
Reverberation chamber for vehicle immunity test
Requirements for bi-directional charging
Investigate on replacement of pulse 4 reference
Better definition of current not conductive charging mode
Off-board receivers below 30 MHz
Electrostatic discharge
Virtual Testing

## Slide 5
Future planning and outlook:
The working group is continuing its work with the aim to develop the 8th series of amendments
IWG-EMC-45: 6 September 2024. Online
IWG-EMC-46: 28 November 2024. Bonn, Germany
IWG EMC - Status Report