Distr.

# GENERAL

# TRANS/WP.29/GRE/2002/49

21 August 2002

# ENGLISH ONLY

# Economic COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonisation of Vehicle Regulations (WP.29)

# Working Party on Lighting and Light-Signalling (GRE)

(Forty-ninth session, 30 September - 4 October 2002,

agenda item 2.5.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 86

(Installation of lighting and light-signalling devices for tractors)

# Transmitted by the Expert from Poland

Note:	The text reproduced below was prepared by the expert from Poland, on the basis of informal document No. 3 of the forty-seventh GRE session, in order to increase the maximum design speed of agricultural and forestry tractors (TRANS/WP.29/GRE/48, para. 35).  The suggested amendment is marked in bold characters.

______________

__________

Note:	This document is distributed to the Experts on lighting and light-signalling only.

## A.	PROPOSAL

Paragraph 1.2.1., amend to read:

"1.2.1.	agricultural or forestry tractors, as defined in paragraph 2.1. below, which are fitted with pneumatic tyres and which have at least two axles and a maximum design speed of between 6 and 40 km/h."

*      *     *

B.	JUSTIFICATION

1.	At present the maximum design speed of large number of the modern agricultural or forestry tractors exceeds 30 km/h.

2.	The Directive 97/54/EC of the European Parliament and of the Council of 23rd September 1997 increases the maximum design speed of wheeled agricultural and forestry tractors from 30 km/h to 40 km/h.

3.	It therefore became necessary to amend paragraph 1.2.1. of Regulation No. 86 by increasing the speed under consideration.

_____________________