#### INF. 36

##### Working Party on the Transport

of Dangerous Goods

(Seventyfirst session,

(Geneva, 5 -9 November 2001)

Part 7 of ADR

Chapter 7.2 Provisions concerning carriage in packages

Transmitted by the Government of Norway

|  | SUMMARY |
| --- | --- |
| Executive Summary: | Provision “V7” of 7.2.4 gives rise to problems of interpretation and practical problems for the transport operators. Norway raised this issue in a proposal at the seventieth session. The proposal was not adopted in the form presented, but EIGA volunteered to help Norway formulating a text that would cover Norway’s concerns as well as taking care of the safety issues in transporting gasses in closed vehicles/containers. This work is now finalized and presented below. |
| Action to be taken: | Change the text provision “V7” into an operational requirement instead of the present technical requirement for the construction of vehicles and containers. |
| Related documents: | TRANS/WP.15/2001/19 |

##### Proposal

Change the wording of  “V7” to read:

“Packages shall preferably be carried in open or ventilated vehicles

or in ventilated containers.

Should packages be carried in a closed vehicle or a closed

container, the nature of the contents and the possibility that leakage may

have caused an unsafe concentration of toxic or flammable gases/vapours or

have produced an oxygen enriched or depleted atmosphere shall be considered

before opening the doors.  Sources of ignition shall not be present in a

closed vehicle or closed container when flammable gases are carried.”

----------- o o o -------------