| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.2/2002/4 15 March 2002 ENGLISH Original: FRENCH |

### ECONOMIC COMMISSION FOR EUROPE

### INLAND TRANSPORT COMMITTEE

Working Party on the Transport

of Dangerous Goods

Joint Meeting of Experts on the Regulations

annexed to the European Agreement concerning

the International Carriage of Dangerous Goods

by Inland Waterways (ADN)*

(Sixth session, Geneva, 27-30 May 2002)

RESTRUCTURING OF THE REGULATIONS ANNEXED TO (ADN)

# Note by the secretariat**

The secretariat reproduces below Table C of Chapter 3.2 in Part 3 of the restructured ADN and the explanations concerning the table.

* This meeting is organized jointly by the Economic Commission for Europe and the Central Commission for the Navigation of the Rhine.

**  Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR-ZKR/ADN/WP.15/AC.2/2002/4.

GE.02-21162  (E)    130502    280502

# 3.2.3	Table C

# List of dangerous goods accepted for carriage

# in tank vessels in numerical order

### Explanations concerning Table C

As a rule, each row of Table C deals with the substance(s) covered by a specific UN number.  However, when substances or articles belonging to the same UN number have different chemical properties, physical properties and/or carriage conditions, several consecutive rows may be used for that UN number or substance identification number.

Each column of Table C is dedicated to a specific subject as indicated in the explanatory notes below. The intersection of columns and rows (cell) contains information concerning the subject treated in that column, for the substance(s) of that row:

- The first four cells identify the substance(s) belonging to that row;

- The following cells give the applicable special provisions, either in the form of complete information or in coded form.  The codes cross-refer to detailed information that is to be found in the numbers indicated in the explanatory notes below.  An empty cell means either that there is no special provision and that only the general requirements apply, or that the carriage restriction indicated in the explanatory notes is in force.

The applicable general requirements are not referred to in the corresponding cells.

### Explanatory notes for each column:

Column (1)	United Nations number/substance identification number

Contains the UN number or substance identification number:

- of the dangerous substance if the substance has been assigned its own specific UN number or substance identification number, or

- of the generic or n.o.s. entry to which the dangerous substances not mentioned by name shall be assigned in accordance with the criteria (“decision trees”) of Part 2.

Column (2)	Name and description

Contains, in upper case characters, the name of the substance or, if the substance has been assigned its own specific UN number or substance identification number, or of the generic or n.o.s. entry to which it has been assigned in accordance with the

criteria (“decision trees”) of Part 2.  This name shall be used as the proper shipping name or, when applicable, as part of the proper shipping name (see 3.1.2 for further details on the proper shipping name).

A descriptive text in lower case characters is added after the proper shipping name to clarify the scope of the entry if the classification and/or carriage conditions of the substance may be different under certain conditions.

Column (3a) 	Class

Contains the number of the class, whose heading covers the dangerous substance.  This class number is assigned in accordance with the procedures and criteria of Part 2.

Column (3b) 	Classification code

Contains the classification code of the dangerous substance.

- For dangerous substances of Class 2, the code consists of a number and hazardous property group, which are explained in 2.2.2.1.2 and 2.2.2.1.3.

- For dangerous substances of Classes 3, 4.1, 4.2, 4.3, 5.1, 5.2, 6.1, 6.2, 8 and 9, the codes are explained in 2.2.x.1.2.

Column (4)	Packing group

Contains the packing group number(s) (I, II or III) assigned to the dangerous substance.  These packing group numbers are assigned on the basis of the procedures and criteria of Part 2.  Certain substances are not assigned to packing groups.

Column (5)	Hazards

This column contains information concerning the hazards of the dangerous substance.  They are included on the basis of the danger labels in Table A, column (5).  In the case of chemically unstable substance, the code “unst” is added to the information.

Column (6)	Type of tank vessel

Contains the type of tank vessel, Type G, C or N

Column (7)	Cargo tank design

Contains information concerning the cargo tank design:

1.	pressure cargo tank

2.	closed cargo tank

3.	open cargo tank with flame-arrester

4.	open cargo tank

Column (8)	Cargo tank type

Contains information concerning the cargo tank type:

1.	independent cargo tank

2.	integral cargo tank

3.	cargo tank with walls distinct from the outer hull

Column (9)	Cargo tank equipment

Contains information concerning the cargo tank equipment:

1.	refrigeration system

2.	heating system

3.	water-spray system

Column (10)	Opening pressure of high-velocity vent valve in kPa

Contains information concerning the opening pressure of the high-velocity vent 	valve in kPa.

Column (11)	Maximum degree of filling (%)

Contains information concerning the maximum degree of filling of cargo tanks

as a percentage.

Column (12)	Relative density

Contains information concerning the relative density of the substance

at 20° C.  Data concerning density are for information only.

Column (13)	Type of sampling device

1.	closed sampling device

2.	partly closed sampling device

3.	open sampling device

Column (14)	Pump-room below deck permitted

Contains  information as to whether a pump-room below deck is permitted:

Yes	pump-room below deck permitted

No	pump-room below deck not permitted

Column (15)	Temperature class

Contains the temperature class of the substance.

Column (16)	Explosion group

Contains the explosion group of the substance.

Column (17)	Protection against explosions required

Contains a code referring to protection against explosions:

+   protection against explosions required

-   protection against explosions not required

Column (18)	Equipment required

This column contains alphanumeric codes for the equipment required for the carriage of the dangerous substance (see 8.1.5).

Column (19)	Number of cones/blue lights

This column contains the number of cones/blue lights which should constitute the marking of the vessel when this dangerous substance or article is carried.

Column (20)	Additional requirements or remarks

This column contains the additional requirements or remarks applicable to the vessel.  These are:

1.	Anhydrous ammonia is liable to cause stress crack corrosion in cargo tanks and cooling systems constructed of carbon-manganese steel or nickel steel.

In order to minimize the risk of stress crack corrosion the following measures shall be taken:

(a)	Where carbon-manganese steel is used, cargo tanks, pressure vessels of cargo refrigeration systems and cargo piping shall be constructed of fine-grained steel having a specified minimum yield stress of not more than 355 N/mm2.  The actual yield stress shall not exceed 440 N/mm2.  In addition, one of the following construction or operational measures shall be taken:

1.	Material with a low tensile strength (Rm < 410 N/mm2) shall be used; or

2.	Cargo tanks, etc., shall undergo a post-weld heat treatment for the purpose of stress relieving; or

3.	The transport temperature shall preferably be maintained close to the evaporation temperature of the cargo of -33° C, but in no case above -20° C; or

4.	Ammonia shall contain not less than 0.1% water, by mass.

(b)	When carbon-manganese steel with yield stress values higher than those referred to in (a) above is used, the completed tanks, pipe sections, etc., shall undergo a post-weld heat treatment for the purpose of stress relieving.

(c)	Pressure vessels of the cargo refrigeration systems and the piping systems of the condenser of the cargo refrigeration system constructed of carbon-manganese steel or nickel steel shall undergo a post-weld heat treatment for the purpose of stress relieving.

(d)	The yield stress and the tensile strength of welding consumables may exceed only by the smallest value possible the corresponding values of the tank and piping material.

(e)	Nickel steels containing more than 5% nickel and carbon-manganese steel which are not in compliance with the requirements of (a) and (b) above may not be used for cargo tanks and piping systems intended for the transport of this substance.

(f)	Nickel steels containing not more than 5% nickel may be used if the transport temperature is within the limits referred to in (a) above.

(g)	The concentration of oxygen dissolved in the ammonia shall not exceed the values given in the table below:

| t in °C | O2 in %, by volume |
| --- | --- |
| -30 and below | 0.90 |
| -20 | 0.50 |
| -10 | 0.28 |
| 0 | 0.16 |
| 10 | 0.10 |
| 20 | 0.05 |
| 30 | 0.03 |

2.	Before loading, air shall be removed and subsequently kept away to a sufficient extent from the cargo tanks and the accessory cargo piping by the means of inert gas (see also 7.2.4.18).

3.	Arrangements shall be made to ensure that the cargo is sufficiently stabilized in order to prevent a reaction at any time during carriage.  The transport document shall contain the following additional particulars:

(a)	Name and amount of inhibitor added;

(b)	Date on which inhibitor was added and expected duration of effectiveness under normal conditions;

(c)	Any temperature limits having an effect on the inhibitor.

When stabilization is ensured solely by blanketing with an inert gas it is sufficient to mention the name of the inert gas used in the transport document.

When stabilization is ensured by another measurement, e.g. the special purity of the substance, this measurement shall be mentioned in the transport document.

4.	The substance shall not be allowed to solidify; the transport temperature shall be maintained above the melting point.  In instances where cargo heating installations are required, they must be so designed that polymerization through heating is not possible in any part of the cargo tank.  Where the temperature of steam-heated coils could give rise to overheating, lower-temperature indirect heating systems shall be provided.

5.	This substance is liable to clog the vapour pipe and its fittings.  Careful surveillance should be ensured.  If a close-type tank vessel is required for the carriage of this substance the vapour pipe shall conform to 9.3.2.22.5 (a) (i), (ii), (iv), (v), (b), (c) or (d) or to 9.3.3.22.5 (a) (i), (ii), (iv), (v), (b),

(c) or (d).  This requirement does not apply when the cargo tanks are inerted in accordance with 7.2.4.18 nor when protection against explosions is not required in column (17) and when flame-arresters have not been installed.

6.	When external temperatures are below or equal to that indicated in column (20), the substance may only be carried in tank vessels meeting the following conditions:

The tank vessels shall be equipped with a cargo heating system conforming to 9.3.2.42 or 9.3.3.2.  The arrangement of heating coils inside the cargo tanks instead of a cargo heating system may be sufficient (possibility of heating the cargo).

In addition, in the event of carriage in a closed-type vessel, if the tank vessel:

- is fitted out in accordance with 9.3.2.22.5 (a) (i) or (d) or 9.3.3.22.5 (a) (i) or (d), it shall be equipped with pressure/vacuum valves capable of being heated,

or

- is fitted out in accordance with 9.3.2.22.5 (a) (ii), (v), (b) or (c) or 9.3.3.22.5 (a) (ii), (v), (b) or (c), it shall be equipped with heatable vapour pipes and heatable pressure/vacuum valves,

or

- is fitted out in accordance with 9.3.2.22.5 (a) (iii) or (iv) or 9.3.3.22.5 (a) (iii) or (iv), it shall be equipped with heatable vapour pipes and with heatable pressure/vacuum valves and heatable flame-arresters.

The temperature of the vapour pipes, pressure/vacuum valves and flame-arresters shall be kept at least above the melting point of the substance.

7.	If a closed-type tank vessel is required to carry this substance or if the substance is carried in a closed-type tank vessel, if this vessel:

- is fitted out in accordance with 9.3.2.22.5 (a) (i) or (d) or 9.3.3.22.5 (a) (i) or (d), it shall be equipped with heatable pressure/vacuum valves,

or

- is fitted out in accordance with 9.3.2.22.5 (a) (ii), (v), (b) or (c)  or 9.3.3.22.5 (a) (ii), (v), (b) or (c), it shall be equipped with heatable vapour pipes and heatable pressure/vacuum valves,

or

- is fitted out in accordance with 9.3.2.22.5 (a) (iii) or (iv) or 9.3.3.22.5 (a) (iii) or (iv), it shall be equipped with heatable vapour pipes and with heatable pressure/vacuum valves and heatable flame-arresters.

The temperature of the vapour pipes, pressure/vacuum valves and flame-arresters shall be kept at least above the melting point of the substance.

8.	Double-hull spaces, double bottoms and heating coils shall not contain any water.

9.	(a)	While the vessel is underway, an inert-gas pad shall be maintained

in the ullage space above the liquid level.

(b)	Cargo piping and vent lines shall be independent of the

corresponding piping used for other cargoes.

(c)	Safety valves shall be made of stainless steel.

10.	Not relevant

11.	(a)	Stainless steel of type 416 or 442 and cast iron shall not be used

for cargo tanks and pipes for loading and unloading.

(b)	The cargo may be discharged only by deep-well pumps or pressure inert gas displacement.  Each cargo pump shall be arranged to ensure that the substance does not heat significantly if the pressure discharge line from the pump is shut off or otherwise blocked.

(c)	The cargo shall be cooled and maintained at temperatures below 30° C.

(d)	The safety valves shall be set at a pressure of not less than 550 kPa (5.5 bar) gauge pressure.  Special authorization is required for the maximum setting pressure.

(e)	While the vessel is underway, a nitrogen pad shall be maintained in the ullage space above the cargo [see also 7.2.4.18].  An automatic nitrogen supply system shall be installed to prevent the pressure from falling below 7 kPa (0.07 bar) gauge within the cargo tank in the event of a cargo temperature fall due to ambient temperature conditions or to some other reason.  In order to satisfy the demand of the automatic pressure control a sufficient amount of nitrogen shall be available on board.  Nitrogen of a commercially pure quality of 99.9%, by volume, shall be used for padding.  A battery of nitrogen cylinders connected to the cargo tanks through a pressure reduction valve satisfies the intention of the expression “automatic” in this context.

The required nitrogen pad shall be such that the nitrogen concentration in the vapour space of the cargo tank is not less than 45% at any time.

(f)	Before loading and while the cargo tank contains this substance in a quid or gaseous form, it shall be inerted with nitrogen.

(g)	The water-spray system shall be fitted with remote-control devices which can be operated from the wheelhouse or from the control station, if any.

(h)	Transfer arrangements shall be provided for emergency transfer of ethylene oxide in the event of an uncontrollable self-reaction.

12.	(a)	The substance shall be acetylene free.

[(b)	Cargo tanks which have not undergone appropriate cleaning shall not be used for the carriage of these substances if one of the previous three cargoes consisted of a substance known to promote polymerization, such as:

1.	mineral acids (e.g. sulphuric acid, hydrochloric acid, nitric acid);

2.	carboxylic acids and anhydrides (e.g. formic acid, acetic acid);

3.	halogenated carboxylic acids (e.g. chloroacetic acid);

4.	sulphonic acids (e.g. benzen sulphonic acid);

5.	caustic alkalis (e.g. sodium hydroxide, potassium hydroxide);

6.	ammonia and ammonia solutions;

7.	amines and amine solutions;

8.	oxidizing substances.]

(c)	[Before loading, cargo tanks and their piping shall be efficiently and thoroughly cleaned so as to eliminate all traces of previous cargoes, except when the last cargo was constituted of propylene oxide or a mixture of ethylene oxide and propylene oxide.  Special precautions shall be taken in the case of ammonia in cargo tanks built of steel other than stainless steel.]

(d)	[In all cases the efficiency of the cleaning of cargo tanks and their piping shall be monitored by means of appropriate tests or inspections to check that no trace of acid or alkaline substance remains that could present a danger in the presence of these substances.]

(e)	The cargo tanks shall be entered and inspected prior to each loading of these substances to ensure freedom from contamination, heavy rust deposits or visible structural defects.

When these cargo tanks are in continuous service for these substances, such inspections shall be performed at intervals of not more than two and a half years.

(f)	[Cargo tanks which have contained these substances may be reused for other cargoes once they and their piping have been thoroughly cleaned by washing and flushing with an inert gas.]

(g)	[Substances shall be loaded and unloaded in such a way that there is no release of gas into the atmosphere.  If gas is returned to the shore installation during loading, the gas return system connected to the tank containing that substance] shall be independent from all other cargo tanks.

(h)	During discharge operations, the pressure in the cargo tanks shall be maintained above 7 kPa (0.07 bar) gauge.

(i)	The cargo shall be discharged only by deep-well pumps, hydraulically operated submerged pumps or pressure inert gas displacement.  Each cargo pump shall be arranged to ensure that the substance does not heat significantly if the pressure discharge line from the pump is shut off or otherwise blocked.

(j)	Each cargo tank carrying these substances shall be ventilated by a system independent from the ventilation systems of other cargo tanks carrying other substances.

(k)	[Loading pipes used for these substances shall be marked as follows:

“To be used only for the transfer of alkylene oxide.”]

(l)	Cargo tanks, cofferdams, double-hull spaces, double bottoms, cargo tank spaces [and service spaces in the cargo area (?)] adjacent to a cargo tank carrying this substance shall either contain compatible cargo (the substances mentioned under (b) are examples of substances considered to be incompatible) or be inerted with an appropriate inert gas.  Spaces so inerted shall be monitored for these substances and oxygen.  The oxygen content shall be maintained below 2%, by volume.  Portable measuring devices are permitted.

(m)	No air shall be allowed to enter the cargo pumps and cargo piping system while these substances are contained within the system.

(n)	[Before the shore connections are disconnected, piping containing liquids or gas shall be depressurised at the shore link by means of appropriate devices.]

(o)	The piping system for cargo tanks to be loaded with these substances shall be separate from piping system for all other cargo tanks, including empty cargo tanks.  If the piping system for the cargo tanks to be loaded is not independent, separation shall be accomplished by the removal of spool pieces, shut-off valves, other pipe sections and by fitting blank flanges at these locations.  The required separation applies to all liquid pipes and vapour vent lines and any other connections which may exist such as common inert gas supply lines.

(p)	These substances may be carried only in accordance with cargo handling plans that have been approved by a competent authority.

Each loading arrangement shall be shown on a separate cargo handling plan.  Cargo handling plans shall show the entire cargo piping system and the locations for installations of blank flanges needed to meet the above piping separation requirements.  A copy of each cargo handling plan shall be kept on board.  Reference to the approved cargo handling plans shall be included in the certificate of approval.

(q)	[Before loading of these substances and before carriage is resumed a qualified person approved by the competent authority shall certify that the prescribed separation of the piping has been effected; this certificate shall be kept on board.  Each connection between a blank flange and a shut-off valve in the piping shall be fitted with a sealed wire to prevent the flange from being disassembled inadvertently.]

(r)	During the voyage, the cargo shall be covered with nitrogen.  An automatic nitrogen make-up system shall be installed to prevent the cargo tank pressure from falling below 7 kPa (0.07 bar) gauge in the event of a cargo temperature fall due to ambient temperature conditions or to some other reason.  Sufficient nitrogen shall be available on board to satisfy the demand of automatic pressure control.  Nitrogen of commercially pure quality of 99.9%, by volume, shall be used for padding.  A battery of nitrogen cylinders connected to the cargo tanks through a pressure reduction valve satisfies the intention of the expression “automatic” in this context.

(s)	The vapour space of the cargo tanks shall be checked before and after each loading operation to ensure that the oxygen content is 2%, by volume, or less.

[(t)	Loading flow

The loading flow (LR) = 3600(U/t (m3/h)

In this formula

U   =	the free volume (m3) during loading for the activation of the overflow prevention system;

T   =	the time required between the activation of the overflow prevention system and the complete stop of the flow of cargo into the cargo tank;

The time is the sum of the partial times needed for successive operations, e.g. reaction time of the service personnel, the time needed to stop the pumps and the time needed to close the shut-off valves;

The loading flow shall also take account of the design pressure of the piping system.]

13.	If no stabilizer is supplied or if the supply is inadequate, the oxygen content in the vapour phase shall not exceed 0.1%.  Overpressure must be constantly maintained in cargo tanks.  This requirement applies also to voyages on ballast or empty with uncleaned cargo tanks between cargo transport operations.

14.	The following substances may not be carried under these conditions:

- substances with self-ignition temperatures ≤ 200º C;

- mixtures containing halogenated hydrocarbons;

- mixtures containing more than 10% benzene;

- substances and mixtures carried in a stabilized state.

15.	Provision shall be made to ensure that alkaline or acidic substances such as sodium hydroxide solution or sulphuric acid do not contaminate this cargo.

16.	If there is a possibility of a dangerous reaction such as polymerization, decomposition, thermal instability or evolution of gases resulting from local overheating of the cargo in either the cargo tank or associated piping system, this cargo shall be loaded and carried adequately segregated from other substances the temperature of which is sufficiently high to initiate such reaction.  Heating coils inside cargo tanks carrying this substance shall be blanked off or secured by equivalent means.

17.	The melting point of the cargo shall be shown in the transport documents.

18.	Not relevant

19.	Provision shall be made to ensure that the cargo does not come into contact with water.  The following additional requirements apply:

Carriage of the cargo is not permitted in cargo tanks adjacent to slop tanks or cargo tanks containing ballast water, slops or any other cargo containing water.  Pumps, piping and vent lines connected to such tanks shall be separated from similar equipment of tanks carrying these substances.  Pipes from slop tanks or ballast water pipes shall not pass through cargo tanks containing this cargo unless they are encased in a tunnel.

20.	The maximum permitted transport temperature given in column (20) shall not be exceeded.

21.	Not relevant

22.	The relative density of the cargo shall be shown in the transport document.

23.	The instrument for measuring the pressure of the vapour phase in the cargo tank shall activate the alarm when the internal pressure reaches 40 kPa.  The water-spray system shall immediately be activated and remain in operation until the internal pressure drops to 30 kPa.

[24.	Substances having a flash-point above 61º C which are handed over for carriage or which are carried heated within a limiting range of 15 K below their flash-point shall be carried under the conditions of substance number 9001.]

25.	Type 3 cargo tank may be used for the carriage of this substance provided that the construction of the cargo tank has been accepted by a recognized classification society for the maximum permitted transport temperature.

26.	Type 2 cargo tank may be used for the carriage of this substance provided that the construction of the cargo tank has been accepted by a recognized classification society for the maximum permitted transport temperature.

[27.	The requirements of 3.1.2.6.1 are applicable.

28.	(a)	When UN 2448, molten sulphur, is carried, the forced ventilation

of the cargo tanks shall be brought into service at latest when the

concentration of hydrogen sulphide reaches 1.0%, by volume.

(b)	When during the carriage of UN 2448, molten sulphur, the

concentration of hydrogen sulphide exceeds 1.85%, the boat master shall immediately notify the nearest competent authority.

When a significant increase in the concentration of hydrogen sulphide in a hold space leads it to be supposed that the sulphur has leaked, the cargo tanks shall be unloaded as rapidly as possible.  A new load may only be taken on board once the authority which issued the certificate of approval has carried out a further inspection.

(c)	When UN 2448, molten sulphur, is carried, the concentration of sulphur sulphide shall be measured in the vapour phase of the cargo tanks and concentrations of sulphur dioxide and hydrogen sulphide in the hold spaces.

(d)	The measurements prescribed in (c) shall be made every eight hours.  The results of the measurements shall be recorded in writing.

29.	When particulars concerning the vapour pressure or the boiling point are given in column (2), the relevant information shall be added to the proper shipping name in the transport document, e.g.

UN 1224 KETONES, LIQUID, N.O.S., 110 kPa < vp 50 < 175 kPa or

UN 2929 TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S., boiling point < 60° C

30.	When these substances are carried, the hold spaces of open type N tank vessels may contain auxiliary equipment.

31.	When these substances are carried, the vessel shall be equipped with a rapid blocking valve placed directly on the shore connection.]

| UN No. or substance identification No. | Name and description | Class | Classification | Packing group | Hazards | Type of tank vessel | Cargo tank design | Cargo tank type | Cargo tank equipment | Opening pressure of the high-velocity vent valve in kPa | Maximum degree of filling in % | Relative density at 20° C | Type of sampling device | Cargo pump room below deck permitted | Temperature class | Explosion group | Protection against explosions required | Equipment required | Number of blue lights/cones | Other requirements/Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | 3 (a) | 3 (b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 1005 | AMMONIA, ANHYDROUS | 2 | 2TC |  | 2.3+8+ 2.1 | G | 1 | 1 | 3 |  | 91 |  | 1 |  | T1 | II A | yes | PP, EP, EX, TOX, A | 2 | 1;.31 |
| 1010 | 1,2 BUTADIENE, STABILIZED | 2 | 2F |  | 2.1+unst | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II B4) | yes | PP, EX, A | 1 | 2 ; 3 ; 31 |
| 1010 | 1,3 BUTADIENE STABILIZED | 2 | 2F |  | 2.1+unst. | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II B | yes | PP, EX, A | 1 | 2 ; 3 ; 31 |
| 1010 | MIXTURES OF 1,3 - BUTADIENE AND HYDROCARBONS, STABILIZED, HAVING A VAPOUR PRESSURE AT 70° C NOT EXCEEDING 1.1 Mpa (11 BAR) AND A DENSITY AT 50° C NOT LOWER THAN 0.525 kg/l | 2 | 2F |  | 2.1+unst. | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II B | yes | PP, EX, A | 1 | 2 ; 3 ; 31 |
| 1011 | BUTANE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II A | yes | PP, EX, A | 1 | 31 |
| 1012 | 1-BUTYLENE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II A | yes | PP, EX, A | 1 | 31 |
| 1020 | CHLOROPENTAFLUOROETHANE (REFRIGERANT GAS R 115) | 2 | 2A |  | 2.2 | G | 1 | 1 |  |  | 91 |  | 1 | yes |  |  | no | PP | 0 | 31 |
| 1030 | 1.1 - DIFLUOROETHANE (REFRIGERANT R GAS R 152 (a)) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T1 | II A | yes | PP, EX, A | 1 | 31 |
| 1033 | DIIMETHYL ETHER | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T3 | II B | yes | PP, EX, A | 1 | 31 |
| 1038 | ETHYLENE, REFRIGERATED LIQUID | 2 | 3F |  | 2.1 | G | 1 | 1 | 1 |  | 95 | 0.57 | 1 | no | T1 | II B | yes | PP, EX, A | 1 | 31 |
| 1040 | ETHYLENE OXIDE WITH NITROGEN UP TO A TOTAL PRESSURE OF Mpa (10 BAR) AT 50° C | 2 | 2TF |  | 2.3+2.1 | G | 1 | 1 |  |  | 91 |  | 1 | no | T2 | II B | yes | PP, EP, EX, TOX, A | 2 | 2 ; 3; 11; 31 |
| 1055 | ISOBUTYLENE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T21) | II A | yes | PP, EX, A | 1 | 31 |
| 1063 | METHYL CHLORIDE (REFRIGERANT GAS R 40) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T1 | II A | yes | PP, EX, A | 1 | 31 |
| 1077 | PROPYLENE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T1 | II A | yes | PP, EX, A | 1 | 31 |
| 1083 | TRIMETHYLAMINE , ANHYDROUS | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T4 | II A | yes | PP, EX, A | 1 | 31 |
| 1086 | VINYL CHLORIDE , STABILIZED | 2 | 2F |  | 2.1+unst. | G | 1 | 1 |  |  | 91 |  | 1 | yes | T2 | II A | yes | PP, EX, A | 1 | 2; 3; 13; 31 |
| 1088 | ACETAL | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.83 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 1089 | ACETALDEHYDE (ethanal) | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 | 0.78 | 1 | yes | T4 | II A | yes | PP, EX, A | 1 |  |
| 1090 | ACETONE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.79 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1092 | ACROLEINE, STABILIZED | 6.1 | TF1 | I | 6.1+3+unst. | C | 2 | 2 | 3 | 50 | 95 | 0.84 | 1 | no | T32) | II B | yes | PP, EP, EX, TOX, A | 2 | 2; 3; 5; 23 |
| 1093 | ACRYLONITRILE, STABILIZED | 3 | FT1 | I | 3+6.1+unst. | C | 2 | 2 | 3 | 50 | 95 | 0.8 | 1 | no | T1 | II B | yes | PP, EP, EX, TOX, A | 2 | 3; 5; 23 |
| 1098 | ALLYL ALCOHOL | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 40 | 95 | 0.85 | 1 | no | T2 | II B | yes | PP, EP, EX, TOX, A | 2 |  |
| 1100 | ALLYL CHLORIDE | 3 | FT1 | I | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 | 0.94 | 1 | no | T2 | II A | yes | PP, EP, EX, TOX, A | 2 | 23 |
| 1105 | PENTANOLS (n-pentanol) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.81 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 1106 | AMYLAMINE (n-amylamine) | 3 | FC | II | 3+8 | C | 2 | 2 |  | 40 | 95 | 0.76 | 2 | yes | T43) | II A7) | yes | PP, EP, EX, A | 1 |  |
| 1107 | AMYL CHLORIDES (l-chloropentane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 40 | 95 | 0.88 | 2 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1107 | AMYL CHLORIDES (1-chloro-3-methylbutane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 45 | 95 | 0.89 | 2 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1107 | AMYL CHLORIDES (2-chloro-2-methylbutane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 | 0.87 | 2 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1107 | AMYL CHLORIDES (1-chloro-2.2-dimenthylpropane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 | 0.87 | 2 | yes | T32) | II A | yes | PP, EX, A | 1 |  |
| 1107 | AMYL CHLORIDES (…) | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 | 0.9 | 1 | yes | T32) | II A | yes | PP, EX, A | 1 | 27 |
| 1108 | 1-PENTENE (n-amylene) | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 | 0.64 | 1 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 1114 | BENZENE | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.88 | 2 | yes | T1 | II A | yes | PP, EP, EX, TOX, A | 1 | 6: +10º C; 17; 23 |
| 1120 | BUTANOLS (n-butyl alcohol) | 3 | F1 | II | 3 | N | 2 | 2 | 2 | 10 | 97 | 0.79 | 3 | yes | T1 | II A7) | yes | PP, EX, A | 1 | 7; 17 |
| 1120 | BUTANOLS (secondary butyl alcohol) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.81 | 3 | yes | T2 | II B7) | yes | PP, EX, A | 0 |  |
| 1120 | BUTANOLS (tertiary butyl alcohol) | 3 | F1 | III | 3 | N | 2 | 2 | 2 | 10 | 97 | 0.81 | 3 | yes | T2 | II B | yes | PP, EX, A | 0 |  |
| 1123 | BUTYL ACETATES sec-butyl acetate) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.86 | 3 | yes | T2 | II A7) | yes | PP, EX, A | 1 |  |
| 1123 | BUTYL ACETATES (see-butyl acetate) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 1125 | n-BUTYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.75 | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (1-chlorobutane) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.89 | 2 | yes | T3 | II A | yes | PP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (2-chlorobutane) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.87 | 2 | yes | T43) | II A | yes | PP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (2-chloro-2-methylpropane) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.88 | 2 | yes | T43) | II A | yes | PP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (1-chlro-2-methylpropane) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.84 | 2 | yes | T1 | II A | yes | PP, EX, A | 1 | 23 |
| 1127 | CHLOROBUTANES (…) | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 | 0.89 | 1 | yes | T43) | II A | yes | PP, EX, A | 1 | 27 |
| 1129 | BUTYRALDEHYDE (n-butyraldehyde) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.8 | 2 | yes | T4 | II A | yes | PP, EX, A | 1 | 15; 23 |
| 1131 | CARBON DISULPHIDE (carbon sulphide) | 3 | FT1 | I | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 | 1.26 | 1 | no | T6 | II C | yes | PP, EP, EX, TOX, A | 2 | 2; 9; 23 |
| 1134 | CHLOROBENZENE (phenyl chloride) | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.11 | 2 | yes | T1 | II A8) | yes | PP, EX, A | 0 |  |
| 1135 | ETHYLENE CHLOROHYDRIN (2-chloroethanol) | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 30 | 95 | 1.21 | 1 | no | T2 | II A8) | yes | PP, EP, EX, TOX, A | 2 |  |
| 1143 | CROTONALDEHYDE, STABILIZED | 6.1 | TF1 | I | 6.1+3+unst. | C | 2 | 2 |  | 40 | 95 | 0.85 | 1 | no | T3 | II B | yes | PP, EP, EX, TOX, A | 2 | 3; 5; 15 |
| 1145 | CYCLOHEXANE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.78 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 6: +11º C; 17 |
| 1146 | CYCLOPENTANE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.75 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1150 | 1,2 DICHLOROETHYLENE (cis) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 1.28 | 2 | yes | T21) | II A | yes | PP, EX, A | 1 | 23 |
| 1150 | 1,2 DICHLOROETHYLENE (trans) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 1.26 | 2 | yes | T2 | II A | yes | PP, EX, A | 1 | 23 |
| 1153 | ETHYLENE GLYCOL DIETHYL ETHER | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.84 | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 |  |
| 1154 | DIETHYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.7 | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 1155 | DIETHYL ETHER (ETHYL ETHER) | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 | 0.71 | 1 | yes | T4 | II B | yes | PP, EX, A | 1 |  |
| 1157 | DIISOBUTYL KETONE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.81 | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 |  |
| 1159 | DIISOPROPYL ETHER | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.72 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1160 | DIMETHYLAMINE AQUEOUS SOLUTION | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.82 | 2 | yes | T2 | II B4) | yes | PP, EP, EX, A | 1 | 23 |
| 1163 | DIMETHYLHYDRAZINE UNSYMMETRICAL | 6.1 | TFC | I | 6.1+3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.78 | 1 | no | T3 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23 |
| 1165 | DIOXANE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 1.03 | 3 | yes | T2 | II B | yes | PP, EX, A | 1 | 6: +14º C; 17 |
| 1167 | DIVINYL ETHER, STABILIZED | 3 | F1 | I | 3+unst. | C | 1 | 1 |  |  | 95 | 0.77 | 1 | yes | T2 | II B7) | yes | PP, EX, A | 1 | 2; 3 |
| 1170 | ETHANOL SOLUTION (ETHYL ALCOHOL SOLUTION) aqueous solution with more than 24% and not more than 70% alcohol by volume | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.79 - 0.87 | 3 | yes | T2 | II B | yes | PP, EX, A | 1 |  |
| 1170 | ETHANOL SOLUTION (ETHYL ALCOHOL SOLUTION) aqueous solution with more than 70% alcohol by volume | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.79 - 0.87 | 3 | yes | T2 | II B | yes | PP, EX, A | 1 |  |
| 1170 | ETHANOL (ETHYL ALCOHOL) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.87 - 0.96 | 3 | yes | T2 | II B | yes | PP, EX, A | 0 |  |
| 1171 | ETHYLENE GLYCOL MONOETHYL ETHER | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.93 | 3 | yes | T3 | II B | yes | PP, EX, A | 0 |  |
| 1172 | ETHYLENE GLYCOL MONOETHYL ETHER ACETATE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.98 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 1173 | ETHYL ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.9 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1175 | ETHYLBENZENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.87 | 3 | yes | T2 | II B | yes | PP, EX, A | 1 |  |
| 1177 | 2-ETHYLBUTYL ACETATE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.88 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 |  |
| 1184 | ETHYLENE DICHLORIDE (1,2 dichloroethane) | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 50 | 95 | 1.25 | 2 | no | T2 | II A | yes | PP, EP, EX, TOX, A | 2 |  |
| 1188 | ETHYLENE GLYCOL MONOETHYL ETHER | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.97 | 3 | yes | T3 | II B | yes | PP, EX, A | 0 |  |
| 1191 | OCTYL ALDEHYDES (2-ethylcapronaldehyde) | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 0.82 | 2 | yes | T4 | II A | yes | PP, EX, A | 0 |  |
| 1191 | OCTYL ALDEHYDES (n-octaldehyde) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.82 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 0 |  |
| 1193 | ETHYL METHYL KETONE (METHYL ETHYLKETONE) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.8 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1198 | FORMALDEHYDE SOLUTION, INFLAMMABLE | 3 | FC | III | 3+8 | N | 3 | 2 |  |  | 97 | 1.09 | 3 | yes | T2 | II B | yes | PP, EP, EX, A | 0 |  |
| 1199 | FURALDEHYDES (a-furfuraldehyde) or furfuraldehydes (a-furfurylaldehyde) | 6.1 | TF1 | II | 6.1+3 | C | 2 | 2 |  | 25 | 95 | 1.16 | 2 | no | T32) | II B | yes | PP, EP, EX, TOX, A | 2 | 15 |
| 1202 | GAS OIL or DIESEL FUEL or HEATING OIL LIGHT | 3 | F1 | III | 3 | N | 4 | 2 |  |  | 97 | 0.74 | 3 | yes |  |  | no | PP | 0 |  |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.68 - 0.7210) | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL, with more than 10% benzen boiling point < 60° C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T3 | II A | yes | PP, EX, A | 1 | 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL with more than 10% benzen 60° C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A | 1 | 23; 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL with more than 10% benzen 85° C < boiling point < 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A | 1 | 29 |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL with more than 10% benzen boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T3 | II A | yes | PP, EX, A | 1 | 29 |
| 1206 | HEPTANES (n-heptane) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.68 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1208 | HEXANES (n-hexane) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.66 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1212 | ISOBUTANOL (ISOBUTYL ALCOHOL) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.8 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 1213 | ISOBUTYL ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.87 | 3 | yes | T2 | II A7) | yes | PP, EX, A | 1 |  |
| 1214 | ISOBUTYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.73 | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 1216 | ISOOCTENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.73 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 1218 | ISOPRENE, STABILIZED | 3 | F1 | I | 3+unst. | N | 1 | 1 |  |  | 95 | 0.68 | 1 | yes | T3 | II B | yes | PP, EX, A | 1 | 2; 3; 5;16 |
| 1219 | ISOPROPANOL (ISOPROPYL ALCOHOL) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.78 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1220 | ISOPROPYLE ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.88 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1221 | ISOPROPYLAMINE | 3 | FC | I | 3+8 | C | 1 | 1 |  |  | 95 | 0.69 | 1 | yes | T2 | II A7) | yes | PP, EP, EX, A | 1 |  |
| 1223 | KEROSENE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | < 0.83 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 | 14 |
| 1224 | KETONES, LIQUID, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1224 | KETONES, LIQUIDE, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1224 | KETONES. LIQUIDE, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1224 | KETONES, LIQUID, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 1229 | MESITYL OXYDE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.85 | 3 | yes | T2 | II B4) | yes | PP, EX, A | 0 |  |
| 1230 | METHANOL | 3 | FT1 | II | 3+6.1 | N | 2 | 2 | 3 | 50 | 95 | 0.79 | 2 | yes | T2 | II A | yes | PP, EP, EX, TOX, A | 1 | 23 |
| 1231 | METHYL ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.93 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1235 | METHYLAMINE, AQUEOUS SOLUTION | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 |  |
| 1243 | METHYLE FORMATE | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 | 0.97 | 1 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1244 | METHYLHYDRAZINE | 6.1 | TFC | I | 6.1+3+8 | C | 2 | 2 |  | 45 | 95 | 0.88 | 1 | no | T4 | II C5) | yes | PP, EP, EX, TOX, A | 2 |  |
| 1245 | METHYL ISOBUTYL KETONE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.8 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1247 | METHYL METHACRYLATE, MONOMER, STABILIZED | 3 | F1 | II | 3+unst. | C | 2 | 2 |  | 40 | 95 | 0.94 | 1 | yes | T2 | II A | yes | PP, EX, A | 1 | 3; 5; 16 |
| 1262 | OCTANES (n-octane) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.7 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1264 | PARALDEHYDE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.99 | 3 | yes | T3 | II A7) | yes | PP, EX, A | 0 | 6: +16º C; 17 |
| 1265 | PENTANES, liquid (2-methylbutane) | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 | 0.62 | 1 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 1265 | PENTANES, liquid (n-pentane) | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 | 0.63 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1265 | PENTANES, liquid (n-pentane) | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 | 0.63 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 |  |
| 1267 | PETROLEUM CRUDE OIL vp50 > 175 kPa | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL vp50 > 175 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 1 | 50 | 97 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen vp50 < 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLOLEUM CRUDE OIL 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen vp50 < 110 kPa boiling point < 60° C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen vp50 < 100 kPa 60° C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 23; 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen vp50 < 110 kPa 85º C < boiling point < 115º C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL with more than 10% benzen vp50 < 110 kPa boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. vp50 > 175 kPa | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S vp50 > 175 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 1 | 50 | 97 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S. with more than 10% benzen vp50 > 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S, with more than 10% benzen 110 kPa <vp50 < 175 kPa | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES N.O.S. or PETROLEUM PRODUCTS, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S. with more than 10% benzen vp50 < 110 kPa boiling point < 85º C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4)yes | yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S. with more than 10% benzen vp50 < 110 kPa 60°C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.765 | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S., BENZENE HEART CUT with more than 10% benzen <vp50 < 110 kPa 60° C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T 3 | II A | yes | PP, EX, A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S, with more than 10% benzen, vp50 < 110 kPa 85º C < boiling point < 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. with more than 10% benzen or PETROLEUM PRODUCTS, N.O.S. with more than 10% benzen vp50 < 110 kPa boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 1268 | PETROLEUM DISTILLATES, N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S or PETROLEUM PRODUCTS, N.O.S. (NAPHTHA) vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.735 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S, or PETROLEUM PRODUCTS, N.O.S. (BENZENE HEART CUT) vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.765 | 3 | yes | T3 | II A | yes | PP, EX, A | 1 | 14; 29 |
| 1274 | n-PROPANOL (PROPYL ALCOHOL, NORMAL) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.8 | 3 | yes | T2 | II B | yes | PP, EX, A | 1 |  |
| 1274 | n-PROPANOL (PROPYL ALCOHOL, NORMAL) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.8 | 3 | yes | T2 | II B | yes | PP, EX, A | 0 |  |
| 1275 | PROPIONALDEHYDE | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.81 | 2 | yes | T4 | II B | yes | PP, EX, A | 1 | 15; 23 |
| 1276 | n-PROPYL ACETATE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.88 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1277 | PROPYLAMINE (1-aminopropane) | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T32) | II A | yes | PP, EP, EX, A | 1 | 23 |
| 1278 | PROPYL CHLORIDE (1-chloropropane) | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.89 | 2 | yes | T1 | II A | yes | PP, EX, A | 1 | 23 |
| 1279 | PROPYL DICHLORIDE (1,2-DICHLOROPROPANE) | 3 | F1 | II | 3 | C | 2 | 2 |  | 45 | 95 | 1.16 | 2 | yes | T1 | II A8) | yes | PP, EX, A | 1 |  |
| 1280 | PROPYLENE OXIDE | 3 | F1 | I | 3+unst. | C | 1 | 1 |  |  | 95 | 0.83 | 1 | yes | T2 | II B | yes | PP, EX, A | 1 | 2; 12; 31 |
| 1282 | PYRIDINE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.98 | 3 | yes | T1 | II A8) | yes | PP, EX, A | 1 |  |
| 1289 | SODIUM METHYLATE SOLUTION in alcohol | 3 | FC | III | 3+8 | N | 3 | 2 |  |  | 97 | 0.969 | 3 | yes | T2 | II A | yes | PP, EP, EX, A | 0 |  |
| 1294 | TOLUENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.87 | 3 | yes | T1 | II A8) | yes | PP, EX, A | 1 |  |
| 1296 | TRIETHYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 | 0.73 | 2 | yes | T3 | II A8) | yes | PP, EP, EX, A | 1 |  |
| 1300 | TURPENTINE SUBSTITUTE (White spirit) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.78 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 0 |  |
| 1301 | VINYL ACETATE, STABILIZED | 3 | F1 | II | 3+unst. | N | 2 | 2 |  | 10 | 97 | 0.93 | 2 | yes | T2 | II A | yes | PP, EX, A | 1 | 3; 5; 16 |
| 1307 | XYLENES (o-XYLENE) | 3 | F1 | II | 3 | N | 3 | 2 |  |  | 97 | 0.88 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1307 | XYLENES (m-XYLENE) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T1 | II A | yes | PP, EX, A | 0 |  |
| 1307 | XYLENES (p-XYLENE) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T1 | II A | yes | PP, EX, A | 0 | 6: +17º C; 17 |
| 1541 | ACETONE CYANOHYDRIN, STABILIZED | 6.1 | T1 | I | 6.1+unst. | C | 2 | 2 |  | 50 | 95 | 0.932 | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 3 |
| 1545 | ALLYL ISOTHIOCYANATE, STABILIZED | 6.1 | TF1 | II | 6.1+3+unst. | C | 2 | 2 |  | 30 | 95 | 1.02 | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 2; 3 |
| 1547 | ANILINE | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.02 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1578 | CHLORONITROBENZENES (p-chloronitrobenzene) | 6.1 | T2 | II | 6.1 | C | 2 | 1 | 2 | 25 | 95 | 1.37 | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17; 26 |
| 1578 | CHLORONITROBENZENES (p-chloronitrobenzene) | 6.1 | T2 | II | 6.1 | C | 2 | 1 | 2 | 25 | 95 | 1.37 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +112º C; 26 |
| 1591 | o-DICHLOROBENZENE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.32 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 1593 | DICHLOROMETHANE (methyl chloride) | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 3 | 50 | 95 | 1.33 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 23 |
| 1594 | DIETHYLSULPHATE | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.18 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1595 | DIMETHYL SULPHATE | 6.1 | TC1 | I | 6.1+8 | C | 2 | 2 |  | 25 | 95 | 1.33 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1604 | ETHYLENEDIAMINE | 8 | CF1 | II | 8+3 | N | 3 | 2 |  |  | 97 | 0.9 | 3 | yes | T2 | II A | yes | PP, EP, EX, A | 1 | 6: +12º C; 17 |
| 1605 | ETHYLENE DIBROMIDE | 6.1 | T1 | I | 6.1 | C | 2 | 2 |  | 30 | 95 | 2.18 | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 6: +14º C; 17 |
| 1648 | ACETONITRILE (methyl cyanide) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.78 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1662 | NITROBENZENE | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.21 | 2 | no | T1 | II B | yes | PP, EP, EX, TOX, A | 2 | 17 |
| 1662 | NITROBENZENE | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.21 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 17; 20: +73º C |
| 1663 | NITROPHENOLS | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no | T1 | II B4) | yes | PP, EP, EX, TOX, A | 0 | 7; 17 |
| 1663 | NITROPHENOLS | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 7; 17; 20: +65º C |
| 1664 | NITROTOLUENES (o-nitrotoluene) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.16 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 17 |
| 1664 | NITROTOLUENES (p-nitrotoluene, molten) | 6.1 | T2 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.16 | 2 | no | T2 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 1664 | NITROTOLUENES (p-nitrotoluene, molten) | 6.1 | T2 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.16 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +88º C |
| 1708 | TOLUIDINES, LIQUID (o-toluidine) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1708 | TOLUIDINES, LIQUID (m-toluidine) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.03 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 1708 | TOLUIDINES, molten (p-toluidine) | 6.1 | T2 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.05 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 1708 | TOLUIDINES, molten (p-toluidine) | 6.1 | T2 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.05 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +60º C |
| 1710 | TRICHLORETHYLENE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 50 | 95 | 1.46 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 15 |
| 1715 | ACETIC ANHYDRIDE | 8 | CF1 | II | 8+3 | N | 2 | 3 |  | 10 | 97 | 1.08 | 3 | yes | T2 | II A | yes | PP, EP, EX, A | 1 |  |
| 1717 | ACETYL CHLORIDE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 1.1 | 2 | yes | T2 | II A8) | yes | PP, EP, EX, A | 1 | 23 |
| 1718 | BUTYL ACIDE PHOSPHATE | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 | 0.98 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27; 30 |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27; 30 |
| 1738 | BENZYL CHLORIDE | 6.1 | TC1 | II | 6.1+8+3 | C | 2 | 2 |  | 25 | 95 | 1.1 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 |  |
| 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX | 8 | C3 | II | 8 | N | 4 | 2 |  |  | 97 | 1.35 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1750 | CHLORACETIC ACID SOLUTION | 6.1 | TC1 | II | 6.1+8 | C | 2 | 2 | 2 | 25 | 95 | 1.58 | 2 | no | T1 | II A | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 1750 | CHLORACETIC ACID SOLUTION | 6.1 | TC1 | II | 6.1+8 | C | 2 | 2 | 2 | 25 | 95 | 1.58 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +111º C |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | I | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | II | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 1760 | CORROSIVE LIQUID, N.O.S. (sodium mercaptobenzothiazole, 50% aqueous solution) | 8 | C9 | II | 8 | N | 4 | 2 |  |  | 97 | 1.25 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1760 | CORROSIVE LIQUID, N.O.S. (fatty alcohol, C12-C14) | 8 | C9 | III | 8 | N | 4 | 2 |  |  | 97 | 0.89 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1760 | CORROSIVE LIQUID, N.O.S. (ethylene diaminetetraacetic acid, tetrasodium salt, 40% aqueous solution) | 8 | C9 | III | 8 | N | 4 | 2 |  |  | 97 | 1.28 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1764 | DICHLOROACETIC ACID | 8 | C3 | II | 8 | N | 3 | 3 |  |  | 97 | 1.56 | 3 | yes | T1 | II A | yes | PP, EP, EX, A | 0 | 17 |
| 1778 | FLUOROSILICIC ACID | 8 | C1 | II | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1779 | FORMIC ACID | 8 | C3 | II | 8 | N | 2 | 3 |  | 10 | 97 | 1.22 | 3 | yes | T1 | II A | yes | PP, EP, EX, A | 1 | 6: +12º C; 17 |
| 1780 | FUMARYL CHLORIDE | 8 | C3 | II | 8 | N | 2 | 3 |  | 10 | 97 | 1.41 | 3 | yes |  |  | no | PP, EP | 0 | 8 |
| 1783 | HEXAMETHYLENEDIAMINE SOLUTION | 8 | C7 | II | 8 | N | 3 | 2 | 2 |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 1783 | HEXAMETHYLENEDIAMINE SOLUTION | 8 | C7 | III | 8 | N | 3 | 2 | 2 |  | 97 |  | 3 | yes | T3 | II B4) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 1789 | HYDROCHLORIC ACID | 8 | C1 | II | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1789 | HYDROCHLORIC ACID | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 1805 | PHOSPHORIC ACID with more than 80% acid, by volume | 8 | C1 | III | 8 | N | 4 | 3 | 2 |  | 95 |  | 3 | yes |  |  | no | PP, EP | 0 | 7; 17; 22 |
| 1805 | PHOSPHORIC ACID with 80% (volume) acid, or less | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 | 1.00 - 1.6 | 3 | yes |  |  | no | PP, EP | 0 | 22 |
| 1814 | POTASSIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 30 |
| 1814 | POTASSIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 30 |
| 1823 | SODIUM HYDROXIDE, molten | 8 | C6 | II | 8 | N | 4 | 1 | 2 |  | 95 | 2.13 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17 |
| 1824 | SODIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 30 |
| 1824 | SODIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 30 |
| 1830 | SULPHURIC ACID with more than 51% acid | 8 | C1 | II | 8 | N | 4 | 3 |  |  | 97 | 1.4 - 1.84 | 3 | yes |  |  | no | PP, EP | 0 | 8; 22; 30 |
| 1831 | SULPHURIC ACID, FUMING (oleum) | 8 | CT1 | I | 8+6.1 | C | 2 | 2 |  | 50 | 95 | 1.94 | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 8 |
| 1832 | SULPHURIC ACID, SPENT | 8 | C1 | II | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 8; 30 |
| 1846 | CARBON TETRACHLORIDE | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 3 | 50 | 95 | 1.59 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23 |
| 1848 | PROPIONIC ACID | 8 | C3 | III | 8+3 | N | 3 | 3 |  |  | 97 | 0.99 | 3 | yes | T1 | II A7) | yes | PP, EP, EX, A | 0 |  |
| 1863 | FUEL, AVIATION, TURBINE ENGINE vp50 > 175 kPa | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE vp50 > 175 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 1 | 50 | 97 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen vp50 > 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen vp50 < 110 kPa boiling point < 60° C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen vp50 < 110 kPa 60° C boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen vp50 < 110 kPa 85° C < boiling point < 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE with more than 10% benzen vp50 < 110 kPa boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 29 |
| 1863 | FUEL, AVIATION, TURBINE ENGINE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14 |
| 1888 | CHLOROFORM | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 3 | 50 | 95 | 1.48 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 23 |
| 1897 | TETRACHLORETHYLENE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 50 | 95 | 1.62 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 1912 | METHYL CHLORIDE AND METHYLENE CHLORIDE MIXTURE (liquefied gas) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T1 | II A8) | yes | PP, EX, A | 1 | 31 |
| 1915 | CYCLOHEXANONE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.95 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 1917 | ETHYL ACRYLATE, STABILIZED | 3 | F1 | II | 3+unst. | C | 2 | 2 |  | 40 | 95 | 0.92 | 1 | yes | T2 | II B | yes | PP, EX, A | 1 | 3; 5 |
| 1918 | ISOPROPYLBENZENE (cumene) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T2 | II A8) | yes | PP, EX, A | 0 |  |
| 1919 | METHYL ACRYLATE, STABILIZED | 3 | F1 | II | 3+unst. | C | 2 | 2 | 3 | 50 | 95 | 0.95 | 1 | yes | T2 | II B | yes | PP, EX, A | 1 | 3; 5; 23 |
| 1920 | NONANES | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.70 - 0.75 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 |  |
| 1922 | PYRROLIDINE | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 | 0.86 | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 |  |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE A) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE A0) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE A01) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE A02) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE A1) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE B) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE B1) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE B2) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1965 | HYDROCARBON GAS MIXTURE LIQUEFIED, N.O.S., (MIXTURE C) | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 31 |
| 1969 | ISOBUTANE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T21) | II A | yes | PP, EX, A | 1 | 31 |
| 1978 | PROPANE | 2 | 2F |  | 2.1 | G | 1 | 1 |  |  | 91 |  | 1 | yes | T1 | II A | yes | PP, EX, A | 1 | 31 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. boiling point < 60° C | 3 | FT1 | I | 3+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. 60° C < boiling point < 85° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23; 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. 85° C < boiling point < 115° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. boiling point > 115° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. 60° C < boiling point < 85° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 23; 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. 85° C < boiling point < 115° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 27; 29 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. boiling point > 115° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 27; 29 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. (tert-butanol 90% (mass)/methanol 10% (mass) mixture) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 | 2 |  | 95 | 0.95 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 | 7; 17 |
| 1987 | ALCOHOLS, FLAMMABLE, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 | 2 |  | 95 | 0.95 | 3 | yes |  |  | no | PP | 0 | 7; 17; 20: +46º C |
| 1989 | ALDEHYDES FLAMMABLE, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1989 | ALDEHYDES FLAMMABLE, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1989 | ALDEHYDES FLAMMABLE, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1989 | ALDEHYDES FLAMMABLE, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 1991 | CHLOROPRENE, STABILIZED | 3 | FT1 | I | 3+6.1+unst. | C | 2 | 2 | 3 | 50 | 95 | 0.96 | 1 | no | T2 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 3; 5; 23 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. boiling point < 60° C | 3 | FT1 | I | 3+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. boiling point < 60° C | 3 | FT1 | II | 3+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. 60° C < boiling point < 85° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23; 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. 85° C < boiling point < 115° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. boiling point > 115° C | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. boiling point < 60° C | 3 | FT1 | III | 3+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. 60° C < boiling point < 85° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 23; 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. 85° C < boiling point < 115° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 27; 29 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. boiling point > 115° C | 3 | FT1 | III | 3+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. vp50 >175 kPa | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. vp50 >175 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 1 | 50 | 97 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) vp50 >175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | I | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. 110 kPa < vp50 < 150 kPa | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) 110 kPa < vp50 < 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) vp50 < 110 kPa boiling point < 60° C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) vp50 < 110 kPa 60° C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 23; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S.(..., with more than 10% benzen) vp50 < 110 kPa 85° C < boiling point < 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) vp50 < 110 kPa boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) 60° C < boiling point < 85° C | 3 | F1 | III | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 23; 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) 85° C < boiling point < 115° C | 3 | F1 | III | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (..., with more than 10% benzen) boiling point > 115° C | 3 | F1 | III | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 27; 29 |
| 1993 | FLAMMABLE LIQUID, N.O.S. (cyclohexanone/cyclohexanol mixture) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.95 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 |  |
| 1999 | TARS, LIQUID 23° C < boiling point < 61° C | 3 | F1 | III | 3 | N | 4 | 2 | 2 |  | 97 |  | 3 | yes | T3 | II A7) | yes | PP, EX, A | 0 |  |
| 2021 | CHLOROPHENOLS LIQUID (2-chlorophenol) | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.23 | 2 | no | T1 | II A7) | yes | PP, EP, EX, TOX, A | 0 | 6: +10º C; 17 |
| 2022 | CRESILIC ACID | 6.1 | TC1 | II | 6.1+8+3 | C | 2 | 2 |  | 25 | 95 | 1.03 | 2 | no | T1 | II A | yes | PP, EP, EX, TOX, A | 2 | 6: +16º C; 17 |
| 2023 | EPICHLORHYDRINE | 6.1 | TF1 | II | 6.1+3 | C | 2 | 2 |  | 35 | 95 | 1.18 | 2 | no | T2 | II B | yes | PP, EP, EX, TOX, A | 2 | 5 |
| 2031 | NITRIC ACID, other than red fuming, with more than 70% acid | 8 | CO1 | I | 8+5.1 | N | 2 | 3 |  | 10 | 97 | 1.41 (at 68% HNO3)) | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2031 | NITRIC ACID, other than red fuming, with not more than 70% acid | 8 | CO1 | II | 8 | N | 2 | 3 |  | 10 | 97 | 1.5111) (at 68% HNO3)) | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2032 | NITRIC ACID, RED FUMING | 8 | COT | I | 8+5.1+6.1 | C | 2 | 2 |  | 50 | 95 | 1.51 | 1 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2045 | ISOBUTYRALDEHYDE | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.79 | 2 | yes | T4 | II A7) | yes | PP, EX, A | 1 | 7 |
| 2046 | CYMENES | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.88 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 2047 | DICHLOROPROPENES (2,3-dichloroprop-1-ene) | 3 | F1 | II | 3 | C | 2 | 2 |  | 45 | 95 | 1.2 | 2 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 2047 | DICHLOROPROPENES (mixtures of 2,3-dichloroprop-1-ene and 1,3-dichloroprop-1-ene) | 3 | F1 | II | 3 | C | 2 | 2 |  | 45 | 95 | 1.23 | 2 | yes | T21) | II A | yes | PP, EX, A | 1 |  |
| 2047 | DICHLOROPROPENES (mixtures of 2,3-dichloroprop-1-ene and 1,3-dichloroprop-1-ene) | 3 | F1 | III | 3 | C | 2 | 2 |  | 45 | 95 | 1.23 | 2 | yes | T21) | II A | yes | PP, EX, A | 0 |  |
| 2047 | DICHLOROPROPENES (1,3-dichloroprop-1-ene) | 3 | F1 | III | 3 | C | 2 | 2 |  | 40 | 95 | 1.23 | 2 | yes | T21) | II A7) | yes | PP, EX, A | 0 |  |
| 2048 | DICYCLOPENTADIENE | 3 | F1 | III | 3 | N | 3 | 2 | 2 |  | 95 | 0.94 | 3 | yes | T1 | II B4) | yes | PP, EX, A | 0 | 7; 17 |
| 2050 | DIISOBUTYLENE, ISOMERIC COMPOUNDS | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.72 | 3 | yes | T32) | II A7) | yes | PP, EX, A | 1 |  |
| 2051 | 2-DIMETHYLAMINOETHANOL | 8 | CF1 | II | 8+3 | N | 3 | 2 |  |  | 97 | 0.89 | 3 | yes | T3 | II A | yes | PP, EP, EX, A | 1 |  |
| 2053 | METHYL ISOBUTIL CARBINOL | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.81 | 3 | yes | T2 | II B4) | yes | PP, EX, A | 0 |  |
| 2054 | MORPHOLINE | 8 | CF1 | I | 8+3 | N | 3 | 2 |  |  | 97 | 1 | 3 | yes | T3 | II A | yes | PP, EP, EX, A | 1 |  |
| 2055 | STYRENE MONOMER, STABILIZED (vinylbenzene monomer, stabilized) | 3 | F1 | III | 3+unst. | N | 3 | 2 |  |  | 97 | 0.91 | 3 | yes | T1 | II A | yes | PP, EX, A | 0 | 3; 5; 16 |
| 2056 | TETRAHYDROFURAN | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.89 | 3 | yes | T3 | II B | yes | PP, EX, A | 1 |  |
| 2057 | TRIPROPYLENE (propylentrimer) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.73 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 0 |  |
| 2074 | ACRYLAMIDE, AQUEOUS SOLUTION | 6.1 | T2 | III | 6.1 | C | 2 | 2 |  | 30 | 95 | 1.03 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 3; 5; 16 |
| 2076 | CRESOLS, molten | 6.1 | TC2 | II | 6.1+8 | C | 2 | 2 | 2 | 25 | 95 | 1.03 - 1.05 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 2076 | CRESOLS, molten | 6.1 | TC2 | II | 6.1+8 | C | 2 | 2 | 2 | 25 | 95 | 1.03 - 1.05 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +66º C |
| 2078 | TOLUENE DIISOCYANATE and isomeric mixtures (2,4-toluene diisocyanate) | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.22 | 2 | no | T1 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 2; 7; 8; 17 |
| 2078 | TOLUENE DIISOCYANATE and isomeric mixtures (2,4-toluene diisocyanate) | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.22 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 2; 7; 8; 17; 20: +112º C |
| 2079 | DIETHYLENETRIAMINE | 8 | C7 | II | 8 | N | 4 | 2 |  |  | 97 | 0.96 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2205 | ADIPONITRILE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.96 | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 17 |
| 2206 | ISOCYANATES, TOXIC, N.O.S. (4-chlorophenyl isocyanate) | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.25 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17 |
| 2209 | FORMALDEHYDE SOLUTION with at least 25% formaldehyde | 8 | C9 | III | 8 | N | 4 | 2 |  |  | 97 | 1.09 | 3 | yes |  |  | no | PP, EP | 0 | 15 |
| 2215 | MALEIC ANHYDRIDE, molten | 8 | C3 | III | 8 | N | 3 | 3 | 2 |  | 95 | 0.93 | 3 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 2215 | MALEIC ANHYDRIDE, molten | 8 | C3 | III | 8 | N | 3 | 3 | 2 |  | 95 | 0.93 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17; 20: +88º C |
| 2218 | ACRYLIC ACID, STABILIZED | 8 | CF1 | II | 8+3+unst. | C | 2 | 2 |  | 30 | 95 | 1.05 | 1 | yes | T2 | II A7) | yes | PP, EP, EX, A | 1 | 3; 4; 5; 17 |
| 2227 | n-BUTYL METHACRYLATE, STABILIZED | 3 | F1 | III | 3+unst. | C | 2 | 2 |  | 25 | 95 | 0.9 | 1 | yes | T3 | II A | yes | PP, EX, A | 0 | 3; 5 |
| 2238 | CHLOROTOLUENES (m-chlorotoluene) | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.08 | 2 | yes | T1 | II A7) | yes | PP, EX, A | 0 |  |
| 2238 | CHLOROTOLUENES (o-chlorotoluene) | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.08 | 2 | yes | T1 | II A7) | yes | PP, EX, A | 0 |  |
| 2238 | CHLOROTOLUENES (p-chlorotoluene) | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.07 | 2 | yes | T1 | II A7) | yes | PP, EX, A | 0 | 6: +11º C; 17 |
| 2239 | CHLOROTOLUIDINES | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.15 | 2 | no | T1 | II A7) | yes | PP, EP, EX, TOX, A | 0 | 6: +6º C; 17 |
| 2241 | CYCLOHEPTANE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.81 | 3 | yes | T43) | II A | yes | PP, EX, A | 1 |  |
| 2247 | n-DECANE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.73 | 3 | yes | T4 | II A | yes | PP, EX, A | 0 |  |
| 2248 | DI-n-BUTYLAMINE | 8 | CF1 | II | 8+3 | N | 3 | 2 |  |  | 97 | 0.76 | 3 | yes | T3 | II A7) | yes | PP, EP, EX, A | 1 |  |
| 2259 | TRIETHYLENETETRAMINE | 8 | C7 | II | 8 | N | 3 | 2 |  |  | 97 | 0.98 | 3 | yes | T2 | II B4) | yes | PP, EP, EX, A | 1 |  |
| 2263 | DIMETHYLCYCLOHEXANES (cis-1,4-dimethylcyclohexane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 | 0.78 | 2 | yes | T43) | II A7) | yes | PP, EX, A | 1 |  |
| 2263 | DIMETHYLCYCLOHEXANES (trans-1,4-dimethylcyclohexane) | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 | 0.76 | 2 | yes | T43) | II A7) | yes | PP, EX, A | 1 |  |
| 2264 | N,N-DIMETHYLCYCLO- HEXYLAMINE | 8 | CF1 | II | 8+3 | N | 3 | 2 |  |  | 97 | 0.85 | 3 | yes | T3 | II B4) | yes | PP, EP, EX, A | 1 |  |
| 2265 | N,N-DIMETHYLFORMAMIDE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.95 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 2266 | DIMETHYL-N-PROPYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T4 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 2276 | ETHYL-2 HEXYLAMINE | 3 | FC | III | 3+8 | N | 3 | 2 |  |  | 97 | 0.79 | 3 | yes | T3 | II A7) | yes | PP, EP, EX, A | 0 |  |
| 2278 | n-HEPTENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.7 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 2280 | HEXAMETHYLENEDIAMINE, molten | 8 | C8 | III | 8 | N | 3 | 3 | 2 |  | 95 | 0.83 | 3 | yes | T3 | II B4) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 2280 | HEXAMETHYLENEDIAMINE, molten | 8 | C8 | III | 8 | N | 3 | 3 | 2 |  | 95 | 0.83 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17; 20: +66º C |
| 2282 | HEXANOLS | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.83 | 3 | yes | T3 | II A | yes | PP, EX, A | 0 |  |
| 2286 | PENTAMETHYLHEPTANE (isododecane) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.75 | 3 | yes | T2 | II A7) | yes | PP, EX, A | 0 |  |
| 2288 | ISOHEXENES | 3 | F1 | II | 3+unst. | C | 2 | 2 | 3 | 50 | 95 | 0.735 | 2 | yes | T2 | II B4) | yes | PP, EX, A | 1 | 3 |
| 2289 | ISOPHORONEDIAMINE | 8 | C7 | III | 8 | N | 3 | 2 |  |  | 97 | 0.92 | 3 | yes | T2 | II A | yes | PP, EP, EX, A | 0 | 17 |
| 2303 | ISOPROPENYLBENZENE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.91 | 3 | yes | T2 | II B | yes | PP, EX, A | 0 | 16 |
| 2309 | OCTADIENE (1,7-octadiene) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.75 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 2311 | PHENETIDINES | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.07 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 6: +7º C; 17 |
| 2312 | PHENOL, molten | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.07 | 2 | no | T1 | II A8) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 2312 | PHENOL, molten | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.07 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17; 20: +67º C |
| 2320 | TETRAETHYLENEPENTAMINE | 8 | C7 | III | 8 | N | 4 | 2 |  |  | 97 | 1 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2321 | TRICHLOROBENZENES, LIQUID (1,2,4-trichlorobenzene) | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.45 | 2 | no | T1 | II A | yes | PP, EP, EX, TOX, A | 0 | 7; 17 |
| 2321 | TRICHLOROBENZENES, LIQUID (1,2,4-trichlorobenzene) | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1.45 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 7; 17; 20: +95º C |
| 2323 | TRIETHYL PHOSPHITE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.8 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 0 |  |
| 2324 | TRIISOBUTYLENE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.76 | 3 | yes | T2 | II B4) | yes | PP, EX, A | 0 |  |
| 2325 | 1,3,5 TRIMETHYLBENZENE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.87 | 3 | yes | T1 | II A | yes | PP, EX, A | 0 |  |
| 2333 | ALLYL ACETATE | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 40 | 95 | 0.93 | 2 | no | T2 | II A7) | yes | PP, EP, EX, TOX, A | 2 |  |
| 2348 | BUTYL ACRYLATES, STABILIZED (n-butylacrylates, stabilized) | 3 | F1 | III | 3+unst. | C | 2 | 2 |  | 30 | 95 | 0.9 | 1 | yes | T3 | II B | yes | PP, EX, A | 0 | 3; 5 |
| 2350 | BUTYL METHYL ETHER | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.74 | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 |  |
| 2356 | 2-CHLOROPROPANE | 3 | F1 | I | 3 | C | 2 | 2 | 3 | 50 | 95 | 0.86 | 2 | yes | T1 | II A | yes | PP, EX, A | 1 | 23 |
| 2357 | CYCLOHEXYLAMINE | 8 | CF1 | II | 8+3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T3 | II A8) | yes | PP, EP, EX, A | 1 |  |
| 2362 | 1,1 DICHLOROETHANE | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 | 1.17 | 2 | yes | T2 | II A | yes | PP, EX, A | 1 | 23 |
| 2370 | 1-HEXENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.67 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 |  |
| 2382 | DIMETHYLHYDRAZINE SYMMETRICAL | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 50 | 95 | 0.83 | 1 | yes | T43) | II C | yes | PP, EP, EX, TOX, A | 2 |  |
| 2383 | DIPROPYLAMINE | 3 | FC | II | 3+8 | C | 2 | 2 |  | 35 | 95 | 0.74 | 2 | no | T3 | II A | yes | PP, EP, EX, A | 1 | 23 |
| 2397 | 3-METHYLBUTAN-2-ONE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.81 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 2398 | METHYL tert-BUTYL ETHER | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.74 | 3 | yes | T1 | II A | yes | PP, EX, A | 1 |  |
| 2404 | PROPIONITRILE | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 45 | 95 | 0.78 | 2 | no | T19) | II A | yes | PP, EP, EX, TOX, A | 2 |  |
| 2414 | THIOPHENE | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 1.06 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 |  |
| 2430 | ALKYLPHENOLS SOLID, N.O.S. (nonylphenol, isomeric mixture, molten) | 8 | C4 | II | 8 | N | 3 | 3 | 2 |  | 95 | 95 | 3 | yes | T2 | II A7) | yes | PP, EP, EX, A | 0 | 7; 17 |
| 2430 | ALKYLPHENOLS SOLID, N.O.S. (nonylphenol, isomeric mixture, molten) | 8 | C4 | II | 8 | N | 3 | 3 | 2 |  | 95 | 95 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17; 20: +125º C |
| 2432 | N,N-DIETHYLANILINE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.93 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 2448 | SULPHUR, molten | 4.1 | F3 | III | 4.1 | N | 4 | 1 | 2 |  | 95 | 2.07 | 3 | yes |  |  | no | PP, EP, TOX*, A | 0 | * Toximeter for H2S; 7; 20: +150º C |
| 2458 | HEXADIENES | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.72 | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 |  |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 | 2 | 35 | 95 | 1.0711) | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 7; 17 |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 35 | 95 | 0.89 | 1 | no | T2 | II B4) | yes | PP, EP, EX, TOX, A | 2 |  |
| 2486 | ISOBUTYL ISOCYANATE | 3 | FT1 | II | 3+6.1 | C | 2 | 2 |  | 40 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 |  |
| 2487 | PHENYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 25 | 95 | 1.1 | 1 | no | T1 | II A | yes | PP, EP, EX, TOX, A | 2 |  |
| 2490 | DICHLOROISOPROPYL ETHER | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.11 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2491 | ETHANOLAMINE or ETHANOLAMINE SOLUTION | 8 | C7 | III | 8 | N | 3 | 2 |  |  | 97 | 1.02 | 3 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 17 |
| 2493 | HEXAMETHYLENEIMINE | 3 | FC | II | 3+8 | N | 3 | 2 |  |  | 97 | 0.88 | 3 | yes | T32) | II A | yes | PP, EP, EX, A | 1 |  |
| 2496 | PROPIONIC ANHYDRIDE | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 | 1.02 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2518 | 1,5,9-CYCLODODECATRIENE | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.9 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 2527 | ISOBUTYL ACRYLATE, STABILIZED | 3 | F1 | III | 3+unst. | C | 2 | 2 |  | 30 | 95 | 0.89 | 1 | yes | T2 | II B9) | yes | PP, EX, A | 0 | 3; 5 |
| 2528 | ISOBUTYL ISOBUTYRATE | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.86 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 2531 | METHACRYLIC ACID, STABILIZED | 8 | C3 | II | 8+unst. | C | 2 | 2 | 2 | 25 | 95 | 1.02 | 1 | yes | T2 | II B4) | yes | PP, EP, EX, A | 0 | 3; 4; 5; 17 |
| 2564 | TRICHLOROACETIC ACID SOLUTION | 8 | C3 | II | 8 | N | 3 | 3 | 2 |  | 95 | 1.6211) | 3 | yes | T1 | II A7) | yes | PP, EP, EX, A | 0 | 7; 17; 22 |
| 2564 | TRICHLOROACETIC ACID SOLUTION | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 | 1.6211) | 3 | yes | T1 | II A7) | yes | PP, EP, EX, A | 0 | 22 |
| 2574 | TRICRESYL PHOSPHATE with more than 3% ortho isomer | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.18 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2579 | PIPERAZINE, molten (diethylenediamine) | 8 | C8 | III | 8 | N | 3 | 3 | 2 |  | 95 | 0.9 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17 |
| 2586 | ALKYLSULFONIC ACIDS, LIQUID with not more than 5% free sulphuric acid | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2608 | NITROPROPANES | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 1 | 3 | yes | T2 | II B7) | yes | PP, EX, A | 0 |  |
| 2615 | ETHYL PROPYL ETHER | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.73 | 3 | yes | T43) | II A7) | yes | PP, EX, A | 1 |  |
| 2618 | VINYLTOLUENES, STABILIZED | 3 | F1 | III | 3+unst. | C | 2 | 2 |  | 25 | 95 | 0.92 | 1 | yes | T1 | II B4) | yes | PP, EX, A | 0 | 3; 5 |
| 2651 | 4,4’- DIAMINODIPHENYL-METHANE | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 1 | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 7; 17 |
| 2672 | AMMONIA SOLUTION (relative density between 0.880 and 0.957 at 15° C in water, with more than 10% but not more than 35% ammonia) | 8 | C5 | III | 8 | N | 2 | 2 |  | 10 | 97 | 0.8810) - 0.9610) | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2683 | AMMONIUM SULPHIDE SOLUTION | 8 | CFT | II | 8+3+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 15; 16 |
| 2693 | BISULPHITES, AQUEOUS SOLUTION, N.O.S. | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 2709 | BUTYLBENZENES | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.87 | 3 | yes | T2 | II A | yes | PP, EX, A | 0 |  |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. (2-aminobutane) | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 | 0.72 | 2 | yes | T43) | II A | yes | PP, EP, EX, A | 1 | 23 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | I | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | 8 | C7 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 2754 | N-ETHYLTOLUIDINES (N-ethyl-o-toluidine) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.94 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2754 | N-ETHYLTOLUIDINES (N-ethyl-m-toluidine) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.94 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2754 | N-ETHYLTOLUIDINES, N-ethyl-o-toluidine and N-ethyl-m-toluidine mixtures | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 25 | 95 | 0.94 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 2754 | N-ETHYLTOLUIDINES (N-ethyl-p-toluidine) | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 2 | 25 | 95 | 0.94 | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 7; 17 |
| 2789 | ACETIC ACID, GLACIAL | 8 | CF1 | II | 8+3 | N | 2 | 3 | 2 | 10 | 95 | 1.05 (with 100% acid) | 3 | yes | T1 | II A | yes | PP, EP, EX, A | 1 | 7; 17 |
| 2789 | ACETIC ACID SOLUTION, more than 80% acid, by mass | 8 | CF1 | II | 8+3 | N | 2 | 3 | 2 | 10 | 95 | 1.05 (with 100% acid) | 3 | yes | T1 | II A | yes | PP, EP, EX, A | 1 | 7; 17 |
| 2790 | ACETIC ACID SOLUTION, more than 50% but not more than 80% acid, by mass | 8 | C3 | II | 8 | N | 2 | 3 |  | 10 | 95 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2790 | ACETIC ACID SOLUTION, more than 10% but not more than 50% acid, by mass | 8 | C3 | III | 8 | N | 2 | 3 |  | 10 | 95 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2796 | BATTERY FLUID, ACID | 8 | C1 | II | 8 | N | 4 | 3 |  |  | 97 | 1.00 - 1.84 | 3 | yes |  |  | no | PP, EP | 0 | 8; 22; 30 |
| 2796 | SULPHURIC ACID with not more than 51% acid | 8 | C1 | II | 8 | N | 4 | 3 |  |  | 97 | 1.00 - 1.41 | 3 | yes |  |  | no | PP, EP | 0 | 8; 22; 30 |
| 2797 | BATTERY FLUID, ALKALI | 8 | C5 | II | 8 | N | 4 | 3 |  |  | 97 | 1.00 - 2.13 | 3 | yes |  |  | no | PP, EP | 0 | 22; 30 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | T1 | I | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T1 | I | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T1 | I | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | T1 | I | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | T1 | II | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T1 | II | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | T1 | III | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 23; 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. (1,2,3-trichlorobenzene, molten) | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 7; 17; 22 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. (1,2,3-trichlorobenzene, molten) | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 7; 17; 20: +92º C; 22 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. (1,3,5-trichlorobenzene, molten) | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 0 | 7; 17; 22 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. (1,3,5-trichlorobenzene, molten) | 6.1 | T2 | III | 6.1 | C | 2 | 2 | 2 | 25 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 7; 17; 20: +92º C; 22 |
| 2815 | N-AMINOETHYLPIPERAZINE | 8 | C7 | III | 8 | N | 4 | 2 |  |  | 97 | 0.98 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2820 | BUTYRIC ACID | 8 | C3 | III | 8 | N | 2 | 3 |  | 10 | 97 | 0.96 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2829 | CAPROIC ACID | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 | 0.92 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 2831 | 1,1,1-TRICHLOROETHANE | 6.1 | T1 | III | 6.1 | C | 2 | 2 | 3 | 50 | 95 | 1.34 | 2 | yes |  |  | no | PP, EP, TOX, A | 0 | 23 |
| 2850 | TETRAPROPYLENE (PROPYLENE TETRAMER) | 3 | F1 | III | 3 | N | 4 | 2 |  |  | 97 | 0.76 | 3 | yes |  |  | no | PP, EX, A | 0 |  |
| 2874 | FURFURYL ALCOHOL | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.13 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. (2-propanol and didecyldimethylammonium chloride, aqueous solution) | 8 | CF1 | II | 8+3 | N | 3 | 3 |  |  | 95 | 0.95 | 3 | yes | T3 | II A | yes | PP, EP, EX, A | 1 |  |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. (aqueous solution of hexadecyltrimethylammonium chloride (50%) and ethanol (35%)) | 8 | CF1 | II | 8+3 | N | 2 | 3 |  | 10 | 95 | 0.9 | 3 | yes | T2 | II B | yes | PP, EP, EX, A | 1 | 6: +7º C; 17 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point < 60° C | 8 | CT1 | I | 8+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 8 | CT1 | I | 8+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 8 | CT1 | I | 8+6.1 | C | 2 | 2 |  | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point > 115° C | 8 | CT1 | I | 8+6.1 | C | 2 | 2 |  | 35 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point < 60° C | 8 | CT1 | II | 8+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 8 | CT1 | II | 8+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 8 | CT1 | II | 8+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point > 115° C | 8 | CT1 | II | 8+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point < 60° C | 8 | CT1 | III | 8+6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 8 | CT1 | III | 8+6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 23; 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 8 | CT1 | III | 8+6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2922 | TOXIC LIQUID CORROSIVE, N.O.S. boiling point > 115° C | 8 | CT1 | III | 8+6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. boiling point < 60° C | 3 | FC | I | 3+8 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EP, EX, A | 1 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. boiling point < 60° C | 3 | FC | II | 3+8 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EP, EX, A | 1 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 3 | FC | II | 3+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 1 | 23; 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 1 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. boiling point > 115° C | 3 | FC | II | 3+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 1 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. boiling point < 60° C | 3 | FC | III | 3+8 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EP, EX, A | 0 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 3 | FC | III | 3+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 0 | 23; 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 3 | FC | III | 3+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 0 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. boiling point > 115° C | 3 | FC | III | 3+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EP, EX, A | 0 | 27; 29 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. (aqueous solution of dialkyl-dimethylammonium chloride (C8-C18) and 2-propanol) | 3 | FC | II | 3+8 | C | 2 | 2 |  | 50 | 95 | 0.88 | 2 | yes | T2 | II A | yes | PP, EP, EX, A | 1 |  |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | TC1 | I | 6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TC1 | I | 6.1+8 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TC1 | I | 6.1+8 | C | 2 | 2 |  | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | TC1 | I | 6.1+8 | C | 2 | 2 |  | 35 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | TC1 | II | 6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TC1 | II | 6.1+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23; 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TC1 | II | 6.1+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2927 | TOXIC LIQUID CORROSIVE, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | TC1 | II | 6.1+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | TF1 | I | 6.1+3 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | TF1 | I | 6.1+3 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23; 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 50 | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | TF1 | I | 6.1+3 | C | 2 | 2 |  | 35 | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. boiling point < 60° C | 6.1 | TF1 | II | 6.1+3 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TF1 | II | 6.1+3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23; 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TF1 | II | 6.1+3 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. boiling point > 115° C | 6.1 | TF1 | II | 6.1+3 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 2935 | ETHYL-2-CHLOROPROPIONATE | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.08 | 2 | yes | T43) | II A | yes | PP, EX, A | 0 |  |
| 2947 | ISOPROPYL CHLOROACETATE | 3 | F1 | III | 3 | C | 2 | 2 |  | 30 | 95 | 1.09 | 2 | yes | T43) | II A | yes | PP, EX, A | 0 |  |
| 2983 | ETHYLENE OXIDE AND PROPYLENE MIXTURE, with not more than 30% ethylene oxide | 3 | FT1 | I | 3+6.1+unst. | C | 1 | 1 | 3 |  | 95 | 0.85 | 1 | no | T2 | II B | yes | PP, EP, EX, TOX, A | 2 | 2; 3; 12; 31 |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S., molten, (alkyl-amine (C12 to C18)) | 9 | M7 | III | 9 | N | 4 | 3 | 2 |  | 95 | 0.79 | 3 | yes |  |  | no | PP | 0 | 7; 17 |
| 3079 | METHACRYLONITRILE, STABILIZED | 3 | FT1 | I | 3+6.1+unst. | C | 2 | 2 |  | 45 | 95 | 0.8 | 1 | no | T1 | II B4) | yes | PP, EP, EX, TOX, A | 2 | 3; 5 |
| 3082 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S. | 9 | M6 | III | 9 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP | 0 | 22; 27 |
| 3082 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S. (bilge water) | 9 | M6 | III | 9 | N | 4 | 2 |  |  | 97 |  |  | yes |  |  | no | PP | 0 |  |
| 3092 | 1-METHOXY-2-PROPANOL | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 0.92 | 3 | yes | T3 | II B | yes | PP, EX, A | 0 |  |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | II | 8 | N | 4 | 3 |  |  | 97 | 0.95 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 | 0.95 | 3 | yes |  |  | no | PP, EP | 0 |  |
| 3175 | SOLIDS CONTAINING FLAMMABLE LIQUID, N.O.S., molten with a flash-point of not more than 61° C (2-propanol and dialkyl (C12 to C18) dimethylammonium chloride) | 4.1 | F1 | II | 4.1 | N | 3 | 3 | 2 |  | 95 | 0.86 | 3 | yes | T2 | II A | yes | PP, EX, A | 1 | 7; 17 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 7; 27 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point (CARBON BLACK REEDSTOCK (PYROLYSIS OIL)) | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T 1 | II B | yes | PP, EX, A | 0 | 7 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point (PYROLYSIS OIL A) | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T 1 | II B | yes | PP, EX, A | 0 | 7 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point (RESIDUAL OIL) | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T 1 | II B | yes | PP, EX, A | 0 | 7 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point (MIXTURE OF CRUDE NAPHTHALINE) | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T 1 | II B | yes | PP, EX, A | 0 | 7 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61° C, at or above its flash-point (CREOSOTE OIL) | 3 | F2 | III | 3 | N | 3 | 2 | 2 |  | 95 |  | 3 | yes | T 2 | II B | yes | PP, EX, A | 0 | 7 |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S. at or above 100° C (including molten metals, molten salts, etc.) | 9 | M9 | III | 9 | N | 4 | 1 | 2 |  | 95 |  | 3 | yes |  |  | no | PP | 0 | 7; 20:+115º C; 22; 24; 25; 27 |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S. at or above 100° C (including molten metals, molten salts, etc.) | 9 | M9 | III | 9 | N | 4 | 1 | 2 |  | 95 |  | 3 | yes |  |  | no | PP | 0 | 7; 20:+225º C; 22; 24; 27 |
| 3259 | AMINES, SOLID, CORROSIVES, N.O.S. molten (monoalkyl (C12 to C18) amine acetate) | 8 | C8 | III | 8 | N | 4 | 3 | 2 |  | 95 | 0.87 | 3 | yes |  |  | no | PP, EP | 0 | 7; 17 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | I | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | II | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. (aqueous solution of phosphoric acid and citric acid) | 8 | C1 | I | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. (aqueous solution of phosphoric acid and citric acid) | 8 | C1 | II | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. (aqueous solution of phosphoric acid and citric acid) | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 |  |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | I | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | II | 8 | N | 2 | 3 |  | 10 | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | III | 8 | N | 4 | 3 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | I | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | I | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | II | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | III | 8 | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP, EP | 0 | 27 |
| 3271 | ETHERS, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14, 27; 29 |
| 3271 | ETHERS, N.O.S. (tert-amylmethyl ether) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.77 | 3 | yes | T2 | II B4) | yes | PP, EX, A | 1 |  |
| 3271 | ETHERS, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14, 27 |
| 3272 | ESTERS, N.O.S. vp50 < 110 kPa | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.77 | 3 | yes | T2 | II B4) | yes | PP, EX, A | 1 | 14, 27; 29 |
| 3272 | ESTERS, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14, 27 |
| 3276 | NITRILES, TOXIC, N.O.S. (2-methylglutaronitrile) | 6.1 | T1 | II | 6.1 | C | 2 | 2 |  | 10 | 97 | 0.95 | 2 | no |  |  | no | PP, EP, TOX, A | 2 |  |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. boiling point < 60° C | 3 | FTC | I | 3+6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. boiling point < 60° C | 3 | FTC | II | 3+6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. 60° C < boiling point < 85° C | 3 | FTC | II | 3+6.1+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 23, 27; 29 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. 85° C < boiling point < 115° C | 3 | FTC | II | 3+6.1+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. boiling point > 115° C | 3 | FTC | II | 3+6.1+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | no | T43) | II B4) | yes | PP, EP, EX, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point < 60° C | 6.1 | T4 | I | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T4 | I | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 23, 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T4 | I | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point > 115° C | 6.1 | T4 | I | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point < 60° C | 6.1 | T4 | II | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T4 | II | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23, 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T4 | II | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point > 115° C | 6.1 | T4 | II | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point < 60° C | 6.1 | T4 | III | 6.1 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | T4 | III | 6.1 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 23, 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | T4 | III | 6.1 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. boiling point > 115° C | 6.1 | T4 | III | 6.1 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 0 | 27; 29 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. (sodium dichromate solution) | 6.1 | T4 | III | 6.1 | C | 2 | 2 |  | 30 | 95 | 1.68 | 2 | no |  |  | no | PP, EP, TOX, A | 0 |  |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. boiling point < 60° C | 6.1 | TC3 | I | 6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TC3 | I | 6.1+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23, 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TC3 | I | 6.1+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. boiling point > 115° C | 6.1 | TC3 | I | 6.1+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. boiling point < 60° C | 6.1 | TC3 | II | 6.1+8 | C | 1 | 1 |  |  | 95 |  | 1 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. 60° C < boiling point < 85° C | 6.1 | TC3 | II | 6.1+8 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 23, 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. 85° C < boiling point < 115° C | 6.1 | TC3 | II | 6.1+8 | C | 2 | 2 |  | 50 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3289 | TOXIC LIQUID CORROSIVE, INORGANIC, N.O.S. boiling point > 115° C | 6.1 | TC3 | II | 6.1+8 | C | 2 | 2 |  | 35 | 95 |  | 2 | no |  |  | no | PP, EP, TOX, A | 2 | 27; 29 |
| 3295 | HYDROCARBON LIQUID, N.O.S. vp50 > 175 kPa) | 3 | F1 | I | 3 | N | 1 | 1 |  |  | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. vp50 > 175 kPa) | 3 | F1 | I | 3 | N | 2 | 2 | 1 | 50 | 97 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. 110 kPa < vp50 < 175 kPa) | 3 | F1 | I | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. 110 kPa < vp50 < 150 kPa) | 3 | F1 | I | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. 110 kPa < vp50 < 175 kPa) | 3 | F1 | II | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. 110 kPa < vp50 < 150 kPa) | 3 | F1 | II | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. vp50 > 110 kPa) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 14; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 14; 27 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (1-Octen) | 3 | F1 | II | 3 | N | 2 | 2 |  | 10 | 97 | 0.71 | 3 | yes | T3 | II B4) | yes | PP, EX, A | 1 | 14 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (polycyclic aromatic hydrocarbons mixture) | 3 | F1 | III | 3 | N | 3 | 2 |  |  | 97 | 1.08 | 3 | yes | T1 | II A | yes | PP, EX, A | 0 | 14 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 > 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) 110 kPa < vp50 < 175 kPa | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) 110 kPa < vp50 < 175 kPa | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa boiling point < 60° C | 3 | F1 | II | 3 | C | 1 | 1 |  |  | 95 |  | 1 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa 60° C < boiling point < 85° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 23; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa 85° C < boiling point < 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa boiling point > 115° C | 3 | F1 | II | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 1 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa 60° C < boiling point < 85° C | 3 | F1 | III | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 23; 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa 85° C < boiling point < 115° C | 3 | F1 | III | 3 | C | 2 | 2 |  | 50 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 27; 29 |
| 3295 | HYDROCARBONS LIQUID, N.O.S. (... with more than 10% benzen) vp50 < 110 kPa boiling point > 115° C | 3 | F1 | III | 3 | C | 2 | 2 |  | 35 | 95 |  | 2 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 27; 29 |
| 9000 | AMMONIA, heavily refrigerated | 2 | 3TC |  | 2.1+2.3+8 | G | 1 | 1 | 1; 3 |  | 95 |  | 1 | yes | T1 | II A | yes | PP, EP, EX, TOX, A | 2 | 1; 31 |
| 9001 | SUBSTANCES with a flash-point above 61° C, heated within a limiting range of 15 K below their flash-point, N.O.S. | 3 |  |  |  | N | 3 | 2 |  |  | 97 |  | 3 | yes | T43) | II B4) | yes | PP, EX, A | 0 | 27 |
| 9002 | SUBSTANCES with a self-ignition temperature of 200° C or below, N.O.S. | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 9003 | SUBSTANCES with a flash-point above 61° C but not more than 100° C, N.O.S. | 9 |  |  |  | N | 4 | 2 |  |  | 97 |  | 3 | yes |  |  | no | PP | 0 | 27 |
| 9003 | SUBSTANCES with a flash-point above 61° C but not more than 100° C, N.O.S. (ethylene glycol monobutyl ether) | 9 |  |  |  | N | 4 | 2 |  |  | 97 | 0.9 | 3 | yes |  |  | no | PP | 0 |  |
| 9003 | SUBSTANCES with a flash-point above 61° C but not more than 100° C, N.O.S. (2-ethylhexylacrylate) | 9 |  |  |  | N | 4 | 2 |  |  | 97 | 0.89 | 3 | yes |  |  | no | PP | 0 | 3; 5; 16 |
| 9004 | DIPHENYLMETHANE-4.4’-DIISOCYANATE | 9 |  |  |  | N | 2 | 3 | 2 | 10 | 95 | 1.2111) | 3 | yes |  |  | no | PP | 0 | 7; 8; 17; 19 |

# Footnotes

x = the Class number of the dangerous substance or article, without dividing point if applicable.

# Text boxes

-----