#### Informal Document No. 5

32nd GRSP, 10-13 December 2002

## Establishment of Regulation for Pedestrian Safety in Japan

In Japan, about 30% of people killed in traffic accidents are pedestrians, so the government decided to establish a regulation for pedestrian head protection based on studies made by the Pedestrian Safety Working Group of IHRA.

The standard will apply to passenger cars and trucks derived from passenger cars of 2,500kg or less. It will be finalized by March 2003 and phased into practice starting September 2005.

At GRSP, the Informal Group on Pedestrian Safety has been working to establish a GTR for the protection of pedestrians. Japan plans to harmonize its pedestrians' head protection criteria with this GTR when it is finalized, while also introducing pedestrians' leg protection criteria.

Japan's regulation for pedestrian head protection is outlined as follows:

Draft Regulation for Pedestrian Safety in Japan

- Scope of vehicles

- Passenger cars having no more than 10 seats

- Trucks having a GVW not exceeding 2,500kg and a similar front shape as the vehicle defined in 1. (1)

- Effective Date

- Vehicles except for vehicles defined in (2)

・New-type vehicles			: September 2005

・Continuously-manufactured vehicles 	: September 2010

- Low height vehicles, Vehicles requiring high endurance, such as SUVs and trucks, Full cab over vehicles, Hybrid-engine vehicles

・New-type vehicles			: September 2007

・Continuously-manufactured vehicles 	: September 2012

Note: New-type vehicles, as a result of the modification on emission performance relating to “4. Kinds of engine and main construction (Only for improvement of emission performance)” and/or “13. Exhaust emission standard values stipulated in the Safety Regulations for Road Vehicles, the low exhaust emission motor vehicle approval enforcement procedure for approval” in the “Judgment Criteria for Identity of Types of Motor Vehicles”, will be considered as continuously-manufactured vehicles.

- Outline of the regulation (See Attachment 1)

- Test Procedure

- Test area (See Attachment 2)

The child and adult head impactor test will be considered for the regulation.

Test area for child head impactor: 1,000mm ( WAD ( 1,700mm

Test area for adult head impactor: 1,700mm ( WAD ( 2,100mm

Note: WAD (Wrap-Around Distance) means the distance from the ground to the point on the bonnet along the vehicle front structure.

- Impactor

Child head impactor: Diameter 165mm, weight 3.5kg

Adult head impactor: Diameter 165mm, weight 4.5kg

- Impact speed and angle

|  | Child head impactor | Adult head impactor |
| --- | --- | --- |
|  | Speed (km/h) | Angle (deg) | Speed (km/h) | Angle (deg) |
| Category 1 | 32 | 65 | 32 | 65 |
| Category 2 | 32 | 60 | 32 | 90 |
| Category 3 | 32 | 25 | 32 | 50 |

|  | Definition | Note |
| --- | --- | --- |
| Category 1 | Vehicle having a BLE height of less than 835mm | Sedan type |
| Category 2 | Vehicle having a BLE height of not less than 835mm | SUV type |
| Category 3 | Vehicle having a bonnet angle of not less than 30 deg. | 1 Box type |

Note: BLE height: Bonnet Leading Edge height (See Attachment 2)

- Criteria

HIC (Head Injury Criteria), defined by the following formula, should not be exceeded by 1,000 on two-thirds or more of the test area. On the remaining area, HIC should not be exceeded by 2,000.