Informal Document No.  7

(130th WP29, 24-27 June,

agenda item 4.2.27.)

# Correction to document TRANS/WP29/2003/34

Transmitted by the expert from IMMA

Proposal for draft supplement 2 to Regulation No. 113

(Headlamps emitting a symmetrical passing beam)

## Correction

# The first five lines of 6.3.2.2. in document TRANS/WP29/2003/34 shall be deleted as follows,

6.3.2.2.	The point of intersection (HV) of lines H-H and V-V shall be situated within the isolux 90

per cent of maximum illumination;

the luminous centre of the driving beam shall be situated not more than 0.6° above or below

the line H-H;

the maximum value (EM) shall not be less than 32 lux;

Starting from point HV, horizontally to the right and left, the illumination shall be not less

than 12 lux for Class B and C headlamp, and 24 lux for Class D headlamp to a distance

of 1125 mm and not less than 3 lux for Class B and C headlamp, and 6 lux for Class D

headlamp to a distance of 2250 mm.

In the case of a Class C and D headlamp, the intensities shall conform to the tables A or B

in annex 3. Table A applies in the case where a primary driving beam is being produced

with a single light source. Table B applies in the case where the driving beam is being

produced by a secondary driving beam headlamp operated with a harmonized passing beam

headlamp or a primary driving beam headlamp.

## Justification

The content of these lines is contained in the earlier paragraph 6.3.2.1, either as duplicate text or in the technical content, and therefore it is redundant in this paragraph. The text was inadvertently included in the final draft, for which IMMA apologises, and should be deleted before the document is approved by WP29.

______________