| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. RESTRICTED TRANS/WP.29/GRPE/2003/9 29 November 2002 ENGLISH Original: ENGLISH AND FRENCH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Pollution and Energy (GRPE)

(Forty-fifth session, 13-17 January 2003,

agenda item 10.3.)

PROPOSAL FOR DRAFT SUPPLEMENT 4 TO THE 01 SERIES

OF AMENDMENTS TO REGULATION No. 67

Transmitted by the expert from the Netherlands

Note:	The text reproduced below was prepared by the expert from Netherlands in order to introduce into the Regulation a test interpretation.  The proposal for a new paragraph 2.3.6.2.2. is based on TRANS/WP.29/2002/72, considered by WP.29 at its one-hundred-and-twenty-eighth session and referred to GRPE for consideration (see TRANS/WP.29/885, para. 89).

_______

__________________

Note:	This document is distributed to the Experts on Pollution and Energy only.

Annex 10,

Insert a new paragraph 2.3.6.2.2., to read:

"2.3.6.2.2.	Test interpretation

The container shall comply with the external leak test requirements as defined in paragraph 2.3.6.3.

The container shall achieve a minimum burst pressure of 85 per cent of the burst pressure."

Paragraph 2.3.6.2.2. (former), renumber as paragraph 2.3.6.2.3.

_________