Неофициальный документ №2							Informal document No.2
Пункт 6 b) повестки дня								Agenda item 6 (b)
Подготовлен секретариатом							Prepared by the secretariat

DRAFT

ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

Working Party on Inland Water Transport

Geneva

##### INVENTORY OF MAIN 
STANDARDS AND PARAMETERS 
OF THE E WATERWAY NETWORK

(“BLUE BOOK”)

Revision 1

NOTE

The designations employed and the presentation of the material in this publication do not imply the expression of any opinion whatsoever on the part of the Secretariat of the United Nations concerning the legal status of any country, territory, city or area, or of its authorities, or concerning the delimitation of its frontiers or boundaries.

*       *       *

# INVENTORY OF MAIN STANDARDS AND PARAMETERS OF 
THE E WATERWAY NETWORK ("BLUE BOOK")

## INTRODUCTION

At its fortieth session, the UN/ECE Working Party on Inland Water Transport (SC.3) agreed to proceed with the drafting of the so-called "blue book" which would contain technical characteristics of European inland waterways and ports of international importance (E waterways and ports) identified in the European Agreement on Main Inland Waterways of International Importance (AGN).

The objective of this publication is to establish an inventory of existing and envisaged standards and parameters of E waterways and ports in Europe and to show, on an internationally comparable basis, the current inland navigation infrastructure parameters in Europe as compared to the minimum standards and parameters prescribed in the AGN Agreement.  This would enable member Governments and intergovernmental organizations concerned to use the “Blue book” as a basic instrument for monitoring the progress made in the implementation of the AGN.

This revised version of the “Blue book” has been prepared by the Transport Division in accordance with the instructions of Governments as set out in TRANS/SC.3/144 and Adds.1-4 and additional information received by the secretariat from member Governments and river commissions.

## INLAND WATERWAYS OF INTERNATIONAL IMPORTANCE

The European Agreement on Main Inland Waterways of International Importance in its annex III stipulates the requirements for the classification of E waterways. In total 27,711 km of European inland waterways have been earmarked by Governments as E waterways. The above length excludes the double counting of sections on which two or more E waterways overlap. The breakdown by classes of inland waterways of international importance may be summarized in the table below.

#### Classification of E waterways

|  | Missing links | Less than class IV | Class IV | Class Va | Class Vb | Class VIa | Class VIb | Class VIc | Class VII | Total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Length (km) | 1,489 | 4,286 | 3,969 | 3,270 | 5,051 | 667 | 5,766 | 1,592 | 1,621 | 27,711 |
| % | 5.37 | 15.47 | 14.32 | 11.80 | 18.23 | 2.41 | 20.81 | 5.74 | 5.85 | 100 |

In accordance with the AGN Agreement only waterways meeting the basic minimum requirements of class IV (minimum dimensions of vessels 80.0 m x 9.50 m) can be considered as E waterways. The Agreement recommends that the new E waterways to be built (for the completion of missing links) should meet at least the requirements of class Vb, while the waterways to be modernized should meet the requirements of at least class Va.

## BOTTLENECKS AND MISSING LINKS IN THE NETWORK OF MAIN INLAND WATERWAYS OF INTERNATIONAL IMPORTANCE

In the course of its work on the draft AGN the Working Party SC.3 endorsed the following definitions of "bottlenecks" and "missing links" in the inland navigation network, elaborated by the ad hoc Group of Experts on Inland Waterway Infrastructure:

"Those sections of the European waterway network of international importance that have parameter values being substantially lower than target requirements are called bottlenecks.

There are two kinds of bottlenecks:

"Basic bottlenecks" are the sections of E waterways whose parameters at the present time are not in conformity with the requirements applicable to inland waterways of international importance in accordance with the new classification of European inland waterways (class IV);

"Strategic bottlenecks" are other sections satisfying the basic requirements of the class IV but which, nevertheless, ought to be modernized in order to improve the structure of the network or to increase the economic capacity of inland navigation traffic.

"Missing links" are such parts of the future network of inland waterways of international importance which do not exist at present.

The basic condition for the elimination of bottlenecks and completion of missing links is the positive result of economic evaluation" (TRANS/SC.3/133, paragraph 18).

In accordance with the above definition the following list of bottlenecks and missing links, by countries, has been established.

Austria

Missing link: Danube-Oder-Elbe Connection (E 20).

Basic bottlenecks: none.

Strategic bottlenecks: Danube (E 80) from 2,038.0 to 2,008.0 km and from 1,921.0 to 1,873.0 km - low fairway depth (in some locations down to 2.20 m).

Belarus

Missing link: none.

Basic bottlenecks: none.

Strategic bottlenecks:

-	Mukhovets (E 40) from Brest to Kobrin - low maximum draught (1.6 m).

-	Dneprovsko-Bugskiy Canal (E 40) from Kobrin to Pererub - low maximum draught (1.6 m).

-	Pina (E 40) from Pererub to Pinsk - low maximum draught (1.6 m).

- Pripyat (E 40) from Stakhovo to Pkhov – low maximum draught (1.3 m).

- Pripyat (E 40) from Pkhov to Belarus/Ukrainian boarder - low maximum draught (1.5 m).

Belgium

Missing link:

-	Meuse - Rhine link. */

-	Maldegem - Zeebrugge (E 07).

Basic bottlenecks:

-	Kanaal Bocholt - Herentals (E 01-01), Bocholt - Dessel section.

-	Zuid - Willemsvaart (E 01-01), section Bocholt - Belgium/Netherlands border.

-	Gent - Oostende Canal (E 02), Brugge - Beernem section.

-	Harelbeke - Halluin lock (E 02) - upgrading from class II to class IV . The project is under way

-	Plassendale - Nieuwpoort Canal (E 02-02-01).

-	Charleroi-Bruxelles Canal (E 04), Lembeek - Bruxelles section - upgrading the height under bridges and improvement of the waterway is required.

-	Bossuit - Kortrijk Canal (E 05-01), Zwevegem - Kortrijk section.

-	Dender (E 05-04), Aalst - Dendermonde section. **/

-	Canal de Lanaye (E 01) - building of a class VIb lock. The project is under way.

Strategic bottlenecks:

-	Meuse (E 01) from Pont d'Ougrée to Liège - upgrading from class Vb to class VIb is envisaged.

-	Lys Mitoyenne - Lys (Menin - Deinze section) and Lys Derivation Canal up to Schipdonk (E 02) - upgrading from class IV to class Vb is envisaged within the Seine - Escaut link project.

-		Bruxelles - Schelde (E 04) - upgrading from class Va to class VIb is envisaged.

-	Albertkanaal (E 05), Wijnegem passage and section Kanne - Liège - upgrading from class Vb to class VIb is envisaged.

Bulgaria

Missing link: none

Basic bottlenecks: none

Strategic bottlenecks: Danube from 845.5 to 375.0 km - low fairway depth at dry seasons (below 2.50 m - value recommended by the Danube Commission) at several critical sections i.e.:

-	from 845.5 to 610.0 km, with fairway depth limited to 2.10-2.20 m for 10-15 days a year, and

-	from 610.0 to 375.0 km, with fairway depth limited to 1.80-2.00 m for 20-40 days a year.

Croatia

Missing link: Danube - Sava Canal (E 80-10) from Vucovar to Samac.

Basic bottlenecks: Sava (E 80-12) from Serbia and Montenegro/Croatian State border to Sisak - upgrading from class III to class Vb is required.

Strategic bottlenecks: none.

Czech Republic

Missing link: Danube - Oder - Elbe Connection (E 20 and E 30).

Basic bottlenecks: none.

Strategic bottlenecks: Elbe (E 20) from State border to Usti nad Labem - low fairway depth at dry seasons (0.9-2.0 m), from Usti nad Labem to Mëlník - narrow width of lock gates (11 m), from Mëlník to Pardubice - low height under bridges (3.7 m).

-	Vltava (E 20-06) - low fairway depth (1.2-1.8 m), low height under bridges (4.5 m) and narrow width of lock gates.

Finland

Missing links: none.

Basic bottlenecks: none.

Strategic bottlenecks: Saimaa Canal (E 60-11) from Vyborg to Kuopio/Joensuu - upgrading to class Va is envisaged.

France

Missing links:

-	Rhône - Rhine Canal (E 10).*/

-	Seine - Moselle Link (E 80).

-	Seine - Escaut Link (E 05).

-	Saône - Moselle Link (E 10-02).

Basic bottlenecks: Meuse (E 01-02) between Givet and the Belgian border - upgrading to class IV.

Strategic bottlenecks:

-	Rhine (E 10) from Iffezheim to Niffer - length of convoys is limited by 183 m, upgrading to class VIb (186.5 m). The project is under way.

-	Oise (E 80) from Conflans to Creil - low height under bridges (5.18 m), from Creil to Compiègne low draught and height under bridges (2.50 m and 5.76 m, respectively).

-	Oise (E 80) increasing the water draught up to 3.5 m between Creil and Conflans - Sainte-Honorine.

-	Moselle (E 80) - lifting of bridges between Metz and Apach enabling 3-layer container transport.

-	Network Nord Pas-de-Calais (E 02 and E 05) - lifting of bridges and upgrading of links with Belgium to class Va.

-	Dunkerque - Escaut link and Escaut (E 01) up to Condé - low height under bridges (4.44 m).

-	Deûle and Deûle Canal (E 02) from Quesnoy/Deûle to Lille - upgrading to class Va is under way, from Lille to Bauvin - low height under bridges (5.06 m).

Germany

Missing links: Link between the Mittellandkanal and the Elbe - Havel - Kanal ("Magdeburg Waterway Crossroad") (E 70).  The project is under way.

Basic bottlenecks:

-	Saale (E 20-04) from Halle to Elbe upgrading to class IV is under way.

-	Mittellandkanal (E 70) - sections which have not yet been modernized are being upgraded to class Vb.  The project is under way.

-	Elbe - Havel - Kanal (E 70) - upgrading to class Vb is under way.

-	Untere - Havel - Wasserstraße (E 70) from Plaue to Spree - upgrading to class Vb is under way.

-	Berlin region waterways (various sections) upgrading to class IV and higher classes is under way.

-	Havel - Oder - Wasserstraße (E 70) - upgrading to class Va is under way.

Strategic bottlenecks:

-	Rhine (E 10) - low fairway depth at dry seasons: downstream from Duisburg (2.5 m) and from St. Goar to Mainz (1.9 m).

-	Datteln - Hamm Kanal (E 10-01) to the West of Hamm Harbour - upgrading to class Vb is under way.

-	Rhine - Herne Kanal (E 10-03) - upgrading to class Vb is under way on sections which have not yet been modernized.

-	Dortmund - Ems Kanal (E 13) from 108.3 km to 21.5 km - upgrading to class Vb is under way.

-	Weser (E 14) from 360.7 km to Minden - low fairway depth (2.5 m).

-	Elbe (E 20) from Lauenburg upstream to the border between Germany and the Czech Republic low fairway depth at dry season (1.4 m).

-	Mosel (E 80) - construction of second lock chambers is under way.

-	Main (E 80) upstream from Würzburg - low fairway depth (2.5 m).

-	Danube (E 80) from Straubing to Vilshofen - low fairway depth (1.55 m).

Other bottlenecks, the elimination of which is anticipated to become economically viable only in the framework of a replacement programme supported by a particular investment scheme:

-	Weser (E 14) - upgrading of Minden and Dörverden Locks.

-	Dortmund - Ems Kanal (E 13) to the North of the Mittellandkanal - a number of locks have a width of only 10.00 m.

-	Datteln - Hamm Kanal (E 10-01) - to the East of the Hamm Harbour.

-	Canals branching off from the Mittellandkanal (E 70-02, 70-04 and 70-06) - low fairway depth and height under bridges (2.00 m and 4.00 m, respectively), insufficient dimensions of locks.

-	Oder - Spree Kanal (E 71) - upgrading from class III to class IV is required especially with regard to locks.

Hungary

Missing links: none.

Basic bottlenecks: none.

Strategic bottlenecks:

- Danube (E 80) joint Slovak - Hungarian section from Sap (1,810.0 km) to 1,708.2 km - low maximum draught at dry seasons (1.70 m) and height under bridges: road bridge Medved’ov (1,806.35 km) – 8.85 m; railway bridge Komarno (1,770.4 km) – 8.10-8.15 m; road bridge Komarno (1,767.8 km) – 7.75 m.  Upgrading to 2.50 m and 9.10 m respectively is required.

- Danube (E 80), the section from 1,708.2 km to Budapest (1,652.0 km) - low maximum draught (1.50 - 1.70 m) and height under the railway bridge Ujpest (1,654.5 km) – 7.66m.  Upgrading to 2.50 m and 9.10 m respectively is required.

Lithuania

Missing links: none.

Basic bottlenecks: Nemunas (E 41) from Jurbarkas to Kaunas - upgrading from class III to class Vb is required.

Luxembourg

Missing links: none.

Basic bottlenecks: none.

Strategic bottlenecks: none.

Moldova

Missing links: none.

Basic bottlenecks: Prut (E 80-07) from the mouth to Branest - upgrading to class Va is required.

-	Nistru (E 90-03) from Ukraine/Moldova State border to Bender - upgrading from class III to class Va is required.

Strategic bottlenecks: none.

Netherlands

Missing links: none.

Basic bottlenecks: Zuid-Willemsvaart up to Veghel (E 70-03) - upgrading to class IV.*/

Strategic bottlenecks:

-	Ijssel (E 70) from Arnhem to Zutphen - upgrading to class Va is envisaged.

-	Upgrading of the Zwartsluis at Meppel-Ramspol (E 12-02) is under way.

-	Upgrading of the Lemmer-Delfzijl section (E 15) to class Va enabling at least 3-layer container transport is under way.

-	Twente Canal (E 70) - upgrading to class Va is under way and an increase of the capacity of the Eefde lock to be carried out after 2010.

-	Lekkanaal (E 11-02) - upgrading of the Beatrix lock.**/

-	Maas route (E 01) - upgrading to class Vb enabling 4-layer container transport.***/

-	E 06 waterway - increasing the capacity of the Kreekrak locks. ****/

-	E 03 waterway - increasing the capacity of the Volkerak locks (expected to be carried out after 2010) and Terneuzen locks****/.

Poland

Missing links: Danube - Oder - Elbe Connection (E 30).

Basic bottlenecks:

-	Oder (E 30) from Widuchova to Kozle - upgrading from classes II and III to class Vb is required.

-	Glivice Canal (E 30-01) - upgrading from class III to class Vb is required.

-	Wisla (E 40) from Biala Gora to Wloclawek and from Plock to Warszawa - upgrading from classes I and II to class Vb is required.

-	Zeran Canal (E 40) from Zeran to Zegrze Lake - upgrading from class III to class Vb is required.

-	Bug (E 40) from Zegrze Lake to Brest - upgrading to class Vb is required.

-	Warta - Notec - Bydgoski Canal (E 70) from Kostrzyn to Bydgoszcz - upgrading from class II to class Vb is required.

-	Wisla (E 70) from Bydgoszcz to Biala Gora - upgrading from class II to class Vb is required.

-	Szkarpawa (E 70) from Gdanska Glova to Elblag - upgrading from class III to class Vb is required.

Strategic bottlenecks: Oder (E 30) from Szczecin to Widuchova - upgrading from class IV to class Vb is expected.

Romania

Missing links:

-	Danube - Bucuresti Canal (E 80-05).

-	Olt (E 80-03) up to Slatina.

Basic bottlenecks:

-	Prut (E 80-07) from the mouth to Ungheni.

-	Bega Canal (E 80-01-02) up to Timisoara.

Strategic bottlenecks:

-	Danube (E 80) from 863 to 175 km - low fairway depth at dry seasons (below 2.50 m - value recommended by the Danube Commission) at several critical sections, i.e.:

from 863 to 845.5 km, with fairway depth limited to 2.20-2.30 m for 7-15 days a year;

from 845.5 to 610 km, with fairway depth limited to 2.10-2.20 m for 
10-15 days a year;

from 610 to 375 km, with fairway depth limited to 1.80-2.00 m for 
20-40 days a year;

from 375 to 300 km, with fairway depth limited to 1.60-2.20 m for 
30-70 days a year;

from 300 to 175 km, with fairway depth limited to 1.90-2.10 m for 
15-30 days a year.

-	Danube (E 80) from 170 km to the Black Sea - low fairway depth at dry seasons (below 7.30 m - value recommended by the Danube Commission) at several critical points, i.e. at 73, 57, 47, 41 and 37 nautical miles and at the Sulina bar at the mouth of the Sulina Canal where it meets the Black Sea, where the fairway depth is limited to 6.90-7.00 mfor 10-20 days a year.

Russian Federation

Missing links: none.

Basic bottlenecks: none.

Strategic bottlenecks:

-	Don (E 90) from Kalach to Azov - low water depth (3.40 m) at sill of the Kochetov Lock (162.0 km).*/

-	Volga (E 50) - low water depth at sill of the Gorodetski Lock (850.0 km).**/

Serbia and Montenegro

Missing links: none

Basic bottlenecks: Begej (E 80-01-02) from its mouth to the Serbia and Montenegro/Romanian border - upgrading from class III to class Vb is required.

Strategic bottlenecks:

-	Danube (E 80) from 863 to 845.5 km - low fairway depth at dry seasons (below 2.50 m - value recommended by the Danube Commission) with fairway depth limited to 2.20-2.30 m for 7-15 days a year.

-	Danube (E 80) at Novi Sad (1,254.25 km) - low height under a temporary road/railway bridge (6.82 m).

-	Sava (E 80-12) from its mouth to the State border - upgrading to class Vb is required.

Slovakia

Missing links:

-	Danube - Oder - Elbe Connection (E 20 and E 30).

-	Vah - Oder Link (E 81).

Basic bottlenecks: Vah (E 81) from Sered'/Hlohovec (75.0 km) to Žilina (250.0 km) - insufficient fairway depth.  Canalization of the river and its upgrading from class III to class VIa in conjunction with the construction of new locks, and reconstruction of existing locks, are required.

Strategic bottlenecks:

-	Danube (E 80) from Devin (1,880.26 km) to Bratislava (1,867.0 km) - upgrading from class VIb to class Vic when going downstream.

-	Danube (E 80) from Devin (1,880.26 km) to Děvínská Nová Ves (Morava (E 30), 6.0 km) - upgrading to class Vb.

-	Danube (E 80) - insufficient height under bridges:  at Bratislava (1,868.14 km) - 7.59 m, at locks of the Gabcikovo Hydro Electrical Complex (1,826.55 km and 1,819.3 km) - 8.90 m.  Upgrading is required up to 9.10 m.

-	Danube (E 80) from Sap (1,810.0 km) to the mouth of the Ipel River (1,708.2 km) - insufficient depth at low water level and insufficient height under the bridges.

-	Vah (E 81) from Kralova (63.1 km) to Hlohovec (101.9 km) - construction of Sered-Hlohovec hydraulic complex and reconstruction of canals and locks is required in order to upgrade this section of the river to class VIa.

-	Vah (E 81) from Komarno (0.0 km) to Selice (42.0 km) - low maximum draught (1.6 m).  Navigable conditions will improve after the construction downstream on the Danube of the Gabcikovo-Nagymaros hydraulic works.

Switzerland

Missing links: none.

Basic bottlenecks: none.

Strategic bottlenecks: none

Ukraine

Missing links: none.

Basic bottlenecks:

-	Desna (E 40-01) from the mouth to Chernihiv - upgrading from class III to class IV is required.*/

-	Dnestr (E 90-03) from Belgorod Dnestrovsky to Ukraine/Moldova border - upgrading from class III to class Vb is required.

*       *       *

## COASTAL ROUTES

Coastal routes mentioned in annex I to AGN are intended to ensure the continuity of the E waterways' network throughout Europe and, in principle, do not impose any restrictions on vessels using them. However, in the event that these coastal shipping vessels are supposed to regularly use inland waterways (mixed river-sea navigation) their dimensions should, where possible and economically viable, meet the requirements for self-propelled units suitable for navigation on inland waterways of classes Va and VIb as indicated in annex III of the Agreement.

## EXPLANATIONS OF TABLES 1, 2 AND 3

The three tables reproduced below reflect data on existing and target parameters of inland waterways, locks and ports of international importance as at 1 October 2005.

Table 1:	Navigational Characteristics of Main Inland Waterways of 
International Importance

Data for each section of E waterways are given in two lines: the upper line represents target values to be achieved as a result of envisaged modernization of existing waterway or construction of a new water link, while the lower one shows existing parameters. Maximum admissible length and width of vessels/convoys are separated by a slash.

The draught (d) and the minimum height under bridges (H) indicated in Table 1 are given in relation to the Low Navigable Water Level (LNWL) for the draught and the Highest Navigable Water Level (HNWL) for the height under bridges. The LNWL corresponds to a long-term mean water level reached or exceeded on all but 20 ice-free days per year (approximately between 5% and 6% of the ice-free period). The HNWL corresponds to a level existing for not less than 1% of the navigation period, established on the basis of observations over a substantial number of years (30 to 40 years), excluding periods when there was ice.

The suitability of a particular waterway for combined transport is marked as follows:

A  -	Waterways suitable for combined transport. This means that inland navigation vessels with a width of 11.40 or 11.45 m and a length of approximately 110 m are able to operate on such waterways carrying three or more layers of containers, 50% of containers being empty. Otherwise a permissible length of pushed convoys of 185 m should be possible, in which case they could operate with two layers of containers, 50% of containers being empty;

B  -	Waterways suitable for combined transport but restrictions apply. This is mainly interpreted by Governments as inland waterways allowing the transport of at least two layers of containers, 50% or less of them being empty, sometimes with the use of ballasting;

C  -	Waterways not suitable for combined transport. These are the waterways where the transport of even two layers of containers is impossible.

Table 2: 	Parameters of locks of inland waterways of international importance

The table contains detailed data on some 600 locks, ship lifts and inclined planes situated on E waterways. This also includes data on locks which are under construction or planned.

Table 3: 	Technical characteristics of inland navigation ports of 
international importance

This table provides data on 370 European inland navigation ports of international importance. E ports are classified in the table in accordance with their annual cargo-handling capacity (0.5-3 million tons, 3-10 million tons and more than 10 million tons). The annual cargo-handling capacity should be interpreted as the potential of a particular port with regard to its existing equipment.

*       *       *

| E WATERWAY | SECTION OF E WATERWAY | LENGTH (km) | MAXIMUM DIMENSIONS OF VESSELS AND PUSHED CONVOYS WHICH MAY BE ACCOMMODATED | MINIMUM HEIGHT UNDER BRIDGES**** (m) | CLASS | SUITABILITY FOR COMBINED TRANSPORT** | COMMENTS |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | LENGTH*** (m) | WIDTH*** (m) | DRAUGHT (m) |  |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| E 01 | DUNKERQUE - VALANCIENNES CANAL | 148.0 | .../143.0 | 11.40/11.40 | 3.00 | 6.50 | Va | A |  |
|  | Dunkerque - Bouchain |  | .../143.0 | 11.40/11.40 | 3.00 | 4.54 | Va | ... |  |
|  | ESCAUT | 13.0 | .../143.0 | 11.40/11.40 | 2.50 | 6.50 | Va | A | Canalized |
|  | Bouchain - Condé |  | .../143.0 | 11.40/11.40 | 2.50 | 4.75 | Va | ... |  |
|  | CONDÉ - POMMEROEUL CANAL | 5.9 | 84.7/143.0 | 10.00/11.40 | 3.00 | 6.80 | IV | A |  |
|  | Condé - Hensies |  | 84.7/143.0 | 10.00/11.40 | 3.00 | 6.80 | IV | A |  |
|  | CONDÉ - POMMEROEUL CANAL | 6.1 | 110.0/110.0 | 11.40/11.40 | 3.00 | 7.10 | Va | A | Currently not in |
|  | Hensies - Pommeroeul |  | 110.0/110.0 | 11.40/11.40 | 3.00 | 7.10 | Va | A | service |
|  | NIMY - BLATON - PERONNES CANAL | 16.8 | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.20 | IV | A |  |
|  | Pommeroeul - Nimy |  | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.20 | IV | A |  |
|  | CANAL DU CENTRE | 24.8 | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.25 | IV | A |  |
|  | Nimy - Seneffe |  | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.25 | IV | A |  |
|  | CHARLEROI - BRUXELLES CANAL | 26.2 | 85.0/85.0 | 10.50/10.50 | 2.50 | 6.05 | IV | A |  |
|  | Seneffe - Charleroi |  | 85.0/85.0 | 10.50/10.50 | 2.50 | 6.05 | IV | A |  |
|  | SAMBRE | 48.8 | 85.0/85.0 | 10.50/10.50 | 2.60 | 5.60 | IV | A |  |
|  | Charleroi - Namur |  | 85.0/85.0 | 10.50/10.50 | 2.60 | 5.60 | IV | A |  |
|  | MEUSE | 50.6 | 135.0/135.0 | 12.50/12.50 | 3.00 | 6.60 | Va | A |  |
|  | Namur - Ivoz-Ramet |  | 135.0/135.0 | 12.50/12.50 | 3.00 | 6.60 | Va | A |  |
|  | MEUSE | 16.6 | 196.0/196.0 | 12.50/12.50 | 3.00 | 7.00 | Vb | A |  |
|  | Ivoz-Ramet - Liège |  | 196.0/196.0 | 12.50/12.50 | 3.00 | 7.00 | Vb | A |  |
|  | ALBERTKANAAL | 17.0 | 196.0/196.0 | 23.00/23.00 | 3.40 | 7.50 | VIb | A |  |
|  | Liège - Lanaye |  | 196.0/196.0 | 23.00/23.00 | 3.40 | 7.50 | VIb | A |  |
|  | CANAL DE LANAYE | 1.9 | 196.0/196.0 | 23.00/23.00 | 3.20 | 8.50 | Vib | A |  |
|  | Lanaye |  | 135.0/135.0 | 15.00/15.00 | 3.20 | 8.50 | Va | A |  |
|  | MAAS | 12.3 | 110.0/185.0 | 12.50/12.50 | 3.40 | 6.70 | Va | A |  |
|  | Lanaye - Maastricht |  | 100.0/100.0 | 12.00/12.00 | 3.40 | 6.70 | Va | A |  |
|  | MAAS | 119.6 | 110.0/185.0 | 12.50/12.50 | 3.00 | 7.00 | Vb | A |  |
|  | Maastricht - Heumen |  | 100.0/100.0 | 12.00/12.00 | 3.00 | 7.00 | Va | A |  |
| E 01 | MAAS | 84.9 | 125.0/185.0 | 13.50/13.50 | 3.00 | 7.00 | Vb | A |  |
| (continued) | Heumen - Moerdijk |  | 110.0/113.5 | 13.50/13.50 | 3.00 | 7.00 | Va | A |  |
|  | DORDTSCHE KIL AND NOORD | 22.0 | 125.0/269.5 | 22.80/22.80 | 5.00 | 42.50 5/ | VIc | A | Sea vessels route |
|  | Moerdijk - Rotterdam |  | 125.0/193.0 | 22.80/34.20 4/ |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 5.00 | 42.50 5/ | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 4/ |  |  |  |  |  |
| E 01-02 | MEUSE | 46.4 | 98.0/99.70 | 11.80/11.80 | 2.50 | 5.63 | IV | A |  |
|  | Namur - Givet |  | 98.0/99.70 | 11.80/11.80 | 2.50 | 5.63 | IV | A |  |
| E 01-04 | BASSE MEUSE | 13.8 | 135.0/135.0 | 15.00/15.00 | 2.40 | 7.90 | Va | A |  |
|  | Liège - Visé |  | 135.0/135.0 | 15.00/15.00 | 2.40 | 7.90 | Va | A |  |
| E 01-04-01 | MONSIN CANAL | 0.7 | 135.0/135.0 | 15.00/15.00 | 3.40 | 9.20 | Va | A |  |
|  |  |  | 135.0/135.0 | 15.00/15.00 | 3.40 | 9.20 | Va | A |  |
| E 01-01 | KANAAL DESSEL - KWAADMECHELEN | 15.8 | 110.0/110.0 | 11.50/11.50 | 2.80 | 5.50 | IV | B |  |
|  | Kwaadmeckelen - Kom van Dessel |  | 110.0/110.0 | 11.50/11.50 | 2.80 | 5.20 | IV | C |  |
|  | KANAAL BOCHOLT - HERENTALS | 4.1 | 85.0/85.0 | 9.50/9.50 | 2.80 | 5.50 | IV | B |  |
|  | Kom Dessel - sluis 1 Lommel |  | 55.0/55.0 | 7.30/7.30 | 2.10 | 4.93 | II | C |  |
|  | KANAAL BOCHOLT - HERENTALS | 27.1 | 85.0/85.0 | 9.50/9.50 | 2.80 | 5.50 | IV | B |  |
|  | Sluis 1 Lommel - Bocholt |  | 85.0/85.0 | 8.30/8.30 | 2.50 | 5.50 | II | C |  |
|  | ZUID - WILLEMSVAART | 4.9 | 85.0/85.0 | 9.50/9.50 | 2.80 | 5.50 | IV | B |  |
|  | Bocholt - up to the Belgium/Netherlands border |  | 52.0/52.0 | 6.70/6.70 | 2.10 | 5.15 | II | C |  |
|  | ZUID - WILLEMSVAART | 14.2 | 85.0/85.0 | 9.50/9.50 | 2.50 | 5.30 | IV | B |  |
|  | From the Belgium/Netherlands border to Nederweert |  | 60.0/60.0 | 7.00/7.00 | 2.10 | 5.30 | II | C |  |
|  | WESSEM - NEDERWEERT KANAAL | 16.3 | 85.0/85.0 | 9.50/9.50 | 2.50 | 5.20 | IV | B |  |
|  |  |  | 65.0/65.0 | 7.20/7.20 | 2.10 | 5.20 | II | C |  |
| E 01-06 | KANAAL VAN ST. ANDRIES | 1.9 | 100.0/100.0 | 12.00/12.00 | 3.00 | 11.90 | Va | A |  |
|  |  |  | 100.0/100.0 | 12.00/12.00 | 3.00 | 11.90 | Va | A |  |
| E 01-03 | ZUID - WILLEMSVAART | 5.9 | 90.0/90.0 | 12.00/12.00 | 2.50 | 5.80 | IV | B |  |
|  | Maas - 's Hertogenbosch |  | 90.0/90.0 | 12.00/12.00 | 2.50 | 5.80 | IV | B |  |
| E 02 | BOUDEWIJN CANAL | 12.0 | .../... | .../... | ... | ... | VIb | A | Sea vessels route |
|  | Zeebrugge - Brugge |  | 125.0/125.0 | 12.00/12.00 | 4.75 | ... | VIb | A |  |
|  | GENT - OOSTENDE CANAL | 13.8 | 89.7/89.7 | 10.20/10.20 | 2.50 | 7.50 | IV | B |  |
|  | Brugge - Beernem |  | 89.7/89.7 | 10.20/10.20 | 2.50 | 7.50 | IV | B |  |
| E 02 | GENT - OOSTENDE CANAL | 19.1 | 100.0/100.0 | 10.20/10.20 | 2.50 | 7.00 | IV | B |  |
| (continued) | Beernem - Schipdonk |  | 100.0/100.0 | 10.20/10.20 | 2.50 | 7.00 | IV | C |  |
|  | LYS BYPASS CANAL | 14.9 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.50 | Vb | A |  |
|  | Schipdonk - Deinze |  | 110.0/110.0 | 11.40/11.40 | 2.50 | 7.50 | Va | A |  |
|  | LYS | 15.5 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Deinze - Ooigem |  | 110.0/110.0 | 11.40/11.40 | 2.50 | 5.53 | Va | A |  |
|  | LYS | 6.5 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Ooigem - Harelbeke lock |  | 110.0/110.0 | 11.40/11.40 | 2.50 | 6.49 | Va | C |  |
|  | LYS | 15.8 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Harelbeke lock - Halluin |  | 70.0/70.0 | 7.60/7.60 | 2.30 | 4.42 | II | C |  |
|  | LYS MITOYENNE | 9.1 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Halluin - Wervik |  | 85.0/85.0 | 10.30/10.30 | 2.30 | 4.73 | IV | C |  |
|  | LYS MITOYENNE | 8.7 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Belgian Commune of Comines |  | 85.0/85.0 | 10.30/10.30 | 2.30 | 5.39 | IV | C |  |
|  | DEÛLE AND DEÛLE CANAL | 6.0 | 110.0/110.0 | 11.40/11.40 | 2.50 | 6.50 | Va | A | Upgrading to class Va |
|  | Deûlémont - Quesnoy |  | 70.0/80.0 | 5.05/7.00 | 2.30 | 5.55 | II | ... | is under way |
|  | DEÛLE AND DEÛLE CANAL | 8.7 | 110.0/110.0 | 11.40/11.40 | 2.50 | 6.50 | Va | A | Upgrading to class Va |
|  | Quesnoy/Deûle - Lille (Grand Carré) |  | 70.0/80.0 | 5.05/7.00 | 2.30 | 4.50 | II | ... | is under way |
|  | DEÛLE AND DEÛLE CANAL | 19.2 | .../143.0 | 11.40/11.40 | 3.00 | 6.50 | Va | A |  |
|  | Lille (Grand Carré) - Bauvin |  | .../143.0 | 11.40/11.40 | 3.00 | 5.09 | Va | B |  |
| E 02-02 | GENT - OOSTENDE CANAL | 21.0 | 125.0/185.0 | 12.00/12.00 | 3.35 | 7.00 | Vb | A |  |
|  | Brugge - Oostende |  | 125.0/185.0 | 12.00/12.00 | 2.50 | 5.50 | Vb | B |  |
| E 02-02-01 | PLASSENDALE - NIEUWPOORT CANAL | 21.0 | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  | Plassendale - Gistelbrug |  | 60.0/60.0 | 6.35/6.35 | 2.00 | 5.40 | I | C |  |
|  | PLASSENDALE - NIEUWPOORT CANAL |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  | Gistelbrug - Snaaskerke |  | 60.0/60.0 | 8.05/8.05 | 2.00 | 5.50 | I | C |  |
|  | PLASSENDALE - NIEUWPOORT CANAL |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  | Snaaskerke - Nieuwpoort |  | 60.0/60.0 | 8.05/8.05 | 2.00 | 7.00 | I | C |  |
| E 02-04 | ROESELARE - LEIE CANAL | 16.5 | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  |  |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 6.00 | Va | A |  |
| E 03 | NIEUWE MERWEDE | 22.5 | 110.0/185.0 | 22.80/22.80 | 4.00 | 7.80 | VIb | ... |  |
|  | Gorinchem - Moerdijk |  | 110.0/185.0 | 22.80/22.80 | 4.00 | 7.80 | VIb | ... |  |
| E 03 | SCHELDE - RIJN CONNECTION | 101.7 | 150.0/200.0 | 23.00/23.00 | 4.00 | 9.10 | VIc | A |  |
| (continued) | Moerdijk - Terneuzen |  | 150.0/200.0 | 23.00/23.00 | 4.00 | 9.10 | VIc | A |  |
|  | TERNEUZEN - GENT CANAL | 32.6 | 110.0/193.0 | 22.80/22.80 | 5.50 - 12.50 | 51.00 | VIb | A | Sea vessels route |
|  |  |  | 110.0/193.0 | 22.80/22.80 | 5.50 - 12.50 | 51.00 | VIb | A |  |
|  | GENT CIRCULAR CANAL | 17.1 | 185.0/185.0 | 16.00/16.00 | 3.50 | 9.10 | Vb | A |  |
|  | Gent - Terneuzen - Boven-Schelde Canal |  | 110.0/110.0 | 11.50/11.50 | 3.50 | 7.00 | Va | A |  |
| E 04 | WESTERSCHELDE | 65.0 | 135.0/195.0 | 15.00/22.80 | 4.50 | No restrictions | VIb | A | Sea vessels route |
|  | Vlissingen - Terneuzen - Hansweert - Antwerpen |  | 135.0/195.0 | 15.00/22.80 | 4.50 | No restrictions | VIb | A |  |
|  | BENEDEN - ZEESCHELDE | 30.8 | 135.0/195.0 | 15.00/22.80 | 4.50 | No restrictions | VIb | A | Sea vessels route |
|  | Antwerpen |  | 135.0/195.0 | 15.00/22.80 | 4.50 | No restrictions | VIb | A |  |
|  | BOVEN - ZEESCHELDE | 8.7 | 135.0/195.0 | 15.00/22.80 | 4.50 | 45.00 | VIb | A | Sea vessels route |
|  | Antwerpen - Wintam |  | 135.0/195.0 | 15.00/22.80 | 4.50 | 45.00 | VIb | A |  |
|  | BRUXELLES - SCHELDE CANAL | 3.6 | 220.0/220.0 | 23.00/23.00 | 9.00 | 45.00 | VIb | A |  |
|  | Wintam - Sauvegarde |  | 220.0/220.0 | 23.00/23.00 | 8.50 | 45.00 | VIb | A |  |
|  | BRUXELLES - SCHELDE CANAL | 28.0 | 205.0/205.0 | 22.80/22.80 | 5.80 | 32.00 | VIb | A |  |
|  | Sauvegarde - Bruxelles |  | 205.0/205.0 | 15.00/15.00 | 5.80 | 30.00 | Vb | A |  |
|  | CHARLEROI - BRUXELLES CANAL | 21.6 | 81.6/81.6 | 10.50/10.50 | 3.00 | 5.25 | IV | B | Canal |
|  | Bruxelles - Clabecq |  | 81.6/81.6 | 10.50/10.50 | 2.50 | 4.50 | IV | C |  |
|  | CHARLEROI - BRUXELLES CANAL | 19.7 | 85.0/85.0 | 10.30/10.30 | 2.50 | 4.75 | IV | B | Dredging in progress |
|  | Clabecq - Seneffe |  | 85.0/85.0 | 10.30/10.30 | 2.50 | 4.75 | IV | B |  |
| E 05 | SEINE - ESCAUT LINK | 48.1 | .../180.0 | 11.40/11.40 | 3.00 | 6.50 | Vb | A | New link to be built |
|  | Compiègne - Escaut |  | .../... | .../... | ... | ... | ... | ... |  |
|  | HAUT ESCAUT | ... | 84.7/84.7 | 10.00/10.00 | 2.50 | 5.80 | IV | B |  |
|  | Condé - Bléharies |  | 84.7/84.7 | 10.00/10.00 | 2.50 | 5.80 | IV | B |  |
|  | HAUT ESCAUT | 32.8 | 110.0/110.0 | 10.50/10.50 | 2.60 | 6.18 | Va | B |  |
|  | Bléharies - Herinnes |  | 110.0/110.0 | 10.50/10.50 | 2.60 | 6.18 | Va | B |  |
|  | BOVEN-SCHELDE | 5.6 | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  | Herinnes - Bossuit |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 6.10 | Va | B |  |
|  | BOVEN-SCHELDE | 30.6 | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.00 | Va | A |  |
|  | Bossuit - Asper Lock |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 6.50 | Va | B |  |
|  | BOVEN-SCHELDE | 14.6 | 110.0/110.0 | 11.50/11.50 | 3.00 | 7.00 | Va | A |  |
|  | Asper Lock - Gent Circular Canal |  | 110.0/110.0 | 11.50/11.50 | 3.00 | 7.00 | Va | A |  |
| E 05 | GENT CIRCULAR CANAL | 0.9 | 110.0/110.0 | 11.50/11.50 | 3.00 | 7.00 | Va | A |  |
| (continued) | Boven-Schelde - Merelbeke lock |  | 110.0/110.0 | 11.50/11.50 | 3.00 | 7.00 | Va | A |  |
|  | GENT CIRCULAR CANAL | 3.7 | 110.0/110.0 | 11.40/11.40 | 7/ | 7.00 | Vb | A |  |
|  | Merelbeke lock - Boven-Zeeschelde |  | 110.0/110.0 | 11.40/11.40 | 7/ | 6.70 | Vb | B |  |
|  | BOVEN-ZEESCHELDE | 28.2 | 110.0/110.0 | 11.40/11.40 | 7/ | 7.00 | Va | A |  |
|  | Gent Circular Canal - Dender |  | 85.0/85.0 | 9.50/9.50 | 7/ | 6.77 | IV | B |  |
|  | BOVEN-ZEESCHELDE | 10.9 | 110.0/110.0 | 12.00/12.00 | 7/ | 7.00 | Va | A |  |
|  | Dender - Baasrode |  | 85.0/85.0 | 12.00/12.00 | 7/ | 7.00 | IV | A |  |
|  | BOVEN-ZEESCHELDE | 10.5 | 110.0/110.0 | 12.00/12.00 | 7/ | 7.00 | Va | A |  |
|  | Baasrode - Durme |  | 95.0/95.0 | 12.00/12.00 | 7/ | 7.00 | Va | A |  |
|  | BOVEN-ZEESCHELDE | 26.5 | 135.0/195.0 | 15.00/22.80 | 7/ | 45.00 | VIb | A |  |
|  | Durme - Antwerpen |  | 135.0/195.0 | 15.00/22.80 | 7/ | 45.00 | VIb | A |  |
|  | ALBERTKANAAL | 9.7 | 134.0/200.0 | 12.50/22.80 | 3.40 | 9.10 | VIb | A |  |
|  | Antwerpen - Wijnegem |  | 134.0/200.0 | 12.50/12.50 | 3.40 | 6.70 | Vb | A |  |
|  | ALBERTKANAAL | 90.0 | 134.0/196.0 | 12.50/23.00 | 3.40 | 9.10 | VIb | A |  |
|  | Wijnegem - Lanaken |  | 134.0/196.0 | 12.50/23.00 | 3.40 | 6.90 | VIb | A |  |
|  | ALBERTKANAAL | 1.0 | 134.0/196.0 | 12.50/23.00 | 3.40 | 9.10 | VIb | A |  |
|  | Lanaken |  | 134.0/134.0 | 12.50/12.50 | 3.40 | 7.00 | Va | A |  |
|  | ALBERTKANAAL | 10.0 | 134.0/196.0 | 12.50/23.00 | 3.40 | 9.10 | VIb | A |  |
|  | Lanaken - Kanne |  | 134.0/196.0 | 12.50/23.00 | 3.40 | 6.90 | VIb | A |  |
|  | ALBERTKANAAL | 20.0 | .../190.0 | .../22.80 | 3.40 | 7.50 | VIb | A |  |
|  | Kanne - Liège 4/ |  | .../134.0 | .../12.50 | 3.40 | 7.50 | Vb | A |  |
|  | ALBERTKANAAL | 1.7 | 196.0/196.0 | 23.00/23.00 | 3.40 | 7.50 | VIb | A |  |
|  | Eben-Emael-Lanaye |  | 196.0/196.0 | 23.00/23.00 | 3.40 | 7.50 | VIb | A |  |
| E 05-02 | NIMY - BLATON - PERONNES CANAL | 22.1 | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.20 | IV | B |  |
|  | Peronnes - Pommeroeul |  | 85.0/85.0 | 10.50/10.50 | 2.50 | 5.20 | IV | B |  |
| E 05-01 | BOSSUIT - KORTRIJK CANAL | 12.7 | 110.0/110.0 | 10.00/10.00 | 2.50 | 6.36 | IV | B |  |
|  | Bossuit - Zwevegem |  | 110.0/110.0 | 10.00/10.00 | 2.50 | 4.50 | IV | C |  |
|  | BOSSUIT - KORTRIJK CANAL | 2.5 | 110.0/110.0 | 10.00/10.00 | 2.50 | 6.50 | IV | B |  |
|  | Zwevegem - Kortrijk |  | 38.7/38.7 | 5.15/5.15 | 1.80 | 3.93 | I | C |  |
| E 05-04 | BLATON - ATH CANAL AND DENDER Limit Flemish region - Railway bridge Erembodegem (incl.) | 32.9 | 41.55/41.55 | 5.00/5.00 | 1.90 | 3.95 | I | C |  |
|  |  |  | 41.55/41.55 | 5.00/5.00 | 1.90 | 3.95 | I | C |  |
| E 05-04 | DENDER | 1.3 | 41.55/41.55 | 5.00/5.00 | 1.90 | 3.95 | I | C |  |
| (continued) | Railway bridge Erembodegem - Aalst Lock (incl.) |  | 41.55/41.55 | 5.00/5.00 | 1.90 | 3.95 | I | C |  |
|  | DENDER | 11.0 | 110.0/110.0 | 9.50/9.50 | 2.50 | 7.00 | IV | B |  |
|  | Aalst Lock - calibrated section of Dendermonde |  | 55.0/55.0 | 7.30/7.30 | 2.50 | 5.06 | II | C |  |
|  | DENDER ; Calibrated section of | 2.4 | 110.0/110.0 | 16.00/16.00 | 2.50 | 7.22 | Va | A |  |
|  | Dendermonde - Dendermonde Lock (incl.) |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.22 | Va | A |  |
|  | DENDER | 0.2 | 110.0/110.0 | 16.00/16.00 | 7/ | 7.00 | Va | A |  |
|  | Sluis Dendermonde - Boven-Zeeschelde |  | 110.0/110.0 | 16.00/16.00 | 7/ | 6.45 | Va | B |  |
| E 05-06 | NETEKANAAL | 0.1 | 81.3/81.3 | 10.30/10.30 | 2.50 | 6.95 | IV | B |  |
|  | Albertkanaal - Vierselsluis |  | 81.3/81.3 | 10.30/10.30 | 2.50 | 6.95 | IV | B |  |
|  | NETEKANAAL | 9.4 | 81.3/81.3 | 10.30/10.30 | 2.50 | 7.00 | IV | B |  |
|  | Vierselsluis - Lier |  | 81.3/81.3 | 10.30/10.30 | 2.50 | 5.00 | IV | B |  |
|  | NETEKANAAL | 5.7 | 95.0/95.0 | 11.40/11.40 | 2.50 | 6.95 | Va | A |  |
|  | Lier - Duffelsluis |  | 95.0/95.0 | 10.30/10.30 | 2.50 | 6.95 | IV | A |  |
|  | NETEKANAAL | 0.4 | 95.0/95.0 | 11.40/11.40 | 7/ | 6.95 | Va | A |  |
|  | From Duffelsluis to Beneden - Nete |  | 95.0/95.0 | 10.30/10.30 | 7/ | 6.95 | IV | A |  |
|  | BENEDEN - NETE | 10.2 | 95.0/95.0 | 11.40/11.40 | 7/ | 7.00 | Va | A |  |
|  |  |  | 80.0/80.0 | 9.50/9.50 | 7/ | 4.50 | IV | C |  |
|  | RUPEL | 12.0 | 110.0/110.0 | 11.40/11.40 | 7/ | 35.00 | Va | A |  |
|  |  |  | 95.0/95.0 | 11.40/11.40 | 7/ | 35.00 | Va | A |  |
| E 06 | SCHELDE - RIJN CONNECTION | 37.8 | 150.0/200.0 | 23.00/23.00 | 4.00 | 9.10 | VIc | A |  |
|  | Antwerpen - Moerdijk |  | 150.0/200.0 | 23.00/23.00 | 4.00 | 9.10 | VIc | A |  |
| E 07 | GENT - OOSTENDE CANAL | 6.8 | 185.0/185.0 | 11.50/11.50 | 2.80 | 7.50 | Vb | A |  |
|  | Gent Circular Canal - Lovendegem |  | 110.0/110.0 | 11.50/11.50 | 2.80 | 7.50 | Va | A |  |
|  | GENT - OOSTENDE CANAL | 5.2 | 185.0/185.0 | 11.50/11.50 | 2.50 | 7.50 | Vb | A |  |
|  | Lovendegem - Leie Bypass Canal |  | 110.0/110.0 | 11.50/11.50 | 2.50 | 7.50 | Va | A |  |
|  | LEIE BYPASS CANAL | 13.4 | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | Gent - Oostende Canal - Balgerhoeke |  | 44.1/44.1 | 6.07/6.07 | 2.30 | 4.50 | I | C |  |
|  | LEIE BYPASS CANAL | ... | 185.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A | New link to be built |
|  | Balgerhoeke - Zeebrugge |  | …/… | …/… | … | … | … | … |  |
| E 10 | HARTELKANAAL | 23.7 | 125.0/269.5 | 22.80/22.80 | 4.00 | 4.00 4/ | VIc | A |  |
|  | Rotterdam/Europoort - Hartelmond |  | 125.0/193.0 | 22.80/34.20 |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 4.00 | 4.00 4/ | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 |  |  |  |  |  |
|  | OUDE MAAS | 30.8 | 125.0/269.5 8/ | 22.80/22.80 8/ | 5.00 8/ | 42.50 5/ | VIc | A |  |
|  | 976.2 km - 1007.0 km |  | 125.0/193.0 | 22.80/34.20 |  |  |  |  |  |
|  |  |  | 110.0/269.5 8/ | 22.80/22.80 8/ | 5.00 8/ | 42.50 5/ | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 |  |  |  |  |  |
|  | BENEDEN MERWEDE | 14.9 | 125.0/269.5 | 22.80/22.80 | 3.80 9/ | No restrictions 10/ | VIc | A |  |
|  | 961.3 km - 976.2 km |  | 125.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 3.80 9/ | No restrictions 10/ | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  | BOVEN MERWEDE | 8.8 | 125.0/269.5 | 22.80/22.80 | 4.15 11/ | No restrictions 12/ | VIc | A |  |
|  | 952.5 km - 961.3 km |  | 125.0/193.0 8/ | 22.80/34.20 86/ |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 4.15 11/ | No restrictions 12/ | VIc | A |  |
|  |  |  | 110.0/193.0 8/ | 22.80/34.20 86/ |  |  |  |  |  |
|  | WAAL | 85.1 | 125.0/269.5 | 22.80/22.80 | 2.50 13/ | 9.00 14/ | VIc | A |  |
|  | 867.4 km - 952.5 km |  | 125.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 2.50 13/ | 9.00 14/ | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  | BOVEN - RIJN | 9.7 | 125.0/269.5 | 22.80/22.80 | 3.50 13/ | No restrictions | VIc | A |  |
|  | 857.0 km - 867.4 km |  | 125.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  |  |  | 110.0/269.5 | 22.80/22.80 | 3.50 13/ | No restrictions | VIc | A |  |
|  |  |  | 110.0/193.0 | 22.80/34.20 86/ |  |  |  |  |  |
|  | RHINE | 175.0 | 135.0/193.0 | 22.90/34.35 | 2.50 15/ | 9.10 | VIc | A |  |
|  | Lobith - Köln |  | /269.5 | /22.90 |  |  |  |  |  |
|  |  |  | /193.0 | /34.35 16/ | 2.50 17/ | 9.10 | VIc | A |  |
|  |  |  | 135.0/269.5 | 22.90/22.90 |  |  |  |  |  |
|  | RHINE | 95.0 | 135.0/193.0 | 22.90/34.35 | 2.50 17/ | 9.10 | VIc | A |  |
|  | Köln - Koblenz |  | /269.5 | /22.90 |  |  |  |  |  |
|  |  |  | 135.0/193.0 | /34.35 16/ | 2.50 17/ | 9.10 | VIc | A |  |
|  |  |  | /269.5 | 22.90/22.90 |  |  |  |  |  |
| E 10 | RHINE | 258.0 | 135.0/186.5 | 22.90/22.90 | 2.10 17/ | 9.10 | VIb | A |  |
| (continued) | Koblenz - Iffezheim |  | 135.0/186.5 | 22.90/22.90 | 2.10 18/ | 9.10 | VIb | A |  |
|  | RHINE | 148.0 | 135.0/186.5 | 22.80/22.80 | 3.50 | 7.00 | VIb | A |  |
|  | Iffezheim - Niffer |  | 110.0/183.0 | 22.80/22.80 | 3.50 | 7.00 | VIb | A |  |
|  | RHÔNE - RHINE CANAL | 15.5 | 110.0/190.0 | 11.40/11.40 | 4.00 | 7.00 | Vb | A |  |
|  | Niffer - Mulhouse |  | 110.0/190.0 | 11.40/11.40 | 4.00 | 5.25 | Vb | B |  |
|  | RHÔNE - RHINE CANAL | 221.1 | .../185.0 | 11.40/11.40 | 3.00 | 7.00 | Vb | A | New link to be built |
|  | Mulhouse - Besançon - St. Symphorien |  | 38.7/38.7 | 5.10/5.10 | 1.80 | 3.50 | I | C |  |
|  | SAÔNE | 81.0 | 110.0/185.0 | 11.40/11.40 | 3.00 | 6.00 | Vb | B |  |
|  | St. Symphorien - Chalon/Saône |  | 110.0/110.0 | 11.40/11.40 | 2.20 | 4.80 | Va | B |  |
|  | SAÔNE | 138.0 | 110.0/185.0 | 11.40/11.40 | 3.00 | 4.90 | Vb | B |  |
|  | From Chalon to the confluance with the Rhône |  | 110.0/185.0 | 11.40/11.40 | 3.00 | 4.90 | Vb | B |  |
|  | RHÔNE | 244.0 | .../190.0 | 11.40/11.40 | 3.00 | ... | Vb | A | Canalized |
|  | Lyon (0.00 km) - Avignon (244.0 km) |  | .../190.0 | 11.40/11.40 | 3.00 | 6.30 19/ | Vb | A |  |
|  | RHÔNE | 22.0 | .../190.0 | 11.40 | 3.00 | ... | Vb | A | Canalized |
|  | Avignon (244.0 km) - Tarascon (268.0 km) |  | .../190.0 | 11.40 | 3.00 | 7.40 19/ | Vb | A |  |
|  | RHÔNE | 15.0 | .../190.0 | 11.40 | 3.00 | ... | Vb | A | Canalized |
|  | Tarascon (268.0 km) - Arle (283.0 km) |  | .../190.0 | 11.40 | 3.00 | 7.88 19/ | Vb | A |  |
|  | RHÔNE | 43.0 | .../190.0 | 11.40 | 3.20 | No restrictions | Vb | A |  |
|  | Arle (283.0 km) - Fos 20/ via the Rhône - Fos Canal |  | .../190.0 | 11.40 | 3.20 | No restrictions | Vb | A |  |
|  | RHÔNE ; Arle (283.0 km) | 45.0 | .../135.0 | .../19.00 | 4.25 | No restrictions | Va | A |  |
|  | - Fos 20/ via the Port of Saint-Louis Canal |  | .../135.0 | .../19.00 | 4.25 | No restrictions | Va | A |  |
| E 10-01 | WESEL - DATTELN - KANAL | 60.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  |  |  | 110.0/185.0 | 11.45/11.45 | 2.80 | 4.50 | Vb 21/ | C |  |
|  | DORTMUND - EMS - KANAL | 2.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  |  |  | 110.0/185.0 | 11.45/11.45 | 2.80 | 4.25 | Vb 21/ | C |  |
|  | DATTELN - HAMM - KANAL | 36.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | To the West of Hamm Harbour |  | 86.0/86.0 | 9.60/9.60 | 2.50 | 4.00 | IV 21/22/ | C |  |
|  | DATTELN - HAMM - KANAL | 11.0 | 85.0/85.0 | 9.50/9.50 | 2.50 | 4.00 | IV 21/22/ | C |  |
|  | To the East of Hamm Harbour |  | 82.0/82.0 | 9.50/9.50 | 2.50 | 4.00 | IV 21/22/ | C |  |
| E 10-03 | RHEIN - HERNE - KANAL | 39.8 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | 0.16 km (Duisburg) - 39.97 km |  | 110.0/185.0 | 11.45/11.45 | 2.50 23/ | 4.50 | Vb 21/22/ | C |  |
|  | RHEIN - HERNE - KANAL | 5.6 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  | 39.97 km - Henrichenburg |  | 105.0/160.0 | 9.60/9.50 | 2.50 | 4.50 | IV 21/ | C |  |
| E 10-05 | RUHR | 4.5 | 110.0/185.0 | 12.00/12.00 | 2.80 | 6.50 | Vb | B |  |
|  | 0.01 km - 4.51 km |  | 110.0/185.0 | 12.00/12.00 | 2.80 | 6.50 | Vb | B |  |
|  | RUHR | 7.2 | 110.0/110.0 | 12.00/12.00 | 2.80 | 6.50 | Va | B |  |
|  | 4.51 km - 11.65 km |  | 110.0/110.0 | 12.00/12.00 | 2.80 | 6.50 | Va | B |  |
| E 10-07 | NECKAR | 136.1 | 105.0/105.0 | 11.45/11.45 | 2.60 | 6.00 24/ | Va | B |  |
|  | 0.0 km - 136.1 km |  | 105.0/105.0 | 11.45/11.45 | 2.60 | 6.00 24/ | Va | B |  |
|  | NECKAR | 65.4 | 105.0/105.0 | 11.45/11.45 | 2.60 | 5.50 | Va | B |  |
|  | 136.1 km - 201.5 km |  | 105.0/105.0 | 11.45/11.45 | 2.60 | 5.50 | Va | B |  |
| E 10-09 | RHINE | 9.1 | 110.0/183.0 | 11.40/22.80 | 3.50 25/ | 8.00 | VIb | A |  |
|  | Niffer (Kembs) - Huningue |  | 110.0/183.0 | 11.40/22.80 | 3.50 25/ | 8.00 | VIb | A |  |
|  | RHINE | 3.4 | 110.0/180.0 | 11.40/22.80 | 3.20 | 7.00 | VIb | A |  |
|  | Huningue - Bâle (Mittlere Brücke) |  | 110.0/180.0 | 11.40/22.80 | 3.20 | 7.00 | VIb | A |  |
|  | RHINE | 17.4 | 110.0/110.0 | 11.45/11.45 | 2.60 26/ | 6.20 27/ | Va | A |  |
|  | Bâle (Mittlere Brücke) - Rheinfelden |  | 110.0/110.0 | 11.45/11.45 | 2.60 26/ | 6.20 27/ | Va | A |  |
| E 10-02 | SAÔNE - MOSELLE LINK | 304.0 | .../185.0 | 11.40/11.40 | 3.00 | 7.00 | Vb | A | New link to be built |
|  |  |  | 38.5/38.5 | 5.00/5.00 | 1.80 | 3.50 | I | C |  |
| E 10-04 | PETIT RHÔNE | 21.0 | .../190.0 | 11.40/11.40 | ... | ... | Vb | ... |  |
|  | Fourque - Saint-Gilles |  | .../190.0 | 11.40/11.40 | 2.20 | 5.24 | Vb | B |  |
|  | RHÔNE - SETE CANAL | 70.0 | .../190.0 | 11.40/11.40 | 3.00 | 7.00 | Vb | A | Modernization planned |
|  | Saint-Gilles - Sète |  | .../110.0 | 10.50/10.50 | 2.50 | 4.95 | IV | B |  |
| E 10-06 | RHÔNE AND SAINT - LOUIS CANAL | ... |  |  |  |  | VII | A | Sea vessels route |
|  | Barcarain - Fos |  |  |  |  |  | VII | A |  |
| E 11 | NOORDZEEKANAAL AND AMSTERDAM - RIJNKANAAL IJmuiden - Zeeburg (A'dam) 5.9 km - 31.7 km | 25.8 | 125.0/193.0 28/ | 22.80/22.80 | 4.00 28/ | No restrictions | VIb | A | Noordzeekanaal and Binnen-iJ |
|  |  |  | 110.0/193.0 28/ | 22.80/22.80 | 4.00 28/ | No restrictions | VIb | A |  |
|  | AMSTERTDAM - RIJNKANAAL | 70.8 | 125.0/193.0 | 22.80/22.80 | 4.00 | 9.05 | VIb | A | Amsterdam-Rijnkanaal |
|  | Zeeburg - Tiel (5.9 km 31.7 km) |  | 110.0/193.0 | 22.80/22.80 | 4.00 | 9.05 | VIb | A |  |
| E 11-01 | ZAAN | 20.3 | 110.0/110.0 | 11.50/11.50 | 2.80 | 2.35 4/ | Va | ... |  |
|  | Noordzeekanaal - Noord Hollands Kanaal |  | 110.0/110.0 | 11.50/11.50 | 2.80 | 2.35 4/ | Va | ... |  |
| E 11-02 | LEKKANAAL 48/ | … | .../... | .../... | ... | ... | ... | ... |  |
|  |  |  | .../... | .../... | ... | ... | ... | ... |  |
| E 12 | MAAS - WAAL KANAAL AND WAAL | ... | .../... | .../... | ... | ... | ... | ... |  |
|  |  |  | .../... | .../... | ... | ... | ... | ... |  |
|  | NEDER - RIJN | 11.0 | 110.0/185.0 | 17.00/17.00 | 2.80 | 9.10 | Vb | A |  |
|  | Pannerdensche Kop - IJsselkop |  | 110.0/110.0 | 17.00/17.00 | 2.50 13/ | 9.10 | Va | A |  |
|  | IJSSEL | 118.5 | 110.0/110.0 | 12.00/12.00 | 3.00 | 9.10 | Va | A |  |
|  | IJsselkop - Ketelmeer |  | 110.0/110.0 | 12.00/12.00 | 3.00 | 5.25 | Va | B |  |
|  | IJSSELMEER | 62.5 | 120.0/190.0 | 13.00/23.00 | 3.90 | 12.70 | Vb | A |  |
|  | Ketelmeer - Lorentzsluis |  | 120.0/120.0 | 13.00/13.00 | 3.50 | 12.70 | Vb | A |  |
| E 12-02 | ZWARTE WATER AND MEPPELERDIEP | 22.7 | 110.0/110.0 | 12.00/12.00 | 2.80 | 5.00 4/ | Va | A |  |
|  | Zwolle - Meppel |  | 100.0/100.0 | 12.00/12.00 | 2.70 | 5.00 4/ | Va | A |  |
| E 12-04 | RAMSDIEP | 23.8 | 110.0/110.0 | 11.50/11.50 | 3.00 | 5.00 | Va | A |  |
|  | Ketelmeer - Zwartsluis |  | 110.0/110.0 | 11.50/11.50 | 3.00 | 5.00 | Va | A |  |
| E 13 | EMS | 68.0 |  |  |  |  | Vb | A | Sea vessels route |
|  | North Sea - Papenburg |  |  |  |  |  | Vb | A |  |
|  | DORTMUND - EMS KANAL | 117.5 | 95.0/95.0 | 9.50/9.50 | 2.50 | 4.50 | IV 21/ | C |  |
|  | 225.82 km (Papenburg) - 108.35 km |  | 95.0/95.0 | 9.50/9.50 | 2.50 | 4.25 | IV 21/22/ | C |  |
|  | DORTMUND - EMS KANAL | 86.9 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  | 108.35 km - 21.50 km |  | 86.0/100.0 | 9.50/9.50 | 2.50/2.00 | 4.25 | IV 21/ | C |  |
|  | DORTMUND - EMS KANAL | 20.1 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  | 21.50 km - 1.44 km |  | 110.0/185.0 | 11.45/11.45 | 2.80 | 4.50 | Vb 21/22/ | C |  |
| E 14 | WESER | 84.0 |  |  |  |  | Vib | A | Sea vessels route |
|  | North Sea - Bremen (Eisenbahnbrücke) |  |  |  |  |  | Vib | A |  |
|  | WESER | 7.0 | 220.0/220.0 | 12.00/12.00 | 3.00 | 4.50 | Vb | A |  |
|  | Bremen (Eisenbahnbrücke) - 360.7 km |  | 110.0/172.0 | 11.45/11.45 | 3.00 | 4.50 | Vb 21/22/ | A |  |
|  | WESER | 136.0 | 110.0/110.0 | 11.45/11.45 | 2.50 | 4.50 | Va 21/22/ | C |  |
|  | 360.7 km - Mittellandkanal |  | 85.0/85.0 | 9.50/9.50 | 2.20 | 4.50 | IV 21/29/ | C |  |
| E 15 | IJSSELMEER | 77.5 | 110.0/190.0 | 17.80/17.80 | 3.50 | No restrictions | Vb | A |  |
|  | Oranjesluizen - Prinses Margrietsluis |  | 110.0/190.0 | 17.80/17.80 | 3.50 | No restrictions | Vb | A |  |
|  | PRINSES MARGARIET KANAAL | 65.0 | 110.0/110.0 | 11.40/11.40 | 3.50 | 7.30 4/ | Va | A |  |
|  |  |  | 90.0/90.0 | 10.50/10.50 | 2.60 | 5.45 4/ | IV | B |  |
| E 15 | VAN STARKENBORGH KANAAL | 27.3 | 110.0/110.0 | 11.40/11.40 | 3.50 | 7.00 | Va | A |  |
| (continued) |  |  | 90.0/90.0 | 10.50/10.50 | 2.75 | 6.80 30/ | IV | B |  |
|  | EEMSKANAAL | 19.7 | 144.0/144.0 | 13.00/13.00 | 4.50 | 7.00 4/ | Va | A |  |
|  | Gronongen - Woldbrug |  | 144.0/144.0 | 13.00/13.00 | 4.50 | 7.00 4/ | Va | A |  |
|  | EEMSKANAAL | 7.0 | 144.0/144.0 | 13.00/13.00 | 5.00 | 7.00 4/ | Va | A |  |
|  | Woldbrug - Delfzijl |  | 144.0/144.0 | 13.00/13.00 | 5.00 | 7.00 4/ | Va | A |  |
|  | EMS | 53.0 |  |  |  |  | Vb | A | Sea vessels route |
|  | Eemskanal - Papenburg |  |  |  |  |  | Vb | A |  |
|  | DORTMUND - EMS KANAL | 25.8 | 86.0/86.0 | 9.60/9.60 | 2.50 | 4.50 | IV 21/ | C |  |
|  | 225.8 km (Papenburg) - 200.0 km |  | 86.0/86.0 | 9.60/9.60 | 2.50 | 4.25 | IV 21/22/ | C |  |
|  | KÜSTENKANAL | 69.6 | 86.0/86.0 | 9.60/9.60 | 2.50 | 4.50 | IV 21/22/ | C |  |
|  | 69.6 - 0.0 km |  | 86.0/86.0 | 9.60/9.60 | 2.50 | 4.50 | IV 21/22/ | C |  |
|  | HUNTE | 24.0 |  |  |  |  | Va | A | Sea vessels route |
|  |  |  |  |  |  |  | IV | B |  |
| E 15-01 | VAN HARINXMA CANAL | 37.8 | 85.0/85.0 | 10.00/10.00 | 2.60 | 5.45 4/ | IV | A |  |
|  | Fonejacht - Harlingen |  | 80.0/80.0 | 10.00/10.00 | 2.60 | 5.45 4/ | IV | A |  |
| E 20 | ELBE | 89.0 |  |  |  |  | VIb | A | Sea vessels route |
|  | Lower Elbe |  |  |  |  |  | VIb | A |  |
|  | ELBE | 38.0 | 110.0/190.0 | 11.45/24.00 | 2.70 | 5.50/9.50 31/ | VIb 29/ | A |  |
|  | Hamburg - Lauenburg |  | 110.0/190.0 | 11.40/24.00 | 2.70 | 5.50/9.50 31/ | VIb 29/ | A |  |
|  | ELBE | 113.0 | 110.0/190.0 | 11.45/24.00 | 1.60 32/ | 6.50 | VIb 29/ | B |  |
|  | Lauenburg - Wittenberge |  | 110.0/190.0 | 11.45/24.00 | 1.40 32/ | 5.29/8.49 31/ | VIb 29/ | B |  |
|  | ELBE | 455.0 | 110.0/137.0 | 11.45/11.45 | 1.60 32/ | 6.50 | Va 29/ | B |  |
|  | Wittenberge - German/Czech Rep. State Border |  | 110.0/137.0 | 11.45/11.45 | 1.40 32/ | 4.33/6.93 31/ | Va 29/ | B |  |
|  | ELBE | 40.0 | 110.0/145.0 | 11.40/22.80 | 2.80 | 7.00 | VIa | A | Regularized, |
|  | German/Czech State border - Usti nad Labem |  | 110.0/110.0 | 12.40/12.40 | 0.90 - 2.00 33/ | 6.50 | Va | B | canalization necessary |
|  | ELBE | 69.0 | 110.0/185.0 | 11.40/22.80 | 2.80 | 7.00 | VIb | A | Regularized, |
|  | Usti nad Labem - Mëlník |  | 110.0/135.0 | 10.60/10.60 | 2.00 | 6.50 | IV | B | canalization necessary |
|  | ELBE | 127.0 | 110.0/185.0 | 11.40/11.40 | 2.80 | 7.00 | Vb | A | Regularized, |
|  | Mëlník - Chvaletice - Pardubice |  | 84.0/84.0 | 11.40/11.40 | 2.10 | 3.70 | IV | C | canalization necessary |
|  | ELBE - DANUBE CONNECTION | 325.0 | 110.0/185.0 | 11.40/11.40 | 2.80 | 7.00 | Vb | A | New link to be built |
|  | Pardubice - PÍerov - Bratislava |  | - | - | - | - | - | C |  |
| E 20-02 | ELBE - SEITENKANAL | 115.0 | 100.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | Lauenburg - Mittellandkanal |  | 100.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 34/ | B |  |
| E 20-04 | SAALE | 88.0 | 90.0/100.0 | 9.50/9.50 | 2.00 | 5.25 | IV 22/29/ | B |  |
|  | 0.0 km - 88.0 km |  | 85.0/110.0 | 9.50/9.50 | 1.00 | 4.10 | IV 22/ | C |  |
|  | SAALE 25/ | 36.2 | .../... | .../... | ... | ... | ... | ... |  |
|  | 88.0 km - 124.2 km |  | .../... | .../... | ... | ... | ... | ... |  |
|  | Kreypau - Leipzig 25/ | ... | .../... | .../... | ... | ... | ... | ... |  |
|  |  |  | .../... | .../... | ... | ... | ... | ... |  |
| E 20-06 | VLTAVA | 91.0 | 110.0/110.0 | 11.40/11.40 | 2.50 | 5.25 | Va | B |  |
|  | Mëlník - Praha - Slapy |  | 110.0/110.0 | 10.50/10.50 | 1.20 - 1.80 | 4.50 | IV | B |  |
| E 21 | TRAVE | 21.0 |  |  |  |  | VIb | A | Sea vessels route |
|  |  |  |  |  |  |  | VIb | A |  |
|  | KANALTRAVE, ELBE - LÜBECK KANAL | 68.0 | 80.0/80.0 | 9.50/9.50 | 2.00 | 4.40 | IV 21/29/35/ | C |  |
|  | Lübeck - Lauenburg |  | 80.0/80.0 | 9.50/9.50 | 2.00 | 4.40 | IV 21/29/35/ | C |  |
| E 30 | ODER | 67.0 | 110.0/185.0 | 22.80/22.80 | 4.00 | 11.00 | VIb | A | Sea vessels route |
|  | Swinoujscie - Szczecin |  | 110.0/185.0 | 22.80/22.80 | 4.00 | 11.00 | VIb | A |  |
|  | ODER | 35.9 | ... | ... | ... | ... | Vb | A | Free-flowing |
|  | Szczecin - Widuchova (740.0 km - 704.1 km) |  | 110.0/156.0 | 11.10/11.10 | 2.50 | 5.00 | IV | A |  |
|  | ODER | 86.5 | ... | ... | ... | ... | Vb 37/ | B | When going downstream |
|  | Widuchova - Mouth of the Warta River 36/ |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 4.00 | III/IV | B |  |
|  | 704.1 km - 617.6 km |  | /137.0 | /11.45 | 1.80 |  |  |  |  |
|  |  |  | .../... | .../... | ... | ... | Vb 37/ |  | When going upstream |
|  |  |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 4.00 | III/IV | C |  |
|  |  |  | /137.0 | /11.45 | 1.50 |  |  |  |  |
|  |  |  | /156.0 | /9.50 | 1.50 |  |  |  |  |
|  | ODER | 75.2 | ... | ... | ... | ... | Vb 37/ | B | When going downstream |
|  | Mouth of the Warta River |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 3.50 | II | C |  |
|  | - Mouth of the Nysa Luzycka River 36/ |  | .../... | .../... | ... | ... | Vb 37/ | B | When going upstream |
|  | 617.6 km - 542.4 km |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 3.50 | II | C |  |
|  |  |  | /137.0 | /11.45 | 1.50 |  |  |  |  |
|  |  |  | /156.0 | /9.50 | 1.50 |  |  |  |  |
| E 30 | ODER | 161.7 | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C | When going downstream |
| (continued) | Widuchova - Mouth of the Nysa Luzycka River 38/ |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C |  |
|  | 704.1 km - 542.4 km |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C | When going upstream |
|  |  |  | /156.0 | /9.50 |  |  |  |  |  |
|  |  |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C |  |
|  |  |  | /156.0 | /9.50 |  |  |  |  |  |
|  | ODER, Mouth of the Nysa Luzycka River | 259.8 | .../... | .../... | ... | ... | Vb | B | Free-flowing |
|  | - Brzeg Dolny (542.4 km - 282.6 km) |  | 71.0/118.0 | 9.00/9.00 | 1.20 33/ | 3.15 | I/II | C |  |
|  | ODER | 187.0 | .../... | .../... | ... | ... | IV | C | Canalized |
|  | Brzeg Dolny - Kozle (282.6 km - 95.6 km) |  | 71.0/118.0 | 9.00/9.00 | 1.80 | 3.15 | III | C |  |
|  | ODER - DANUBE CONNECTION | 154.4 | .../185.0 | 11.40/11.40 | 2.80 | 7.00 | Vb | A | New link to be built |
|  | Kozle - PÍerov |  | - | - | - | - | - | C |  |
|  | ODER - DANUBE CONNECTION | 173.0 | .../185.0 | 11.40/11.40 | 2.80 | 7.00 | Vb | A | New link to be built |
|  | PÍerov - Bratislava |  | - | - | - | - | - | C |  |
| E 30-01 | GLIWICE CANAL | ... | .../... | .../... | ... | ... | ... | ... | Canal |
|  |  |  | 70.0/70.0 | 11.40/11.40 | 1.80 | 4.04 | III | C |  |
| E 31 | WESTODER | 14.0 | 110.0/156.0 | 11.45/11.45 | 2.20 | 5.25 | Va 29/ | B |  |
|  |  |  | 82.0/156.0 | 11.45/11.45 | 2.00 | 4.25 | IV 21/29/ | C |  |
|  | HOHENSAATEN - FRIEDRICHSTHALER | 43.0 | 110.0/156.0 | 11.45/9.50 | 2.20 | 5.25 | Va 29/ | B |  |
|  | WASSERSTRAßE |  | 82.0/135.0 | 9.50/8.25 | 2.00 | 4.25 | IV 21/29/ | C |  |
| E 40 | WISLA | 68.0 | .../... | .../... | ... | ... | Vb | B | Free-flowing |
|  | Gdansk - Biala Gora |  | 110.0/185.0 | 11.40/11.40 | 2.50 | 5.20 | Vb | B |  |
|  | WISLA | 114.2 | .../... | .../... | ... | ... | IV | B | Free-flowing |
|  | Biala Gora - Bydgoszcz (886.6 km - 772.4 km) |  | 70.0/113.0 | 11.40/11.40 | 1.40 33/ | 5.00 | II | B |  |
|  | WISLA | 97.6 | .../... | .../... | ... | ... | IV | B | Practically non-navigable free-flowing section |
|  | Bydgoszcz - Wloclawek (772.4 km - 674.8 km) |  | 70.0/113.0 | 11.40/11.40 | 0.80 33/ | 4.90 | - | C |  |
|  | WISLA | 42.0 | .../... | .../... | ... | ... | IV | A | Canalized |
|  | Wloclawek - Plock (674.8 km - 632.8 km) |  | 110.0/113.0 | 11.40/11.40 | 2.50 | 7.00 | IV | A |  |
|  | WISLA | 112.8 | .../... | .../... | ... | ... | IV | A | Practically non-navigable free-flowing section |
|  | Plock - Warszawa (632.8 km - 520.0 km) |  | 60.0/- | 11.40/- | 0.80 33/ | 5.80 | - | B |  |
|  | ZERAN CANAL | 25.0 | .../... | .../... | ... | ... | ... | B |  |
|  | Zeran - Zegrze Lake |  | 80.0/- | 11.40/- | 2.00 | 5.90 | III | B |  |
| E 40 | BUG | 220.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
| (continued) | Zegrze Lake - Brest 40/ |  | - | - | - | - | - | C | Canalization necessary |
|  | MUKHOVETS | 61.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | Brest - Kobrin |  | 100.0/100.0 41/ | 10.20/10.20 | 1.60 | 8.70 | IV 29/ | B |  |
|  | DNEPROVSKO - BUGSKIY KANAL | 92.0 | .../... | .../... | ... | ... | ... | ... |  |
|  | Kobrin - Pererub |  | 100.0/100.0 41/ | 10.20 | 1.60 | No restrictions | IV 29/ | B |  |
|  | PINA | 41.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | Pererub - Pinsk |  | 100.0/100.0 41/ | 10.20/10.20 | 1.60 | No restrictions | IV 29/ | B |  |
|  | PRIPYAT | 50.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | Pinsk - Stakhovo |  | 100.0/100.0 | 10.20/10.20 | 2.10 | No restrictions | IV 29/ | B |  |
|  | PRIPYAT | 455.0 | .../... | .../... | ... | ... | ... | ... |  |
|  | Stakhovo - Mouth of the Pripyat River |  | 100.0/100.0 | 10.20/10.20 | 1.30 | 7.00 | IV 29/ | B |  |
|  | DNIPRO | 83.0 | 150.0/150.0 | 18.00/18.00 | 2.65 | No restrictions | Va | A | Canalized |
|  | Mouth of the Pripyat River - Kyiv |  | 85.2/114.8 | 15.30/15.20 | 2.65 | No restrictions | Va | A |  |
|  | DNIPRO Kyiv - Kanev Hydroelectric | 134.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | No restrictions | Vb | A | Canalized |
|  | Power Plant (GES) (856.0 km - 722.0 km) |  | 114.1/170.0 | 13.23/15.20 | 3.65 | No restrictions | Vb | A |  |
|  | DNIPRO, Kanev GES - Kremenchuk GES | 166.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | 13.20 | Vb | A | Canalized |
|  | 722.0 km - 556.0 km |  | 114.0/170.0 | 13.23/15.20 | 3.65 | 13.20 | Vb | A |  |
|  | DNIPRO Kremenchuk GES - | 123.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | No restrictions | Vb | A | Canalized |
|  | Dniprodzerzhynsk GES (556.0 km - 433.0 km) |  | 138.3/170.0 | 16.70/15.20 | 3.65 | No restrictions | Vb | A |  |
|  | DNIPRO, Dniprodzerzhynsk GES - Dnipro GES | 128.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | 14.70 | Vb | A | Canalized |
|  | 433.0 km - 305.0 km |  | 138.3/170.0 | 16.70/15.20 | 3.65 85/ | 14.70 | Vb | A |  |
|  | DNIPRO | 212.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | No restrictions | Vb | A | Canalized |
|  | Dnipro GES - Kakhovka GES (305.0 km - 93.0 km) |  | 138.3/170.0 | 16.70/15.20 | 3.65 | No restrictions | Vb | A |  |
|  | DNIPRO | 65.0 | 270.0/270.0 | 18.00/18.00 | 3.65 | No restrictions | Vb | A | Free-flowing |
|  | Kakhovka GES - Kherson (93.0 km - 28.0 km) |  | 138.3/170.0 | 16.70/15.20 | 3.65 | No restrictions | Vb | A |  |
| E 40-01 | DESNA 48/ | 198.0 | …/… | …/… | 1.60 | … | IV | … | Free-flowing |
|  | From the mouth to Chernihiv (0.00 km - 198.0 km) |  | …/… | …/… | 1.30 | … | III | … |  |
| E 40-02 | PIVDENNY BUH | ... | 270.0/270.0 | 16.00/18.00 | 4.00 | No restrictions | Vb | A | Sea vessels route |
|  | Up to Mykolaiv |  | 138.3/170.0 | 18.00/18.00 | 4.00 | No restrictions | Vb | A |  |
| E 41 | KURSHSKIY ZALIV AND NEMUNAS | 190.5 | 110.0/110.0 | 12.00/12.00 | 1.60 | 8.98 | IV | A | Free-flowing |
|  | Klaipeda - Jurbarkas |  | 100.0/100.0 | 10.00/10.00 | 1.50 1/ | 8.98 | IV | B |  |
|  | NEMUNAS | 87.8 | 110.0/110.0 | 12.00/12.00 | 1.40 | 9.22 | IV | A | Free-flowing |
|  | Jurbarkas - Kaunas |  | 100.0/100.0 | 8.00/8.00 | 1.20 | 9.22 | IV | B |  |
| E 50 | VOLGO - BALTIJSKIY WATERWAY AND RYBINSK | 933.0 | .../192.0 | 16.80/16.80 | 3.60 | 14.60 | Vb | A | Canalized |
|  | RESERVOIR, St. Petersburg - Rybinsk Lock |  | .../192.0 | 16.80/16.80 | 3.60 | 14.60 | Vb | A |  |
|  | VOLGA | 2697.0 | .../280.0 | .../28.50 | 3.10 | 12.10 | VIc | A |  |
|  | Rybinsk lock - Astrakhan |  | .../280.0 | .../28.50 | 3.10 42/ | 12.10 | VIc | A |  |
| E 50-02 | VOLGA | 256.0 | .../280.0 | .../29.00 | 3.60 | 15.10 | VIc | A | Canalized |
|  | Rybinsk - Dubna |  | .../280.0 | .../29.00 | 3.60 | 15.10 | VIc | A |  |
|  | KANAL IMENI MOSKVI | 126.0 | .../280.0 | .../29.00 | 3.60 | 11.89 | VIc | A | Canalized |
|  | Dubna - Moscow Nothern Port |  | .../280.0 | .../29.00 | 3.60 | 11.89 | VIc | A |  |
|  | KANAL IMENI MOSKVI AND MOSKVA | 42.0 | .../280.0 | .../29.00 | 2.80 | 8.30 43/ | VIc | A | Canalized |
|  | Moscow Northern Port - Moscow Southern Port |  | .../280.0 | .../29.00 | 2.80 | 8.30 43/ | VIc | A |  |
| E 50-02-02 | VOLGA | 115.0 | 135.0/135.0 | .../29.00 | 3.70 | No restrictions | VIa | A | Canalized |
|  | Dubna - Tver |  | 135.0/135.0 | .../29.00 | 3.70 | No restrictions | VIa | A |  |
| E 50-01 | KAMA | 1133.0 | .../230.0 | .../27.90 | 2.90 44/ | 12.20 | VIb | A | Canalized |
|  | Mouth of the Kama River - Solikamsk |  | .../230.0 | .../27.90 | 2.90 44/ | 12.20 | VIb | A |  |
| E 60 | KIEL CANAL | 99.0 |  |  |  |  | VIb | A | Sea vessels route |
|  | Brunsbüttel - Kiel - Holtenau |  |  |  |  |  | VIb | A |  |
|  | VOLGO - BALTIJSKIY WATERWAY | 503.0 | .../192.0 | 16.80/16.80 | 3.60 | 14.60 | Vb | A | Canalized |
|  | St. Petersburg - Vytegra |  | .../192.0 | 16.80/16.80 | 3.60 | 14.60 | Vb | A |  |
|  | ONEGA LAKE | 217.0 | .../250.0 | 23.00/23.00 | 3.70 | No restrictions | VIb | A |  |
|  | Vytegra - Povenets |  | .../250.0 | 23.00/23.00 | 3.70 | No restrictions | VIb | A |  |
|  | BELOMORSKO - BALTIJSKIY CANAL | 222.0 | 126.0/126.0 | 13.20/13.20 | 3.60 | No restrictions | Va | A | Canalized |
|  | Povenets - Belomorsk |  | 126.0/126.0 | 13.20/13.20 | 3.60 | No restrictions | Va | A |  |
| E 60-02 | GUADALQUIVIR | 80.0 | .../220.0 | .../24.36 | 7.00 | 42.00 | VIb | A | Sea vessels route |
|  | From the mouth to Sevilla |  | .../220.0 | .../24.36 | 7.00 | 42.00 | VIb | A |  |
| E 60-04 | DOURO | 210.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | Porto - Spanish border |  | 83.0/83.0 45/ | 11.40/11.40 | 3.80 46/ | 7.00 47/ | IV | A |  |
| E 60-06 | GIRONDE AND GARONNE | 70.0 |  |  |  |  | VII | A | Sea vessels route |
|  | From the mouth to Bec d'Ambes/le Verdon |  |  |  |  |  | VII | A |  |
|  | GIRONDE AND GARONNE | 49.0 | .../... | .../... | 3.50 | ... | ... | ... |  |
|  | Bec d'Ambes/le Verdon - Cadillac |  | 100.0/100.0 | 15.00/15.00 | 3.50 | 6.50 | Va | A |  |
|  | GIRONDE AND GARONNE | 19.0 | .../... | .../... | ... | ... |  | A |  |
|  | From Cadillac to Castets-en-Dorthe |  | 90.0/90.0 | 15.00/15.00 | 2.50 | 7.00 | IV | A |  |
| E 60-08 | LOIRE | 52.0 |  |  |  |  | VII | A | Sea vessels route |
|  | From Saint Nazaire to Nante |  |  |  |  |  | VII | A |  |
| E 60-10 | WADDENZEE | 44.6 | 140.0/140.0 | No restrictions | 6.00 | No restrictions | VIc | A | Sea vessels route |
|  | From Outer Buoy to Harlingen |  | 140.0/140.0 | No restrictions | 6.00 | No restrictions | VIc | A |  |
| E 60-12 | WADDENZEE | 60.0 | 260.0/260.0 | 40.00/40.00 | 10.60 | No restrictions | VIc | A | Sea vessels route |
|  | From Outer Buoy to Delfzijl |  | 260.0/260.0 | 40.00/40.00 | 10.60 | No restrictions | VIc | A |  |
| E 60-01 | MERSEY | 17.0 |  |  | 10.00 |  | VIa | A | Sea vessels route |
|  | Waterway Limit - Eastham Locks |  |  |  | 10.00 |  | VIa | A |  |
|  | MANCHESTER SHIP CANAL | 8.0 | 170.7/170.7 | 21.94/21.94 | 8.78 | No restrictions | VIa | A | Sea vessels route |
|  | Eastham Locks - Ince |  | 170.7/170.7 | 21.94/21.94 | 8.78 | No restrictions | VIa | A |  |
|  | MANCHESTER SHIP CANAL | 10.0 | 161.5/161.5 | 19.35/19.35 | 8.07 | No restrictions | VIa | A | Sea vessels route |
|  | Ince - Runcom |  | 161.5/161.5 | 19.35/19.35 | 8.07 | No restrictions | VIa | A |  |
|  | MANCHESTER SHIP CANAL | 36.0 | 161.5/161.5 | 19.35/19.35 | 7.31 | 21.33 | VIa | A | Sea vessels route |
|  | Runcom - Mode Wheel Locks |  | 161.5/161.5 | 19.35/19.35 | 7.31 | 21.33 | VIa | A |  |
|  | MANCHESTER SHIP CANAL | 2.0 | 161.5/161.5 | 19.35/19.35 | 5.48 | 21.33 | VIa | A | Sea vessels route |
|  | Mode Wheel Locks - Trafford Road Bridge |  | 161.5/161.5 | 19.35/19.35 | 5.48 | 21.33 | VIa | A |  |
| E 60-01-01 | MEDWAY / SWALE 48/ | 10.0 | 102.0/102.0 | 17.00/17.00 | 6.20 | No restrictions | Va | A | Sea vessels route |
|  | Sheerness - Ridham |  | 102.0/102.0 | 17.00/17.00 | 6.20 | No restrictions | Va | A |  |
| E 60-01-03 | MEDWAY 48/ | 11.0 |  |  | 13.00 | No restrictions | VIb | A | Sea vessels route |
|  | Sheerness - Kings North |  |  |  | 13.00 | No restrictions | VIb | A |  |
|  | MEDWAY 87/ | 11.0 | 118.8/118.8 | No restrictions | 8.00 | No restrictions | VIa | A | Sea vessels route |
|  | Kings North - Rochester |  | 118.8/118.8 | No restrictions | 8.00 | No restrictions | VIa | A |  |
| E 60-01-05 | THAMES 48/ | 50.0 |  |  | 13.00 7/ | 54.00 | VIb | A | Sea vessels route |
|  | Canvey Point - Thames Barrier |  |  |  | 13.00 7/ | 54.00 | VIb | A |  |
|  | THAMES | 14.0 | 160.0/160.0 | 30.00/30.00 | 4.20+ 7/ | 42.00 | VIa | A | Sea vessels route |
|  | Thames Barrier - London Bridge |  | 160.0/160.0 | 30.00/30.00 | 4.20+ 7/ | 42.00 | VIa | A |  |
|  | THAMES | 15.0 | 90.0/90.0 | 20.00/20.00 | 1.40+ 7/ | 4.90 88/ | Va | B |  |
|  | London Bridge - Hammersmith Bridge |  | 90.0/90.0 | 20.00/20.00 | 1.40+ 7/ | 4.90 88/ | Va | B |  |
| E 60-01-07 | COLNE 48/ | 12.0 | 96.0/96.0 |  | 4.50 | No restrictions | Va | A | Sea vessels route |
|  | Up to Rowhedge |  | 96.0/96.0 |  | 4.50 | No restrictions | Va | A |  |
| E 60-01-09 | STOUR (SUFFOLK) 48/ | 15.0 | 75.0/75.0 | 18.00/18.00 | 4.00 | No restrictions | IV | A | Sea vessels route |
|  | Up to Mistley |  | 75.0/75.0 | 18.00/18.00 | 4.00 | No restrictions | IV | A |  |
| E 60-01-11 | ORWELL 48/ | 20.0 | 140.0/140.0 |  | 7.40 |  | VIa | A | Sea vessels route |
|  | Up to Ipswich |  | 140.0/140.0 |  | 7.40 |  | VIa | A |  |
| E 60-01-13 | GREAT OUSE | 3.0 | 140.0/140.0 | 20.00/20.00 | 5.52 | No restrictions | VIa | A | Sea vessels route |
|  | The Wash - Kings Lyn |  | 140.0/140.0 | 20.00/20.00 | 5.52 | No restrictions | VIa | A |  |
| E 60-01-15 | NENE 48/ | 23.0 | 120.0/120.0 | 17.00/17.00 | 6.00 | No restrictions | Va | A | Sea vessels route |
|  | The Wash - Bevis Hill (nr Wisbech) |  | 120.0/120.0 | 17.00/17.00 | 6.00 | No restrictions | Va | A |  |
| E 60-01-17 | WELLAND 48/ | 8.0 | 90.0/90.0 |  |  | No restrictions | Va | A | Sea vessels route |
|  | The Wash - Fossdyke Bridge |  | 90.0/90.0 |  |  | No restrictions | Va | A |  |
| E 60-01-19 | WITHAM 48/ | 8.0 | 120.0/120.0 | 13.60/13.60 | 5.30 | No restrictions | Va | A | Sea vessels route |
|  | The Wash - Boston (i.e,the Haven) |  | 120.0/120.0 | 13.60/13.60 | 5.30 | No restrictions | Va | A |  |
| E 60-01-21 | TRENT 48/ | 15.0 |  |  | 5.00 | No restrictions | Va | A | Sea vessels route |
|  | Trent Falls - Keadby Bridge |  |  |  | 5.00 | No restrictions | Va | A |  |
|  | TRENT 87/ | 27.0 |  |  | 3.05 | 5.10 | IV | C | Sea vessels route |
|  | Keadby Bridge - Gainsborough |  |  |  | 3.05 | 5.10 | IV | C |  |
| E 60-03 | HUMBER | 18.0 |  |  |  |  | VIb | A | Sea vessels route |
|  | Up to Hull |  |  |  |  |  | VIb | A |  |
|  | HUMBER | 27.0 |  |  |  | 30.00 | VIb | A | Sea vessels route |
|  | Hull - Trent Falls |  |  |  |  | 30.00 | VIb | A |  |
|  | OUSE (YORKSHIRE) | 2.0 | 88.0/88.0 | 14.00/14.00 | 5.00 | No restrictions | Va | A | Sea vessels route |
|  | Goole - Howdendyke |  | 88.0/88.0 | 14.00/14.00 | 5.00 | No restrictions | Va | A |  |
| E 60-03-02 | TAY 87/ | 12.0 | 240.0/240.0 | 40.00/40.00 | 8.90 | No restrictions | VIb | A | Sea vessels route |
|  | Buddon Ness - Tay Road Bridge |  | 240.0/240.0 | 40.00/40.00 | 8.90 | No restrictions | VIb | A |  |
|  | TAY 87/ | 10.0 | 240.0/240.0 | 40.00/40.00 | 8.90 | 22.00 | VIb | A | Sea vessels route |
|  | Tay Road Bridge - Balmerino |  | 240.0/240.0 | 40.00/40.00 | 8.90 | 22.00 | VIb | A |  |
|  | TAY 87/ | 28.0 | 90.0/90.0 | 13.50/13.50 | 4.90 | 22.00 | Va | A | Sea vessels route |
|  | Belmerino - Perth |  | 90.0/90.0 | 13.50/13.50 | 4.90 | 22.00 | Va | A |  |
| E 60-03-04 | FORTH 48/ | 21.0 | 183.0/183.0 | 26.20/26.20 | 11.00 | No restrictions | VIb | A | Sea vessels route |
|  | Inland Waterway Limit - Gransen Mouth |  | 183.0/183.0 | 26.20/26.20 | 11.00 | No restrictions | VIb | A |  |
| E 60-03-06 | TYNE 48/ | 18.0 |  |  | 11.00 | No restrictions | VIb | A | Sea vessels route |
|  | Mouth - Newcastle |  |  |  | 11.00 | No restrictions | VIb | A |  |
| E 60-03-08 | TEES 48/ | 14.0 |  |  | 10.90 | No restrictions | VIb | A | Sea vessels route |
|  | Mouth - Middlesbrough |  |  |  | 10.90 | No restrictions | VIb | A |  |
| E 60-07 | GÖTA ÄLV | ... | 125.0/125.0 | 16.50/16.50 | 5.40 | ... | Va | A |  |
|  |  |  | 125.0/125.0 | 16.50/16.50 | 5.40 | ... | Va | A |  |
|  | TROLLHÄTTE CANAL | 82.0 | 89.0/89.0 | 13.40/13.40 | 5.40 | … | IV | A |  |
|  |  |  | 89.0/89.0 | 13.40/13.40 | 5.40 | … | IV | A |  |
| E 60-09 | LAKE MÄLAREN | ... | .../... | .../... | ... | ... | ... | ... |  |
|  |  |  | .../... | .../... | ... | ... | ... | ... |  |
|  | SÖDERTÄLJE CANAL 89/ | 6.0 | 124.0/124.0 | 18.00/18.00 | 6.50 | … | Va | A |  |
|  |  |  | 124.0/124.0 | 18.00/18.00 | 6.50 | … | Va | A |  |
| E 60-14 | Stralsund - Peenemünde - Wolgast - Szczecin | ... |  |  |  |  | VIb | A | Sea vessels route |
|  |  |  |  |  |  |  | VIb | A |  |
| E 60-11 | SAIMAA CANAL | 40.0 | 110.0/110.0 | 15.00/15.00 | 4.35 | 24.50 | Va | A | Canalized |
|  | Vyborg - Mälkiä Lock |  | 82.5/82.5 | 12.60/12.60 | 4.35 | 24.50 | IV | A |  |
|  | Mälkiä Lock - Kuopio | 300.0 | 110.0/110.0 | 15.00/15.00 | 4.35 | 24.50 | Va | A |  |
|  |  |  | 110.0/110.0 | 12.60/12.60 | 4.35 | 24.50 | Va | A |  |
|  | Kuopio - Iisalmi | 100.0 | 110.0/110.0 | 12.60/12.60 | 3.60 | 12.00 | Va | A |  |
|  |  |  | 110.0/110.0 | 12.60/12.60 | 2.40 | 12.00 | Va | A |  |
| E 60-11-02 | From E 60 - 11 to Joensuu | 140.0 | 110.0/110.0 | 12.60/12.60 | 4.35 | 24.50 | Va | A | Canalized |
|  |  |  | 110.0/110.0 | 12.60/12.60 | 4.35 | 24.50 | Va | A |  |
|  | Joensuu - Nurmes | 150.0 | 80.0/80.0 | 11.80/11.80 | 2.40 | 10.50 | Va/IV | A | Partly canalized |
|  |  |  | 80.0/80.0 | 11.80/11.80 | 2.40 | 10.50 | Va/IV | A |  |
| E 61 | PEENE | 65.0 | 82.0/156.0 | 9.50/9.50 | 2.20 | 5.00 | IV 21/ | C |  |
|  | From Peenestrom to Demmin |  | 82.0/156.0 | 9.50/9.50 | 2.20 | 5.00 | IV 21/ | C |  |
| E 70 | NIEUWE WATERWEG | 19.7 | 200.0/200.0 | 23.00/23.00 | 12.20 | No restrictions | VIb | A | Sea vessels route |
|  | Europoort - Botlek |  | 200.0/200.0 | 23.00/23.00 | 12.20 | No restrictions | VIb | A |  |
|  | NIEUWE MAAS | 23.8 | 200.0/200.0 | 23.00/23.00 | 6.00 | 11.50 4/ | VIb | A | Sea vessels route |
|  | Botlek - Krimpen |  | 200.0/200.0 | 23.00/23.00 | 6.00 | 11.50 4/ | VIb | A |  |
|  | LEK | 60.7 | 110.0/185.0 | 11.50/22.80 | 3.00 | 9.10 | Vb | A |  |
|  | Krimpen - Wijk bij Duurstede |  | 110.0/185.0 | 11.50/22.80 | 3.00 | 9.10 | Vb | A |  |
|  | NEDER RIJN | 52.7 | 110.0/185.0 | 11.50/17.00 | 3.00 | 9.10 | Vb | A | Canalized |
|  | Wijk bij Duurstede - IJsselkop |  | 110.0/185.0 | 11.50/17.00 | 3.00 | 9.10 | Vb | A |  |
|  | IJSSELI | 43.6 | 110.0/185.0 | 11.50/11.50 | 3.00 | 9.10 | Vb | A |  |
|  | IJsselkop - Zutphen |  | 80.0/80.0 | 9.50/9.50 | 3.00 | 5.25 | Va | B |  |
|  | TWENTEKANAAL | 49.8 | 80.0/80.0 | 9.50/9.50 | 2.50 | 6.00 | Va/IV | A |  |
|  | Zutphen - Enschede |  | 80.0/80.0 | 9.50/9.50 | 2.50 | 6.00 | Va/IV | A |  |
|  | TWENTE - MITTELLANDKANAL 25/ | 55.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | Enschede - Bergeshövede |  | - | - | - | - | - | - |  |
|  | MITTELLANDKANAL | 326.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | (including the Rothenseer - Verbindungskanal) |  | 85.0/85.0 | 9.50/9.50 | 2.50 | 4.00 | IV 21/29/ | C |  |
|  | ELBE - HAVEL KANAL | 56.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  |  |  | 80.0/125.0 | 9.00/8.25 | 2.00 | 4.30 | IV 21/29/50/ | C |  |
|  | UNTERE HAVEL - WASSERSTRAßE | 68.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  | Plaue - Spree |  | 86.0/86.0 | 9.50/9.50 | 1.90 | 3.55 | IV 21/29/ | C |  |
|  | HAVEL - ODER - WASSERSTRAßE | 92.5 | 110.0/110.0 | 11.45/11.45 | 2.20 | 5.25 | Va 29/ | B | Spandau Lock not in |
|  | 0.0 km - 92.5 km |  | /156.0 | /9.00 |  |  |  |  | operation |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 1.65 | 4.25 | IV 21/29/ | C |  |
| E 70-04 | Mittellandkanal branch to Hannover - Linden | 10.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 2.20 | 4.00 | IV 21/29/ | C |  |
| E 70-06 | Mittellandkanal branch to Hildesheim | 15.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 2.20 | 4.00 | IV 21/29/ | C |  |
| E 70-06 | ODER | 49.4 | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C | When going downstream |
| (continued) | Mouth of the Havel - Oder Wasserstraße - Kostrzyn 38/ |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C |  |
|  |  |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C | When going upstream |
|  |  |  | /156.0 | /9.50 |  |  |  |  |  |
|  |  |  | 82.0/125.0 | 11.45/11.45 | 1.20 39/ | 4.20 | IV 21/29/ | C |  |
|  |  |  | /156.0 | /9.50 |  |  |  |  |  |
|  | ODER | 49.4 | .../... | .../... | .../... | .../... | Vb 37/ | B | When going downstream |
|  | Mouth of the Havel - Oder- Wasserstraße - Kostrzyn 36/ |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 4.00 | III | C |  |
|  |  |  | /137.0 | /11.45 | 1.80 |  |  |  |  |
|  |  |  | .../... | .../... | .../... | .../... | Vb 37/ | B | When going upstream |
|  |  |  | 82.0/125.0 | 11.45/11.45 | … 33/ | 4.00 | III | C |  |
|  |  |  | /137.0 | /11.45 | 1.50 |  |  |  |  |
|  |  |  | /156.0 | /9.50 | 1.50 |  |  |  |  |
|  | WARTA - NOTEC - BYDGOSKI CANAL | 294.0 | .../... | .../... | ... | ... | IV | B |  |
|  | Kostrzyn - Bydgoszcz |  | 56.0/- | 9.00/- | 1.60 | 3.57 | II | C |  |
|  | WISLA | 116.2 | .../... | .../... | ... | ... | IV | B | Free-flowing |
|  | Bydgoszcz - Biala Gora (772.4 km - 886.6 km) |  | 70.0/113.0 | 11.40/11.40 | 1.40 33/ | 5.00 | II | B |  |
|  | WISLA | 44.4 | .../... | .../... | ... | ... | Vb | A | Free-flowing |
|  | Biala Gora - Gdanska Glova (886.6 km - 931.0 km) |  | 110.0/185.0 | 11.40/11.40 | 2.50 | 7.00 | Vb | A |  |
|  | SZKARPAWA | 25.4 | .../... | .../... | ... | ... | IV | A |  |
|  | Gdanska Glova - Elblag |  | 56.0/- | 11.40/- | 2.50 | 7.08 | III | B |  |
|  | NOGAT | 62.0 | ... | .../... | ... | ... | ... | ... |  |
|  | Biala Gora - Elblag 51/ |  | 56.0/- | 9.00/- | 2.00 | 5.00 | II | C |  |
|  | ZALEW WISLANY | 96.0 | 110.0/185.0 | 11.40/11.40 | 2.50 | No restrictions | Vb | A |  |
|  | Elblag - Kaliningrad |  | 110.0/185.0 | 11.40/11.40 | 2.50 | No restrictions | Vb | A |  |
|  | Kaliningrad - Klajpeda | ... | .../... | .../... | ... | ... | ... | ... |  |
|  |  |  | .../... | .../... | ... | ... | ... | ... |  |
| E 70-01 | HOLLANDSCHE IJSSEL | 19.7 | 110.0/110.0 | 11.50/11.50 | 3.60 | 8.50 4/ | Va | A |  |
|  | Krimpen - Gouda |  | 110.0/110.0 | 11.50/11.50 | 3.60 | 8.50 4/ | Va | A |  |
| E 70-03 | ZIJKANAAL | 17.6 | 90.0/90.0 | 9.75/9.75 | 2.50 | 6.00 | IV | B |  |
|  | From Twentekanaal to Almelo |  | 90.0/90.0 | 9.75/9.75 | 2.50 | 6.00 | IV | B |  |
| E 70-02 | Mittellandkanal branch to Osnabrück | 13.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | IVa 22/ | B |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 2.00 | 4.00 | IV 21/22/29/ | C |  |
| E 70-04 | Mittellandkanal branch to Hannover - Linden | 10.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | IV | B |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 2.00 | 4.00 | IV 21/29/ | C |  |
| E 70-06 | Mittellandkanal branch to Hildesheim | 15.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 2.00 | 4.00 | IV 21/29/ | C |  |
| E 70-08 | Mittellandkanal branch to Salzgitter | 18.0 | 100.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
|  |  |  | 100.0/185.0 | 11.45/11.45 | 2.50 | 5.25 | Vb | B |  |
| E 70-05 | HAVELKANAL | 35.0 | 110.0/110.0 | 11.45/11.45 | 2.00 | 5.25 | Va 22/29/52/ | B |  |
|  |  |  | 86.0/125.0 | 9.50/8.25 | 1.90 | 4.50 | IV 21/29/ | C |  |
| E 70-10 | SPREE | 9.0 | 110.0/110.0 | 11.45/11.45 | 2.80 | 5.25 | Va/Vb | B |  |
|  | From km 0.0 to Westhafenkanal and Westhafenkanal |  | 110.0/185.0 |  |  |  |  |  |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 1.90 | 4.60 | IV 21/29/ | C |  |
|  | SPREE | 14.0 | 85.0/85.0 | 9.50/9.50 | 2.00 | 4.00 | IV 21/29/ | C |  |
|  | From Westhafen Berlin to Britzer Verbindungskanal |  | 82.0/82.0 | 9.50/9.50 | 2.00 | 3.51 | IV 21/29/ | C |  |
| E 70-12 | BERLIN - SPANDAUER SCHIFFAHRTSKANAL | 8.0 | 110.0/110.0 | 11.45/11.45 | 2.20 | 4.00 | Va 21/29/ | C |  |
|  | From km 0.0 to Westhafen Berlin |  | /156.0 | /9.00 |  |  |  |  |  |
|  |  |  | 67.0/91.0 | 9.00/9.00 | 2.00 | 3.72 | III | C |  |
| E 71 | TELTOWKANAL AND BRITZER | 31.0 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  | VERBINDUNGSKANAL |  | 80.0/91.0 | 9.00/9.00 | 1.75 | 4.40 | IV 21/29/ | C |  |
|  | SPREE - ODER - WASSERSTRAßE | 18.0 | 82.0/156.0 | 9.50/8.25 | 2.00 | 2.97 | IV 21/29/ | C |  |
|  | From the Britzer Verbindungskanal |  | /91.0 | /9.00 |  |  |  |  |  |
|  | to Oder - Spree Kanal |  | 82.0/125.0 | 9.50/8.25 | 2.00 | 2.97 | IV 21/29/ | C |  |
|  |  |  | /91.0 | /9.00 |  |  |  |  |  |
|  | SPREE - ODER - WASSERSTRAßE | 86.0 | 67.0/91.0 | 8.25/8.25 | 2.00 | 4.00 | III | C |  |
|  | From Oder - Spree Kanal to Oder |  | 67.0/91.0 | 8.25/8.25 | 1.85 | 4.00 | III | C |  |
| E 71-02 | POTSDAMER HAVEL | 30.0 | 86.0/86.0 | 9.50/9.50 | 2.00 | 3.80 | IV 21/29/ | C |  |
|  |  |  | 86.0/86.0 | 9.50/9.50 | 1.90 | 3.80 | IV 21/29/ | C |  |
| E 71-04 | TELTOWKANAL - OSTSTRECKE | 7.0 | 82.0/82.0 | 9.50/9.50 | 2.00 | 4.30 | IV 21/29/ | C |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 1.75 | 4.30 | IV 21/29/ | C |  |
| E 71-06 | DAHME - WASSERSTRASSE | 10.0 | 82.0/82.0 | 9.50/9.50 | 2.00 | 3.95 | IV 21/29/ | C |  |
|  | From 0.0 km to 8.65 km and Notte |  | /156.0 | /8.25 |  |  |  |  |  |
|  |  |  | 82.0/82.0 | 9.50/9.50 | 1.90 | 3.95 | IV 21/29/ | C |  |
|  |  |  | /156.0 | /8.25 |  |  |  |  |  |
| E 80 | LE HAVRE - TANCARVILLE CANAL | 19.0 | .../185.0 | 14.00/14.00 | 3.50 | 7.00 53/ | Vb | A |  |
|  |  |  | .../185.0 | 14.00/14.00 | 3.50 | 7.00 53/ | Vb | A |  |
|  | SEINE | 96.1 |  |  |  |  | VII | A | Free-flowing |
|  | Tancarville - Rouen |  |  |  |  |  | VII | A | Sea vessels route |
|  | SEINE | 171.0 | .../180.0 | 11.40/15.00 | 3.50 | ... | Vb | A | Canalized |
|  | Rouen - Conflant |  | .../180.0 | 11.40/15.00 | 3.50 | 5.95 - 11.82 | Vb | A |  |
|  | OISE | 59.0 | .../180.0 | 11.40/11.40 | 3.00 | 6.50 | Vb | A |  |
|  | Conflans - Creil |  | .../180.0 | 11.40/11.40 | 3.00 | 5.25 | Vb | B |  |
|  | OISE | 39.7 | .../180.0 | 11.40/11.40 | 3.00 | 6.50 | Vb | A |  |
|  | Creil - Compiègne |  | .../180.0 | 11.40/11.40 | 2.50 | 5.25 | Vb | B |  |
|  | SEINE - MOSELLE LINK | 250.0 | .../185.0 | 11.40/11.40 | 3.00 | 7.00 | Vb | A | New link to be built |
|  | Compiègne - Reims - Ambly-sur-Meuse - Toul |  | - | - | - | - | - | - |  |
|  | MOSELLE | 128.4 | .../170.0 | 11.40/11.40 | 3.00 | 6.00 | Vb | A |  |
|  | Toul - Apach |  | .../170.0 | 11.40/11.40 | 2.50 | 5.04 | Vb | B |  |
|  | MOSELLE | 242.4 | 110.0/185.0 | 11.45/11.45 | 2.80 | 6.00 | Vb | B |  |
|  | Apach - Koblenz (242.4 km - 0.0 km) |  | 110.0/172.0 | 11.40/11.40 | 2.80 | 6.00 54/ | Vb | B |  |
|  | RHINE | 27.0 | 135.0/193.0 | 22.90/22.90 | 2.10 17/ | 9.10 | VIc | A |  |
|  | Koblenz - Bad Salzig |  | 110.0/193.0 | 22.90/34.35 16/ | 2.10 17/ | 9.10 | VIc | A |  |
|  |  |  | 110.0/269.5 | 22.90/22.90 |  |  |  |  |  |
|  | RHINE | 61.0 | 135.0/186.5 | 22.90/22.90 | 2.10 | 9.10 | VIb | A |  |
|  | Bad Salzig - Mainz |  | 110.0/186.5 | 22.90/22.90 | 2.10 18/ | 9.10 | VIb | A |  |
|  | MAIN | 37.2 | 110.0/190.0 | 14.00/14.00 | 2.90 | 6.00 | Vb | B |  |
|  | 0.0 km - 37.2 km |  | 110.0/190.0 | 14.00/14.00 | 2.70 | 6.00 | Vb | B |  |
|  | MAIN | 46.8 | 110.0/190.0 | 11.45/11.45 | 2.90 | 6.00 56/ | Vb | B |  |
|  | 37.2 km - 84.0 km |  | 110.0/190.0 | 11.45/11.45 | 2.70 | 6.00 56/ | Vb | B |  |
|  | MAIN | 176.0 | 110.0/190.0 | 11.45/11.45 | 2.70 | 6.00 | Vb | B |  |
|  | 84.0 km – 260.0 km |  | 110.0/190.0 | 11.45/11.45 | 2.70 | 6.00 | Vb | B |  |
| E 80 | MAIN | 124.0 | 110.0/190.0 | 11.45/11.45 | 2.70 | 6.00 | Vb 22/ | B |  |
| (continued) | 260.0 km - 384.0 km |  | 110.0 57//110.0 | 11.45/11.45 | 2.30 | 6.00 | Va 22/29/ | B |  |
|  | MAIN - DONAU KANAL | 7.4 | 110.0 57//190.0 | 11.45/11.45 | 2.80 | 6.00 58/ | Vb 22/ | B |  |
|  | 0.0 km - 7.4 km |  | 110.0 57//190.0 | 11.45/11.45 | 2.60 | 6.00 58/ | Vb 22/ | B |  |
|  | MAIN - DONAU KANAL | 163.6 | 110.0 57//190.0 | 11.45/11.45 | 2.80 59/ | 6.00 | Vb 22/ | B |  |
|  | 7.4 km - 171.0 km |  | 110.0 57//190.0 | 11.45/11.45 | 2.70 59/ | 6.00 | Vb 22/ | B |  |
|  | DANUBE | 34.8 | 110.0/185.0 | 11.45/11.45 | 2.70 60/ | 6.00 | Vb 22/ | B |  |
|  | 2411.6 km - 2376.8 km |  | 110.0/185.0 | 11.40/11.40 | 2.70 60/ | 6.00 | Vb 22/ | B |  |
|  | DANUBE | 48.4 | 110.0/185.0 | 11.45/22.90 | 2.70 60/ | 8.00 | VIb 61/ | A |  |
|  | 2376.8 km - 2328.4 km |  | 110.0/185.0 | 11.40/22.80 | 2.70 60/ | 5.75 63/ | VIb 61/ | A |  |
|  | DANUBE | 79.4 | 110.0/185.0 | 11.45/22.90 62/ | 2.70 60/ | 8.00 | VIb 22/61/ | A |  |
|  | 2328.4 km - 2249.0 km |  | 110.0/110.0 | 11.40/22.80 62/ | 2.70 60/ | 4.74 63/64/ | VIa 21/22/29/ | B |  |
|  | DANUBE | 47.2 | 120.0/180.0 | 22.90/22.90 | 2.70 60/ | 8.00 | VIb 21/22/29/ | A |  |
|  | 2249.0 km - 2201.8 km |  | 120.0/185.0 | 22.80/22.80 | 2.70 60/ | 4.61 65/ | VIb 21/22/61/ | B |  |
|  | DANUBE | 163.6 | .../230.0 | 23.00/23.00 | 3.00 66/ | 8.00 | VIb | A |  |
|  | 2201.8 km - 2038.2 km |  | .../230.0 | 23.00/23.00 | 3.00 66/ | 7.42 67/ | VIb | A |  |
|  | DANUBE | 30.2 | .../230.0 | 23.00/23.00 | 3.00 68/ | 8.00 | VIb | A |  |
|  | 2038.2 km - 2008.0 km |  | .../230.0 | 23.00/23.00 | 3.00 69/ | 8.00 | VIb | A |  |
|  | DANUBE | 58.8 | .../230.0 | 23.00/23.00 | 3.00 66/ | 8.00 | VIb | A |  |
|  | 2008.0 km - 1949.2 km |  | .../230.0 | 23.00/23.00 | 3.00 66/ | 7.85 70/ | VIb | A |  |
|  | DANUBE | 28.2 | .../275.0 | 23.00/23.00 | 3.00 66/ | 8.00 | VIc | A |  |
|  | 1949.2 km - 1921.0 km |  | .../275.0 | 23.00/23.00 | 3.00 66/ | 8.00 | VIc | A |  |
|  | DANUBE | 40.7 | .../195.0 | 23.00/23.00 | 3.00 68/ | 10.00 | VIb | A | When going downstream, max. 4 barges/cargo vessels |
|  | 1921.0 km - 1880.3 km |  | .../110.0 | 23.00/35.00 |  |  |  |  |  |
|  |  |  | .../195.0 | 23.00/23.00 | 3.00 69/ | 10.00 | VIb | A |  |
|  |  |  | .../110.0 | 23.00/35.00 |  |  |  |  |  |
|  |  |  | .../275.0 | 23.00/12.00 | 3.00 68/ | 10.00 | VIb | A | When going upstream, max. 4 barges/cargo vessels |
|  |  |  | .../195.0 | 23.00/23.00 |  |  |  |  |  |
|  |  |  | .../275.0 | 23.00/12.00 | 3.00 69/ | 10.00 | VIb | A |  |
|  |  |  | .../195.0 | 23.00/23.00 |  |  |  |  |  |
| E 80 | DANUBE | 18.3 | 110.0/230.0 | 11.40/22.80 | 3.50 | 9.10 | VIc | A | When going downstream |
| (continued) | Devin - Bratislava |  | 110.0/185.0 | 11.40/34.20 | 2.50 | 7.06 71/ | VIb | A |  |
|  | 1880.3 km - 1862.0 km |  | 110.0/230.0 | 11.40/22.80 | 3.50 | 9.10 | VIc | A | When going upstream |
|  |  |  | 110.0/230.0 | 11.40/22.80 | 2.50 | 7.06 71/ | VIc | A |  |
|  | DANUBE DERIVATION CANAL | 51.0 | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going downstream |
|  | Bratislava - Sap |  | 135.0/195.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A |  |
|  | 1862.0 km - 1811.0 km |  | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going upstream |
|  |  |  | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A |  |
|  | DANUBE 55/ | 20.0 | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going downstream |
|  | Sap - Klizska Nema |  | 135.0/140.0 | 16.00/33.40 | 1.70 | 9.10 | VIc | A |  |
|  | 1811.0 km - 1791.0 km |  | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going upstream |
|  |  |  | 135.0/195.0 | 16.00/33.40 | 1.70 | 9.10 | VIc | A |  |
|  | DANUBE | 82.8 | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going downstream |
|  | Klizska Nema - Szob |  | 135.0/275.0 | 16.00/33.40 | 1.70 | 9.10 | VIc | A |  |
|  | 1791.0 km - 1708.2 km |  | 135.0/275.0 | 16.00/33.40 | 3.50 | 9.10 | VIc | A | When going upstream |
|  |  |  | 135.0/275.0 | 16.00/33.40 | 1.70 | 9.10 | VIc | A |  |
|  | DANUBE | 56.2 | .../... | .../... | ... | ... | ... | A |  |
|  | Szob - Budapest (1708.2 km - 1652.0 km) |  | No restrictions | No restrictions | 1.70 | ... | VIb | A |  |
|  | DANUBE | 9.5 | .../... | .../... | ... | ... | ... | A | When going downstream |
|  | 1652.0 km - 1642.5 km |  | .../175.0 | .../50.00 | 2.50 | 7.30 78/ | VIb | A |  |
|  |  |  | .../... | .../... | ... | ... | ... | A | When going upstream |
|  |  |  | .../240.0 | .../35.00 | 2.50 | 7.30 78/ | VIb | A |  |
|  | DANUBE | 109.5 | .../... | .../... | ... | ... | ... | A | Free-flowing |
|  | 1642.5 km - 1433.0 km |  | No restrictions | No restrictions | 1.70 | 8.40 79/ | VIc | A |  |
|  | DANUBE | 67.0 | 110.0/185.0 | 11.40/22.80 | ... | 9.10 | ... | A | Free-flowing |
|  | 1433.0 km - 1366.0 km |  | No restrictions | No restrictions | 2.50 | 8.15 | VIc | A |  |
|  | DANUBE | 70.5 | 110.0/185.0 | 11.40/22.80 | ... | 9.10 | ... | A | Free-flowing |
|  | 1366.0 km - 1295.5 km |  | No restrictions | No restrictions | 2.50 | 9.70 | VIc | A |  |
|  | DANUBE | 80.5 | 110.0/285.0 | 11.40/22.80 | ... | 8.15 | VIc | A | Free-flowing |
|  | 1295.5 km - 1215.0 km |  | 110.0/285.0 | 11.40/22.80 | 2.50 | 6.82 3/ | VIc | B |  |
|  | DANUBE | 40.0 | 110.0/285.0 | 11.40/35.00 | ... | ... | ... | A | Free-flowing |
|  | 1215.0 km - 1175.0 km |  | No restrictions | No restrictions | 2.50 | No restrictions | VIc | A |  |
| E 80 | DANUBE | 100.0 | .../... | .../... | ... | ... | VII | A | Canalized |
| (continued) | 1175.0 km - 1075.0 km |  | No restrictions | No restrictions | 3.50 | 9.15 | VII | A |  |
|  | DANUBE | 128.0 | .../... | .../... | ... | ... | VII | A | Canalized |
|  | 1075.0 km - 947.0 km |  | No restrictions | No restrictions | 3.50 | No restrictions | VII | A |  |
|  | DANUBE | 16.0 | .../... | .../... | ... | ... | VII | A | Canalized |
|  | 947.0 km - 931.0 km |  | .../300.0 | .../33.00 | 4.50 80/ | 10.00 80/ | VII | A |  |
|  | DANUBE | 65.0 | .../... | .../... | ... | ... | VII | A | Canalized |
|  | 931.0 km - 866.0 km |  | No restrictions | No restrictions | 3.50 | No restrictions | VII | A |  |
|  | DANUBE | 6.0 | .../... | .../... | ... | ... | VII | A | Free-flowing from |
|  | 866.0 km - 860.0 km |  | .../300.0 | .../33.00 | 4.50 80/ | 10.00 80/ | VII | A | 863.0 km |
|  |  |  |  |  | 3.50 81/ | 17.70 81/ |  |  |  |
|  | DANUBE | 15.0 | .../... | .../... | ... | ... | VII | A | Free-flowing |
|  | 860.0 km - 845.0 km |  | No restrictions | No restrictions | 2.50 | No restrictions | VII | A |  |
|  | DANUBE | 675.0 | .../... | .../... | ... | ... | VII | A | Free-flowing |
|  | 845.0 km - 170.0 km |  | No restrictions | No restrictions | 2.50 17/ | 9.50 | VII | A |  |
|  | DANUBE | 170.0 | .../... | .../... | ... | ... | VII | A | Free-flowing |
|  | 170.0 km - 0.0 km |  | No restrictions | No restrictions | 7.30 17/ | 38.00 | VII | A |  |
| E 80-02 | SEINE | 26.0 |  |  |  |  | VII | A | Free-flowing |
|  | Tancarville - Estuary |  |  |  |  |  | VII | A | Sea vessels route |
| E 80-04 | SEINE | 62.0 | .../180.0 | 11.40/11.40 | 3.00 - 3.50 | 5.15 82/ | Vb | ... | Canalized |
|  | Conflant - Paris |  | .../180.0 | 11.40/11.40 | 3.00 - 3.50 | 5.15 82/ | Vb | ... |  |
|  | SEINE | 110.0 | .../180.0 | 11.40/11.40 | 2.80 | ... | Vb | ... | Canalized |
|  | Paris - Montereau (178.0 km - 68.0 km) |  | .../180.0 | 11.40/11.40 | 2.80 | 5.50 | Vb | B |  |
|  | SEINE | 22.7 | .../180.0 | 11.40/11.40 | 3.00 | ... | Vb | ... | Canalized |
|  | Montereau - Bray (68.0 km - 46.0 km) |  | .../180.0 | 11.40/11.40 | 2.20 | 5.20 | Vb | B |  |
|  | SEINE | 31.0 | .../... | .../... | ... | ... | III | ... | Upgrading to class III is under way |
|  | Bray - Nogent (46.0 km - 19.0 km) |  | 100.0/100.0 | 6.00/6.00 | 1.80 | 4.20 | I | C |  |
| E 80-06 | SAAR | 73.7 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.75 | Vb | B |  |
|  | Moselle - Völklingen |  | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.75 | Vb | B |  |
|  | SAAR | 17.7 | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb 22/ | B |  |
|  | Völklingen - Saarbrücken |  | 110.0/185.0 | 11.45/11.45 | 2.80 | 5.25 | Vb | B |  |
| E 80-08 | DRAVA | 156.0 | 80.0/85.0 | 9.50/9.50 | 2.50 | ... | IV | ... |  |
|  | 170.0 km - 14.0 km |  | .../... | .../... | ... | ... | ... | ... |  |
|  | DRAVA | 14.0 | 110.0/185.0 | 11.40/11.40 | 2.50 | ... | Vb | A |  |
|  | 14.0 km - 0.0 km |  | 110.0/... | 11.40/11.40 | 1.80 | ... | Va | B |  |
| E 80-10 | DANUBE - SAVA CANAL | 61.0 | 110.0/185.0 | 11.40/11.40 | 2.50 | ... | Vb | ... | New link to be built |
|  | Vucovar - Samac |  | - | - | - | - | - | - |  |
| E 80-01 | TISZA, From the mouth to | 164.0 | .../... | .../... | ... | ... | ... | B | Canalized |
|  | Serbia and Montenegro/Hungarian border |  | 85.0/172.0 | 8.20/11.40 | 2.50 | 77.70 | Va | B |  |
|  | TISZA | 13.0 | .../140.0 | .../22.80 | 2.50 | 6.48 | VIa | ... |  |
|  | 160.0 - 173.0 km |  | .../... | .../... | ... | ... | ... | ... |  |
| E 80-01-02 | BEGEJ | 34.1 | .../... | .../... | ... | ... | ... | B | Canalized |
|  | From the mouth to the Klek Lock |  | 85.0/132.0 | 8.20/11.40 | 2.50 | ... | VIa | B |  |
|  | BEGEJ | 31.5 | .../... | .../... | ... | ... | ... | B | Lock Itebej is out of order |
|  | From the Klek Lock to the Itebej Lock |  | 70.0/... | 8.20/9.00 | 2.00 | ... | III | B |  |
|  | BEGA | ... | .../... | .../... | ... | ... | ... | ... |  |
|  | Up to Timisoara |  | .../... | .../... | ... | ... | ... | ... |  |
| E 80-12 | SAVA, from the mouth to the | 207.0 | 85.0/172.0 | 8.20/22.80 | 2.50 | 5.44 | Vb | ... | Free-flowing |
|  | Serbia and Montenegro/Croatian border |  | 85.0/172.0 | 8.20/11.40 | 2.00 | 5.44 | Vb 29/ | ... |  |
|  | SAVA | 376.0 | 110.0/185.0 | 11.40/11.40 | 2.50 | 9.10 | Vb | A |  |
|  | 583.0 km - 207.0 km |  | 85.0/110.0 | 11.40/11.40 | 2.00 | 7.20 | IV | B |  |
| E 80-03 | OLT | ... | .../... | .../... | ... | ... | ... | ... |  |
|  | Up to Slatina |  | .../... | .../... | ... | ... | ... | ... |  |
| E 80-05 | DANUBE - BUCURESTI CANAL | 73.0 | .../106.6 | .../11.40 | 3.00 | 11.00 | Va | ... | Under construction |
|  |  |  | - | - | - | - | - | - |  |
| E 80-14 | DANUBE - BLACK SEA CANAL | 64.4 | 183.0/296.0 | 16.80/22.80 | ... | 16.50 | VIc | A |  |
|  |  |  | 183.0/296.0 | 16.80/22.80 | 5.50/3.80 | 16.50 | VIc | A |  |
| E 80-14-01 | POARTA ALBA - MIDIA - NAVODARY | 27.5 | 110.0/120.0 | 11.50/11.50 | 3.80 | 12.50 | Va | ... |  |
|  |  |  | 110.0/120.0 | 11.50/11.50 | 3.80 | 12.50 | Va | ... |  |
| E 80-07 | PRUT | 85.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From the mouth to Kakhul |  | 42.0/60.3 | 7.80/7.80 | 1.00 | 9.00 | II | C |  |
|  | PRUT | 322.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From Kakhul to Ungheni |  | 42.0/60.3 | 7.80/7.80 | 1.00 | 8.50 | II | C |  |
| E 80-09 | DANUBE - KILIA ARM 90/ | 98.0 | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A | Free-flowing |
|  | Ismail Cape - Chatal - Vilkovo (116.0 km - 18.0 km) |  | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A |  |
|  | DANUBE - KILIA ARM, Vilkovo - Bistroe Arm Outlet | 7.0 | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A | Free-flowing |
|  | (Old Istanbul Arm) (18.0 km - 11.0 km) |  | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A |  |
|  | DANUBE - KILIA ARM, Bistroe Arm Outlet - | 9.43 | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A | Free-flowing |
|  | Sea approach canal (11.0 km - 1.57 km) |  | 125.0/300.0 | 17.50/40.00 | 5.85 | No restrictions | VII | A |  |
|  | SEA APPROACH CANAL | 3.42 | 125.0/300.0 | 17.50/40.00 | 7.20 | No restrictions | VII | A | Sea vessels route |
|  | 1.57 - (-1.85) km |  | 125.0/300.0 | 17.50/40.00 | 5.85 | No restrictions | VII | A |  |
| E 80-16 | DANUBE - ST. GEORGE ARM | 89.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | 0.0 km - 89.0 km |  | .../... | .../... | 2.50 | ... | Vb | ... |  |
|  | DANUBE - ST. GEORGE ARM | 19.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | 89.0 km - 108.0 km |  | .../... | .../... | 2.50 | ... | VIb | ... |  |
| E 81 | VÁH | 42.1 | 100.0/230.0 | 22.80/22.80 | 2.80 | 7.00 | VIb | A | Modernization |
|  | Komárno - Selice (0.0 km - 42.1 km) |  | 85.0/85.0 | 9.50/9.50 | 1.60 | 7.00 | IV | B | necessary |
|  | VÁH | 21.9 | 110.0/110.0 | 22.80/22.80 | 2.80 | 7.00 | VIa | A | Local navigation only |
|  | Selice - Král'ová (42.1 km - 63.1 km) |  | 110.0/110.0 | 24.00/24.00 | 2.00 | 7.00 | VIa | B |  |
|  | VÁH | 38.8 | 110.0/110.0 | 22.80/22.80 | 2.80 | 7.00 | VIa | A | Partly canalized |
|  | Král'ová - Hlohovec (63.1 km - 101.9 km) |  | 85.0/85.0 | 9.50/9.50 | 2.00 | 5.50 | IV | B | Modernization necessary |
|  | VÁH | 143.1 | 110.0/110.0 | 11.40/11.40 | 2.80 | 7.00 | Va | A | Canalization |
|  | Hlohoven - Žilina (101.9 km - 245.0 km) |  | 70.0/70.0 | 9.00/9.00 | 1.00 | 5.50 | III | B | necessary |
|  | VAH - ODER LINK | 38.2 | 110.0/110.0 | 11.40/11.40 | 2.80 | 5.25 | Va | A | New link to be built |
|  |  |  | - | - | - | - | - | - |  |
| E 90 | KORINTHOS CANAL | ... | .../... | 24.60/24.60 | 6.70 | ... | VIc | ... |  |
|  |  |  | .../... | 24.60/24.60 | 6.70 | ... | VIc | ... |  |
|  | DON AND VOLGO - DONSKOY KANAL | 581.0 | .../141.0 | .../16.20 | 3.20 83/ | 11.00 | Va | A | Canalized upstream from Oust-Donetsk |
|  | Azov - Krasnoarmeysk |  | .../141.0 | .../16.20 | 3.20 83/ | 11.00 | Va | A |  |
|  | VOLGA | 466.0 | .../269.0 | .../28.50 | 3.80 | 13.20 | VIb | A |  |
|  | Krasnoarmeysk - Astrakhan |  | .../269.0 | .../28.50 | 3.80 | 13.20 | VIb | A |  |
| E 90-03 | DNESTR | 39.0 | 65.0/85.0 | 14.00/14.00 | 1.80 | 6.30 | III | B | Free-flowing |
|  | Belgorod Dnestrovskiy - Ukraine/Moldova border |  | .../85.0 | .../14.00 | 1.70 | 6.30 | III | B |  |
|  | NISTRU (DNESTR) | 98.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | Ukraine/Moldova border - Reskeet |  | 85.0/85.0 | 14.00/14.00 | 1.80 | 6.30 | III | B |  |
|  | NISTRU (DNESTR) | 103.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | Reskeet - Bender |  | 85.0/85.0 | 14.00/14.00 | 1.80 | 13.50 | III | B |  |
| E 91 | MILANO - PO CANAL | ... | .../... | .../... | ... | ... | Va | A | New link to be built |
|  |  |  | - | - | - | - | - | - |  |
|  | PO | ... | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From Cremona to Mantova |  | .../... | .../... | 2.33 | 6.60 | Vb/VIa | B |  |
|  | PO | ... | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From Mantova to Volta Grimana |  | .../... | .../... | 2.39 | 5.07 | Va/VIb | C |  |
|  | PO | ... | .../... | .../... | ... | ... | Vb | ... |  |
|  | From Volta Grimana to Adria |  | .../... | .../... | ... | ... | Vb | ... |  |
|  | PO - BRONDOLO CANAL | 35.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | From Adria to Marghera |  | .../... | .../... | 2.50 | 5.00 | Va | C |  |
|  | VENETA LATERAL WATERWAY | 110.0 | .../... | .../... | ... | ... | ... | ... |  |
|  | From Marghera to Monfalcone |  | .../... | .../... | 1.60 | 4.00 | III | C |  |
| E 91-02 | PO | 98.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | Conca di Cremona - Pavia |  | .../... | .../... | 1.60 | 7.00 | IV | A |  |
|  | PO | 85.0 | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | Pavia - Casale Monferrato |  | .../... | .../... | ... | ... | ... | ... |  |
| E 91-04 | FERRARA WATERWAY | 80.0 | .../... | .../... | ... | ... | ... | ... | Canalized |
|  | Ferrarra - Porto Garibaldi |  | .../... | .../... | 2.50 | 4.00 | IV | C |  |
| E 91-06 | PO GRANDE 83/ | ... | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From Volta Grimana to the mouth |  | .../... | .../... | 2.80 | 6.36 | Va/VIb | B |  |
| E 91-01 | FISSERO - TARTARO - CANALBIANCO | 170.0 | .../... | .../... | ... | ... | ... | ... | Under construction |
|  | WATERWAY, Mantova - Volta Grimana |  | .../... | .../... | 2.50 | 6.50 | IV | B |  |
| E 91-08 | PO DI LEVANTE | ... | .../... | .../... | ... | ... | ... | ... | Free-flowing |
|  | From Po - Brondolo Canal to the Adriatic Sea 84/ |  | .../... | .../... | 2.80 | 7.00 | Va | A |  |
| E 91-03 | PADOVA - VENEZIA CANAL | ... | .../... | .../... | ... | ... | ... | ... | Under construction |
|  |  |  | - | - | - | - | - | - |  |

##### Footnotes to Table 1

1/	Fairway depth.

2/	Provisionally restricted to 2.20 m because of silting.

3/	Temporary road/railway bridge at Novy Sad ((1,254 km).

4/	All bridges are movable.

5/	When bridge is not open air draught is 11.50 m for mean high water (MHW) at normal Amsterdam Peil (Dutch reference water level = mean sea tide level) (NAP) + 0.96 m.

6/	Limitation of 1.50 m is only effective on a section of one kilometre (at the old Hermalle-sous-Argentaux dam) and will be eliminated in the nearest future.

7/	Depending on the tide water level prevailing.

8/	Sea-going vessels measuring 175.00 m x 25.00 m x 8.80 m are admitted.

9/	For fixed low water level for rivers (OLW) NAP - 0.20 m.

10/	When bridge is not open air draught is 12.00 m for MHW NAP + 0.96 m.

11/	For OLW NAP + 0.15 m.

12/	For sea-going vessels measuring 256.00 m x 34.00 m x 12.25 m.

13/	For fixed low water level (OLR) at Lobith NAP + 7.95.

14/	For water level at high river discharge at Lobith NAP + 15.58 m (Marke II).  For mean water level at Lobith NAP + 10.10 m.

15/	Fairway depth, below GLW 92 (between Emmerich and Duisburg: 2.80 m below GLW).

16/	When going downstream; reduced to 22.90 m in low water conditions.

17/	Fairway depth, below high water level (GLW) 92.

18/	Fairway depth, below GLW 92 (between St. Goar and Mainz: 1.90 m below GLW).

19/	Bridge at Avignon - 6.30 m, Bridge at Tarascon - 7.40 m, bridge at Arle - 7.88 m.

20/	Fos - Port of Marseille section is not operable because of closure of the Rove tunnel.  Alternative route is via the sea.

21/	The under-bridge headroom requirement for this class cannot be met.

22/	Restrictions apply with regard to two-way traffic.

23/	Single units and convoys of up to 90 m in length and 9.60 m in width, may draw up to 2.80 m.

24/	From 113.0 km to 124.0 km - 5.50 m.

25/	This project is not expected to be realized in the near future.

26/	These figures correspond to a level of 1.75 m on the scale at Rheinfelden.

27/	The Mittlere Brücke has 4.80 m headroom for each arch over a width of 17.00 m at the highest navigable flood level.

28/	No dimension established for inland navigation vessels; sea-going ships measuring 325.0 m x 42.00 m x 13.10 m are admitted.

29/	The depth required for this category cannot be guaranteed (depending on the water level prevailing).

30/	At the fixed water level in channel (KP).

31/	Above mean water level.

32/	Fairway depth, below GLW 89.

33/	Depending on the water level prevailing.

34/	The total length of the Lüneburg Shiplift is 100 m; single units of up to 100 m in length are accepted.

35/	The permissible length-of-convoy requirement for this class cannot be met.

36/	According to the information of the Government of Poland.

37/	Class to be agreed by the Governments of Poland and Germany.

38/	According to the information received from the Government of Germany.

39/	Estimated depth of the channel exceeded during 20 ice-free days a year on average.

40/	Non-navigable waterway. A weir in Kozlowice, downstream of Brest, has no navigational locks and constitutes a main obstacle.

41/	During the locking procedure the pusher is to enter the chamber alongside the barges.

42/	Limitation draught on the section from Gorodetski Lock to Nizhniy Novgorod (length, 56 km).

43/	At a project water level.

44/	On the Sarapul-Chaikovsky section (68 km in length). On other sections the maximum navigable draught is 3.50 m.

45/	Vessels of a greater length may be allowed if their width is approved. The length of pushed convoys of 83.0 m is allowed only up to 126.0 km; from this point up to 210.0 km the length of up to 60.0 m is allowed.

46/	The draught of 3.80 m is ensured on 162 km of the river (from its mouth to 135.0 km and on 27 km between the Pocinho weir and Spanish port Vega Terron). On the rest of the river the draught of 2.00 m is ensured.

47/	This figure is reduced to 6.60 m under the bridge of Ferradosa at 151.0 km.

48/	This waterway is not mentioned in the AGN Agreement.

49/	Vessels with a beam not exceeding 9.00 m may draw up to 2.20 m.

50/	Single units of 86.0 m x 9.50 m and convoys of 147.0 m x 9.00 m may obtain special permission for navigation.

51/	As an alternative to the waterway via the Szkarpawa River.

52/	Improvement of the Untere Havel Wasserstraße is under way to the south of Wustermark.

53/	No restriction when bridges are open.

54/	Under-bridge headroom at the Koblenz rail bridge is reduced to less than 6.00 m on about 50 days per year.

55/	Data concerning target values for this section have been submitted by the Slovak Government. They are expected to be reviewed in the course of joint Hungarian/Slovak consultations.

56/	Except for road bridge Auheim at 59.56 km, where an under-bridge headroom of 4.39 m applies.

57/	Vessels exceeding 90 m in length are subject to additional requirements regarding the carriage of equipment.

58/	Except for Kettenbrücke and Löwenbrücke Bridges at Bamberg, where an under-bridge headroom of 5.41 m applies.

59/	A special permit is required when the draught exceeds 2.50 m.

60/	At the minimum regulated navigable water level (ENR) existing for 96% of the ice-free period, established on the basis of the flows observed over a period of 40 years (fairway depth).

61/	The single-unit permissible length and width requirement for this class cannot be met.

62/	Only vessels with a beam of up to 11.40 m may navigate downstream.

63/	Road bridge at Pfatter.

64/	Railway bridge at Deggendorf.

65/	Luitpolbrücke at Passau.

66/	Maximum draught according to Police Regulations; 2.70 m fairway depth at LNWL.

67/	Road/railway bridge at Linz.

68/	Maximum draught according to Police Regulations; 3.00 m fairway depth at LNWL.

69/	Maximum draught according to Police Regulations; 2.20 m fairway depth at LNWL at several bars.

70/	Road bridge at Stein/Mautern.

71/	Bridge at Bratislava (1868.1 km). At a water level of + 619 cm according to the Bratislava/Devin hydrometric station.

72/	These maximum dimensions of pushed convoys are only allowed if they are capable of reaching a speed of at least 8 km/h on this section of the Danube.

73/	Bridge over the lock at Gabcikovo. Target parameters will be reached after completion of the dredging in the old arm of the Danube downstream of the mouth of the derivation canal and in the derivation canal of the Gabcikovo hydroelectric complex.

74/	1.40 m - according to the Hungarian Government and 1.70 m - according to information received from the Government of Slovakia.

75/	VIa - according to the Hungarian Government and VIc according to the Government of Slovakia which believes that, although at present this section of the river has insufficient depth and width of the channel at low water flow, the navigation conditions will improve after the construction of the lower hydraulic works of the Gabcikovo - Nagymaros complex.

76/	VIb - according to the Hungarian Government and VIc according to information received from the Government of Slovakia which believes that, although at present this section of the river has insufficient depth and width of the channel at low water flow, the navigation conditions will improve after the construction of the lower hydraulic works of the Gabcikovo - Nagymaros complex.

77/	1.50 m - according to the Hungarian Government and 1.70 m - according to information received from the Government of Slovakia.

78/	Bridge at Budapest - Lánchid (1647.0 km).

79/	Bridge at Bajá (1480 km).

80/	Data received from the Government of Serbia and Montenegro. The higher values of draught and air draught of up to 5 m and 13.50 m, respectively, are ensured on request and against payment of costs.

81/	Data received from the Government of Romania.

82/	Minimum height at normal water level varies from 8.54 m to 9.31 m; at the highest navigable water level (HNWL) it varies from 5.15 m to 6.89 m.

83/	On the section from the Kochetovsky hydroelectric complex to Azov (165 km in length). On other sections the maximum navigable draught is 3.50 m.

84/	No direct link Po - Adriatic Sea is possible because of sand banks at the estuary of the Po River.

85/	Periodically, at a low water level, the maximum draught is limited to 3.00 m.

86/	Only permitted when proceeding downstream.

87/	Non-navigable waterway. A weir in Kozlowice, downstream of Brest, has no navigational locks and constitutes a main obstacle.

88/	The lowest height is under the Westminster Bridge.

89/	The maximum dimensions of vessels are applicable in daylight and good visibility.  The Swedish Maritime Administration can grant exceptions from the maximum size up to 130 m x 19 m x 6.80 m.

90/	Footnote by Ukraine: Data concerning this section of the E80-09 waterway are based on the results of the completion of stage one of the Ukrainian project on the reopening of the Danube-Black Sea navigable waterway.  Definitive data related to the project will be presented after the full completion of the project, to be undertaken in accordance with the provisions of applicable international environmental agreements and conventions.

Footnote by Romania: Data concerning this section of the E 80-09 waterway are provisional.  Definitive data related to the Ukrainian project of building a deep-water navigable waterway on the Kilia Arm and Bystroe outlet into the sea of the Danube River are pending the full assessment of the environmental impact and the full and faithful observance of applicable international agreements and conventions.

| E WATERWAY | SECTION OF E WATERWAY | DIMENSION OF LOCKS | COMMENTS |
| --- | --- | --- | --- |
|  |  | LENGTH (m) | WIDTH (m) | DEPTH AT SILLS (m) |  |
| 1 | 2 | 3 | 4 | 5 | 6 |
| E 01 | DUNKERQUE-VALANCIENNES CANAL | 144.6 | 12.00 | 3.50 |  |
|  | Dunkerque - Bouchain | 143.3 | 12.00 | 3.50 | Flandres locks |
|  | 148.0 km - 0.0 km |  |  |  |  |
|  | ESCAUT Bouchain - Condé | 144.6 | 12.00 | 3.00 |  |
|  | CONDÉ - POMMEROEUL CANAL | 149.0 | 12.50 | 4.00 | Hensies lock |
|  | Pommeroeul - Hensies | 151.75 | 12.50 | 4.00 | Pommeroeul lock |
|  | NIMY - BLATON - PÉRONNES CANAL | … | … | … | No structures |
|  | Pommeroeul - Nimy |  |  |  |  |
|  | CANAL DU CENTRE | 96.0 | 12.00 | 4.00 | Obourg lock |
|  | Nimy - Seneffe | 124.0 | 12.50 | 4.00 | Havre lock |
|  |  | 2x112.0 | 2x12.0 | 4.00 | Strépy-Thieu I lift |
|  | CHARLEROI - BRUXELLES CANAL | 85.92 | 11.50 | 4.60 | Viesville lock |
|  | Seneffe - Charleroi | 85.80 | 11.50 | 4.30 | Gosselies lock |
|  |  | 85.10 | 11.50 | 3.10 | Marchienne lock |
|  | SAMBRE | 119.40 | 12.50 | 3.44 | Marcinelle lock |
|  | Charleroi - Namur | 112.00 | 12.50 | 3.50 | Montignies lock |
|  |  | 111.90 | 12.50 | 3.50 | Roselies locks |
|  |  | 136.30 | 12.50 | 3.10 | Auvelais lock |
|  |  | 111.90 | 12.50 | 4.00 | Mornimont lock |
|  |  | 111.90 | 12.50 | 3.55 | Floriffoux lock |
|  |  | 136.90 | 12.50 | 3.25 | Salzinnes lock |
|  | MEUSE | 200.0 | 25.00 | 4.95 | Grand Malades lock |
|  | Namur - Liège | 200.0 | 25.00 | 3.90 | Andenne-Seilles lock |
|  |  | 136.0 | 16.00 | 4.00 | Ampsin-Neuville parallel locks |
|  |  | 135.5 | 14.00 | 3.80 | Ivoz-Ramet parallel locks |
|  | LANAYE CANAL | 136.0 | 16.00 | 4.00 | Lanaye lock |
|  |  | 220.0 | 25.00 | - | Project |
|  | JULIANAKANAAL | 136.0 | 16.00 | 3.60 | Limmel lock complex |
|  |  | 136.0 | 16.00 | 3.60 |  |
|  | JULIANAKANAAL | 142.0 | 16.00 | 4.00 | Born lock complex |
|  |  | 136.0 | 14.00 | 3.60 |  |
|  | JULIANAKANAAL | 142.0 | 16.00 | 7.90 | Drielingsluis lock complex |
|  |  | 142.0 | 16.00 | 7.90 |  |
|  |  | 142.0 | 16.00 | 7.90 |  |
|  | MAAS LATERAL CANAL | 142.0 | 16.00 | 4.00 | Heel lock complex |
|  |  | 142.0 | 16.00 | 4.00 |  |
|  | MAAS | 260.0 | 14.00 | 3.30 | Belfeld lock complex |
|  |  | 142.0 | 16.00 | 6.75 |  |
|  |  | 142.0 | 16.00 | 6.75 |  |
|  | MAAS | 260.0 | 14.00 | 3.30 | Sambeek lock complex |
|  |  | 142.0 | 16.00 | 6.75 |  |
|  |  | 142.0 | 16.00 | 6.75 |  |
| E 01 | MAAS | 270.0 | 16.00 | 3.80 | Heumen lock complex |
| (continued) | MAAS - WAAL CANAL | 260.0 | 16.00 | 4.50 | Weurt lock complex |
|  |  | 260.0 | 16.00 | 6.00 |  |
| E 01-02 | MEUS | 100.0 | 12.00 | 2.79 | La Plante lock |
|  | Namur - Givet | 100.0 | 12.00 | 2.75 | Tailfer lock |
|  |  | 100.0 | 12.00 | 2.75 | Hun lock |
|  |  | 100.0 | 12.00 | 2.75 | Dinant lock |
|  |  | 100.0 | 12.00 | 2.76 | Houx lock |
|  |  | 100.0 | 12.00 | 2.75 | Anseremme lock |
|  |  | 100.0 | 12.00 | 2.75 | Waulsort lock |
|  |  | 100.0 | 12.00 | 2.75 | Hastière lock |
|  | MEUSE | 98.3 | 12.00 | 2.57 | Anseremme lock |
|  | Dinant - Hastière | 98.3 | 12.00 | 2.57 | Waulsort lock |
|  |  | 100.0 | 12.00 | 2.49 | Hastière lock |
|  | Hastière - Givet | ... | ... | ... | One lock |
|  | CANAL DE L'EST |  |  |  |  |
|  | Givet (0.0 km) - Givet (2.95 km) | 95.0 | 12.00 | 2.60 | One lock |
| E 01-04-01 | MONSIN CANAL | 136.0 | 16.00 | 3.10 | Monsin lock |
| E 01-01 | Kwaadmechlen - Belgium/Netherlands border | 52.0 | 7.00 | 2.50 | Bocholt and Lozen locks (Nos. 18 and 17) |
|  |  | 55.0 | 7.50 | 2.50 | Mol and Lommel locks (Nos. 1, 2 and 3) |
|  | ZUID - WILLEMSVAART | 65.0 | 7.50 | 2.85 | Lock No.15 |
|  |  | 70.0 | 7.50 | 2.85 | Lock No.16 |
|  | KANAAL WESSEM - NEDERWEERT | 145.0 | 7.50 | 2.90 | Panheel lock Complex |
|  |  | 150.0 | 12.60 | 3.80 |  |
| E 01-06 | KANAAL VAN ST. ANDRIES | 110.0 | 14.00 | 3.00 | St. Andries lock |
| E 01-03 | ZUID - WILLEMSVAART | 92.0 | 13.00 | 2.70 | Engelen lock |
| E 02 | Zeebrugge - Brugge (12.0 km) | 125.0 | 12.00 | 4.75 | Boudewijn lock |
|  |  | 165.0 | 19.00 | 5.50 | Visart lock |
|  |  | 500.0 | 57.00 | 15.00 | Vandamme lock |
|  | Brugge - Schipdonk | 89.7 | 10.20 | 3.00 | Dammepoort lock |
|  | Schipdonk - Ooigem | 136.0 | 16.00 | 3.50 | Sint-Baafs-Vijve lock |
|  | Ooigem - Harelbeke lock | 115.0 | 12.50 | 3.50 | Harelbeke lock |
|  | Harelbeke lock - Warneton | 195.0 | 12.50 | 3.50 | Menin lock |
|  |  | 185.0 | 12.50 | 4.50 | Comines lock |
|  | Deulémont - Quesnoy | 110.0 | 12.00 | 2.80 | Quesnoy lock |
|  | Quesnoy - Lambersart | 144.6 | 12.00 | 3.50 | Grand Carré lock |
|  | Lambersart - Bauvin | 146.2 | 12.00 | 3.50 | Don lock |
| E 02-02 | GENT - OOSTENDE CANAL | 120.0 | 17.50 | 4.70 | Demey lock |
|  |  | 282.5 | 18.00 | ... | Dok lock |
| E 02-02-01 | PLASSENDALE - NIEUWPOORT | 90.0 | 6.35 | ... | Plassendale lock |
|  |  | 124.0 | 12.50 | ... | Saint. Joris lock |
| E 02-04 | LEIE - ROESELARE CANAL | 115.0 | 12.50 | 3.50 | Ooigem lock |
| E 03 | SCHELDE - RIJN CONNECTION | 290.0 | 24.00 | 6.25 | Volkeraksluizen |
|  |  | 290.0 | 24.00 | 6.25 |  |
|  |  | 290.0 | 24.00 | 6.25 |  |
|  | SCHELDE - RIJN CONNECTION | 280.0 | 24.00 | 5.05 | Krammersluizen |
|  |  | 280.0 | 24.00 | 5.05 |  |
|  | ZUID - BEVELAND CANAL | 285.0 | 24.00 | 7.30 |  |
|  | Hansweert | 285.0 | 24.00 | 7.30 |  |
|  | TERNEUZEN - GENT CANAL | 290.0 | 38.00 | 13.50 | Terneuzen Westsluis Complex |
|  |  | 140.0 | 24.00 | 8.35 | Middensluis |
|  |  | 280.0 | 24.00 | 6.63 | Oostsluis |
|  | GENT CIRCULAR CANAL | 136.0 | 16.00 | 3.80 | Evergem lock |
| E 04 | BRUXELLES - SCHELDE CANAL | 225.0 | 25.00 | 9.50 | New Wintam lock |
|  |  | 205.0 | 24.00 | 6.50 | Zemst lock |
|  | CHARLEROI - BRUXELLES CANAL |  |  |  |  |
|  | Bruxelles - Clabecq | 81.6 | 10.50 | 3.70 | Six locks |
|  | CHARLEROI - BRUXELLES CANAL | 90.0 | 12.00 | 3.48 | Ittre lock |
|  | Clabecq - Seneffe | 2 x 85.5 | 2 x 11.60 | 4.20 | Ronquières inclined plan |
| E 05 | HAUTE ESCAUT | 125.0 | 14.05 | 2.89 | Herinnes lock |
|  | Blénaries - Herinnes | 124.5 | 14.00 | 2.89 | Kain lock |
|  | BOVEN-SCHELDE | 124.5 | 14.05 | 3.50 | Kerkhove lock |
|  | Herinnes - Gent Circular Canal | 125.0 | 14.00 | 3.50 | Oudenaarde lock |
|  |  | 125.0 | 14.00 | 3.50 | Asper lock |
|  | GENT CIRCULAR CANAL | 180.0 | 18.00 | variable | Two Merelbeke locks |
|  | BENEDEN - ZEESCHELDE | 180.0 | 22.00 | variable | Royers lock |
|  | Port of Antwerpen |  |  |  |  |
|  | ALBERTKANAAL |  |  |  | Six lock complexes of: |
|  | Antwerpen - Eben - Emael | 136.0 | 16.00 | 5.00 | Two locks |
|  |  | 200.0 | 24.00 | 5.00 | One lock |
| E 05-02 | NIMY-BLATON-PERONNES CANAL | 86.0 | 12.00 | 3.50 | Peronnes I lock |
|  | Péronnes - Pommeroeul | 86.0 | 12.00 | 3.50 | Peronnes II lock |
| E 05-01 | BOSSUIT - KORTRIJK CANAL | 38.7 | 5.15 | 1.80 | Three locks |
|  |  | 115.0 | 12.50 | 3.50 | Zwevegem lock |
|  |  | 115.0 | 12.50 | 3.50 | Bossuit lock |
|  |  | 115.0 | 12.50 | 3.50 | Moen lock |
| E 05-04 | DENDER | 55.0 | 7.50 | … | Denderbelle lock |
|  | Aalst - Dendermonde | 168.0 | 16.00 | variable | Dendermonde lock |
| E 06 | SCHELDE - RIJN CONNECTION | 320.0 | 24.00 | 5.05 | Kreekraksluizen |
|  |  | 320.0 | 24.00 | 5.05 |  |
| E 10 | HARTELKANAAL | 280.0 | 24.00 | 5.50 | Grote Hartelsluis In operation in case of storm flood, otherwise open connection |
|  | HARTELKANAAL | 306.3 | 24.00 | 6.50 | Rozenburgsesluis |
|  | RHINE, downstream of Strasbourg | 270.0 | 24.00 | 3.30 2/ | Iffezheim and Gambsheim locks |
| E 10 | RHINE | 189.0 | 24.00 | 3.50 | Strasbourg, large lock |
| (continued) | Strasbourg - Niffer | 189.0 | 12.00 | 3.50 | Strasbourg, small lock |
|  |  | 190.0 | 24.00 | 4.25 | Gerstheim, large lock |
|  |  | 190.0 | 12.00 | 4.25 | Gerstheim, small lock |
|  |  | 185.0 | 24.00 | 5.20 | Rhinau, large lock |
|  |  | 185.0 | 12.00 | 5.20 | Rhinau, small lock |
|  |  | 185.0 | 23.00 | 5.30 | Markolsheim, large lock |
|  |  | 185.0 | 12.00 | 5.30 | Markolsheim, small lock |
|  |  | 185.0 | 23.00 | 5.75 | Vogelgrun, large lock |
|  |  | 185.0 | 12.00 | 5.75 | Vogelgrun, small lock |
|  |  | 185.0 | 23.00 | 5.65 | Fessenheim, large lock |
|  |  | 185.0 | 12.00 | 5.65 | Fessenheim, small lock |
|  |  | 185.0 | 23.00 | 5.05 | Ottmarsheim, large lock |
|  |  | 185.0 | 12.00 | 5.85 | Ottmarsheim, small lock |
|  |  | 182.9 | 25.00 | 5.00 | Kembs, western lock 16/ |
|  |  | 190.0 | 25.00 | 5.00 | Kembs, eastern lock 16/ |
|  | RHÔNE - RHINE CANAL | 190.0 | 12.00 | 5.25 | Large chamber, draught 4.0 m |
|  | Niffer - Mulouse | 85.0 | 12.00 | 4.00 | Small chamber, draught 3.0 m |
|  | RHÔNE - RHINE CANAL | 39.20 | 5.20 | 2.20 | Existing locks, draught 1.8 m |
|  | Mulouse - St. Symphorien | 190.0 | 12.00 | 5.70 | 24 new locks to be built |
|  | SAÔNE |  |  |  |  |
|  | St. Symphorien - Lyon | 185.0 | 12.00 | 3.50 |  |
|  | 219.0 km - 0.0 km |  |  |  |  |
|  | RHÔNE AND RHÔNE - FOS CANAL |  |  |  |  |
|  | Lyon - Darse I | 190.0 | 12.00 | 3.00 |  |
|  | Fos - Etand de Berre | 123.0 | 12.00 | 3.00 |  |
| E 10-01 | WESEL - DATTELN KANAL | 222.0 | 12.00 | 4.00 3/ |  |
|  | DATTELN - HAMM KANAL | 82.0 | 9.90 | 3.05 3/ | Hamm lock |
| E 10-03 | RHEIN - HERNE KANAL | 190.0 | 12.00 | 4.00 3/ |  |
| E 10-05 | RUHR | 127.0 | 12.80 | 5.11 4/ | Raffelberg lock |
| E 10-07 | NECKAR, downstream of Plochingen | 106.0 | 11.88 | 3.20 4/ | Besigheim lock |
| E 10-09 | RHINE |  |  |  |  |
|  | Niffer - Huningue | 183.0 | 22.80 | 3.50 |  |
|  | RHINE |  |  |  |  |
|  | Huningue - Birsfelden | 180.0/187.5 | 11.45 | 3.20 |  |
|  | RHINE |  |  |  |  |
|  | Birsfelden - Rheinfelden | 110.0 | 11.45 | 3.20 |  |
| E 10-04 | RHÔNE - SÈTE CONNECTION |  |  |  |  |
|  | Ecluse Sainte-Gilles - Espeyran | 195.0 | 12.00 | 3.60 |  |
| E 10-06 | RHÔNE AND SAINT-LOUIS CANAL |  |  |  |  |
|  | Barcarin - Fos | ... | ... | ... |  |
| E 11 | AMSTERDAM - RIJNKANAAL | - | 50.00 | 5.13 | Keersluis Zeeburg, normally open |
|  |  | 120.0 | 14.00 | 4.20 | Zeeburg lock complex |
|  | AMSTERDAM - RIJNKANAAL | 260.0 | 24.00 | 5.10 | Prinses Irenesluis |
|  |  | 350.0 | 18.00 | 4.20 |  |
| E 11 | AMSTERDAM - RIJNKANAAL | ... | 80.00 | 2.35 | Keersluis, normally open |
| (continued) |  | 260.0 | 18.00 | 2.35 | Prinses Marijkesluis |
|  |  | 260.0 | 18.00 | 2.35 | Two chambers |
|  | AMSTERDAM - RIJNKANAAL | 260.0 | 24.00 | 2.35 | Prins Bernardsluis |
|  |  | 350.0 | 18.00 | 2.35 |  |
| E 11-01 | ZAAN | 116.8 | 12.00 | 3.10 | Wilhelminasluis |
| E 11-02 | LEKKANAAL 17/ | … | … | … | … |
| E 12 | IJSSELMEER | 127.6 | 14.00 | 4.40 | Lorentzsluis Complex |
|  |  | 60.4 | 9.00 | 4.40 |  |
| E 12-02 | MEPPELDIEP | 142.0 | 14.00 | 4.50 | Spooldersluis |
| E 13 | DORTMUND - EMS KANAL | 165.0 | 12.00 | 3.50 4/6/ | Herbrum locks |
|  | To the North of the Mittellandkanal | 163.0 | 9.93 | 3.50 3/ | Gleesen lock |
|  | DORTMUND - EMS KANAL | 223.0 | 12.00 | 3.50 3/ | Münster lock |
|  | To the South of the Mittellandkanal | 190.0 | 12.00 | 4.00 3/ | Henrichenburg lock |
| E 14 | WESER | 350.0 | 12.40 | 4.50 4/5/ | Hemelingen locks |
|  | From estuary to Minden | 85.0 | 12.30 | 3.25 4/ | Dörverden Kleine Schleuse |
|  |  | 85.0 | 10.00 | 4.00 4/ | Minden Schachtschleuse |
|  |  | 214.0 | 12.30 | 3.00 4/ | Other locks |
| E 15 | IJSSELMEER | 200.0 | 24.00 | 4.70 |  |
|  | Oranjesluizen | 67.0 | 14.00 | 4.50 |  |
|  |  | 90.0 | 18.00 | 4.50 |  |
|  |  | 64.0 | 14.00 | 4.50 |  |
|  | IJSSELMEER | 190.0 | 18.04 | 4.50 |  |
|  | Houtribsluizen | 190.0 | 18.04 | 4.50 |  |
|  | PRINSES MARGRIET KANAAL Prinses Margrietsluis | 260.0 | 15.90 | 3.84 |  |
|  | PRINSES MARGRIET KANAAL Terhornstersluis | 260.0 | 16.00 | 4.00 | Gates are kept open |
|  | VAN STARKENBORGH KANAAL |  |  |  |  |
|  | Gaarkeuken | 190.0 | 16.00 | 4.75 |  |
|  | EEMSKANAAL | 184.0 | 11.70 | 3.40 | Oostersluis |
|  | EEMSKANAAL | 123.0 | 7.00 | 3.02 | Zeesluizen Delfzijl |
|  |  | 119.0 | 16.00 | 6.07 |  |
|  | DORTMUND - EMS - KANAL | 165.0 | 12.00 | 3.50 4/5/ | Herbrum locks |
|  | KÜSTENKANAL | 104.0 | 11.90 | 3.00 3/ | Dörpen lock |
|  |  | 102.0 | 12.00 | 3.00 3/5/ | Oldenburg lock |
| E 15-01 | VAN HARINXMA CANAL | 127.5 | 12.00 | 3.75 | Tjerk Hiddes Locks |
|  |  | 40.0 | 7.00 | 2.05 |  |
| E 20 | ELBE |  |  |  |  |
|  | From estuary to Czech border | 220.0 | 25.00 | 4.00 4/ | Geesthacht locks |
|  | ELBE |  |  |  |  |
|  | German border - Usti nad Labem | 200.0 | 24.00 | 4.00 | Construction of two locks is planned |
| E 20 | ELBE | 173.5 | 13.00 | 3.00 | StÍekov parallel locks |
| (continued) | Usti nad Labem - Strekov - Mëlník | 170.0 | 24.00 | 3.00 |  |
|  |  | 155.0 | 22.00 | 3.00 | Lovosice parallel locks |
|  |  | 110.0 | 12.00 | 2.50 |  |
|  |  | 85.0 | 11.00 | 3.00 | České Kopisty parallel locks |
|  |  | 155.0 | 22.00 | 3.00 |  |
|  |  | 155.0 | 22.00 | 3.10 | Roudnice nad Labem parallel locks |
|  |  | 85.0 | 11.00 | 2.70 |  |
|  |  | 155.0 | 22.00 | 3.00 | Štëtí parallel locks |
|  |  | 85.0 | 11.00 | 3.00 |  |
|  |  | 85.0 | 11.00 | 3.00 | Dolní Beřkovice parallel locks 6/ |
|  |  | 200.0 | 22.00 | 3.00 |  |
|  | ELBE | 85.0 | 12.00 | 3.50 | Three locks |
|  | Mëlník - Chvaletice | 85.0 | 12.00 | 3.00 | Twelve locks |
|  | ELBE | 115.0 | 12.00 | 3.50 | Přelouc lock (in project) |
|  | Chvaletice - Pardubice | 85.0 | 12.00 | 3.00 | Přelouc I lock |
|  |  | 85.0 | 12.00 | 3.00 | Srnojedy lock (to be reconstructed) |
| E 20-02 | ELBE - SEITENKANAL | 100.0 | 12.00 | 3.50 3/ | Lüneburg shiplift |
|  |  | 185.0 | 12.00 | 4.00 3/ | Uelzen lock |
| E 20-04 | SAALE (0.0 km - 88.0 km) | 102.5 8/ | 12.00 8/ | 3.31 4/ | Wettin lock |
| E 20-06 | VLTAVA | 73.0 | 11.00 | 2.50 | Hořín parallel locks 7/ |
|  | Mëlník - Praha - Slapy | 137.0 | 20.00 | 2.50 |  |
|  |  | 73.0 | 11.00 | 2.50 | Miřejovice double locks 7/9/ |
|  |  | 133.0 | 20.00 | 2.50 |  |
|  |  | 52.0 | 11.00 | 2.50 | Dolánky double locks 7/9/ |
|  |  | 136.2 | 19.00 | 2.50 |  |
|  |  | 59.0 | 11.00 | 2.50 | Roztoky double locks 7/9/ |
|  |  | 135.0 | 12.00 | 4.00 |  |
|  |  | 73.0 | 11.00 | 2.50 | Podbaba parallel locks 7/ |
|  |  | 137.5 | 20.00 | 2.50 |  |
|  |  | 100.0 | 11.00 | 2.50 | Štvanice parallel locks |
|  |  | 175.0 | 11.00 | 2.50 |  |
|  |  | 175.0 | 11.00 | 2.50 | Smíchov lock |
|  |  | 190.0 | 12.00 | 3.50 | Modřany lock |
|  |  | 134.0 | 12.00 | 3.00 | Vrané nad Vltavou parallel locks |
|  |  | 85.0 | 12.00 | 3.00 |  |
|  |  | 118.4 | 12.00 | 3.00 | Štëchovice lock |
| E 21 | TRAVE, ELBE - LÜBECK KANAL | 80.0 | 12.00 | 2.44 3/ | Büssau lock |
| E 30 | ODER |  |  |  |  |
|  | Brzeg Dolny - Kozle | 187.0 | 9.60 | 2.50 | Twenty-three locks |
| E 30-01 | GLIWICKI CANAL | 72.0 | 12.00 | 3.50 | Six locks |
| E 31 | WESTODER, HOHENSAATEN - FRIEDRICHSTHALER WASSERSTRAßE | 172.0 | 11.92 | 4.07 4/ | Hohensaaten West lock |
| E 40 | WISLA |  |  |  |  |
|  | Gdansk - Bydgoszcz | 192.0 | 12.00 | 3.60 | Przegalina lock |
|  | Bydgoszcz - Warszawa | 115.0 | 12.00 | 3.50 | Wloclavek lock |
|  | ZERAN CANAL | 85.0 | 12.00 | 3.00 | One lock |
|  | MUKHOVETS |  |  |  |  |
|  | Brest - Kobrin | 80.0 | 11.10 10/ | 1.80 | Three locks (Nos. 8 to 10) |
|  | DNEPROVSKO - BUGSKIY KANAL |  |  |  |  |
|  | Kobrin - Pererub | 80.0 | 11.10 10/ | 1.80 | Six locks (Nos. 2 to 7) |
|  | PINA |  |  |  |  |
|  | Pererub - Pinsk | 80.0 | 11.10 10/ | 1.80 | Lock No. 1 at 27.0 km |
|  | PRIPYAT |  |  |  |  |
|  | Pinsk - Stakhovo | 110.0 | 12.00 10/ | 2.20 | Locks Nos. 11 and 12 |
|  | DNIPRO | 150.0 | 18.00 | 4.00 | Kyiv lock |
|  | Mouth of the Pripyat River - Kherson | 270.0 | 18.00 | 4.25 | Kanev lock |
|  |  | 270.0 | 18.00 | 3.85 | Kremenchuk lock |
|  |  | 270.0 | 18.00 | 3.65 | Dniprodzerzhynsk lock |
|  |  | 120.0 | 18.00 | 4.40 | Zaporizhya three chambers lock |
|  |  | 290.0 | 18.00 | 5.50 | Zaporizhya one chamber lock |
|  |  | 270.0 | 18.00 | 3.65 | Kakhovka lock |
| E 50 | VOLGO - BALTIJSKIY WATERWAY |  |  |  |  |
|  | St. Petersburg - Cherepovets | 198.0 | 17.60 | 4.00 | Ten locks |
|  | VOLGA Rybinsk - Astrakhan | 280.0 | 29.50 | 3.50 11/ | Sixteen locks |
| E 50-02 | VOLGA |  |  |  |  |
|  | Rybinsk - Dubna | 290.0 | 30.00 | 4.00 | One lock |
|  | KANAL IMENI MOSKVI AND RIVER MOSKVA |  |  |  |  |
|  | Dubna - Moskva (Southern Port) | 290.0 | 30.00 | 3.20 12/ | Nine locks |
| E 50-01 | KAMA |  |  |  |  |
|  | Mouth of the Kama - Solikamsk | 240.0 | 28.90 | 3.30 | Six locks |
| E 60 | KIEL CANAL | 310.0 | 42.00 | 14.00 3/5/ |  |
|  | BELOMORSKO - BALTIJSKIY CANAL |  |  |  |  |
|  | St. Petersburg - Vytegra | 198.0 | 17.60 | 4.00 |  |
|  | BELOMORSKO - BALTIJSKIY CANAL |  |  |  |  |
|  | Povenets - Belomorsk | 130.0 | 14.00 | 4.00 | Nineteen locks |
| E 60-02 | GUADALQUIVIR | 190.0 | 24.36 | 7.00 | One lock |
| E 60-04 | DOURO Porto - Spanish border | 86.0 - 92.0 | 12.10 | 4.20 | In total there are five locks on the Douro River |
|  | 0.0 km - 210.0 km |  |  |  |  |
| E 60-07 | TROLLHÄTTE CANAL | 90.0 | 13.07 | 5.85 | Six locks |
| E 60-09 | SÖDERTÄLJE CANAL | 135.0 | 19.60 | 8.00 | One lock |
| E 60-11 | SAIMAA CANAL |  |  |  |  |
|  | Vyborg - Mälkiä Lock | 85.0 | 13.20 | 4.80 |  |
|  | Mälkiä Lock - Kuopio/Joensuu | 160.0 | 13.20 | 4.80 |  |
|  | Kuopio - Iisalmi | 165.0 | 16.00 | 4.00 |  |
| E 60-11-02 | Joensuu - Nurmes | 165.0 | 16.00 | 3.00 | Joensuu lock |
|  |  | 85.0 | 16.00 | 3.00 | Other two locks |
| E 61 | PEENE, downstream of Dommin | - | - | - |  |
| E 70 | NEDER RIJN |  |  |  |  |
|  | Driel, 891.2 km | 260.0 | 18.00 | 3.50 | Normally passage through weir openings: 2x48.0 m |
|  | Amerongen, 922.0 km | 260.0 | 18.00 | 3.50 |  |
|  | Hagestein, 946.8 km | 260.0 | 18.00 | 3.50 |  |
|  | TWENTEKANAAL | 200.0 | 24.00 | 1.30 | Eefde lock complex |
|  |  | 133.0 | 12.00 | 3.50 | Eefde lock complex |
|  |  | 133.0 | 12.00 | 3.45 | Delden lock complex |
|  |  | 133.0 | 12.00 | 3.75 | Hengelo lock complex |
|  | MITTELLANDKANAL | 220.0 | 12.00 | 3.50 3/ | Anderten locks |
|  |  | 224.0 | 12.00 | 3.00 3/ | Sülfeld locks |
|  | MITTELLANDKANAL-ELBE CANAL | 190.0 | 12.50 | 4.00 | Rothensee lock |
|  | MITTELLANDKANAL | 190.0 | 12.50 | 4.00 | Hohenwarthe parallel locks |
|  | ELBE - HAVEL - KANAL | 165.0 | 11.70 | 3.49 3/ | Niegripp lock |
|  |  | 220.0 | 12.00 | 3.05 3/ | Zerben lock |
|  |  | 220.0 | 12.00 | 3.25 3/ | Wusterwitz lock |
|  | UNTERE HAVEL - WASSERSTRAßE | 210.0 | 9.93 | 3.24 4/ | Southern Brandenburg lock |
|  |  | 167.4 | 12.10 | 3.74 4/ | Northern Brandenburg lock |
|  | HAVEL - ODER - WASSERSTRAßE | … | … | … | Spandau lock not in operation |
|  |  | 82.0 | 11.90 | 2.50 4/ | Niederfinow shiplift |
|  | WARTA - NOTEC - BYDGOSKI CANAL |  |  |  |  |
|  | Kostrzyn - Bydgoszcz | 57.4 | 9.60 | 2.50 | Twenty-two locks |
|  | SZKARPAWA |  |  |  |  |
|  | Gdanska Glowa - Elblag | 61.0 | 12.50 | 3.00 | One lock |
|  | NOGAT |  |  |  |  |
|  | Biala Gora - Elblag | 57.1 - 62.0 | 9.60 | 2.50 | Four locks |
| E 70-01 | HOLLANDSCHE IJSSEL | 120.0 | 24.00 | 5.20 | Algera lock. Normally passage through barrier opening of 80.0 m width |
| E 70-02 | Mittellandkanal branch to Osnabrück | 82.0 | 10.00 | 3.50 3/ | Hollage lock |
|  |  |  |  |  | Haste lock |
| E 70-04 | Mittellandkanal branch to Hannover - Linden | 83.0 | 10.00 | 3.50 3/ | Hannover-Linden lock |
| E 70-06 | Mittellandkanal branch to Hildesheim | 82.0 | 12.00 | 3.00 3/ | Bolzum lock |
| E 70-08 | Mittellandkanal branch to Salzgitter | 223.0 | 12.00 | 3.30 3/ | Wedtlenstedt locks |
| E 70-05 | HAVELKANAL | 82.2 | 12.00 | 3.21 4/ | Schönwalde lock |
| E 70-10 | SPREE | 82.0 | 10.00 | 2.30 4/ | Charlottenburg lock |
| E 70-12 | BERLIN - SPANDAUER SCHIFFAHRTSKANAL | 67.2 | 10.00 | 3.00 4/ | Plötzensee locks |
| E 71 | TELTOWKANAL, BRITZER VERBINDUNGSKANAL | 83.5 | 12.00 | 3.48 3/ | Northern Kleinmachnow lock |
|  | SPREE - ODER - WASSERSTRAßE | 54.1 | 9.70 | 3.06 4/ | Northern Kersdorf lock |
|  |  | 65.6 | 8.54 | 2.49 4/ | Southern Kersdorf lock |
| E 80 | LE HAVRE - TANCARVILLE CANAL | 205.3 | 24.00 | 10.40 | New lock |
|  |  | 180.0 | 30.00 | 7.85 | Old lock |
|  | SEINE | 220.0 | 17.00 | 4.50 | Locks of Poses-Amfreville |
|  | Rouen - Conflant | 141.0 | 12.00 | 4.50 |  |
|  |  | 185.0 | 12.00 | 5.00 | Locks of Notre-Dame-de-la-Garenne |
|  |  | 185.0 | 24.00 | 5.00 |  |
|  |  | 141.0 | 17.00 | 3.20 |  |
|  |  | 53.0 | 8.00 | 3.20 |  |
|  |  | 160.0 | 17.00 | 4.50 | Locks of Méricourt |
|  |  | 185.0 | 12.00 | 4.50 |  |
|  |  | 185.0 | 24.00 | 5.00 | Locks of Andrésy |
|  |  | 160.0 | 12.00 | 5.00 |  |
|  | OISE | 185.0 | 12.00 | 4.00 | Locks of Pontoise |
|  | Conflans - Creil | 125.0 | 12.00 | 2.50 | Locks of Ile Adam |
|  | OISE |  |  |  |  |
|  | Creil - Compiègne | 185.0 | 12.00 | 4.00 | Authorized draught 2.50 m |
|  | Compiègne - Reims | 46.2 | 8.00 | 2.25 | Authorized draught 2.00 m |
|  | MOSELLE | 185.0 | 12.00 | 8.65 | 15 locks altogether |
|  | Toul - Apach | 100.0 | 12.00 | 2.70 |  |
|  | MOSELLE |  |  |  |  |
|  | Apach - Koblenz | 172.0 | 12.00 | 3.20 4/ |  |
|  | MAIN, downstream of Frankfurt/Main | 341.5 | 15.00 | 4.66 4/ | Northern Kostheim lock |
|  | MAIN, upstream of Frankfurt/Main | 289.8 | 12.00 | 3.00 4/ | Viereth lock |
|  | MAIN - DONAU KANAL | 190.0 | 12.00 | 4.00 3/ |  |
|  | DANUBE |  |  |  |  |
|  | Upstream of Regensburg | 190.0 | 12.00 | 4.00 4/ | Bad Abbach lock |
|  | DANUBE | 226.5 | 24.00 | 4.70 4/ | Kachlet locks |
|  | Downstream of Regensburg to 2201.8 km | 230.0 | 24.00 | 3.65 13/ | Geisling lock |
|  | DANUBE |  |  |  |  |
|  | 2201.8 km - 1880.3 km |  |  |  |  |
|  | Aschach, 2162.7 km | 230.0 | 24.00 | 4.00 | Two locks at each power station |
|  | Ottensheim - Wilhering, 2146.7 km | 230.0 | 24.00 | 4.00 |  |
|  | Abwinden - Asten, 2119.5 km | 230.0 | 24.00 | 4.00 |  |
|  | Wallsee - Mitterkirchen, 2094.5 km | 230.0 | 24.00 | 4.00 | Depth at sills referring to LNWL |
|  | Ybbs Persenbeug, 2060.4 km | 230.0 | 24.00 | 4.00 |  |
|  | Melk, 2038.2 km | 230.0 | 24.00 | 3.40 |  |
|  | Altenwörth, 1979.8 km | 230.0 | 24.00 | 4.00 |  |
|  | Greifenstein, 1949.2 km | 230.0 | 24.00 | 4.00 |  |
|  | Wien Freudenau, 1921.0 km | 275.0 | 24.00 | 4.00 |  |
|  | DERIVATION CANAL GABČIKOVO, 1819.15 km | 280.0 | 34.00 | 4.50 | Two locks |
|  | DANUBE | 310.0 | 34.00 | 4.50 | Iron Gates I locks, 942.95 km |
|  | 1075.0 km - 0.0 km | 310.0 | 34.00 | 5.00 |  |
|  |  | 310.0 | 34.00 | 5.00 | Iron Gates II locks, 864.00 km |
|  |  | 310.0 | 34.00 | 4.50 | 863.00 km |
|  |  | 140.0 | 14.00 | 2.50 | Iron Gates II reserve lock |
| E 80-01 | TISZA, 164.0 km - 0.0 km | 85.0 | 12.00 | 3.00 | Becej lock |
| E 80-01-02 | BEGEJ, 65.6 km - 0.0 km | 72.1 | 10.00 | 2.40 | Itebej lock (out of order) |
|  |  | 72.1 | 10.00 | 2.40 | Klek lock |
|  |  | 85.0 | 12.00 | 3.00 | Stojcevo lock |
| E 80-02 | SEINE Tancarville - Estuary | 180.0 | 24.00 | 3.50 | Access to the Port of Le Havre (Seine, 338.5 km) |
| E 80-04 | SEINE | 185.0 | 18.00 | 5.00 | 7 locks altogether |
|  | Conflans - Paris | 55.0 | 8.20 | 1.80 |  |
|  | SEINE Paris - Montereau 165.2 km - 67.7 km | 180.0 | 12.00 | 3.16 |  |
|  | SEINE | 185.0 | 12.05 | 4.00 |  |
|  | Montereau - Bray 67.7 km - 45.0 km | 121.0 | 10.50 | 2.24 |  |
| E 80-06 | SAAR, downstream of Völklingen | 190.0 | 12.00 | 4.00 4/ |  |
| E 80-05 | DANUBE - BUCURESTI CANAL | 130.0 | 12.50 | 5.00 | Four double locks under construction |
| E 80-14 | DANUBE - BLACK SEA CANAL | 310.0 | 25.00 | 7.50 | Cernavoda (63.3 km) and Agigea (1.9 km) locks |
| E 80-14-01 | POARTA ALBA – MIDIA - NAVODARI | 145.0 | 12.50 | 6.50 4.25 | Navodari lock, 1.5 km Ovidiu lock, 11.0 km |
| E 81 | VÁH |  |  |  |  |
|  | Kolarovo, 27.4 km | 110.0 | 24.00 | 4.00 | Construction is underway |
|  | Selice, 43.9 km | 110.0 | 24.00 | 4.00 | One lock |
|  | Kralova, 62.8 km | 110.0 | 24.00 | 4.00 | One lock |
|  | Sered - Hlohovec 82.8 km | 110.0 | 24.00 | 4.00 | One lock to be built |
|  | Hlohovec - Žilina | 110.0/191.0 14/ | 12.00 | 4.00 | Twelve locks to be reconstructed |
|  | VAH - ODER LINK | 110.0 | 12.00 | 3.50 | New link to be built |
| E 90 | DON Azov - Kalach | 145.0 | 17.00 | 3.60 15/ | Five locks |
|  | VOLGO - DONSKOY CANAL Kalach - Krasnoarmeysk | 145.0 | 17.80 | 4.00 | Thirteen locks |
| E 91 | MILANO - PO CANAL Milano - Cremona | ... | ... | ... | Six locks to be built |
|  | PO - BRONDOLO Conca di Cremona-Conca di Volta Grimana | ... | ... | ... |  |
| E 91-02 | PO Conca di Cremona - Casale Monferrato | ... | ... | ... |  |
| E 91-04 | FERRARA WATERWAY Ferrara - Porto Garibaldi | ... | ... | ... |  |
| E 91-06 | PO GRANDE Volta Grimana - Estuary | ... | ... | ... |  |
| E 91-03 | PADOVA - VENEZIA CANAL | ... | ... | ... |  |

##### Footnotes to table 2

1/	Left void

2/	Datum: Gleichwertiger Wasserstand "GLW" i.e. a long-term mean water level exceeded on all but 20 ice-free days per year.

3/	Datum: normal canal water level.

4/	Datum: hydrostatic water level.

5/	Depending on the tide water level prevailing.

6/	The smaller lock chamber is planned to be upgraded.

7/	Lock gate width is 11.00 m.

8/	On account of the particular shape and outline of the locks’ chambers, single units of not more than 80.0 m in length and 8.25 m in width are admitted.

9/	These locks are located one after the other allowing the passage of convoys of up to 190.0 m in length.

10/	This is the width of gates. The width of chambers is 16.00 m.

11/	Limitation draught at the Gorodetski Lock. At other locks a draught of 4.00 m is ensured.

12/	From Dubna to the Moskva Northern Port depth at sills is 4.00 m.

13/	Datum: Low regulated navigable water level (LRN) i.e. a mean water level exceeded on 94 per cent of ice-free days per year.

14/	190.0 m after the compilation of the reconstruction.

15/	Limitation draught at the Kochetovski Lock.

16/	Maximum dimenstions of convoys admitted are 180.0 x 22.90 m and 186.5 x 22.90 m, respectively.

17/	This new E waterway is expected to be introduced into the AGN Agreement through the amendment procedure underway.

*       *       *

| E PORTS | CARGO HANDLING CAPACITY | CARGO HANDLING EQUIPMENT AVAILABLE FOR | RAIL ACCESS ** | OTHER CHARACTERISTICS AND COMMENTS |
| --- | --- | --- | --- | --- |
|  | 0.5-3.0 million tonnes | 3.0-10.0 million tonnes | >10.0 million tonnes | CONTAINERS | RO - RO ** |  |  |
|  |  |  |  | 20’ | 40' |  |  |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| P 01-01 | Dunkerque (Dunkerque-Valenciennes Canal, 20.5 km) | … | … | … | … | … | … | … |  |
| P 01-02 | Charleroi (Lower Sambre, 38.8 km) |  |  | x | x | x | x | x |  |
| P 01-03 | Namur (Meuse, 46.3 km) |  | x |  | - | - | - | x |  |
| P 01-04 | Liège (Meuse, 113.7 km) |  |  | x | x | x | x | x |  |
| P 01-05 | Maastricht (Maas, 4.5 km) | x |  |  | - | - | - | x |  |
| P 01-06 | Stein (Maas, 21.9 km) | x |  |  | - | - | - | - |  |
| P 01-07 | Born (Maas, 29.7 km) | x |  |  | x | x | - | - |  |
| P 01-08 | Maasbracht (Maas, 41.8 km) | x |  |  | - | - | - | x |  |
| P 01-09 | Roermond (Maas, 74.3 km) | x |  |  | - | - | - | - |  |
| P 01-10 | Oss (Maas, 159.1 km) | x |  |  | x | x | - | x |  |
| P 01-11 | Dordrecht (Merwede, 974.4 km) | x |  |  | - | - | - | x |  |
| P 01-12 | Zwijndrecht (Oude Maas, 980.6 km) | x |  |  | - | - | - | x |  |
| P 01-13 | Vlaardingen (Nieuwe Waterweg, 1010.5 km) | x |  |  | - | - | - | x |  |
| P 01-14 | Maassluis (Nieuwe Waterweg, 1018.7 km) | x |  |  | x | x | - | - |  |
| P 01-01-01 | Overpelt (Kanaal Bocholt-Herentals, 14.8 km) | … | … | … | … | … | … | … |  |
| P 01-03-01 | 's-Hertogenbosch (Zuid-Willemsvaart, 4.0 km) | x |  |  | x | x | - | - |  |
| P 02-01 | Zeebrugge (North Sea) | x |  | x 2/ | x | x | x | x |  |
| P 02-02 | Aalter (Gent Oostende Canal, 22.5 km) | … | … | … | … | … | … | … |  |
| P 02-03 | Lille (Deûle, 42.0 km) | … | … | … | … | … | … | … |  |
| P 02-02-01 | Oostende (North Sea) | … | … | … | … | … | … | … |  |
| P 02-04-01 | Roeselare (Leie-Roeselare Canal, 0.5 km) | … | … | … | … | … | … | … |  |
| P 02-04-02 | Izegem (Leie-Roeselare Canal, 6.4 km) | … | … | … | … | … | … | … |  |
| P 03-01 | Moerdijk (Hollands Diep) | x |  |  | x | x | - | x |  |
| P 03-02 | Terneuzen (Terneuzen-Gent Canal, 32.5 km) | x |  |  | - | - | - | x |  |
| P 03-03 | Zelzate (Terneuzen-Gent Canal, 19.6 km) | … | … | … | … | … | … | … |  |
| P 03-04 | Gent (Terneuzen-Gent Canal, 4.6 km) | … | … | … | … | … | … | … |  |
| P 04-01 | Vlissingen (Westerschelde) | x |  |  | x | x | x | x |  |
| P 04-02 | Beveren (Beneden Zeeschelde, 22.9 km) | … | … | … | … | … | … | … |  |
| P 04-03 | Ruisbroek (Charleroi-Bruxelles Canal, 58.8 km) | … | … | … | … | … | … | … |  |
| P 04-03bis | Willebroek (Bruxelles-Schelde Canal, 61.3 km) 3/ | x |  |  | x | x | x | x |  |
| P 04-04 | Grimbergen (Bruxelles-Schelde Canal, 75.8 km) | x |  |  | - | - | - | - |  |
| P 04-05 | Bruxelles (Bruxelles-Schelde Canal, 81.5 km) | … | … | … | … | … | … | … |  |
| P 05-01 | Avelgem (Bovenschelde, 35.7 km) | x |  |  | x | x | … | … |  |
| P 05-02 | Melle (Boven-Zeeschelde, 9.9 km) | … | … | … | … | … | … | … |  |
| P 05-03 | Meerhout (Albertkanaal, 80.7 km) | x |  |  | x | x | … | … |  |
| P 05-04 | Ham (Albertkanaal, 73.7 km) | x |  |  | … | … | … | … |  |
| P 05-05 | Hasselt (Albertkanaal, 51.5 km) | x |  |  | … | … | … | … |  |
| P 05-06 | Genk (Albertkanaal, 42.9 km) | x |  |  | … | … | … | … |  |
| P 05-07 | Centre and West (Schelde, 22.0 km) 3/ |  |  | x | x | x | x | x |  |
| P 05-04-01 | Aalst (Dender, 53.7km) | … | … | … | … | … | … | … |  |
| P 06-01 | Antwerpen (Schelde, 102.9 km) | … | … | … | … | … | … | … |  |
| P 06-02 | Bergen op Zoom (Scheld-Rijn Connection, 1031.8 km) | x |  |  | - | - | - | - |  |
| P 10-01 | Rotterdam (Nieuwe Maas, 1002.5 km) |  |  | x | x | x | x | x |  |
| P 10-02 | Alblasserdam (Noord, 981.1 km) | x |  |  | - | - | - | - |  |
| P 10-03 | Tiel (Waal, 914.6 km) | x |  |  | - | - | - | - |  |
| P 10-04 | Emmerich (Rhine, 852.0 km) | x |  |  | x | x | … | x |  |
| P 10-05 | Wesel (Rhine, 814.0 km) | x |  |  | x | x | … | x |  |
| P 10-06 | Rheinberg-Ossenberg* (Rhine, 806.0 km) | x |  |  | … | … | … | … |  |
| P 10-07 | Orsoy (Rhine, 794.0 km) | x |  |  | … | … | … | … |  |
| P 10-08 | Walsum-Nordhafen* (Rhine, 793.0 km) | x |  |  | … | … | … | … |  |
| P 10-09 | Walsum-Sud* (Rhine, 791.0 km) | x |  |  | … | … | … | … |  |
| P 10-10 | Schwelgern* (Rhine, 790.0 km) |  |  | x | … | … | … | … |  |
| P 10-11 | Homberg, Sachtleben* (Rhine, 774.0 km) |  |  | x | x | x | x | x |  |
| P 10-12 | Duisburg-Ruhrort Häfen (Rhine, 774.0 km) |  |  | x | x | x | x | x |  |
| P 10-13 | Krefeld (Rhine, 762.0 km) |  | x |  | x | x | … | x |  |
| P 10-14 | Düsseldorf (Rhine, 743.0 km) | x |  |  | x | x | … | x |  |
| P 10-15 | Neuss (Rhine, 740.0 km) |  | x |  | x | x | … | x |  |
| P 10-16 | Stürzelberg* (Rhine, 726.0 km) | x |  |  | … | … | … | x |  |
| P 10-17 | Leverkusen* (Rhine, 699.0 km) | x |  |  | x | x | … | x |  |
| P 10-18 | Köln (Rhine, 688.0 km) |  | x |  | x | x | … | x |  |
| P 10-19 | Wesseling-Godorf* (Rhine, 672.0 km) | x |  |  | … | … | … | x |  |
| P 10-20 | Bonn (Rhine, 658.0 km) | x |  |  | x | x | - | - |  |
| P 10-21 | Andernach (Rhine, 612.0 km) | x |  |  | - | - | - | x |  |
| P 10-22 | Neuwied (Rhine, 606.0 km) | x |  |  | - | - | - | x |  |
| P 10-23 | Bendorf (Rhine, 599.0 km) | x |  |  | - | - | - | x |  |
| P 10-24 | Koblenz (Rhine, 596.0 km) | x |  |  | x | x | - | x |  |
| P 10-25 | Bingen (Rhine, 527.0 km) | x |  |  | - | - | - | x |  |
| P 10-26 | Wiesbaden (Rhine, 500.0 km) | x |  |  | - | - | - | x |  |
| P 10-27 | Gernsheim (Rhine, 462.0 km) | x |  |  | - | - | - | x |  |
| P 10-28 | Worms (Rhine, 444.0 km) | x |  |  | - | - | - | x |  |
| P 10-29 | Mannheim (Rhine, 424.0 km) |  | x |  | x | x | x | x |  |
| P 10-30 | Ludwigshafen (Rhine, 420.0 km) |  | x |  | x | x | x | x |  |
| P 10-31 | Speyer (Rhine, 400.0 km) | x |  |  | - | - | - | x |  |
| P 10-32 | Germersheim (Rhine, 385.0 km) | x |  |  | x | x | - | x |  |
| P 10-33 | Wörth (Rhine, 366.0 km) | x |  | x | x | x | - | x |  |
| P 10-34 | Karlsruhe (Rhine, 360.0 km) |  |  |  | x | x | x | x |  |
| P 10-35 | Kehl (Rhine, 297.0 km) | x |  |  | x | x | - | x |  |
| P 10-36 | Strasbourg (Rhine, 296.0 km) |  | x |  | x | x | - | x | Sand, gravel, oil products, cereals |
| P 10-37 | Breisach (Rhine, 226.0 km) | x |  |  | - | - | - | - |  |
| P 10-38 | Colmar-Neuf Brisach (Rhine, 225.8 km) | x |  |  | - | - | - | x | Minerals, agricultural/metallurgical products |
| P 10-39 | Mulhouse-Ottmarsheim (Grand Canal d'Alsace, 21.0 km) | x |  |  | x | x | - | x | Minerals, agricultural/chemical products |
| P 10-40 | Fort Louis Stattmatten (Grand Canal d'Alsace, 322.0 km) | … | … | … | … | … | … | … |  |
| P 10-41 | Ile Napoléon (Rhône-Rhine Canal, 37.6 km) | x |  |  | - | - | - | x | Oil products, minerals, fertilizers |
| P 10-42 | Mulhouse (Rhône-Rhine Canal, 31.0 km) | … | … | … | … | … | … | … |  |
| P 10-43 | Aproport (Chalon, Mâcon, Villfranche-sur-Saône) | x |  |  | x | x | - | x |  |
|  | (Saône, 230.0 km, 296.0, km and 335.0 km) |  |  |  |  |  |  |  |  |
| P 10-44 | Lyon (Rhône, 375.0 km) | x |  |  | x | x | x | x | Oil and metallurgical products, minerals |
| P 10-45 | Marseille-Fos (Marseille-Rhône Canal, 0.0 km) | x |  |  | x | x | x | x | Oil products, minerals |
| P 10-01-01 | Rhein-Lippe-Hafen* (Wesel-Datteln-Kanal, 1.0 km) | x |  |  | … | … | … | x |  |
| P 10-01-02 | Marl Hüls-AG* (Wesel-Datteln-Kanal, 38.0 km) | x |  |  | … | … | … | x |  |
| P 10-01-03 | Auguste Victoria* (Wesel-Datteln-Kanal, 39.0 km) | x |  |  | … | … | … | … |  |
| P 10-01-04 | Lünen (Datteln-Hamm-Kanal, 11.0 km) | x |  |  | … | … | … | x |  |
| P 10-01-05 | Berkamen* (Datteln-Hamm-Kanal, 22.0 km) | x |  |  | … | … | … | … |  |
| P 10-01-06 | Hamm (Datteln-Hamm-Kanal, 34.0 km) | x |  |  | x | x | … | x |  |
| P 10-01-07 | Schmehausen* (Datteln-Hamm-Kanal, 47.0 km) | x |  |  | … | … | … | … |  |
| P 10-03-01 | Essen (Rhein-Herne-Kanal, 16.0 km) | x |  |  | … | … | … | x |  |
| P 10-03-02 | Coelln-Neuessen* (Rhein-Herne-Kanal, 17.0 km) | x |  |  | … | … | … | … |  |
| P 10-03-03 | Ruhr-Oel* (Rhein-Herne-Kanal, 22.0 km) | x |  |  | x | x | … | x |  |
| P 10-03-04 | Gelsenkirchen (Rhein-Herne-Kanal, 24.0 km) | x |  |  | x | x | … | x |  |
| P 10-03-05 | Wanne-Eickel (Rhein-Herne-Kanal, 32.0 km) | x |  |  | … | … | … | x |  |
| P 10-05-01 | Mühlheim (Ruhr, 8.0 km) | x |  |  | x | x | … | … |  |
| P 10-07-01 | Heilbronn (Neckar, 110.0 km) |  | x |  | x | x | x | x |  |
| P 10-07-02 | Stuttgart (Neckar, 186.0 km) | x |  |  | - | - | - | x |  |
| P 10-07-03 | Plochingen (Neckar, 200.0 km) | x |  |  | - | - | - | x |  |
| P 10-09-01 | Huningue (Rhine, 168.4 km) | x |  |  | x | x | - | x | Oil products, minerals, fertilizers |
| P 10-09-02 | Rheinhäfen beider Basel (Rhine, 159.15-170.0 km) |  |  | x | x | x | x | x |  |
| P 10-04-01 | Sète (Rhône-Sète Canal, 96.0 km) | x |  |  | x | x | x | x | Coal, cereals, oilcake |
| P 10-06-01 | Fos (Fos Bay, sea section) | … | … | … | … | … | … | … |  |
| P 11-01 | IJmond (Noordzeekanaal, 4.7 km) |  |  | x | x | x | x | x |  |
| P 11-02 | Zaanstad (Zaan, 1.4 km) | x |  |  | - | - | - | x |  |
| P 11-03 | Amsterdam (Noordsee Kanaal, 20.6 km) |  |  | x | x | x | x | x |  |
| P 11-04 | Utrecht (Amsterdam-Rijnkanaal, 35.0 km) | x |  |  | x | x | - | x |  |
| P 11-01-01 | Zaandam (Zaan, 2.0 km) | x |  |  | - | - | - | - |  |
| P 12-01 | Nijmegen (Waal, 884.6 km) | x |  |  | x | x | - | - |  |
| P 12-02 | Arnhem (Nederrijn, 885.8 km) | x |  |  | - | - | - | - |  |
| P 12-03 | Zwolle (IJssel, 980.7 km) | x |  |  | - | - | - | - |  |
| P 12-02-01 | Meppel (Meppelerdiep, 10.5 km) | x |  |  | x | x | - | - |  |
| P 13-01 | Emsland* (Dortmund-Ems-Kanal, 151.0 km) | x |  |  | … | … | … | x |  |
| P 13-02 | Münster (Dortmund-Ems-Kanal, 68.0 km) | x |  |  | … | … | … | x |  |
| P 13-03 | Dortmund (Dortmund-Ems-Kanal, 1.0 km) |  | x |  | x | x | … | x |  |
| P 14-01 | Bremerhafen (Weser, 66.0-68.0 km) | x |  |  | x | x | x | x |  |
| P 14-02 | Nordenham (Weser, 54.0-64.0 km) | x |  |  | x | x | - | x |  |
| P 14-03 | Brake (Weser, 41.0 km) | x |  |  | x | x | - | x |  |
| P 14-04 | Bremen (Weser, 4.0-8.0 km) |  | x |  | x | x | x | x |  |
| P 15-01 | Lelystad (IJselmeer) | x |  |  | - | - | - | - |  |
| P 15-02 | Lemmer (Pr. Margrietkanaal, 90.5 km) | x |  |  | - | - | - | - |  |
| P 15-03 | Groningen (Starkenborghkanaal, 7.0 km) | x |  |  | - | - | - | x |  |
| P 15-04 | Emden (Ems, 41.0 km) | x |  |  | x | x | x | x |  |
| P 15-05 | Leer (Ems, 14.0 km) | x |  |  | - | - | - | x |  |
| P 15-06 | Oldenburg* (Hunte, 0.0 - 5.0 km) | x |  |  | - | - | - | x |  |
| P 15-01-01 | Leenwarden (Haringsmakanaal, 23.7 km) | x |  |  | - | - | - | - |  |
| P 20-01 | Cuxhaven (Elbe, 724.0 km) | x |  |  | x | x | x | x |  |
| P 20-02 | Brunsbüttel (Elbehafen, 693.0 km) |  | x |  | - | - | - | - |  |
| P 20-03 | Bützfleet* (Elbe, 668.0 km) |  | x |  | - | - | - | - |  |
| P 20-04 | Hamburg (Elbe, 618.0-639.0 km) |  |  | x | x | x | x | x |  |
| P 20-05 | Lauenburg (Elbe, 568.0 km) | x |  |  | - | - | - | - |  |
| P 20-06 | Tangermünde (Elbe, 388.0 km) | x |  |  | - | - | - | - |  |
| P 20-07 | Kieswerk Rogätz* (Elbe, 354.0 km) | x |  |  | - | - | - | x |  |
| P 20-08 | Magdeburger Häfen (Elbe, 330.0 and 333.0 km) |  | x |  | - | - | - | x |  |
| P 20-09 | Schönebeck (Elbe, 315.0km) | x |  |  | - | - | - | - |  |
| P 20-10 | Aken (Elbe, 277.0 km) | x |  |  | - | - | - | - |  |
| P 20-11 | Torgau (Elbe, 154.0 km) | x |  |  | - | - | - | - |  |
| P 20-12 | Kieswerk Mühlberg* (Elbe, 125.0 km) | x |  |  | - | - | - | x |  |
| P 20-13 | Riesa (Elbe, 109.0 km) | x |  |  | - | - | - | - |  |
| P 20-14 | Dresden (Elbe, 57.0 and 61.0 km) | x |  |  | - | - | - | - |  |
| P 20-15 | Decin (Elbe, 98.2 and 94.2 km) 4/ | x |  |  | x | x | - | x | Bulk cargoes |
| P 20-16 | Usti nad Labem (Elbe, 75.3 and 72.5 km) 4/ | x |  |  | x | x | - | x | Bulk cargoes |
| P 20-17 | Mëlník (Elbe, 3.0 km) 4/ | x |  |  | x | x | - | x | Bulk cargoes |
| P 20-04-01 | Halle-Trotha (Saale, 86.0 km) | x |  |  | - | - | - | - |  |
| P 20-06-01 | Praha (Vltava, 46.5 and 55.5 km) | x |  |  | x | x | - | x |  |
| P 21-01 | Lübeck (Trave, 2.0 - 8.0 km) | x |  |  | x | x | x | x |  |
| P 30-01 | Swinoujscie (Baltic Sea-mouth of the Oder) |  | x |  | x | x | x | x |  |
| P 30-02 | Szczecin (Oder, 741.0 km) |  |  | x | x | x | x | x |  |
| P 30-03 | Kostrzyn (Oder, 617.0 km) | x |  |  | - | - | - | x |  |
| P 30-04 | Wroclaw (Oder, 255.0 km) | x |  |  | - | - | - | x |  |
| P 30-05 | Kozle (Oder, 96.0 km) | x |  |  | - | - | - | x |  |
| P 30-01-01 | Glivice (Gliwicki Canal, 41.0 km) | x |  |  | - | - | - | x |  |
| P 40-01 | Gdansk (Baltic Sea- mouth of the Wisla) |  |  | x | x | x | x | x |  |
| P 40-02 | Bydgoszcz (Wisla, 772.3 km and Brda, 2.0 km) | x |  |  | - | - | - | - |  |
| P 40-03 | Warszawa (Wisla, 520.0 km and Zeran Canal, 2.0 km) | x |  |  | - | - | - | x |  |
| P 40-04 | Brest (Mukhovets) 3/ | x |  |  | - | - | - | x | General and bulk cargo |
| P 40-04bis | Pinsk (Pina, 12.0 km) 3/ | x |  |  | - | - | - | x | General and bulk cargo |
| P 40-04ter | Mozyr (Pripyat, 185.0 km) 3/ | x |  |  | - | - | - | x | General and bulk cargo |
| P 40-05 | Kyiv (Dnipro, 856.0 km) |  |  | x | x |  | - | x | Bulk and general cargo |
| P 40-06 | Cherkassy (Dnipro, 653.0 km) |  | x |  | x | - | - | x | Bulk and general cargo |
| P 40-07 | Kremenchuk (Dnipro, 541.0 km) |  |  | x | x | - | - | x | Bulk and general cargo |
| P 40-07bis | Poltava Ore Mining and Processing Enterprize (Dnipro, 521.0 km) 3/ |  | x |  | - | - | - | x | Ore, minerals |
| P 40-08 | Dniprodzerzhynsk (Dnipro, 429.0 km) |  | x |  | - | - | - | x | Bulk and general cargo |
| P 40-08bis | Cargo Handling terminal (Dnipro, 422.0 km) 3/ | x |  |  | - | - | - | x | Bulk and general cargo |
| P 40-09 | Dnipropetrovsk (Dnipro, 393.0 km) |  |  | x | x |  | - | x | Bulk and general cargo |
| P 40-10 | Zaporizhya (Dnipro, 308.0 km) |  |  | x | x | x | - | x | Bulk and general cargo, lighters |
| P 40-11 | Nova Kakhovka (Dnipro, 96.0 km) | x |  |  | - | - | - | - | Bulk and general cargo |
| P 40-12 | Kherson (Dnipro, 28.0 km) |  | x |  | x | - | - | x | Bulk and general cargo, lighters |
| P 40-01-01 | Chernihiv (Desna, 194.5 km) 3/ |  | x |  | - | - | - | x | General and bulk cargo |
| P 40-02-01 | Mykolaiv, river port (Pivdenny Buh, 40.0 km) | x |  |  |  |  |  |  | Cereals, scrap, minerals |
| P 40-02-02 | Mykolaiv, sea port (Pivdenny Buh, 35.0 km) |  | x |  | x | x | - | x | Timber, oil products, metals, cereals, bulk cargo, scrap |
| P 40-02-03 | Dnipro-Buhskiy (Pivdenny Buh, 16.0 km) |  | x |  | - | - | - | x | Ore, general cargo |
| P 41-01 | Klaipeda river port (Kurshinskiy Zaliv) |  |  | x | x | x | x | x |  |
| P 41-02 | Neringa (Kurshinskiy Zaliv) | … | … | … | … | … | … | … |  |
| P 41-03 | Jurbarkas (Nemunas, 126.0 km) | … | … | … | … | … | … | … |  |
| P 41-04 | Kaunas (Nemunas, 219.0 km) | x |  |  | - | - | - | x |  |
| P 50-01 | Sankt-Petersburg sea port (Neva, 1397.0 km) 5/ |  |  | x | x | x | x | x | General cargoes, timber, cereals, coal |
| P 50-02 | Sankt-Petersburg river port (Neva, 1385.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal |
| P 50-03 | Podporozhie (Volgo-Baltijskiy Waterway, 1045.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, ore, pipes |
| P 50-04 | Cherepovets (Volgo-Baltijskiy Waterway, 540.0 km) 5/ | x |  |  | x | x | - | x | General cargoes, timber, construction materials, coal |
| P 50-05 | Yaroslavl (Volga, 520.0 km) 5/ | x |  |  | x | - | - | x | General cargoes, timber, construction materials, fertilisers |
| P 50-06 | Nizhniy Novgorod (Volga, 907.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal |
| P 50-07 | Kazan (Volga, 1313.0 km) 5/ | … | … | … | … | … | … | … |  |
| P 50-08 | Ulianovsk (Volga, 1541.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, construction materials, coal |
| P 50-09 | Samara (Volga, 1746.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal |
| P 50-10 | Saratov (Volga, 2175.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal, cereals |
| P 50-11 | Volgograd (Volga, 2560.0 km) 5/ | x |  |  | x | - | - | x | General cargoes, timber, construction materials, coal |
| P 50-12 | Astrakhan (Volga, 3051.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, construction materials, timber |
| P 50-02-01 | Moskva Northern Port (Kanal imeni Moskvi, 42.0 km) 5/ | x |  |  | x | x | - | - | General cargoes, timber, construction materials, salt |
| P 50-02-02 | Moskva Western Port (Kanal imeni Moskvi, 32.0 km) 5/ | … | … |  | … | … | … | … |  |
| P 50-02-03 | Moskva Southern Port (Kanal imeni Moskvi, 0.0 km) 5/ | … | … |  | … | … | … | … |  |
| P 50-02-02-01 | Tver (Volga, 279.0 km) 5/ | x |  |  | - | - | - | - | General cargoes, construction materials |
| P 50-01-01 | Perm (Kama, 2269.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal, ore, cereals |
| P 60-01 | Scheveningen (North Sea) | x |  | x | x | x | x | - |  |
| P 60-02 | Den Helder (North Sea) | x |  |  | - | - | x | - |  |
| P 60-03 | Brunsbüttel (Kiel Canal, 2.0 - 5.0 km) |  | x |  | - | - | - | x |  |
| P 60-04 | Rendsburg (Kiel Canal, 62.0 km) | x |  |  | - | - | - | x |  |
| P 60-05 | Kiel (Kiel Canal, 96.0 km) | x |  |  | x | x | x | x |  |
| P 60-06 | Flensburg | x |  |  | - | - | - | x |  |
| P 60-07 | Wismar | x |  |  | x | x | x | x |  |
| P 60-08 | Rostock | x |  |  | x | x | x | x |  |
| P 60-09 | Stralsund | x |  |  | - | - | - | x |  |
| P 60-10 | Greifswald | x |  |  | - | - | - | - |  |
| P 60-11 | Sventoji (Baltic Sea) | … | … | … | … | … | … | … |  |
| P 60-12 | Vyborg (Vyborg Bay) | … | … | … | … | … | … | … |  |
| P 60-13 | Petrozavodsk (Lake Onega, 1009.0 km) 5/ | x |  |  | - | - | - | x | General cargoes, construction materials |
| P 60-14 | Arkhangelsk sea port (Mouth of Severnaja Dvina) | … | … | … | … | … | … | … |  |
| P 60-15 | Arkhangelsk river port (Mouth of Severnaja Dvina) | … | … | … | … | … | … | … |  |
| P 60-02-01 | Sevilla (Guadalquivir, 80.0 km) |  | x |  | x | x | x | x | General and bulk cargoes |
| P 60-04-01 | Douro (Douro, 5.0 km) | … | … | … | … | … | … | … |  |
| P 60-04-02 | Sardoura (Douro, 49.0 km) | … | … | … | … | … | … | … |  |
| P 60-04-03 | Régua-Lamego (Douro, 101.0 km) | … | … | … | … | … | … | … |  |
| P 60-06-01 | Bordeaux (Gironde and Garonne, 359.0 km) | … | … | … | … | … | … | … |  |
| P 60-08-01 | Nante (Loire, 645.0 km) | x |  |  | … | … | … | … | Minerals, construction materials |
| P 60-10-01 | Harlingen (Waddenzee) |  | x |  | x | x | x | x |  |
| P 60-12-01 | Delfzijl (Waddenzee) |  | x |  | x | x | x | x |  |
| P 60-11-01 | Mustola (39.0 km from the mouth of Saimaa Canal) | x |  |  | x | x | x | x | Timber |
| P 60-11-02 | Kaukas* (52.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-03 | Rapasaari* (52.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-04 | Joutseno* (67.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-05 | Vuoksi* (85.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | - | Timber |
| P 60-11-06 | Varkaus (Port of Taipale)(270.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-07 | Varkaus (Port of Kosulanniemi*) (270.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | - | Timber |
| P 60-11-08 | Varkaus (Port of Akonniemi)(270.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-09 | Kuopio (352.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 60-11-02-01 | Puhos* (311.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | - | Timber |
| P 60-11-02-02 | Joensuu (346.0 km from the mouth of Saimaa Canal) | x |  |  | - | - | - | x | Timber |
| P 61-01 | Anklam (Peene, 95.0 km) | x |  |  | - | - | - | x |  |
| P 70-01 | Wageningen (Neder-Rijn, 903.2 km) | x |  |  | - | - | - | - |  |
| P 70-02 | Enchede (Twentekanaal, 49.8 km) | x |  |  | - | - | - | - |  |
| P 70-03 | Ibbenbüren (Mittellandkanal, 5.0 km) | x |  |  | - | - | - | x |  |
| P 70-04 | Minden (Mittellandkanal, 100.0-104.0 km) | x |  |  | - | - | - | x |  |
| P 70-05 | Hannover (Mittellandkanal, 155.0-159.0 km) | x |  |  | x | x | - | x |  |
| P 70-06 | Mehrum* (Mittellandkanal, 194.0 km) | x |  |  | - | - | - | - |  |
| P 70-07 | Braunschweig (Mittellandkanal, 220.0 km) | x |  |  | - | - | - | x |  |
| P 70-08 | Braunschweig/Thune* (Mittellandkanal, 223.0 km) | x |  |  | - | - | - | - |  |
| P 70-09 | Haldensleben (Mittellandkanal, 301.0 km) | x |  |  | - | - | - | x |  |
| P 70-10 | Niegripp* (Elbe-Havel-Kanal, 330.0 km) | x |  |  | - | - | - | - |  |
| P 70-11 | Brandenburg* (Untere Havel-Wasserstraße, 60.0 km) | x |  |  | - | - | - | - |  |
| P 70-12 | Brandenburg (Untere Havel-Wasserstraße, 57.0 km) | x |  |  | - | - | - | - | Gravel works |
| P 70-13 | Deponie Deetz* (Untere Havel-Wasserstraße, 40.0 km) | x |  |  | - | - | - | x |  |
| P 70-14 | Spandau South Harbour (Untere Havel-Wasserstraße, 2.0 km) | x |  |  | - | - | - | x |  |
| P 70-15 | Elblag (Zalew Wislany) | x |  |  | - | - | - | - |  |
| P 70-16 | Kaliningrad sea port (Pregolia, 8.0 km) | … | … | … | … | … | … | … |  |
| P 70-17 | Kaliningrad river port (Pregolia, 9.0 km) | … | … | … | … | … | … | … |  |
| P 70-01-01 | Gouda (Hollandse IJssel, 1.4 km) | x |  |  | - | - | - | - |  |
| P 70-03-01 | Hengelo (Twentekanaal, 45.1 km) | x |  |  | x | x | - | x |  |
| P 70-03-02 | Almelo (Zijkanaal, 17.6 km) | x |  |  | - | - | - | - |  |
| P 70-02-01 | Osnabrück (Stichkanal, 13.0 km) | x |  |  | - | - | x | x |  |
| P 70-04-01 | Hannover-Linden (Stichkanal, 11.0 km) | x |  |  | - | - | - | x |  |
| P 70-06-01 | Hildesheim (Stichkanal, 15.0 km) | x |  |  | - | - | - | x |  |
| P 70-08-01 | Salzgitter (Stichkanal, 15.0 km) | x |  |  | x | - | - | x |  |
| P 70-10-01 | Cargo-Handling Complex* (branch of the Spree at 0.0 km) | x |  |  | - | - | - | - |  |
| P 70-10-02 | Nonnendamm (Spree, 2.0 km) | x |  |  | - | - | - | x |  |
| P 70-10-03 | Reuter Power Station* (Spree, 3.0 km) | x |  |  | - | - | - | x |  |
| P 70-10-04 | Charlottenburg Power Station (Spree, 8.0 km) | x |  |  | - | - | - | - |  |
| P 70-10-05 | Westhafen Berlin (Westhafenkanal, 3.0 km) |  | x |  | - | - | - | x |  |
| P 70-10-06 | Osthafen Berlin (Spree, 21.0 km) | x |  |  | - | - | - | x |  |
| P 70-10-07 | Klingenberg Heating Station (Spree, 25.0 km) | x |  |  | - | - | - | x |  |
| P 70-12-01 | Moabit Power Station* (Berlin-SpandauerSchiffahrtskanal, 9.0 km) | x |  |  | - | - | - | - |  |
| P 71-01 | Teltowkanal Cargo-Handling Point* (Teltowkanal, 31.0-34.0 km) | x |  |  | - | - | - | x |  |
| P 71-02 | Oberschöneweide Cargo-Handling Point (Spree-Oder Wasserstraße, 28.0-29.0 km) | x |  |  | - | - | - | x |  |
| P 71-03 | Eisenhüttenstadt EKO* (Spree-Oder Wasserstraße, 122.0 km) | x |  |  | - | - | - | x |  |
| P 71-04 | Eisenhüttenstadt (Spree-Oder Wasserstraße, 124.0 km) | x |  |  | - | - | - | x |  |
| P 71-02-01 | Potsdam (Potsdamer Havel, 3.0 km) | x |  |  | - | - | - | - |  |
| P 71-06-01 | Niederlehme* (Dahme-Wasserstraße, 8.0 km) | x |  |  | - | - | - | - |  |
| P 71-06-02 | Königs Wusterhausen (Dahme-Wasserstraße, 8.0 km) |  | x |  | - | - | - | x |  |
| P 80-01 | Le Havre (Le Havre-Tancarville Canal, 20.0 km) | x |  |  | x | x | x | x | Oil products, fuels, minerals |
| P 80-02 | Rouen (Seine, 242.0 km) |  | x |  | x | x | x | x | Oil, cereals, sand, coal |
| P 80-03 | Conflant (Seine, 239.0 km) | x |  |  | … | … | … | … |  |
| P 80-04 | Frouard (Moselle, 346.5 km) | … | … | … | … | … | … | … |  |
| P 80-05 | Metz (Moselle, 297.0-294.0 km) | … | … | … | … | … | … | … |  |
| P 80-06 | Mondelange-Richemont (Moselle, 279.5-277.9 km) | … | … | … | … | … | … | … |  |
| P 80-07 | Thionville-Illange (Moselle, 271.9-270.1 km) | … | … | … | … | … | … | … |  |
| P 80-08 | Mertert (Moselle, 208.0 km) | x |  |  | - | - | - | x |  |
| P 80-09 | Trier (Moselle, 184.0 km) | x |  |  | - | - | - | x |  |
| P 80-10 | Bingen (Rhine, 527.0 km) | x |  |  | - | - | - | x |  |
| P 80-11 | Wiesbaden (Rhine, 500.0 km) | x |  |  | - | - | - | x |  |
| P 80-12 | Mainz (Rhine, 500.0 km) |  | x |  | x | x | x | x |  |
| P 80-13 | Flörsheim* (Main, 9.0 km) | x |  |  | - | - | - | - |  |
| P 80-14 | Raunheim* (Main, 14.0 km) | x |  |  | - | - | - | - |  |
| P 80-15 | Hattersheim* (Main, 17.0 km) | x |  |  | - | - | - | - |  |
| P 80-16 | Kelsterbach* (Main, 19.0 km) | x |  |  | - | - | - | - |  |
| P 80-17 | Frankfurt* (Main, 22.0 - 29.0 km) | x |  |  | x | x | - | x |  |
| P 80-18 | Frankfurt (Main, 31.0 - 37.0 km) |  | x |  | x | x | - | x |  |
| P 80-19 | Offenbach (Main, 40.0 km) | x |  |  | - | - | - | x |  |
| P 80-20 | Hanau (Main, 56.0 - 60.0 km) | x |  |  | - | - | - | x |  |
| P 80-21 | Grosskotzenburg* (Main, 62.0 km) | x |  |  | - | - | - | - |  |
| P 80-22 | Stockstadt (Main, 82.0 km) | x |  |  | x | - | - | x |  |
| P 80-23 | Aschaffenburg (Main, 83.0 km) | x |  |  | x | - | - | x |  |
| P 80-24 | Triefenstein* (Main, 173.0 km) | x |  |  | - | - | - | - |  |
| P 80-25 | Karlstadt* (Main, 227.0 km) | x |  |  | - | - | - | - |  |
| P 80-26 | Würzburg (Main, 246.0-251.0 km) | x |  |  | x | - | x | x |  |
| P 80-27 | Schweinfurt (Main, 330.0 km) | x |  |  | - | - | - | x |  |
| P 80-28 | Bamberg (Main-Donau-Kanal, 3.0 km) | x |  |  | - | - | - | x |  |
| P 80-29 | Erlangen (Main-Donau-Kanal, 46.0 km) | x |  |  | - | - | - | x |  |
| P 80-30 | Nürnberg (Main-Donau-Kanal, 72.0 km) | x |  |  | - | - | x | x |  |
| P 80-31 | Regensburg (Danube, 2370.0-2378.0 km) | x |  |  | x | x | - | x |  |
| P 80-32 | Deggendorf* (Danube, 2281.0-2284.0 km) | x |  |  | x | x | - | - |  |
| P 80-33 | Linz (Danube, 2128.2 - 2130.6 km) | x |  |  | x | x | x | x | All cargoes |
| P 80-34 | Linz-Vöest* (Danube, 2127.2 km) |  | x |  | x | x | - | x | Metallurgical products |
| P 80-35 | Enns-Ennsdorf (Danube, 2111.8 km) | x |  |  | x | x | x | x | General and bulk cargoes, liquid gas |
| P 80-36 | Krems (Danube, 998.0 km) | x |  |  | x | - | - | x | All cargoes but oil and oil products |
| P 80-37 | Wien (Danube, 1916.8-1920.2 km) | x |  |  | x | x | x | x | All cargoes |
| P 80-38 | Bratislava (Danube, 1867.0 km) |  | x |  | x | x | x | x |  |
| P 80-39 | Györ-Gönyü (Danube, 1807.0 km) | x |  |  | ... | ... | ... | ... | Mainly bulk cargoes and oil products |
| P 80-40 | Komarno (Danube, 1767.1 km) |  | x |  | x | x | - | x |  |
| P 80-41 | Sturovo (Danube, 1722.0 km) | x |  |  | - | - | - | - |  |
| P 80-42 | Budapest (Danube, 1640.0 km) |  | x |  | x | ... | x | x |  |
| P 80-43 | Szàzhalombatta (Danube, 1618.7 km) | x |  |  | ... | ... | ... | ... | Oil products |
| P 80-44 | Dunaujvaros (Danube, 1579.0 km) | x |  |  | - | - | - | x | Mainly bulk cargo |
| P 80-45 | Dunaföldvàr (Danube, 1563.0 km) | x |  |  | ... | ... | ... | ... | Oil products |
| P 80-46 | Baja (Danube, 1480.0 km) | x |  |  | x |  |  | x |  |
| P 80-46bis | Apatin (Danube, 1401.5 km) 3/ | x |  |  | x |  | ... | x |  |
| P 80-47 | Vukovar (Danube, 1333.1 km) | x |  |  | x | x | - | x |  |
| P 80-47bis | Backa Palanka (Danube, 1295.0 km) 3/ | x |  |  | x |  |  | x |  |
| P 80-47ter | Novi Sad (Danube, 1253.5 km) 3/ | x |  |  | x |  |  | x |  |
| P 80-48 | Beograd (Danube, 1170.0 km) | ... | ... | ... | ... | ... | ... | ... |  |
| P 80-48bis | Pangevo (Danube, 1152.8 km) 3/ | x |  |  | x |  |  | x |  |
| P 80-49 | Smederevo (Danube, 1116.3 km) | ... |  |  | ... | ... | ... | ... |  |
| P 80-50 | Orsova (Danube, 954.0 km) | x |  |  | ... | ... | ... | x |  |
| P 80-51 | Turnu Severin (Danube, 931.0 km) | x |  |  | ... | ... | x | x |  |
| P 80-52 | Prahovo (Danube, 861.0 km) | ... | ... | ... | ... | ... | ... | ... |  |
| P 80-53 | Lom (Danube, 743.0 km) | ... | ... | ... | ... | ... | ... | ... |  |
| P 80-54 | Turnu Magurele (Danube, 597.0 km) | x |  |  | ... | ... | ... | x |  |
| P 80-55 | Svistov (Danube, 554.0 km) | ... | ... | ... | ... | ... | ... | ... |  |
| P 80-56 | Roussse (Danube, 495.0 km) | ... | ... | ... | ... | ... | ... | ... |  |
| P 80-57 | Giurgiu (Danube, 493.0 km) | x |  |  | - | - | x | x |  |
| P 80-58 | Oltenita (Danube, 430.0 km) | x |  |  | - | - | - | x |  |
| P 80-59 | Calarasi (Danube, 370.5 km) | x |  |  | - | - | x | x |  |
| P 80-60 | Braila (Danube, 164.0-172.0 km) |  | x |  | - | - | - | x |  |
| P 80-61 | Galati (Danube, 157.0-145.4 km) |  |  | x | - | - | x | x |  |
| P 80-62 | Giurgiulesti (Danube, 133.0 km) | ... | ... | ... | ... | ... | ... | ... | Under construction |
| P 80-63 | Reni (Danube, 128.0 km) |  |  | x | x | x | x | x | General and bulk cargo, oil products |
| P 80-64 | Tulcea (Danube, 73.5-70.0 km) | x |  |  | - | - | - | x |  |
| P 80-04-01 | Port autonome de Paris : |  |  | x | x | x | x | x | Agriculture products, fuels, construction materials |
|  | Gennevilliers (Seine, 194.7 km) |  |  |  |  |  |  |  |  |
|  | Bonneuil-Vigneux (Seine, 169.7 km) |  |  |  |  |  |  |  |  |
|  | Evry (Seine, 137.8 km) |  |  |  |  |  |  |  |  |
|  | Melun (Seine, 110.0 km) |  |  |  |  |  |  |  |  |
|  | Limay-Porcheville (Seine, 109.0 km) |  |  |  |  |  |  |  |  |
|  | Montereau (Seine, 67.4 km) |  |  |  |  |  |  |  |  |
|  | Nanterre (Seine, 39.4 km) |  |  |  |  |  |  |  |  |
|  | Bruyères-sur-Oise (Oise, 96.9 km) |  |  |  |  |  |  |  |  |
|  | St. Ouen-l'Aumône (Oise, 119.2 km) |  |  |  |  |  |  |  |  |
|  | Lagny (Marne, 149.8 km) |  |  |  |  |  |  |  |  |
| P 80-06-01 | Dillingen (Saar, 59.0 km) |  | x |  | x | x | x | x |  |
| P 80-08-01 | Osijek (Drava, 14.0 km) |  | x |  | x | x | - | x |  |
| P 80-01-01 | Szeged (Tisza, 170.0 km) | x |  |  | … | … | … | x |  |
| P 80-01-02 | Senta (Tisza, 122.0 km) 3/ | x |  |  | x |  |  | x |  |
| P 80-14-01 | Cernavoda (Danube-Black Sea Canal, 64.0 km) | x |  |  | - | - | x | x |  |
| P 80-14-02 | Medgidia (Danube-Black Sea Canal, 37.5 km) |  | x |  | - | - | - | x |  |
| P 80-14-02bis | Basarabi (Danube-Black Sea Canal, 25.0 km) | x |  |  | - | - | - | - |  |
| P 80-14-03 | Constanta (Danube-Black Sea Canal, 0.0 km) |  |  | x | x | x | x | x |  |
| P 80-09-01 | Ismail (Danube-Kilia Arm, 93.0 km) |  | x |  | x | x | - | x | General and bulk cargo |
| P 80-09-02 | Kilia (Danube-Kilia Arm, 47.0 km) | x |  |  | x | - | - | - | General cargo |
| P 80-09-03 | Oust-Dunajsk (Danube-Kilia Arm, 0 km) |  |  | x | x | x | - | - | General and bulk cargo |
| P 81-01 | Komarno (Vah, 0.0 km) 3/ |  | x |  | x | x | - | x |  |
| P 81-02 | Sala (Vah, 54.4 - 54.8 km) 3/ | x |  |  |  |  |  | x |  |
| P 81-03 | Sered (Vah, 73.8 - 74.3 km) 3/ | x |  |  | x | x | x | x |  |
| P 81-04 | Hlohovec (Vah, 102.5 - 103.0 km) 3/ | x |  |  |  |  | x | x |  |
| P 81-05 | Piestany (Vah, 124.4 - 124.7 km) 3/ | x |  |  |  |  |  |  |  |
| P 81-06 | Nove mesto nad Vahom (Vah, 137.4 - 137.7 km) 3/ | x |  |  |  |  |  | x |  |
| P 81-07 | Trencin (Vah, 158.5-159.0 km) 3/ | x |  |  |  |  |  | x |  |
| P 81-08 | Dubnica (Vah, 168.1-168.5 km) 3/ | x |  |  | x | x | x | x |  |
| P 81-09 | Puchov (Vah, 192.4-192.9 km) 3/ | x |  |  |  |  | x | x |  |
| P 81-10 | Povazska Bystrica (Vah, 210.8-211.2 km) 3/ | x |  |  |  |  |  | x |  |
| P 81-11 | Zilina (Vah, 242.0-243.0 km) 3/ | x |  |  | x | x | x | x |  |
| P 81-12 | Cadca (Vah-Oder Link, ... km) 3/6/ | x |  |  |  |  | x | x |  |
| P 90-01 | Taganrog (Taganrog Bay) | … | … | … | … | … | … | … |  |
| P 90-02 | Eysk (Taganrog Bay) | … | … | … | … | … | … | … |  |
| P 90-03 | Azov (Don, 3168.0 km) 5/ | x |  |  | x | - | - | x | General cargoes, timber, construction materials, ore, dross |
| P 90-04 | Rostov (Don, 3134.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal, dross |
| P 90-05 | Oust-Donetsk (Don, 2997.0 km) 5/ |  | x |  | x | - | - | x | General cargoes, timber, construction materials, coal, ore |
| P 90-03-01 | Belgorod Dnestrovskiy (mouth of the Dnestr River) | … | … | … | … | … | … | … |  |
| P 90-03-02 | Bender (Nistru, 228.0 km) | x |  |  | - | - | - | x | Dry bulk and general cargoes |
| P 91-01 | Milano Terminale (Milano-Po Canal, 0.0 km) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-02 | Lodi (Milano-Po Canal, 20.0 km from Milano Terminale) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-03 | Pizzighetone (Milano-Po Canal, 40.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-04 | Cremona (Milano-Po Canal, 55.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-05 | Emilia Centrale (Milano-Po Canal, 20.0 km from Milano Terminale) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-06 | Ferrara (Po, 200.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-07 | Adria (Veneta Lateral Waterway, 265.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-08 | Chioggia (Veneta Lateral Waterway, 285.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-09 | Marghera (Veneta Lateral Waterway, 300.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-10 | Nogaro (Veneta Lateral Waterway, 355.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-11 | Monfalcone (Veneta Lateral Waterway, 410.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-12 | Trieste (Adriatic Sea) | … | … | … | … | … | … | … |  |
| P 91-02-01 | Piacenza (Po, 35.0 km from Conca di Cremona) | … | … | … | … | … | … | … |  |
| P 91-02-02 | Pavia (Ticino, 98.0 km from Conca di Cremona) | … | … | … | … | … | … | … |  |
| P 91-02-03 | Casale Monferrato (Po, 183.0 km from Conca di Cremona) | … | … | … | … | … | … | … |  |
| P 91-04-01 | Garibaldi (Ferrara Waterway, 80.0 km from Ferrara) | … | … | … | … | … | … | … |  |
| P 91-06-01 | Porto Tolle (Po Grande, 260.0 km from Milano Terminale) | … | … | … | … | … | … | … |  |
| P 91-01-01 | Mantova (Fissero-Tartaro-Canalbianco Waterway, 0.0 km) | … | … | … | … | … | … | … |  |
| P 91-01-02 | Ostiglia (Fissero-Tartaro-Canalbianco Waterway, 30.0 km) | … | … | … | … | … | … | … |  |
| P 91-01-03 | Legnago (Fissero-Tartaro-Canalbianco Waterway, 65.0m) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-01-04 | Rovigo (Fissero-Tartaro-Canalbianco Waterway, 140.0 km) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-01-04 | Rovigo (Fissero-Tartaro-Canalbianco Waterway, 140.0 km) | … | … | … | … | … | … | … | Under construction or planned |
| P 91-01-05 | Conca di Volta Grimana (Fissero-Tartaro-Canalbianco Waterway, 170.0 km) | … | … | … | … | … | … | … |  |

##### Footnotes to Table 3

1/	Necessary development is envisaged.

2/	After the construction of a new link Gent-Zeebrugge (E 07).

3/	This new E port is expected to be introduced into the AGN Agreement through the amendment procedure under way.

4/	Distances to ports on the River Elbe are measured: in Germany - from the Czech/German State border; in the Czech Republic - from the junction of the rivers Elbe and Vltava at Mëlník.

5/	Distance from Moskva Southern Port.

6/	New port to be built.

*      *      *

INLAND WATERWAYS ON INTERNATIONAL IMPORTANCE

in conformity with Annex I of the European Agreement

on Main Inland Waterways of International Importance (AGN) of 19 January 1996.

# Footnotes

*/ 	This link is not mentioned in the AGN Agreement and its inclusion into the Inventory has been suggested by the Government of Belgium.

**/ 	The Government of Belgium informed the secretariat that according to the Flemish Region E 05-04 should be limited to the Bovenzeeschelde - Aalst section and should not include the rest of the Dender and the Blaton - Ath Canal as provided for in the AGN Agreement.

*/ 	The secretariat has been informed by the Government of France that the project concerning the Rhône - Rhine Canal (E 10) had been abandoned.

*/ 	Project is under study and is expected to be carried out after 2006.

**/ 	This new E waterway is expected to be included into the AGN through the amendment procedure under way.

***/ 	The project is under study and is expected to be carried out in 2005-2019.

****/ 	The realization of this project is conditional upon agreement between the Governments of the Netherlands and Belgium.

*/ 	The construction of a second parallel lock is envisaged with a depth at sill of 4.00 m.

**/ 	Due to the lowering during recent years of the level of the lower pond of the Gorodetski Lock by 90 cm the water depth at sill of 3.50 m can only be ensured for 2-3 hours a day.  Study is currently under way aimed at step-by-step improvement of navigational conditions on the lower pond.

*/ 	This new E waterway is expected to be included into the AGN through the amendment procedure under way.