INF.59

Original document TRANS/WP.15/AC.1/2005/68 (Secretariat)

Carriage in a transport chain including maritime or air carriage

Proposed changes:

Add a new paragraph 1.1.4.2.3 to read:

“Packages, which are in conformity with the provisions of chapter 3.4 Limited Quantities, other than 3.4.7, of the IMDG Code or with the provisions of Part 1 chapter 2.4 Excepted Quantities or Part 3 chapter 4 Limited Quantities of the ICAO Technical Instructions  are not subject to RID/ADR/ADN before or after maritime or air carriage.

Packages, which are in conformity with the provisions of chapter 3.4.7 of the IMDG Code and which are in vehicles, wagons or containers, marked and placarded in accordance with chapter 5.3 of the IMDG Code, are not subject to RID/ADR/ADN before or after maritime carriage.

In addition, other provisions of the RID/ADR/ADN do not apply.”