| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/2006/17 4 August 2006 ENGLISH Original: FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Eighty-first session
Geneva, 25-27 October 2006
Agenda item 7

# ANY OTHER BUSINESS

## Application of sub-section 1.8.5.2

## Transmitted by the Government of Belgium

1.	Accident at the port of Antwerp, 4 March 2004

2.	–	Tractor + semi-trailer chassis;

- 8,000-litre tank container transporting liquid bromine (UN No. 1744), density 3.1;

- Filled to 90 per cent of capacity.

3.	Circumstances:

- Vehicle became unstable in 90º bend (at speed of 32 km/h);

- Bolts attaching container to chassis tore off;

- Protective cap over top-mounted loading/unloading hatches unable to withstand impact.

GE.06-24596  (E)

4.	Consequences:

- Discharge of bromine through hatches and loss of about 6,000 litres;

- Evacuation of significant number of persons;

- Closure of road network and complete stoppage of port traffic;

- Soil pollution.

5.	Cause of accident:

- Excessive speed of vehicle (32 km/h);

- Use of a semi-trailer with two axles and floor height of 1.40 m.

6.	Comparative calculations of the stability of semi-trailers with two and three axles were
	performed by a Belgian manufacturer under the following conditions:

- Identical floor height;

- Fitted with identical 8,000-litre lead-lined tank container;

- Loaded with 19,120 kg of bromine (UN No. 1744), density 3.1, equivalent to a load of 6,000 kg (tare weight of container) + 19,120 kg of bromine or 25,120 kg in total.

The results indicated that:

(1)	The centre of gravity of the loaded semi-trailer shifted from 2,006 mm (two axles) to 1,943 mm (three axles) and the lateral stability, as per Rule 111, from 0.375 g (two axles) to 0.448 g (three axles);

(2)	When semi-trailer with three axles is filled with 23,560 kg of bromine (to 95 per cent of maximum capacity), centre of gravity is 1,964 mm and lateral stability is 0.442 g (these critical values offer greater security than corresponding values for two axles).

7.	Proposed measures:

- Use of a more stable container platform (maximum height + 1.10 m, three axles);

- Special training for drivers transporting high-density liquids.

-----