| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/112 13 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

item 4.2.6. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 3 TO THE

06 SERIES OF AMENDMENTS TO REGULATION No. 14

(Safety belt anchorages)

Transmitted by the Working Party on Passive Safety (GRSP)

Note:  The text reproduced below was adopted by GRSP at its thirty-ninth session.  It is based on ECE/TRANS/WP.29/GRSP/2006/8, not amended.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRSP/39, para. 37).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

Paragraph 1., amend to read:

"1.	SCOPE

This Regulation applies to:

(a)	Vehicles of categories M and N 1/ with regard to their anchorages for safety belts intended for adult occupants of forward-facing or rearward-facing seats.

(b)	Vehicles of categories M1 and N1 with regard to their ISOFIX anchorage systems and their ISOFIX top tether anchorages intended for child restraint systems.

___________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of vehicles (R.E.3), document TRANS/WP.29/78/Rev.1/Amend.2, as last amended by Amendment 4."

Paragraph 5.3.1., amend to read (inserting also a reference to footnote 1/):

"5.3.1.	Any vehicle in categories M and N (except those vehicles of categories M2 or M3 which belong to Classes I, II or A 1/) shall be equipped with safety-belt anchorages which satisfy the requirements of this Regulation.

Vehicles of category M1 shall be equipped with ISOFIX anchorage systems, which satisfy the requirements of this Regulation in accordance with paragraph 5.3.9.

N1 vehicles fitted with ISOFIX anchorages have also to comply with the provisions of this Regulation.

___________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of vehicles (R.E.3), document TRANS/WP.29/78/Rev.1/Amend.2, as last amended by Amendment 4."

- - - - -