| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/82 17 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.17. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 28 TO THE 03 SERIES OF AMENDMENTS

TO REGULATION No. 37

(Filament lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-sixth session.  It is based on ECE/TRANS/WP.29/GRPE/2006/11, as amended by para. 8 of the report.  It is submitted to WP.29 and AC.1 for consideration and vote (ECE/TRANS/WP.29/GRE/56, paras. 8 and 9).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

Text of the Regulation,

Insert new paragraphs 8.3. and 8.4., to read:

"8.3.	As from 12 months after the entry into force of the Supplement 28 to the 03 series of amendments to Regulation No. 37, no filament lamps of the categories R2, S1 and C21W shall be used in lamps for type approval purposes.

8.4	However, Contracting Parties applying this Regulation may continue to grant approvals for lamps where filament lamps of categories R2, S1 and C21W are used, provided that these lamps are intended as replacement parts for installation on vehicles in use."

Annex 1,

The list of categories of filament lamps and their sheets, amend to read:

"….

|  | Category |  | Sheet number(s) |  |
| --- | --- | --- | --- | --- |
|  | … |  |  |  |
|  | PX24W | **/ | P24W/1 to 3 |  |
|  |  | ****/ |  |  |
|  | R2 | *****/ | R2/1 to 3 |  |
|  | S1 | *****/ | S1/S2/1 to 2 |  |
|  | S2 |  | S1/S2/1 to 2 |  |
|  | S3 |  | S3/1 |  |
|  | only for signalling lamps: |  |  |
|  | C5W |  | C5W/1 |  |
|  | C21W | *****/ | C21W/1 to 2 |  |
|  | H6W |  | H6W/1 |  |
|  | …. " |  |  |  |

Insert a new footnote *****/, to read:

"*****/	For replacement purposes only (see transitional provisions in paragraphs 8.3 and 8.4."

Sheet R2/1, delete the note after the footnote 5/.

- - - - -