| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRSG/2006/32 7 August 2006 Original: ENGLISH ENGLISH AND FRENCH ONLY |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

Ninety-first session

Geneva, 17-20 October 2006

Item 1.2.4. of the provisional agenda

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 107

(M2 and M3 vehicles)

Submitted by the experts from Sweden and the International Organization of

Motor Vehicle Manufacturers (OICA)

Note:	The text reproduced below was prepared by the experts from Sweden and OICA in order to introduce into the Regulation provisions for service-door lighting.  The proposal consolidates and supersedes TRANS/WP.29/GRSG/2005/16 and informal documents Nos. GRSG-90-12 and GRSG-90-29, distributed during the ninetieth GRSG session (ECE/TRANS/WP.29/GRSG/69, para. 16).  The modifications to the current text of the Regulation are marked in bold characters.

A.	PROPOSAL

Text of the Regulation,

Insert a new paragraph 2.40., to read:

"2.40.	"Service-door lighting" means a lighting device(s) of the vehicle designed to illuminate the exterior vicinity of service doors and wheels."

Annex 3,

Insert new paragraphs 7.6.12. to 7.6.12.2.5., to read:

"7.6.12.	Service-door lighting

7.6.12.1.	Service-door lighting may be provided to illuminate the flat, horizontal portion of the ground defined in paragraph 7.6.12.2.3. so as to enable the presence of a passenger within this portion of the ground to be detected by the driver from his seat.

7.6.12.2.	Service-door lighting, if fitted, shall be of white colour and:

7.6.12.2.1.	be placed adjacent to at least any service door for which the driver's direct view is not adequate;

7.6.12.2.2.	if the lower edge of the lighting device is less than 2 m from the ground, not project more than 50 mm beyond the overall width of the vehicle measured without this device;

7.6.12.2.3.	illuminate a flat, horizontal portion of the ground having a width of 2 m measured from a plane parallel to the median longitudinal vertical plane of the vehicle which passes through the outermost point of the closed service door and over a length extending from a transverse plane which passes through the foremost edge of the closed service door to a transverse plane passing through the centre line of the foremost wheels situated to the rear of the service door, or, in the case where there are no such wheels, to a transverse plane passing through the rear of the vehicle;

7.6.12.2.4.	have limited dazzle outside a zone on the ground having a maximum width of [5 m] measured from the side of the vehicle and a maximum length limited by a transverse plane passing through the front of the vehicle and a transverse plane passing through the rear of the vehicle, and

7.6.12.2.5.	be installed so that the device can only be switched on when a service door is operated and the vehicle speed does not exceed 5 km/h and is switched off automatically before the vehicle reaches a speed exceeding 5 km/h."

Annex 11,

Paragraph 2.4.2., amend to read:

" .… on guided bus systems, if not retracted,

- service-door lighting devices."

B.	JUSTIFICATION

At the eighty-ninth session, the expert from Sweden presented TRANS/WP.29/GRSG/2005/16, introducing provisions for optional installation of lighting devices that adequately illuminate the area outside the service doors (service-door lighting) of vehicles of categories M2 and M3.  At the ninetieth session, GRSG considered informal documents Nos. GRSG-90-29 (tabled by Sweden) and GRSG-90-12 (tabled by OICA) on the same subject.

This joint proposal by Sweden and OICA supersedes the above-mentioned documents.

- - - - -