| Transmitted by the expert from Japan | Informal Document No. GRE-58-01 58th GRE, 1-5 October 2007 agenda item 15(c) |
| --- | --- |

COMMENTS TO THE DRAFT 03 SERIES OF AMENDMENTS

TO REGULATION No. 10

(Electromagnetic compatibility)

Note: The text reproduced below was prepared by the expert from JASIC.  It refers to ECE/TRANS/WP.29/GRE/2006/51 and ECE/TRANS/WP.29/2007/60

### A. 	PROPOSAL

3.	Application for Approval

Paragraph 3.2.9., to be deleted:

"[3.2.9.]	Components sold as aftermarket equipment and intended for the installation in motor vehicles need no type approval if they are not related to immunity related functions (see paragraph 2.12.).  In this case a declaration must be issued by the manufacturer that the ESA fulfils the requirements of this Regulation and in particular the limits defined in paragraphs 6.5., 6.6., 6.8. and 6.9.

During the transition period, ending on 4 November 2008, the person or legal entity responsible for placing on the market of such a product has to submit all relevant information and/or a sample to a Technical Service which will determine if the equipment is immunity related or not.  The result of the inspection shall be available within three weeks and not require additional testing.  A document according to the example given in Annex 3C shall be issued by the Technical Service within the same period.  In case of doubts and if the Technical Service refuses to issue an attestation according to Annex 3C, the manufacturer has to apply for type approval for his product."

### B. 	JUSTIFICATION

Under the 1958 Agreement, there is no equivalent Regulation to the EU Directives 89/336/EEC and 1995/5/EC and double testing according to other Regulations is not possible.  Japan supports German proposal of the deletion of 3.2.9, ECE/Trans/WP.29/GRE /2006/51 /Amend.1.

Japan is going to resume Reg. No. 10, 03 series of amendments.  It doesn’t need to adapt an additional EMC regulation to aftermarket equipments, which are not related to immunity related functions also in Japan.

Other Editorial Comments

| Clause/ Subclause | Paragraph Figure/Table | Type of comment (General/ Technical/Editorial) | Proposed change | JUSTIFICATION |
| --- | --- | --- | --- | --- |
| 8.3.1 |  | Editorial | 2dB (25%) to 4dB (60%) | 2004/104/EC describes 4dB (60%) |
| Appendix 1 8 Annex 9 1.2.1. Annex 9 4.2.2. |  | Editorial | (TEM) cell (ISO 11452-3, third edition 2001. to 2nd edition) | Editorial |
| Appendix 1 6. Annex 4 4.3. Annex 5 3.3. Annex 6 4.1.1. Annex 7 4.3. Annex 8 4.3. Annex 9 3.2. |  | Editorial | ISO 17025 (first edition 1999) to ISO 17025 (2nd edition) | Ineffective of 1st edition |
| Annex 1 | 6th line | Editorial | Nos.10 to No. 10 | Editorial |
| Annex 1 | Model A Model B | Editorial | 02 2439 to 03 2439 | To prevent from misunderstanding |
| Annex 4 1.2. Annex 4 2.1. Annex 4 3.1. Annex 4 4.2. Annex 4 4.3. Annex 5 1.2. Annex 5 3.3. Annex 7 4.2. Annex 8 4.3. |  | Editorial | CISPR 12(fifth edition 2005) to CISPR 12(sixth edition 2007) | Sixth edition is available |
| Annex 6 4.1. Annex 9 3.1. |  | Editorial | 4,600us to 4 600 us | In general numerical description should follow ISO standard. http://www.physics.nist.gov/Document/sp811.pdf |
| Annex 6 4.1.1. Annex 9 3.2. |  | Editorial | 1,300 MHz to 1 300 MHz | In general numerical description should follow ISO standard. http://www.physics.nist.gov/Document/sp811.pdf |
| Annex 6 4.1.1. Annex 9 3.1. |  | Editorial | 1,800 MHz to 1 800 MHz | In general numerical description should follow ISO standard. http://www.physics.nist.gov/Document/sp811.pdf |
| Annex 8 1.1. |  | Editorial | 8 1.1. Annex 4 to 5 |  |
| Annex 7 4.1. Annex 8 4.1. |  | Editorial | A semi anechoic chamber to ALSE method | Due to CISPR 25 |
| Annex 8 4.1. |  | Editorial | Outdoor test sites to OATS | Due to CISPR 16-1 |
| Annex 9 1.2.1. |  | Editorial | 800 mm Stripline: according to clause 4.5. of this Annex. |  |
| Appendix I 1. |  | Editorial | CISPR 12 "Vehicles, boats, and internal combustion engine - Radio disturbance characteristics - Limits and methods of measurement for the protection of off-board receivers", sixth edition 2007. |  |
| Appendix I 5. |  | Editorial | ISO 7637-2 "Road vehicles - Electrical disturbance from conduction and coupling - Part 2: Electrical transient conduction along supply lines only (deleted)", second edition 2004. |  |
| Appendix I 7. |  | Editorial | ISO 11451 " Road vehicles - Vehicle test methods for electrical disturbances from narrowband radiated electromagnetic energy -": Part 1: General principles and terminology (ISO 11451-1, third edition 2005); Part 2: Off-vehicle radiation source (ISO 11451-2, third edition 2005); Part 4: Bulk current injection (BCI) (ISO 11451-4, second edition 2006). | Second edition of Part 4 has published in 2006. |

- - - - -