Proposal for amendments to ECE/TRANS/WP.29/GRRF/2008/19

Paragraph 6.5.1., amend to read:

"6.5.1.	After curing, whilst a degree of heat is retained in a tyre, each retreaded tyre shall be examined to ensure that it is free from any apparent defects.  During or after retreading the tyre shall be inflated to at least 150 kPa (1.5 bar) for examination.  When the tyre presents a visible defect, it has to be subjected to a specific examination to determine the appropriate action on the tyre.  Other methods more adapted than visual inspection which do not require tyre inflation can also be used with the agreement of the approval authority.  Where there is any apparent defect in the profile of the tyre (e.g. blister, depression, etc.) the tyre shall be specifically examined to determine the cause of this defect."

- - - - -