| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/50 7 April 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-eighth session

Geneva, 23 - 26 June 2009

Item 4.2.2 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 2 to Revision 3 to Regulation No. 12

(Steering wheel)

Submitted by the Working Party on Passive Safety (/

The text reproduced below was adopted by the Working Party on Passive Safety (GRSP) at its forty-fourth session.  It is based on ECE/TRANS/WP.29/GRSP/2008/26, proposal A1, as amended by Annex IV to the report.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRSP/44, para. 52).

Annex 3,

Paragraph 2.2., amend to read:

"2.2.	Barrier

The barrier shall consist of a block of reinforced concrete not less than 3 m wide in front and not less than 1.5 m high.  The barrier shall be of such thickness that it weighs at least 70 metric tons.  The front face shall be flat, vertical and perpendicular to the axis of the run-up track.  It shall be covered with plywood boards 20 ± 2 mm thick, in good condition.  A structure on a steel plate at least 25 mm thick may be placed between the plywood board and the barrier.  A barrier with different characteristics may likewise be used, provided that the area of the impact surface is greater than the frontal crash area of the vehicle being tested and provided that it gives equivalent results."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.