| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRE/2009/37 14 July 2009 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-second session

Geneva, 6 - 9 October 2009

Item 5(e) of the provisional agenda

COLLECTIVE AMENDMENTS

Regulations Nos. 7 and 48

Proposal for Supplement 5 to the 04 series of amendments to Regulation No. 48

Submitted by the expert from France (/

The text reproduced below was prepared by the expert from France in order to ensure consistency between Regulations Nos. 7 and 48 as regards the end-outline marker lamps geometric visibility.  The proposal is based on a document without symbol (informal document No. GRE-61-39), distributed during the sixty-first session of the Working Party on Lighting and Light-Signalling (GRE) (see report ECE/TRANS/WP.29/GRE/61, para. 17).  The modifications to the current text of the Regulation No. 48, including Supplement 3 to the 04 series of amendments, are marked in bold characters.

A. 	PROPOSAL

Paragraph 6.13.1., amend to read:

"6.13.1. 	Presence

Devices of A or AM categories (visible from the front), and devices of R, R1, R2, RM1 or RM2 Categories (visible from the rear): 	Mandatory on vehicles exceeding

2.10 m in width.  Optional on vehicles between 1.80 and 2.10 m in width. On chassis-cabs the rear end-outline marker lamps are optional."

B. 	JUSTIFICATION

This proposal aims at ensuring consistency between Regulations Nos. 7 and 48 as regards the end-outline marker lamps geometric visibility.

A combined proposal introduces new categories of lamps in Regulation No. 7 (AM for front end-outline marker lamps, RM1 and RM2 for rear end-outline marker lamps), with a geometric visibility consistent with Regulation No. 48.

This proposal refers to the new categories of lamps, and introduces also an editorial correction in order to mention category A lamps as possible lamps for front end-outline marker lamps.

- - - - -

# Footnotes

(/  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.